## Slide 1: Linac design as the new baseline
C. Meng, Jingru Zhang, Xiaoping Li
on behalf of CEPC AP group, IHEP
环形正负电子对撞机
Circular Electron Positron Collider
CEPC DAY 2021-8

## Slide 2: Outline
Introduction
Progress on CEPC Linac design
Summary

## Slide 3: Introduction
CEPC as a Higgs (W, Z) Factory
  ~100 km
CEPC layout
  20 GeV injector - Linac
  Full energy Booster
  Collider
  Transport lines
Linac design
  Many versions from 2016.4 to 2021.8
  High Availability and Reliability
CEPC layout

## Slide 4: Introduction
Linac evolution
Meet the design requirements of Booster: Energy/Emittance
Pre-CDR
CDR
TDR

## Slide 5: Introduction
Baseline scheme
  20 GeV
    Low magnetic field & large magnetic field range
    C-band
      Higher gradient  Shorter linac tunnel length
      Small aperture & Strong wakefield
  10 nm
    High luminosity
  100 Hz
    Injection efficiency
    High luminosity Z need faster injection process
      200 Hz
      100 Hz & two-bunch-per-pulse
      200 Hz & two-bunch-per-pulse (?)
Baseline scheme
Parameter | Symbol | Unit | Baseline
e- /e+ beam energy | Ee-/Ee+ | GeV | 20
Repetition rate | frep | Hz | 100
e- /e+ bunch population | Ne-/Ne+ | ×1010 | 0.94(1.88)
 |  | nC | 1.5 (3)
Energy spread (e- /e+ ) | σE |  | 1.5×10-3
Emittance (e- /e+ ) | εr | nm | 10
Parameter | Unit | S-band | C-band
Frequency | MHz | 2860 | 5720
Length | m | 3.1 | 1.8
Cavity mode |  | 2π/3 | 3π/4
Aperture diameter | mm | 20~24 | 11.8~16
Gradient | MV/m | 21 | 45
D. Wang ,Problems and considerations about the timing & bunch pattern

## Slide 6: Introduction
EBTL is in vertical plane with 1.2 m separation
  Avoid interference with energy analyzing station, transport lines between the Linac and damping ring, waveguide and positron source
  Reduce the tunnel width
Accelerating structure
  S-band: FAS/PSPAS/SAS
  C-band: TAS
Linac layout

## Slide 7: Linac design
Electron Linac
  EBTL
Positron Linac
  ESBS
  FAS
  PSPAS
  SAS
  TAS
Layout

## Slide 8: Linac design
Thermionic electron gun
  Bunch charge: 11nC
  Bunch length(FWHM): 1ns
Sub-harmonic pre-buncher
  143 MHz
  572 MHz
Buncher & A0
  2860 MHz
Focusing structure
  Solenoid
Emittance
  <100 mm-mrad (Norm.Rms)
Transmission
  >90%
Electron source & Bunching system

## Slide 9: Linac design
C-band accelerating structure is introduced in the TAS
  RF frequency: 5720 MHz
  Bunch length: 1mm  0.5mm
Bunch compressor
  First order
  Second order
Bunch compressor
@Andy Wolski

## Slide 10: Linac design
Bunch compressor
Bunch compressor
 |  | Value | Units
Initial rms bunch length |  | 0.923 | mm
Initial rms energy spread |  | 0.235% | 
Final rms bunch length |  |  | mm
Initial energy | E0 | 1.1 | GeV
 |  | Value | Units
Initial rms bunch length |  | 0.923 | mm
Initial rms energy spread |  | 0.235% | 
Final rms bunch length |  |  | mm
Initial energy | E0 | 1.1 | GeV

## Slide 11: Linac design
Bunch compressor
  Accelerating structure
    Voltage=72MV100MV
    Phase=-10.8°0 °
  Chicane
    Angle: 10°
    a= 2.65m
Bunch compressor

## Slide 12: Linac design
Lattice design
  FAS
    4*(Triplet+2 S-band)
    (2+1+1) * (Triplet+4 S-band)
    Triplet for matching
    (13+2) *(Triplet + 4 S-band)
    Triplet for matching on Target
  ETBL
    B+3Q+B
    10* Triplet
    B+3Q+B
  TAS
    Triplet+2 S-band acc for chirp
    Chicane type bunch compressor
    Triplet for matching
    10*(Triplet + 2 C-band)
    Triplet for matching (AM)
    12*(Triplet + 4 C-band)
    6+2 *(Triplet + 8 C-band)
    Triplet for matching
    8+1 **(Triplet + 8 C-band)
Electron linac

## Slide 13: Linac design
Simulation results( including Wakefield & CSR)
Electron linac
Parameter | Unit | Baseline | Electron
e- /e+ beam energy | GeV | 20 | 20.38
Repetition rate | Hz | 100 | 100
e- /e+ bunch population | ×1010 | 0.94(1.88) | 1.88
 | nC | 1.5 (3) | 3
Energy spread (e- /e+ ) |  | 1.5×10-3 | 1.3×10-3
Emittance (e- /e+ ) | nm | 10 | 2.5

## Slide 14: Linac design
Emittance growth
  Wakefield
  Error study is still in progress
    BPM resolution ~ 10µm
    Wakefield free steering(WFS)
Electron linac

## Slide 15: Linac design
Positron source
  Target (Conventional)
    tungsten@15 mm
    Beam size: 0.5 mm
AMD (Adiabatic Matching Device)
  Length: 100mm
  Aperture: 8mm26mm
  Magnetic field: (5.5T0T) + 0.5T
Capture & Pre-accelerating structure
  Length:2 m
  Aperture: 25 mm
  Gradient: 22 MV/m
Chicane
  Wasted electron separation
PSPAS
Positron source | Unit | Requirement | Simulation results
e- beam energy on the target | GeV | 4 | 
e- bunch charge on the target | nC | 10 | 
e+ bunch charge | nC | ≥3 | ~5.5
e+ Energy | MeV | ≥200 | 250
e+ Norm. RMS emittance | mm-mrad | ≤2400 | 2370

## Slide 16: Linac design
Damping Ring
  Norm. Rms. Emittance: 200 mm-mrad
  Energy: 1.1 GeV
  Energy spread: 0.5% (chirped)
  Bunch length: 0.7mm
Positron Linac
@ D. Wang

## Slide 17: Linac design
Simulation results( including Wakefield & CSR)
Positron Linac
Parameter | Unit | Baseline | Electron | Positron
e- /e+ beam energy | GeV | 20 | 20.38 | 20.37
Repetition rate | Hz | 100 | 100 | 100
e- /e+ bunch population | ×1010 | 0.94(1.88) | 1.88 | 1.88
 | nC | 1.5 (3) | 3 | 3
Energy spread (e- /e+ ) |  | 1.5×10-3 | 1.3×10-3 | 1.3×10-3
Emittance (e- /e+ ) | nm | 10 | 2.5 | 5.2

## Slide 18: Linac design
Linac
  200 Hz
  100 Hz & two-bunch-per-pulse
    ESBS(electron source and bunching system)
    RF gun system (L-band, high bunch charge for positron production)
      Electron gun cathode material Vs. Laser system
  200 Hz & two-bunch-per-pulse (?)
Two bunch acceleration
  SLED
    Top-flat type
  Two bunch orbit correction
  Energy spread
    Energy spread compressor at Linac exit
High luminosity Z

## Slide 19: Summary
The new baseline scheme of the Linac was determined at May 2021
The Linac energy is increased to 20 GeV to ease the booster magnet design difficulties (low field at injection energy and large magnetic field range) and the emittance is decreased to 10 nm for high luminosity Higgs scheme.
The C-band accelerating structure is used from 1.1 GeV to 20 GeV to save cost, however more difficulties in design need to be solved.
The lattice design and dynamic simulation have been finished, until now, the design can meet the requirements of booster.
Error study is still in progress, which requires careful consideration and simulation, need smaller alignment error and BPM resolution.
Thank you for your attention!

## Slide 20
Wakefield