## Slide 1: Problems and considerations about the timing & bunch pattern
Control group: Ge Lei, Gang Li
Linac group: Jingru Zhang, Cai Meng, Zusheng Zhou, Xiaoping Li
Injection group: Jinhui Chen
RF group: Jiyuan Zhai
AP group: Dou Wang, Xiaohao Cui, Meng Li, Jie Gao, Tianmu Xin, Chenghui Yu

## Slide 2: CEPC high luminosity Parameters
 | tt | Higgs | W | Z | 
Number of IPs | 2 |  |  |  | 
Energy (GeV) | 180 | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  |  | 
SR loss/turn (GeV) | 8.53 | 1.80 | 0.34 | 0.036 | 
Half crossing angle (mrad) | 16.5 |  |  |  | 
Piwinski angle | 1.16 | 4.30 | 7.25 | 24.9 | 
Ne/bunch (1010) | 20.1 | 14.5 | 15.0 | 15.2 | 
Bunch number (bunch spacing) | 37 (4.2s) | 240(0.64us) | 1230 (0.27s) | 3816 (86ns) | 11520 (25ns)
Beam current (mA) | 3.5 | 16.7 | 88.6 | 278.8 | 839.9
SR power /beam (MW) | 30 | 30 | 30 | 10 | 30
Bending radius (km) | 10.7 |  |  |  | 
Phase advance of arc cell | 90/90 | 90/90 | 60/60 | 60/60 | 
Momentum compaction (10-5) | 0.71 | 0.71 | 1.43 | 1.43 | 
IP x/y (m) | 1.0/0.0027 | 0.33/0.001 | 0.18/0.001 | 0.15/0.001 | 
Emittance x/y (nm) | 1.45/0.0047 | 0.64/0.0014 | 0.84/0.00187 | 0.27/0.00135 | 
Transverse IP (um) | 37.9/0.11 | 15.0/0.037 | 12.3/0.043 | 6.36/0.037 | 
x/y/IP | 0.076/0.106 | 0.021/0.115 | 0.0096/0.11 | 0.0046/0.131 | 
VRF (GV) | 9.52 | 2.20 | 0.62 | 0.1 | 
f RF (MHz) (harmonic) | 650 (216816) | 650 (216816) | 650 (216816) | 650 (216816) | 
Nature bunch length z (mm) | 2.23 | 2.3 | 2.7 | 2.75 | 
Bunch length z (mm) | 2.66 | 3.9 | 5.4 | 9.6 | 
HOM power/cavity (kw) | 0.45 (5cell) | 0.47 (2cell) | 1.0 (2cell) | 2.0 (2cell) | 3.02 (1cell)
Energy spread (%) | 0.17 | 0.17 | 0.12 | 0.12 | 
Energy acceptance requirement (DA) (%) | 2.0 | 1.7 | 1.3 | 1.3 | 
Energy acceptance by RF (%) | 2.61 | 2.3 | 2.1 | 1.48 | 
Lifetime (hour) | 0.59 | 0.33 | 1.4 | 1.7 | 1.4
L/IP (1034cm-2s-1) | 0.5 | 5.0 | 15.4 | 35.0 | 105.5

## Slide 3: Requirements in collider ring
 | tt | H | W | Z
Energy (GeV) | 180 | 120 | 80 | 45.5
Beam lifetime (min) | 36 | 20 | 80 | 84
Bunch number | 37 | 240 | 1230 | 11520
Bunch population (×1011) | 2.01 | 1.45 | 1.50 | 1.52
Interval for top up* (s) | 65 | 38 | 155 | 153
* Beam current in collider decays by 3%.
Both top up injection and full injection from empty for the collider ring needs to be fulfilled.
Injection & extraction hardware should be compatible for four energy modes.

## Slide 4: Linac
 | tt & H & W | Z
Repetition (Hz) | 100 | 100
Bunch number/pulse | 1 | 2
 | tt & H & W | Z
Repetition (Hz) | 100 | 200
Bunch number/pulse | 1 | 1
Double bunch
200Hz
Lina 200 Hz or double bunch (100Hz) scheme is only needed for Z.

## Slide 5: DR
 | tt | H | W | Z
Circumference (m) | 150 |  |  | 
Energy(GeV) | 1.1 |  |  | 
Store time for a train (ms) | 20 |  |  | 
Number of trains | 2 | 2 | 2 | 2
Number of bunches/trian | 1 | 1 | 1 | 2
Bunch intensity (nC) | 1.1 | 0.9 | 0.85 | 1.0
Injection scheme | Bunch by bunch |  |  | Two by two
Kicker frequency (Hz) | 100 |  |  | 
 | tt | H | W | Z
Circumference (m) | 150 |  |  | 
Energy(GeV) | 1.1 |  |  | 
Store time for a train (ms) | 20 |  |  | 
Number of trains | 2 | 2 | 2 | 4
Number of bunches/trian | 1 | 1 | 1 | 1
Bunch intensity (nC) | 1.1 | 0.9 | 0.85 | 1.0
Injection scheme | Bunch by bunch |  |  | 
Kicker frequency (Hz) | 100 |  |  | 200
Double bunch
200Hz
At each linac RF pulse a train is injected into the DR.
Z-mode is the most challenging operation in terms of charge flux delivered by the injectors.
After 4 bunches are stored, each train which cooled for 20 ms will be extracted and re-injected into the linac. At the same time, a new train will be injected into the DR.
Jinhui Chen, Xiaohao Cui, Dou Wang

## Slide 6: DR
Double bunch
200Hz
Meng Li

## Slide 7: DR
Double bunch
200Hz
Meng Li

## Slide 8: Injection to booster @20GeV ─ tt
 | tt
Energy（GeV） | 20
Bunch number | 37
Bunch seperation（us） | 4.2
Injection scheme | bunch by bunch
Kicker frequency(Hz) | 100
Kicker pules duration (us) | <8.4
Kicker rise up/ fall down (us) | <4.2
Timing delay(us) | 4.2
Injection duration (s) | 0.37
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.

## Slide 9: Injection to booster @20GeV ─ H
 | H
Energy（GeV） | 20
Bunch number | 240
Bunch seperation（us） | 0.647
Injection scheme | bunch by bunch
Kicker frequency(Hz) | 100
Kicker pules duration (us) | <1.29
Kicker rise up/ fall down (us) | <0.647
Timing delay(us) | 0.647
Injection duration (s) | 2.4
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.

## Slide 10: Injection to booster @20GeV ─ W
 | W
Energy（GeV） | 20
Bunch number | 1230
Bunch seperation（us） | 0.2677
Injection scheme | bunch by bunch
Kicker frequency(Hz) | 100
Kicker pules duration (us) | <0.535
Kicker rise up/ fall down (us) | <0.2677
Timing delay(us) | 0.2677
Injection duration (s) | 12.3
The RF system is independent for e- and e+ beam in the collider ring.
Bunches per beam are uniform in the whole ring both for booster and collider.

## Slide 11: Timing problem for Z
f (MHz) | SHB1 | SHB2 | Linac | DR | Pre-booster | booster | collider
CEPC | 143 | 572 | 2860 | 650 | ─ | 1300 | 650
FCC | ─ | ─ | 2855.98 | 400 | 400 | 400 | 400
For CEPC, the common frequency is 13MHz, so the minimum time separation= 76.92ns.
For Z, bunch separation requirement in collider: 20ns~28ns.
If the SHB1&SHB2 is cancelled, the minimum time separation=7.692ns.
@Cai Meng
2020.07.17
Ge Lei, Gang Li

## Slide 12: Luminosity reduction @Z due to timing issue
 | design | reality
Bunch number | 11520 | 6720 (10080?)
Bunch population (×1011) | 1.52 | 1.52
Beam current (mA) | 840 | 490
SR power /beam (MW) | 30 | 17.5
L/IP (1034cm-2s-1) | 105.5 | 61.5(92.3?)
With current Linac design, the minimum bunch separation@Linac = 76.92ns, the minimum bunch separation@ring=38.46ns .
The max bunch number in collider is decreased.  luminosity reduction @Z (42%)
*Bunch separation is limited by the common frequency of collider (650MHz), booster(1.3GHz) and Linac(2860MHz/572MHz/143MHz).
*Subharmonic bunchers are cancelled and the thermionic gun is replaced by RF gun.
@X. H. Cui

## Slide 13: Injection to booster @20GeV ─ Z
 | Z (Linac- 200Hz) | Z (Linac- 2 bunches)
Energy（GeV） | 20 | 
Bunch number/train | 80 | 
Bunch separation（ns） | 23.076 | 
Number of trains | 48 | 
Train separation (us) | 5.11 | 
Injection scheme | bunch by bunch | two by two
Kicker frequency(Hz) | 200 | 100
Kicker pules duration (ns) | <46.15 | <69.23
Flat top (ns) | ─ | 23.1
Kicker rise up/ fall down (ns) | <23.076 | <23.076
Timing delay(us) | 5.11 & 0.023 | 5.11 & 0.046
Injection duration (s) | 19.2 | 
The RF system is independent for e- and e+ beam in the collider ring.
bunches per beam are distributed train by train both in booster and collider.
The number of train in booster is one third of the value in collider.

## Slide 14: Booster ramping
3 cycles/beam
tt
Higgs
W
Z
1 cycles/beam
1 cycles/beam
1 cycles/beam
7.3s
7.3s
0.37s
4.5s
4.5s
2.4s
12.3s
2.7s
2.7s
19.2s
19.2s
19.2s
4.5s
4.5s
2.4s
5s damping
off-axis
on-axis
0.037s
0.24s
1.23s
0.048s
0.37s+7.3s+0.037s+7.3s=15.0s
2.4s+4.5s+5.0s+4.5s=16.4s
12.3s+2.7s+1.23s+2.7s=18.9s
(19.2s+1.6s+0.048s+1.6s)*3=67.34s
Dou Wang, Xiaohao Cui

## Slide 15: Extraction from booster @180GeV ─ tt
 | tt
Energy（GeV） | 180
Bunch number | 37
Bunch seperation（us） | 4.2
Extraction scheme | bunch by bunch
Kicker frequency(Hz) | 1000
Kicker pules duration (us) | <8.4
Kicker rise up/ fall down (us) | <4.2
Timing delay(us) | 4.2
Extraction duration (s) | 0.037
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.

## Slide 16: Extraction from booster @120GeV ─ H
 | H-off axis | H-on axis
Energy（GeV） | 120 | 
Bunch number | 240 | 7*
Bunch seperation（us） | 0.647 | 22.1
Extraction scheme | bunch by bunch | bunch by bunch
Kicker frequency(Hz) | 1000 | 
Kicker pules duration (us) | <1.29 | <1.29
Kicker rise up/ fall down (us) | <0.647 | <0.647
Timing delay(us) | 0.647 | 22.1
Extraction duration (s) | 0.24 | 0.007
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.
* 7 bunches are uniform in the half ring. The bunches which are injected/extracted to/from booster each time can become more than 7 while the total current in booster is getting lower and lower.

## Slide 17: Extraction from booster @80GeV ─ W
 | W
Energy（GeV） | 80
Bunch number | 1230
Bunch seperation（us） | 0.2677
Extraction scheme | bunch by bunch
Kicker frequency(Hz) | 1000
Kicker pules duration (us) | <0.535
Kicker rise up/ fall down (us) | <0.2677
Timing delay(us) | 0.2677
Extraction duration (s) | 1.23
The RF system is independent for e- and e+ beam in the collider ring.
Bunches per beam are uniform in the whole ring both for booster and collider.

## Slide 18: Extraction from booster @45.5GeV ─ Z
 | Z
Energy（GeV） | 45.5
Bunch number/train | 80
Bunch separation（ns） | 23.076
Number of trains | 48
Train separation (us) | 5.11
Extraction scheme | train by train
Kicker frequency(Hz) | 1000
Flat top (us) | 1.83
Kicker pules duration (us) | <12.05
Kicker rise up/ fall down (us) | <5.11
Timing delay(us) | 6.94
Extraction duration (s) | 0.048
The RF system is independent for e- and e+ beam in the collider ring.
bunches per beam are distributed train by train both in booster and collider.
The number of train in booster is one third of the value in collider.

## Slide 19: Injection to collider@180GeV ─ tt
 | tt
Energy（GeV） | 180
Bunch number | 37
Bunch seperation（us） | 4.2
Injection scheme | bunch by bunch
Kicker frequency(Hz) | 1000
Kicker pules duration (us) | <8.4
Kicker rise up/ fall down (us) | <4.2
Timing delay(us) | 4.2
Injection duration (s) | 0.037
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.

## Slide 20: Injection to collider@120GeV ─ H
 | H-off axis | H-on axis
Energy（GeV） | 120 | 
Bunch number | 240 | 7*
Bunch seperation（us） | 0.647 | 22.1
Injection scheme | bunch by bunch | bunch by bunch
Kicker frequency(Hz) | 1000 | 
Kicker pules duration (us) | <1.29 | <1.29
Kicker rise up/ fall down (us) | <0.647 | <0.647
Timing delay(us) | 0.647 | 22.1
Injection duration (s) | 0.24 | 0.007
The RF system is shared by e- and e+ beam in the collider ring.
Bunches per beam are in the half ring both for booster and collider.

## Slide 21: Injection to collider@80GeV ─ W
 | W
Energy（GeV） | 80
Bunch number | 1230
Bunch seperation（us） | 0.2677
Injection scheme | bunch by bunch
Kicker frequency(Hz) | 1000
Kicker pules duration (us) | <0.535
Kicker rise up/ fall down (us) | <0.2677
Timing delay(us) | 0.2677
Injection duration (s) | 1.23
The RF system is independent for e- and e+ beam in the collider ring.
Bunches per beam are uniform in the whole ring both for booster and collider.

## Slide 22: Injection to collider@45.5GeV ─ Z
 | Z
Energy（GeV） | 45.5
Bunch number/train | 80
Bunch separation（ns） | 23.076
Number of trains | 144
Train separation (us) | 0.492
Injection scheme | train by train
Kicker frequency(Hz) | 1000
Flat top (us) | 1.83
Kicker pules duration (us) | <2.81
Kicker rise up/ fall down (us) | <0.49
Timing delay(us) | 6.94 & 2.32
Injection duration (s) | 0.144
The RF system is independent for e- and e+ beam in the collider ring.
bunches per beam are distributed train by train both in booster and collider.
The number of train in booster is one third of the value in collider.

## Slide 23: Requirement of timing system
Choose 130MHz as clock beat  minimum time separation=7.69ns (FPGA clock &EVG/EVR transmission can be realized)
Length of transfer line between DR and Linac: （（N*150+75+104*2-8.3）109/(3*108))/(1000/2860)=integer
Circumference of collider/booster: (L*1000*109/(3*108))/(1000/650)=integer
Length of transfer line between booster and collider: (L*109/(3*108))/(1000/650)=integer
104m 101.65m
252m or 246m
Circumference of damping ring: (L*1000*109/(3*108))/(1000/650)=integer
Gang Li, Ge Lei

## Slide 24: Full injection from empty-tt
Design current in collider is 3.5mA.
Total current in booster limited by RF system: < 0.3mA
Collider lifetime (non-collision): ~2600 hours ─ dominated by Toucheck lifetime
Full injection from empty for each beam  3 min (6 min for two beams)
Collision start after each beam is injected to full current independently.

## Slide 25: Full injection from empty-Higgs
Design current in collider is 16.7mA.
Total current in booster limited by RF system: < 1mA
Collider lifetime (non-collision): ~290 hours ─ dominated by Toucheck lifetime
Full injection from empty for each beam  5 min (10 min for two beams)*
Collision start after each beam is injected to full current independently.
*on-axis injection for collider is assumed

## Slide 26: Full injection from empty-W
Design current in collider is 88.6mA.
Total current in booster limited by RF system: < 4mA
Collider lifetime (non-collision): ~150 hours ─ dominated by Toucheck lifetime
Full injection from empty for each beam  8 min (16 min for two beams)
Collision start after each beam is injected to full current independently.

## Slide 27: Full injection from empty-Z (bootstrapping)
Design current in collider is 840mA.
Total current in booster limited by RF system: < 10 mA (will be increased to 16mA)
Collider lifetime: 19 hours (non-collision), 1.9~1.4 hours (w. collision)*
Bootstrapping from 220mA
Full injection from empty for both beam  2 hours (50min)
Booster threshold: 10mA
Booster threshold: 16mA
*the beam lifetime with collision is related to the current.
Dou Wang, Xiaohao Cui, Yuan Zhang

## Slide 28
Z mode injection (top-up)
Meng Li

## Slide 29
Z mode injection (full injection)
Meng Li

## Slide 30: Summary
The inj./ext. chain and timing structure of CEPC for four energy modes and different injection scheme have been designed with the consideration of clock system, RF frequency choice, bunch pattern, injection hardware and so on.
The problem was found only for Z pole.
The RF frequency is not compatible for Linac and rings according to the requirement of timing system.
The minimum timing separation is relatively large due to small common frequency.  lose filling flexibility
Possible optimization
 | Common frequency | Bunch separation | Luminosity@Z | Filling flexibility
1. Keep current Linac | 13MHz | 38.46ns | 58% | No
2. Cancel SHBs, use RF gun | 130MHz | 23.07ns | 100% | No
3. f(Linac):28602600MHz | 130MHz | 23.07ns | 100% | No
4. New frequency for Linac and rings (hope) |  | 20.00ns,21.54ns,23.07ns,24.62ns,26.15ns, 27.69ns | 100% | Yes
Discussion about timing and filling scheme for Z is continuous.