## Slide 1: CEPC booster and damping ring update
Dou Wang (IHEP)
on behalf of CEPC AP group
The 2nd CEPC International Accelerator Review Committee Meeting, Oct. 11-14, 2021. IHEP.

## Slide 2: outline
Design update for CEPC booster
Summary
Design update for CEPC positron damping ring

## Slide 3: outline
Design update for CEPC booster
Summary
Design update for CEPC positron damping ring

## Slide 4: CEPC injector chain
20 GeV linac provides electron and positron beams for booster.
Top up injection for collider ring ~ 3% current decay
Booster is in the same tunnel as collider ring, above the collider ring, bypass in IR.
Budget for transfer efficiency 90%: 92% for booster + 99% for transport lines.
Beam current threshold in booster is limited by RF system.
Feedback systems (Transverse & longitudinal) are need to damp the instability at low energy.
Injection energy: 20GeV
100km
20GeV
20180GeV

## Slide 5
Collider ring | Higgs (CDR) | Higgs (TDR)
Number of IPs | 2 | 2
Energy (GeV) | 120 | 120
Circumference (km) | 100 | 100
SR loss/turn (GeV) | 1.73 | 1.8
Half crossing angle (mrad) | 16.5 | 
Piwinski angle | 3.48 | 4.30
Ne/bunch (1010) | 15.0 | 14.5
Bunch number | 242 | 240
Beam current (mA) | 17.4 | 16.7
SR power /beam (MW) | 30 | 30
Bending radius (km) | 10.7 | 10.2
Momentum compaction (10-6) | 11.1 | 7.1
IP x/y (m) | 0.36/0.0015 | 0.33/0.001
Emittance x/y (nm) | 1.21/0.0024 | 0.64/0.0013
Transverse IP (um) | 20.9/0.06 | 15.0/0.037
x/y/IP | 0.018/0.109 | 0.021/0.115
VRF (GV) | 2.17 | 2.20
f RF (MHz) (harmonic) | 650 (217500) | 
Nature bunch length z (mm) | 2.72 | 2.3
Bunch length z (mm) | 4.4 | 3.9
Energy spread (%) (SR/BS) | 0.1/0.134 | 0.1/0.17
Energy acceptance requirement (%) | 1.35 | 1.7
Energy acceptance by RF (%) | 2.06 | 2.3
Lifetime due to beamstrahlung (min) | 80 | 40
Lifetime (min) | 25 | 20
F (hour glass) | 0.89 | 0.88
Lmax/IP (1034cm-2s-1) | 2.93 | 5.0
Requirement update for booster
Horizontal DA requirement of collider ring due to injection
X. H. Cui
Booster emittance @120 GeV <1.7nm (3.6nm in CDR)

## Slide 6: Booster TDR optics
TME like structure (cell length=80m)
Interleave sextupole scheme
Emittance@120GeV=1.26nm
D. Wang, C. H. Yu, Y. M. Peng…
Arc cell
Overall idea: uniform distribution for the Q
Combined magnet (B+S) scheme possible
Dispersion sup.
Half ring

## Slide 7
DA results @ 20GeV
Booster energy: 20GeV~180GeV
20GeV: BSCxy=(4xy+5mm)*2
Inj. emittance from Linac:10nm
Energy spread from Linac: 0.16%

## Slide 8
DA results with errors and correction
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | -
Longitudinal shift Z (μm) | 100 | 150 | -
Tilt about X/Y (mrad) | 0.2 | 0.2 | -
Tilt about Z (mrad) | 0.1 | 0.2 | -
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
D. H. Ji
Almost impossible to obtain the initial closed orbit naturally
  Start from sextupole off
Orbit correction (COD)(100 Seeds)
  Response matrix method(RM)
  SVD method
Optics correction(96 Seeds)
  Response matrix method
  LOCO code
  Dispersion corrected

## Slide 9: Beam beam instability for on-axis injection
Collision stability check for on-axis injection scheme at 120GeV
• Emittance X = 1.26nm
• Energy spread = 0.1%
• Bunch length=2.1mm
• Coupling=1.0%
• Emittance X = 0.68nm
• Energy spread = 0.1%
• Bunch length=2.25mm
• Coupling=0.2%
e- (Ne=14×1010)
e+ (Ne=14×1010)
Yuan Zhang

## Slide 10: SR & Sawtooth effect@180GeV
W/O taper
W taper
2 RF stations
Maximum sawtooth orbit: 3 mm
Energy deviation: 1.1%
Emittance growth: ~2.9%
DA reduction due to strong SR
Combined effects of sawtooth and magnets’ errors will be studied:
Taper dipoles in 8 sections
No need to taper the quad and sext
Orbit (optics) correction
D. Wang, D. H. Ji
DA tracking (50 seeds, 100 turns)
DA > requirement (injection)
- DA_X=5x+3mm=7.0mm
- DA_Y=39y+3mm=4.3mm
Sawtooth orbit was corrected by tapering
No DA reduction due to sawtooth orbit

## Slide 11: Dipole reproducibility requirement@20GeV
Increase/decrease the strength of all the dipoles by the same amount.
Evaluate the influence: working point, closed orbit, DA, energy acceptance
Working point should not pass through the lower order resonance
Small shrink for dynamic aperture
Reproducibility requirement for dipoles: ~0.04%
Stability requirement for power supply: ~0.01%
Dipole field error tolerance slightly loser than FODO.
 | original | +0.01% | -0.01% | +0.03% | -0.03% | +0.05% | -0.05%
nux | 321.271 | 321.234 | 321.308 | 321.158 | 321.383 | 321.084 | 321.458
nuy | 117.193 | 117.166 | 117.220 | 117.112 | 117.274 | 117.058 | 117.328
x (um) | 0 | -26 | 26 | -77 | 77 | -130 | 130
DA (%) | 100 | 95 | 100 | 97 | 95 | 97 | 95

## Slide 12: Effect of earthfield @20GeV
~20% vacuum pipe (drift) is exposed in earthfield directly.
treat drifts as week dipole to simulate the effect of earthfield
Assume earthfield: 0.6 gauss (simple model: perpendicular component only )
Working point can be corrected by weaken the dipoles systematically (-0.07%)
Earthfield problem can be solved by global orbit correction.
first turn trajectory
D. H. Ji, D. Wang

## Slide 13: Booster ramping scheme
3 cycles/beam
tt
Higgs
W
Z
1 cycles/beam
1 cycles/beam
1 cycles/beam
7.3s
7.3s
0.37s
4.5s
4.5s
2.4s
12.3s
2.7s
2.7s
19.2s
19.2s
19.2s
4.5s
4.5s
2.4s
5s damping
off-axis
on-axis
0.037s
0.24s
1.23s
0.048s
0.37s+7.3s+0.037s+7.3s=15.0s
2.4s+4.5s+5.0s+4.5s=16.4s
12.3s+2.7s+1.23s+2.7s=18.9s
(19.2s+1.6s+0.048s+1.6s)*3=67.34s
Dou Wang, Xiaohao Cui

## Slide 14
emittance
Beam parameter evolution
Injection emittance: 10nm @20GeV
5s damping time (CDR) for Z can be canceled.
energy
energy spread
bunch length

## Slide 15: RF ramping curve
Different RF ramping curve for each energy mode
Max RF voltage @tt determined by longitudinal quantum lifetime.
s for tt: 0.13
s for Higgs: 0.087
s for W & Z: 0.069
RF: ~ 9 
VRF (180GeV)=9.3GV
W &Z
Higgs
tt

## Slide 16: Eddy current effect and correction
Max K2=0.000037 (m-3)
Dedicated ramping curve to control the maximum K2.
K2 reaches max at 30GeV.
Dynamic chromaticity correction is not used.
- Sextupole field is attached to dipole
Al beam pipe (round shape)
- inner diameter: 55mm, thickness: 2mm
Analytical estimation for eddy effect*
*Yuan Chen et al., Analytical expression development for eddy ﬁeld and the beam dynamics eﬀect on the CEPC booster, IJMPA, Vol. 36, No. 22 (2021) 2142010

## Slide 17
Lattice | FODO 0 （CDR） | FODO | TME (combine magnets)
Emittance X (nm) @120GeV | 3.57 | 1.29 | 1.26
Momentum compaction (×10-5) | 2.44 | 1.18 | 1.12
Tunes | [263.201/261.219] | [353.180/353.280] | [321.271/117.193]
Quad amount | 2110 | 2816 | 3458
Quad Strength (K1L rms） | 0.0383 | 0.0407 | 0.0259
Sext amount | 512 | 896 | 0
Sexts Strength (K2L rms) | 0.179 | 0.4091 | 0.0492
H Corrector | 1053 | 1408 | 1218
V Corrector | 1054 | 1408 | 2240
BPM | 2108 | 2816 | 3458
Optics parameter comparison
Magnets’ cost of TME is lower than FODO
No independent sextupole for TME
Quadrupole strength of TME is lower
D. H. Ji, W. Kang

## Slide 18: Booster TDR parameters
Injection
Extraction
*Diameter of beam pipe is 55mm for re-injection with high single bunch current @120GeV.
Injection energy: 10GeV  20GeV
Max energy: 120GeV  180GeV
Lower emittance ─ new lattice (TME)

## Slide 19: outline
Design update for CEPC booster
Summary
Design update for CEPC positron damping ring

## Slide 20: Damping ring layout (CDR)
Linac repetition: 100Hz
Only for positron beam
Storage time: 20 ms
Emittance (norm.): 2500 530 mm.mrad
e +

## Slide 21: Requirements update for the Damping ring
Emittance
  High luminosity of Higgs (lower emittance collider  lower emittance booster)
    Lower emittance Linac:10nm@20GeV  Norm. RMS emittance is 392mmmrad
    DR emittance requirement: < 200mmmrad
      Keep the margin for emittance growth
        -- high bunch charge
        -- C-band accelerating structure
      Could use C-band accelerating structure just after the Damping Ring (@1.1GeV)
Damping time
100Hz Linac & two-train scheme/200Hz Linac storage time: 20ms
Requirement for damping time: <13ms
Bunch length
  RMS bunch length after DR <1mm
    -- a bunch length compressor was introduced after the DR for electron and positron beam
Cai Meng

## Slide 22: Comparison of damping ring design requirement
 | CDR | TDR | remark
Energy (GeV) | 1.1 | 1.1 | 
Inj. Emittance (mmmrad) | 2500 | 2500 | 
Ext. emittance (mmmrad) | 530 | <200 | 1) Linac lower emittance: 10nm@20GeV, 2)use C band acc. structure as early as possible
Storage time (ms) | 20 | 20 | 
Damping time (ms) | 15 | <13 | 1) Smaller ext. emittance with same storage time
Circumference (m) | 75 | ~150 | 1) Smaller nature emittance for DR
lower emittance collider  lower emittance booster  lower emittance linac

## Slide 23: DR parameters
 | DR V3.0 | 
Energy (Gev) | 1.1 | 
Circumference (m) | 147 | 
Number of trains | 2 | 
Number of bunches/trian | 2 | 
Total current (mA) | 12.4 | 
Bending radius (m) | 2.87 | 
Dipole strength B0 (T) | 1.28 | 
U0 (kev/turn) | 94.6 | 
Damping time x/y/z (ms) | 11.4/11.4/5.7 | 
Phase/cell (degree) | 60/60 | 75/75
Momentum compaction | 0.013 | 0.007485
Storage time (ms) | 20 | 
0 (%) | 0.056 | 
0 (mm.mrad) | 94.4 | 56.7
injection z (mm) | 5 | 5
Extract z (mm) | 5.6 | 4.2
inj (mm.mrad) | 2500 | 2500
ext x/y (mm.mrad) | 166/75 | 123/68
inj /ext (%) | 0.18 /0.056 | 0.18 /0.056
Energy acceptance by RF(%) | 1.4 | 1.8
fRF (MHz) | 650 | 
VRF (MV) | 1.5 | 
Longitudinal tune | 0.0299 | 0.0224
Damping with reversed bending magnet
Four-bunch storage, storage time: 20 ms
Emittance: 2500 166 (123) mm.mrad
Flexibility for extr. emittance

## Slide 24: DR time structure
Double bunch (Inj./Ext.: two by two)
200Hz (Inj./Ext.: bunch by bunch)
Meng Li

## Slide 25
Phase/cell: 60/60 ~ 90/90 FODO
Interleave sextupole scheme
2 sex. families
DR optics
Arc
Straight
B=1.28T

## Slide 26
DR DA results
Phase/cell: 60/60
Phase/cell: 75/75
Large trans. acceptance inj. efficiency
- DA > 5 inj. beam size

## Slide 27: Impedance Instabilities
Resistive wall impedance was considered *.
Design bunch current: 3.1mA < threshold due to TMCI
Yudong Liu
* Circular Al pipe with 30mm inner diameter

## Slide 28: Transport lines between DR and Linac
LinacDR | EC
E0 (Gev) | 1.1
0 (%) | 0.6
z0 (mm) | 1.5
fRF (MHz) | 2860
VRF (MV) | 22.0
Length of acc. Structure (m) | 0.82
RF (degree) | 89.7
R56 (m) | -0.833
Ef (Gev) | 1.1
f (%) | 0.18
zf (mm) | 5
DRLinac | BC
E0 (Gev) | 1.1
0 (%) | 0.061
z0 (mm) | 5.7
fRF (MHz) | 2860
VRF (MV) | 16
Length of acc. Structure (m) | 0.6
RF (degree) | 89.6
R56 (m) | -1.15
Ef (Gev) | 1.1
f (%) | 0.50
zf (mm) | 0.7
Dou Wang, Xiaohao Cui

## Slide 29: Optics for the transport lines
LinacDR
DRLinac
Xiaohao Cui

## Slide 30: Summary
Update booster design with smaller emittance in TDR─ support for CEPC high lum. scheme
TME structure with combined magnets (B+S)
DA with error effects fulfill the requirements
Booster parameters update ─ consistent with CEPC TDR parameters at 4 energy
Booster energy range is enlarged in TDR. (10GeV/120GeV  20GeV/180GeV)
Damping ring update is the requirement of higher luminosity goal for TDR.
Circumference: 150m, energy: 1.1GeV
Reversed bending, extracted emittance=120~166 mmmrad
Damping time: 15ms (CDR)  11ms (new)
Transport lines similar as CDR

## Slide 31
Back up

## Slide 32
dipole | quadrupole
B1/B0  210-4 | 
B2/B0  310-4 | B2/B1  310-4
B3/B0  210-5 | B3/B1  110-4
B4/B0  810-5 | B4/B1  110-4
B5/B0  210-5 | B5/B1  110-4
B6/B0  810-5 | B6/B1  510-5
B7/B0  210-5 | B7/B1  510-5
B8/B0  810-5 | B8/B1  510-5
B9/B0  210-5 | B9/B1  510-5
B10/B0  810-5 | B10/B1  510-5
Multipole errors @ 20GeV-TME
Multipole errors only

## Slide 33
DA results with errors and correction-FODO
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | 100
Longitudinal shift Z (μm) | 100 | 150 | 100
Tilt about X/Y (mrad) | 0.2 | 0.2 | 0.2
Tilt about Z (mrad) | 0.1 | 0.2 | 0.2
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
D. H. Ji
Almost impossible to obtain the initial closed orbit naturally
  Start from sextupole off
Orbit correction (COD)(60 Seeds)
  Response matrix method(RM)
  SVD method
Optics correction(60 Seeds)
  Response matrix method
  LOCO code
  Dispersion corrected

## Slide 34
Multipole errors @ 20GeV-FODO
FODO
dipole | quadrupole | sextupole
B1/B0  210-4 |  | 
B2/B0  310-4 | B2/B1  310-4 | 
B3/B0  210-5 | B3/B1  110-4 | B3/B2 110-3
B4/B0  810-5 | B4/B1  110-4 | B4/B2  310-4
B5/B0  210-5 | B5/B1  110-4 | B5/B2  110-3
B6/B0  810-5 | B6/B1  510-5 | B6/B2  310-4
B7/B0  210-5 | B7/B1  510-5 | B7/B2  110-3
B8/B0  810-5 | B8/B1  510-5 | B8/B2  310-4
B9/B0  210-5 | B9/B1  510-5 | B9/B2  110-3
B10/B0  810-5 | B10/B1  510-5 | B10/B2  310-4

## Slide 35: SR & Sawtooth effect@180GeV-FODO
W/O taper
W taper
2 RF stations
Maximum sawtooth orbit: 3 mm
Energy deviation: 1.1%
Emittance growth: ~210%
DA reduction due to strong SR
Optics distortion due to sawtooth orbit is serious.
Magnets tapering is essential.
Taper dipoles one by one
need to taper the quad & sext
D. Wang, D. H. Ji
DA tracking (50 seeds, 100 turns)
DA < requirement (injection)
- DA_X=5x+3mm=6.0mm
- DA_Y=39y+3mm=4.2mm
Sawtooth orbit was corrected by tapering
DA reduction due to sawtooth orbit

## Slide 36
DA@20GeV
FODO
TME
BSCxy=(4xy+5mm)*2

## Slide 37
DA@45GeV
FODO
TME
BSCxy=(4xy+5mm)*2
Off axis injection to collider

## Slide 38
DA@80GeV
FODO
TME
BSCxy=(5xy+3mm)*2
Off axis injection to collider

## Slide 39
DA@120GeV
FODO
TME
BSCx=(5x+3mm)*2
BSCy=(39y+3mm)*2 (on axis-injection scheme for collider)

## Slide 40
DA@180GeV
FODO
TME
BSCxy=(5xy+3mm)*2
Off axis injection to collider

## Slide 41
DA@180GeV (after tapering)
FODO
TME
BSCx=(5x+3mm)*2=7mm*2
BSCy=(5y+3mm)*2=4mm*2
Off axis injection to collider