## Slide 1
IARC meetings and Recommendations
Yuhui Li
On behalf of CEPC accelerator team
The 7th CEPC IAC meeting, 1-5 Novermber 2021

## Slide 2
Contents
Introductions
Theoretical design high lights and IARC recommendations
Collider ring parameters update
Booster scheme
Linac new baseline
MDI issues
Collective instabilities
SRF development (platform, cavities, cryomodules, …)
650M high efficiency klystrons
Normal temperature magnets (booster dipoles, dual aperture quadrupoles and sextupoles
Electrostatic-magnet deflector
Hardware for injection/extraction
Final focus Superconducting quadrupoles
Mechanics
III. IARC recommendations to the key technology hardware R&D
IV. Summary

## Slide 3
IAC request and IARC in 2021
IAC recommend the IARC meeting twice a year:
Chair:
Biagini Maria Enrica (INFN-LNF, Italy)
Members：
Bambade Philip (IJCLab, France)
Foster Brian (Oxford-DESY, England-GER)
Ko In Soo (Postech, Korea)
Levichev Eugene (BINP, Russia)
Ohuchi Norihito (KEK, Japan)
Oide Katsunobu (KEK/CERN, Japan/Swiss)
Pagani Carlo (Univ. Milan, Italy)
Sidorin Anatoly (JINR, Russia)
Stapnes Steinar (CERN, Swiss)
Tobiyama Makoto (KEK, Japan)
Zhao Zhentang (SINAP, China)
IARC Committee
Assignments
Foster Brian
Levichev Eugene
Biagini Maria Enrica
Oide Katsunobu
Sidorin Anatoly
Bambade Philip
Pagani Carlo
Ohuchi Norihito
Stapnes Steinar
Ko In Soo
Tobiyama Makoto
Zhao Zhentang
Talk No.
13 , 15
1 , 7
2 , 3
4 , 8
17 , 18
9 , 23
14 , 11
10 , 22
15 , 16
6 , 12
5 , 21
19 , 20
Principal
reviewer
Talk No.
14 , 16
4 , 17
1 , 9
2 , 3
19 , 20
7 , 21
12 , 22
6 , 19
11 , 23
13 , 15
8 , 18
5 , 10
help
reviewer

## Slide 4
IAC request and IARC in 2021
Two online IARC meetings took place in May and October
Presentations, programs are available:
IARC delivered two dedicated reports to the meetings:

## Slide 5
Talks in IARC
IARC in May, 11 talks
Status Overview of CEPC Project
CEPC Accelerator TDR Status
Status of CEPC Collider Ring
Status of CEPC Booster Ring
Status of CEPC Linac
Progress on MDI Design
Progress on CEPC RF system
Progress on HTS Magnets
CEPC accelerator TDR status overview
CEPC collider lattice & error for High Lumi.
CEPC Booster and Damping Ring Update
S2E simulation Linac & crucial component
MDI Studies for CEPC
CEPC SRF Progress on Cavities, Modules,...
High Field Magnet R&D for CEPC/SppC
650MHz High Efficiency Klystron Progress
Progress on High Efficiency Klystrons
Progress on Plasma Injection
Progress on IP SC Magnet
CEPC Plasma Injection Update
Coherent BB instability with long. Imped.
Instrumentation, BPM, …
Normal conducting Mag., dipoles, quads,
Investigation on the Polarization
Collective instability with high Lumi.
Mechanical and MDI pipes & support
Cyrogenic System
Installation, Alignment Technologies
Timing strategy& Injec/Extrac. philosophy
Hardware preparation for Injec/Extra.
Electromagnet separator Prototype
Control system challenge & collaboration
Electron dump system and safety issues
IARC in Oct, 22 talks

## Slide 6
IARC General Comments
IARC in May
IARC in Oct

## Slide 7
Report representative to single presentation
General Comments:
Progress High lights
Critical analysis
Recommendation:
Encouragement
Suggestions for weak points

## Slide 8
Contents
Introductions
Theoretical design high lights and IARC recommendations
Collider ring parameters update
Booster scheme
Linac new baseline
MDI issues
Collective instabilities
SRF development (platform, cavities, cryomodules, …)
650M high efficiency klystrons
Normal temperature magnets (booster dipoles, dual aperture quadrupoles and sextupoles
Electrostatic-magnet deflector
Hardware for injection/extraction
Final focus Superconducting quadrupoles
Mechanics
III. IARC recommendations to the key technology hardware R&D
IV. Summary

## Slide 9
High lights to Collider: Lattice, IP and Main Parameters
Arc and IP region lattice & parameters updated: more arc sextupoles, MDI layout change, lower βy, smaller ε, … → Hi-Lumi & ttbar energy
Phase Advance
90˚
60˚

## Slide 10
High lights to Collider: Dynamic Aperture and Errors
DA for Higgs and ttbar: 8 sigma-x with 2% momentum aperture; Z and W is on-going
Higgs: On-axis injection; (w/o error):
418 error seeds (50um for IR QUAD, 100um for others):
8
ttbar: On-axis injection; (w/o error):
Z: Off-axis injection; momentum acceptance <1%

## Slide 11
Recommendations to Collider
Error correction with advanced technologies such as Machine Learning,…
IR QUAD misalignment increasing from 50 microns to 100 to be simulated
Investigations on the error impacts to emittance
Further studies on error correction to increase the DA for Higgs (on-axis injection) is needed, try beta-beating correction scheme. → Other modes using off-axis with larger DA
Increase the momentum acceptance, for energy deviation larger than 1-2%
Bunch dump issues,…
A comprehensive review of DA for all modes: with larger IP errors, bigger momentum acceptance, …
The total diagram for the injection: on-axis for H, injection interference with collision, …
Further DA studies: bigger momentum acceptance, bigger DA for H, …
Injection study: on-axis or off-axis to tt,…
Error studies: new method, larger error, impacts to emittance,…

## Slide 12
High lights to Booster: Parameters for H-Lumi.
Parameters for H-Lumi: lower extraction emittance, 20GeV Injection energy, 180GeV for tt, …
CDR
High Luminosity

## Slide 13
High lights to Booster: Parameters for H-Lumi.
Lattice converge to TME
DA @ 20 GeV with earth field & errors
Beam beam instability for on-axis injection
SR & Sawtooth error & tapered dipole compensation

## Slide 14
Recommendations to Booster
More detailed studies for the on-axis injection for Higgs
Develop the error correction procedure for sufficient DA at each energies (100 seeds）
Check booster combined-function dipole strength to ensure required DA at all energies
Reconsider the option of bypassing the baseline RF system for high Z current
Feedback components especially the kicker & high-power amplifiers should be optimized
Timeline of injection complex from e-gun to the full current collider at all energies for on&off-axis
DA including errors should be given
Hardware check: kicker, dipole, SRF cavities
DA studies with error
Injection details, especially to on-axis injection for Higgs

## Slide 15
High lights to Linac & Damping ring: New Baseline
New baseline for linac: 20GeV by C-band cavity, lower ε (40nm→10nm), layout optimization, …
S2E simulations for LINAC

## Slide 16
High lights to Linac & Damping ring: Damping Ring
Layout, basic comparison
Lattice design (60~90 FODO)
Preliminary DA studies
(>5 injection beam size)

## Slide 17
High lights to Linac & Damping ring: Hardware
Flux concentrator for positron source
High perform. S-band Acc. Struc.
S band pulse compressor
pulsed magnetic field of 6 T to 0.5 T
15kA/15kV/50Hz solid state pulse source

## Slide 18
High lights to Linac & Damping ring: Hardware
Preliminary study for C-band Acc. Structure
Design work for 650M DR RF cavity
Waiting for C-band Klystron for the test

## Slide 19
Recommendations to Linac & Damping ring
Check all parameters whether compatible with H-Lumi for Z mode
DR design seems not mature, reconsider the design based on simulated Positrons from the target through the linac and energy compressor with the realistic distributions
Check the reason of the emittance growth after about 800m even without error
Establish a consistent injection diagram for the collider, booster, damping ring and linac
More info. for C-band structure
Check the injector diagram for all modes from DR and Linac
Check the parameters, including LINAC, consistency for H-Lumi Z
Further studies for DR

## Slide 20
High lights to MDI: SR heat & Beam loss
SR heat load in normal & extreme conditions
Extreme Condition
Normal Condition
Extreme condition, eg, if a magnet power is lost, a large distortion will appear immediately for the whole ring orbit.
In extreme cases ~ at least 10 times per day. The beam will be stopped within 0.5ms when abnormal.
Beam loss effects due to Radiative BhaBha, Beam gas inelastic scattering, Beam thermal photon scattering, with multipole & beambeam
RBB
with multipole
BG
with multipole
BTH
with multipole
RBB
with BB
BG
with BB
BTH
with BB

## Slide 21
High lights to MDI: HOM

## Slide 22
High lights to MDI: Collimator & Shield
Two pairs of vertical collimators added for one IP in one ring, with which the beam loss background with multipole errors and beam-beam effects reduced 20%.

## Slide 23
Recommendations to MDI
Try different charge distribution more than Gaussian for the SR heat load
Beam loss simulations with average effect over many seeds instead of specific seeds; More detailed simulations to each multipole error individually
Extend the detector GEANT4 simulations to include the beam line components some meters around the IP on both sides
A full simulation including detector, to evaluate the impact of beam losses in IR
Heat load for the Hi-Lumi. Z should be investigated
Complete scheme of collimation including near-IR ones
An IP feedback procedure for keeping beams in collision and stable luminosity
Electromagnetic force with interference between the detector-solenoid and compensation coil
Take into accound the tungsten shield weight for the cryostat into the deformation/alignment studies
A fast beam-abort system to protect the most sensitive components in detector and SCQ
Beam loss from continuous top-up injection to be analyzed; Tolerances to imperfect beam from booster (large emittance, non-Gausian distribution) should be investigated for collimation-system parameters
Comprehensive simulation with detector
More detailed studies on beam loss effect
Imperfect beam instead of Gaussian for simulations

## Slide 24
High lights to Collective Instability
Impedance budget for H-Lumi. Z

## Slide 25
High lights to Collective Instability
Instabilities: MWI & bunch lengthening; Transverse mode coupling; Trans. Resistive wall;

## Slide 26
High lights to Collective Instability
Instabilities: beam ion; electron cloud;

## Slide 27
Recommendations to Collective Instability
The requirement for the transverse feedback damping time of 3 turns is difficult to realize: fundamental stability limitation of the feedback system & broadband noise injected to the FB works to excite the beam
Develop a dedicated feedback system ofr the resistive-wall instability
Consider the feasibility to the FB requirement

## Slide 28
Contents
Introductions
Theoretical design high lights and IARC recommendations
Collider ring parameters update
Booster scheme
Linac new baseline
MDI issues
Collective instabilities
SRF development (platform, cavities, cryomodules, …)
650M high efficiency klystrons
Normal temperature magnets (booster dipoles, dual aperture quadrupoles and sextupoles
Electrostatic-magnet deflector
Hardware for injection/extraction
Final focus Superconducting quadrupoles
Mechanics
III. IARC recommendations to the key technology hardware R&D
IV. Summary

## Slide 29
High lights to SRF: 650M 1&2 cell cavity
Cavity | Processing | Result
650S4 (FG) | Bulk BCP 200 um + light EP 20 um + 950C 3h + light EP 20 um + 120C 48h | 2.7E10@ 35.0MV/m
650S7 (LG) | Bulk FP 200 um + 950C 3h + light EP 20 um + 900C 3h + light EP 20 um + 120C 48h | 3.1E10@ 33.0MV/m
650S5 (FG) | Bulk EP 200 um + 120C 48h | 1.5E10@ 37.5MV/m
650S8 (LG) | Bulk BCP 200 um + light EP 20 um + 950C 3h + light EP 20 um + 120C 48h | 4.6E10@ 28.2MV/m
Studies on EP process for 650 MHz 2-cell cavities were carried on.
New jigs and cathodes special for the EP on 650 MHz 2-cell cavities was made.
Parameters were scanned and optimized for the process like voltage, temperatures, flow rates and so on.
Some technological processes like on-site DI water cleaning were re-developed.
The new-treated cavities will be ready soon.

## Slide 30
High lights to SRF: 650M 1&2 cell cavity
Cavity | Processing | Result
650S4 (FG) | Bulk BCP 200 um + light EP 20 um + 950C 3h + light EP 20 um + 120C 48h | 2.7E10@ 35.0MV/m
650S7 (LG) | Bulk FP 200 um + 950C 3h + light EP 20 um + 900C 3h + light EP 20 um + 120C 48h | 3.1E10@ 33.0MV/m
650S5 (FG) | Bulk EP 200 um + 120C 48h | 1.5E10@ 37.5MV/m
650S8 (LG) | Bulk BCP 200 um + light EP 20 um + 950C 3h + light EP 20 um + 120C 48h | 4.6E10@ 28.2MV/m
Studies on EP process for 650 MHz 2-cell cavities were carried on.
New jigs and cathodes special for the EP on 650 MHz 2-cell cavities was made.
Parameters were scanned and optimized for the process like voltage, temperatures, flow rates and so on.
Some technological processes like on-site DI water cleaning were re-developed.
The new-treated cavities will be ready soon.

## Slide 31
High lights to SRF: SRF beam test facility
Cavity string and module assembly in March to May 2021.
Modul installation in beamline, 2 K cool down test and RT coupler conditioning in May to July. Horizontal and beam test soon.
IR laser output to 116 W. Photo-cathode QE to 5 %. DC gun vacuum to 1.5E-10 Pa, voltage to 350 kV. Buncher cavity high power tested.

## Slide 32
High lights to SRF: 1.3 GHz 9-Cell TESLA cavity
1.3 GHz High Q Mid-T Cavity Horizontal Test
IHEP PAPS established in July 2021
Horizontal test stand, 1.3GHz 9cell cavities, and couplers...
1.3 GHz 8x9-cell high Q cryomodule prototype
Component fabrication in 2021 to mid 2022
Assemble and horizontal test in 2022
Ship to Dalian in 2023

## Slide 33
Recommendations to SRF Cavity
Further improve he collaboration with SCRF groups in China, engaged in FEL and ADS
TESLA type 1.3GHz cavities use HOM couplers with a power limit of ~1W. Verify HOM coupler consistency also for the Hi-Lumi. Z mode.
Continue the successful collaborations with industry
Never mix the long-term R&D, like the one required for the ttbar cavities, with the R&D for routine produced industrial components
Reinforce and extend international collaborations on critical components
Maintain and extend collaboration with international laboratories also with strong expertise in SCRF
Pay attention to the Nb material and avoid a single supplier situation
Further industrialize the SRF technique

## Slide 34
High lights to 650MHz Klystron: Plans & cost saving
Chart: 
| 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 576 | 460.8 | 384 | 329.1429 | 288 | 256 | 230.4
CEPC at 800 RMB/MWh and 6000 hours/year
Excessive electricity bill, M RMB
1 year
Efficiency, %
90 M RMB
130M RMB
2020
2021
2022
Save Money
Efficiency impact on operation cost (Only considering operation efficiency of 650MHz klystrons)
Klystron No. 1
Efficiency 62%
(2020)
Klystron No. 2
Efficiency 77%
(2021)
Klystron No. 3
Efficiency 80.5%
(2022)

## Slide 35
High lights to 650MHz Klystron: Fabrication Status
The preliminary 3d mechanical drawing of 650MHz multi beam klystron is finished (80% efficiency)
Z.S.Zhou
The 650MHz high voltage single beam klystron is fabricated under baking (77% efficiency) and test will start soon in PAPS

## Slide 36
Recommendations to 650MHz Klystron
The strategy for the injector C-band klystron and modulator system should be included in the plans
Test and evaluate carefully the high-efficiency and MBK designs that already have the capability to reach 80% efficiency, before introducing further changes
Consider already large-scale production and system-operation challenge that feed back to the design
The RF sources for the injector and booster should be presented
A more detailed description of the injector and booster RF systems should be presented at the next meeting
In similar effort for MBKs for other projects, collector stability in some cases not seen in the simulations has been a concern.
Complete the 1st high efficiency klystron
MBK fabrication
C-band RF power source: modulator, klystron

## Slide 37
High lights to normal conducting magnets in booster
Two kinds of the subscale prototype magnet w/wo iron cores have been developed.
As for the CDR parameters with 10 GeV injection energy the low field performance of the magnet without iron cores meets the requirements whereas the magnet with iron cores not
With the new baseline of 20GeV injection both prototypes fullfill the requirement
The full scale prototypes are under the development

## Slide 38
High lights to normal conducting magnets in collider
Item | Value
Center field (Gs) | 141.6@45.5GeV，373@120GeV，568@182.5GeV
Gap (mm) | 66
Magnetic Length (m) | 5.737
Good field region (mm) | ±13.5
Field harmonics | <0.05%
Field adjustability | ±1.5%
Field difference between two apertures | <0.5%
Full size dual aperture dipole
Trim coil
harmonic variations are accepted at different energies.

## Slide 39
Recommendations to normal conducting magnets
The IARC expects the normal conducting magnet team to push the magnet study with the prototype in calculation and production forward to the production magnet
The magnetic field performance of the prototypes should be confirmed by magnetic field measurements as soon as possible to allow the final design of the production magnets
The measurement accuracy of the harmonic coil system should be checked for the low field and high quality magnets
Manufacture the full length booster dipoles
Verify the designed quality of the dual-aperture QUAD with measurements

## Slide 40
Layout of RF region
Electrostatic-Magnetic Deflector for Higgs
Higgs Energy requires the acceleration of e- & +by both RF stations
Electro-Magnetic Seperator are installed to deflect e-/e+ to inner/outer rings
 | Filed | Effective Length | Good field region | Stability
Electrostatic separator | 2.0MV/m | 4m | 46mm ⅹ11mm | 5ⅹ10-4
Dipole | 66.7Gauss | 4m | 46mm ⅹ11mm | 5ⅹ10-4
Schematic of Electrostatic-Magnetic separator
B. Chen

## Slide 41
CEPC Electrostatic-Magnetic Deflector
B. Chen
Index | indicators | Factory test | Test results
Vacuum leakage rate |  | ≤1x10-10Pa.m3/s | 2×10-13Pa·m3/s
Vacuum pressure | ≤2.0×10-10Torr | ≤4.0×10-10Torr | ≤1.0×10-10Torr
Maximum conditioning voltage |  | ±135KV，8 hours non-stop operation，Vacuum ≤ 4.0×10-10Torr | －108KV ＋97.6KV
  The mechanical design of electrostatic separator was completed. The prototype of the separator was fabricated in factory and the factory test had been done.
  The factory test showed that the vacuum reached the target. However, due to the arc of the high voltage test, two power supplies failed to be used.
  The magnet yoke is H-type. The prototype is being fabricated. It is planned to complete production in next month.
Prototypes for Booster power supply and Correctors with Multi-unit combination structure has been fabricated and finished the test.
Electrostatic-Magnetic Deflector Manufacture & Test

## Slide 42
Recommendations to Electrostatic-Magnetic Deflector
Carry out test of the dipole-magnet prototype to achieve the required performance
Solve the problems and accomplish the test as soon as possible

## Slide 43
 | Sub-system | Kicker Type | Kicker waveform | Septa Type | Thickness of septum
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | Horizontal LMS | ф22/3.5mm
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal LMS | ф55/5.5mm
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф55/6mm
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/2mm
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф55/6mm
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical LMS | Ф55/6mm
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/6mm
The same team is in charge of both HEPS and CEPC inj. & ext. system
Experience gained in HEPS applies for CEPC
CPEC Injection & Extraction Hardware Types

## Slide 44
Stored beam pipe(VP) inner diameter= ø55mm, Thickness=4mm
Injected beam pipe (SS): inner diameter=ø29mm, Thickness=1mm
Septum thickness=4+1+0.5=5.5mm
Magnet gap: 32mm
Winding: W=70mm,H=140mm,T=128
Exciting current=188A
Inductance=0.0682H
Lambertson Septum Prototype for HEPS BST

## Slide 45
Slotted-pipe Kicker Prototype Design & Fabrication

## Slide 46
Scheme: 20-stage inductive adder based on SiC-MOSFETs.
The co-axial transformer is configured as bipolar output.
The pulser is located outside tunnel and ten 50 Ω cables with length more than 30m are applied to connect with kicker.
Matching terminal resistor is 10Ω.
250ns Fast Kicker Pulser

## Slide 47
Chart: Wall thickness/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
octagon | 2.37 | 3.17 | 4.38 | 6.38 | 9.83 | 16.4 | 30.5 | 66.2 | 172
race track | 1.78 | 2.29 | 3.04 | 4.15 | 5.83 | 8.34 | 12 | 17.5 | 25.4
ellipse | 1.4 | 1.73 | 2.24 | 2.95 | 4.01 | 5.49 | 7.4 | 10.2 | 13.5
L=1.2m，thickness=5mm
ceramic vacuum chamber with special pattern metallic coating is key component for outside-vacuum kicker magnet.
ellipse
octagon
Race track
Ceramic material: 99% AL2O3
√
Integrated sintering
Ceramic Vacuum Chamber

## Slide 48
Movable solenoid
Solenoid coil
Inner diameter=208mm
Length =700mm
Good field region=500mm
According to the experience of coating, the cathode target discharge is unstable for long vacuum chamber more than 600mm and it is easy to cause ignition or local film formation failure.
Sectional coating method by a movable solenoid is proposed for our 1.2m ceramic vacuum chamber. The coating experiment shows uniform coating achieved in one antechamber of 1m.
In order to obtain uniform coating inner racing track shape vacuum chamber, a horizontal movable cathode wire target solution is proposed.
The antechamber for HEPS
(inner aperture=6mm)
1m
Cathode wire
Moving track
view window
Cathode pole
Graduated bellows is used to adjust the horizontal position of cathode wire (compression at one end and tension at the other end)
Magnetron Sputtering Coating Prepare

## Slide 49
Recommendations to Injection & Extraction Hardware
Check the field quality, impedance and associated technical issues, like water cooling, insulation support and HV feedthroughs of the kicker prototype
The design of the dipole and kicker systems need further detailed work
Investigate further the beam coupling impedance for the ceramic vacuum chamber coating
Prototyping the components for CEPC by HEPS
Accumulate the experience on the beam coupling impedance from similar investigations for HEPS

## Slide 50
Weight Reduction for the MDI SC Quadrupole
There are big challenges about the weight of SC QUAD
- narrow space; - crosstalk
Focused on reducing the magnet weight of Q1a.
Paths:
  1. Relax the dipole field requirement of crosstalk (<30Gs)
  2. Use special iron material (FeCoV)
  using 1+2, Weight: 78.9Kg (55% of original value 143.6kg)
  3. Reduce coil layer to 1, expecting excitation current 3585A
  using 1+2+3, Weight: 60.2Kg (42% of original value)
Magnet | Central field gradient (T/m) | Magnetic length (m) | Width of GFR (mm) | Minimal distance between two aperture beam lines (mm)
Q1a | 141 | 1.21 | 15.21 | 62.71
Q1b | 84.7 | 1.21 | 17.92 | 105.28
Q2 | 94.8 | 1.5 | 24.14 | 155.11
High luminosity requirements

## Slide 51
Fabrication of QD0 short model magnet is in progress
Fabrication of NbTi Rutherford cable is finished (12 strands). SC quadrupole
coil winding machine, coil heating and curing system has been finished.
Magnet name | 0.5m QD0 model magnet
Field gradient (T/m) | 136
Magnetic length (m) | 0.5
Coil turns per pole | 21
Excitation current (A） | 2070
Coil layers | 2
Conductor | Rutherford Cable, width 3 mm, mid thickness 0.93 mm, keystone angle 1.9 deg, Cu:Sc=1.3, 12 strands
Stored energy (KJ) (Single aperture) | 2.6
Inductance (H） | 0.001
Peak field in coil (T) | 3.4
Coil inner diameter (mm) | 40
Coil outer diameter (mm) | 53
Yoke outer diameter (mm) | 108
X direction Lorentz force/octant (kN) | 24.6
Y direction Lorentz force/octant (kN) | -23.7
Net weight (kg) | 25
CEPC QD0 SC Magnet R&D (0.5 m short model)

## Slide 52
Recommendations to SC Magnet
Estimate the electromagnetic force between the detector solenoid and the compensation solenoids, iron yokes of the quadrupoles ect
Evaluate the load line ratio for each magnet
The field cross-talk between the magnets, such as Q1a and Q1b should be estimated and taken into account in the design
Clarify the required number and kinds of corrector magnets. Collaboration with the optics group is essential
Clarify the structure of the cryostat. Collaboration with the MDI group will be needed
Check the solenoid field profile of the detector solenoid along z, which has a large field gradient in the detector, which produces the large electro-magnetic force on the compensation solenoid
The priority is accomplish the on-going cos2θ type SCQ prototype
Doing the magnet measurement, collect needed data for further studies, such as magnet field crosstalk
Cryostat prototyping with available funding
Comprehensive magnetic force studies including detector coils

## Slide 53
Dazhang Li, CPS, September 2019
Booster Requirement | 
Energy（GeV） | 45.5 (0.2%)
Bunch Charge（nC） | 0.78
Bunch length(um) | <3000
Energy Spread(%) | 0.2
εN(μm⸱rad) | <800
Bunch Size(um) | <2000
HTR e- acceleration
  Start-to-end simulation performed, CPI requirement to linac updated
  Without extra damping mechanism, the growth of hosing instability from statistical noise is acceptable when transformer ratio is 1-1.5
  There are other powerful damping mechanisms. HTR is still possible
e+ acceleration
  Asymmetry beam scheme is well accepted by PRL reviewers
  More schemes are under consideration
Experiments Plasma dechirper experiment got good results.
  Experiment on SXFEL is still ongoing. Dedicated TF for PWFA is crucial and under consideration
Positron acceleration scheme
W. Lu, D.Z. Li
Plasma Acceleration Investigation

## Slide 54
Recommendations to Plasma Acceleration
Update the simulations to use the parameters for the beams exiting the C-band linac, according to the new baseline
Consider how to shape the linac pulses at the photocathode gun in order to optimize the transformer ratio and avoid hosing instability
Consider relaxing the beam size requirements in the linac and focusing the beam at the entrance to the PWFA stage using a plasma lens
Continue the excellent work on simulation of the PWFA acceleration process for electron and the experimental work on plasma dechirping and plasma lenses
Collaborate with the linac group to understand to what extent the requirements of the PWFA injection can be met by hardware that would be suitable both for PWFA injection or direct injection into the booster. Think its compatibility with the current baseline
Continue to investigate the possibility of a dedicated experimental facility to test the idea
Propose and schedule appropriate experiments to test the new ideas on positron acceleration at the FACET-II facility whenever positions become available
Continue the theoretical studies for plasma injection as the backup solution for CEPC
Try PWFA test

## Slide 55
High lights Mechanics: MDI
vacuum chamber
vacuum connector

## Slide 56
High lights Mechanics: MDI
Collimator temperature rise
SC Magnet Support

## Slide 57
Recommendations to MDI
The space of the detector signal cables, cooling pipes, pressure gas pipe for RVC and the BPM signal cables between the acos line and the outer surface of the magnet cryostat is required
In the mechanical calculation model, the adjustment mechanism for evaluating the deformation of the component due to the electromagnetic field of 270kN should be included
For evaluating the magnet displacement during beam operation, the thermal contraction of the cold mass and the support rods should be included
In the study of the machine protection, fast sensors to detect the beam loss must be designed and included
Further studies for the MDI mechanical system
Find solutions for the collimator etc. protection

## Slide 58
Summary
CEPC accelerator system is optimized for the high luminosity operation including ttbar energy.
CEPC key technology hardware R&D is progressing with the aim of TDR accomplishment by the end of 2022
More efforts are needed to the TDR completion and EDR preparation

## Slide 59
Acknowledgement
Materials of this presentation are from various talks in the recent IARC meeting
Thanks to the CEPC –SppC accelerator team’s hard works as well as international and CIPC collaborations
Special thanks to the IARC’s contribution: encouragement, critical analysis and suggestions