## Slide 1: Update on TDAQ Proposal for CEPC Project
Trigger Group
2021.9.15

## Slide 2: Outline
Background about trigger meaning and function
New ideas in CEPC and future experiment
  Triggerless=triggerless readout,not triggerless system
  Continuous:L0 based, data driven readout
  Unified link for data and control
  New backend
Proposal
  New idea:UCaML, fast/slow control data sharing
  Compliant to Trigger/triggerless readout in FEE readout
  Simulation
  R&D plan
Summary

## Slide 3: What is Trigger
Trigger
  lever that activates the firing mechanism of a gun（WIKI）
  a small device that releases a spring or catch and so sets off a mechanism, especially in order to fire a gun(bing)
Oscilloscope（Signal catching）
  Trigger Level: Adjustable level to get a stable signal shape on the screen, only sweeps if the input signal reaches the set trigger point; otherwise (on an analog oscilloscope) the screen is blank or (on a digital oscilloscope) frozen on the last acquired waveform.
Digital signal analyzer (debugging)
  Trigger mode: a number of advanced trigger types that enable you to capture a stable waveform even with complex signals. This makes them ideal for troubleshooting glitches, timing violations, overvoltages and dropouts in analog and digital circuits.

## Slide 4: Trigger Function in Small Physics Experiment
Time Reference to ADC/TDC, also readout
  Radiation Source based
    Collimized particle as start of digitization
    Gate for ADC
    Common Start/Stop for TDC
  CosmicRay based
    Coincident cosmic as start of digitization
    Gate for ADC
    Common Start/Stop for TDC
准直
放射源
探测器
电子学
DISC
读出/DAQ

## Slide 5: Trigger Function in Large Physics Experiment
BES/BESII Trigger
  Providing timing signals for digitization(B ADC)
    Start
    Reset
  Still reference
  Readout
    LaM from CAMAC

## Slide 6: Early Trigger + Online
Process in Levels
  Level 1: Fast signals from Detectors in one collision
  Level 2: Slow signals from slow detectors in second collision
  Processor based processing
1st collision cycle
2nd collision cycle

## Slide 7
Nowday’s Trigger + DAQ
To keep only pink hexagonal widgets moving down a conveyor belt.
y/n
y
y
n
n
Trigger
Stamp “y” on the pink hexagonal widgets Stamp “n” on the others
n
y
trash
SAVE
DAQ
Saves only widgets labeled “y”
The problem is: Working fast means you make some mistakes !
电子储存环
对撞周期
对撞点
谱仪

## Slide 8: Trigger/DAQ Function in Preset Physics Experiment
Trigger（hardware）
  Providing Index for digitized data(Fast ADC)
    Hardware trigger Output L1Accept
    Known latency L1a
    Pipelined processing
  Fast control
DAQ
  Event Building
  Monitoring
  Run control
  High level trigger
  (Event fildter)
FEE
  ADC
    No gate signal
    Fast continuous
    Pipelined data
  TDC
    No common start/stop
    Reference of Clock edge
    Coarse time of clocks
  Readout
    L1 based
    Window size

## Slide 9: Exa：Block Diagram BESIII Trigger System
TCBA
Global Trigger Logic
6.4 s
TOF FEE
MDC FEE
EMC FEE
MU FEE
TOFPR
MFT
Mu track
FastOR
Track Finder
Etotal Energy
Hit/Seg Count
Track Seg. Finder
BEPCII RF
TTC
TC Sum
L1P
41.65 MHz
Track Match
Energy Balance
Cluster Counting
Fast Control
FC Daughters
Near Detectors
Counting Room
499.8 MHz
High Lights: Optical Isolation-no ground loop current

## Slide 10
Network based DAQ as in BESIII

## Slide 11: Trigger Definitions
Required rejection is orders of magnitude
  Algorithms to attain required rejection are too sophisticated.
  Accelerator backgrounds can also contribute to the problem
     e+e- vs pp
Level 1 is hardware based
  Crude signatures (hits, local energy deposit over threshold…)
  Operates on reduced or coarse detector data
Level 2 is often a composite
  Hardware to preprocess data
    Some Muon processors, Silicon Triggers
  Software to combine
    Matches, Jet finders, etc.
Level 3 is a farm  General Purpose CPUs
Almost every one uses this scheme
  Vary number and function of levels.

## Slide 12: Trigger on LHC
“Local” identification of high Pt objects  use coarse dedicated data
  Electrons /Photons , Hadrons & Jets  Energy clusters
  Muons Track segments
  Neutrinos  Missing Et
Particle signature (e/g,h,Jet, µ ...)  use final digitized data
  Refine Pt cuts  fine granularity & track reconstruction
  Combine detectors  Converted electron ,“Punchthrough”, decays
Global topology  multiplicity & thresholds
Identification & classification of physics process  trigger menu
  Partial event reconstruction  Vertices , Masses ,Missing Et....
Physics analysis
  “Off-line” type analysis of classified events
L3
40 MHz
100 KHz
100 Hz
1 KHz
L1
3
L3
L2

## Slide 13: Trigger Structure on LHC
Level 1
Level 2
ROI
Level 3
ATLAS
CMS
Level 1
High
Levels
Front end buffers
( ~107 channels)
Region Of Interest
Read Out Buffers
1000-1500 units
256 x 256
40 MHz
100 KHz
1KHz
100 Hz
Switching Network
(Event builder)
Processor farm
(~2 to 5 x 10 MIPS)
6
Sub- Detectors
10KHz
“Virtual”
level 2
Synchronous
Asynchronous
1-10 s
variable
2.5 ms
fixed
Custom made
Hardware pipelined
rigger processor
Commercial DSPs,
RISCs, etc.
Farms of RISCs,
workstations, etc.
1000 - 1500Gbit/s
20 Gbit/s
10 Gbit/s
1 Gbit/sec
1000 x1000
100 Mbit/sec
250-500 Gbit/s
few m s
variable
Permanent storage
100 MBytes/sec --> TBytes/day

## Slide 14: unclear margins
10
10
10
10
10
10
10
10
10
10
10
10
- 2
0
2
4
6
8
- 8
- 6
- 4
- 2
0
2
Hardwired processors
(ASIC , FPGA)
Standard CPUs farms
& Networks
Level 1
Level 2
Level 3
# / sec
QCD
W,Z
Top
Higgs
Z’
25ns
few µsec
~ms
> Sec
Recorded
Events
H L T
Production Rate

## Slide 15: New trend in FEE
Digitization:
  Faster
  Continuously
E,T,Q
Pipelined register
clock
digital filter
photo
detector
APD
PMT
LOCAL
BUFFER
Other ROI channels
crystal
Trigger
logic
ROI Data
SiPM
Discri
PA
SH
Pulse
Shape
Digitizer
Array
Pixel
Slow control
  Parameter setting
Readout:
  Trigger based or
  data driven

## Slide 16
Triggerless readout in PANDA
Self-triggered Data Push Architecture
Timestamp with data production
Triggerless readout
4. Feature extraction as local computing node in level 1 network (ATCA)
5. Event reconstruction and selection(high level trigger) in level 2 on farm

## Slide 17
Modern Experiment Architecture
Detectors
Weak signal
PA+MA+ Digi
FEE/RO
SubTrg+GTL
DAQ storage
Physics
particle
FEE + TriDAS
FEE(on Detector)
  AM+Digi+triggerbasedROboard(8-12b、40-500MSps、800Mb/s-1.6Gb/sBW)
  triggerPrimitive（signal+data transmitter）
  digitizedParameterSetting（SC）
FEE
On-detector
For TRG
CLK+FC
Counting Room
off-detector
SC/PS
Off-detector
  FC
  Remote SC
  radiationMonitoring（SEU）
Data link
Trigger link
FC link
SC link

## Slide 18
Future Trend of Experiment architecture
Detectors
Weak signal
PA+MA+ Digi(ASIC)
HSL chip
Subtrg+GTL+DAQ
SW + Farms
Physics
particles
FEE(ASIC)
  12-16b、500M-4GSps、MultiCH,highdensity(high RO BW）
  picoSec timing,largedynamicRange（Hpclocks,synchronized）
HS,MCHlinks:1.6G/4.8G/10Gbps（triggerless continuousRO）
Unified BE（complexRO,trig,clk,FC,SC）
FE Electronics
clock + FC
BE electronics
SC
clock FC
SC
GLT+TCDS
Console PC
Shared
HSL

## Slide 19: TDAQ Proposal for CEPC
Baselines
  Supports both readout
    Trigger based and
    Triggerless
  Supports continuous /data driven data read
  Develop unified down link to FEE
    Fast control(clock, Synch, BXs, L1,…)
    Slow control(parameter setting, run controls,…)
  Provide FEE high BW data way
    4.8-10 Gbps links
  Provides DAQ
    10-100 Gbps data links

## Slide 20: TDAQ Proposal for CEPC(2)
Baselines
  Fiber optics data links
  Open structure to FEE
  xTCA based architecture
    High speed interconnection
    High speed data throughput
  commercial equipment based Post-DAQ (further discussion with LiFei)

## Slide 21: Tasks and Plan
Key processor module R&D
  Fast control + TCDS prototyping
  Slow control prototyping
  Processor/computing module prototyping
  Data producer/concentrator module prototyping
Physics Simulation
Trigger/selection simulation
  Starting from a detector system
Test Model system

## Slide 22: Roadmap
Hardware Development(Key boards)
Firmware/Software Development
  Simulation
  Emulator
  Data transmission
  FC/SC implementation(FEE/BEE sides)
  Trigger (Detector specific)
  DAQ/RO(general/detector specific)
Demo System
Application/verification with example Detector

## Slide 23: Data flow in the Mini-system
PC Server
IP Bus
MicroTCA crate
Reply
Board
Request
Board
MCH
AMC13
Fiber Loopback
backplane
2 Fibers(3m each)
ILA capture
ILA capture
PC
PC
bitFile download
bitFile download
Data capture
Data capture
Local Mini-system diagram
FEE
BEE

## Slide 24
GBT link
120bit@40Mhz 4.8Gb/s
BEB
PC
Link2
Slow module
Link1
Slow module
Command
analysis
FEE emulator
FEE emulator
FEE
Slow module
Response command
Demo system firmware blockdiagram
Firmware design：
  Data path
  Slow control
Link2.dat
FEE emulator
FEB emulator
data source
FEE
data preparation
MUX FIFO
hit finding
Link1.dat
BEB
GBT link
120bit@40Mhz 4.8Gb/s
data DEMUX
cluster finding
Θ-φ angle conversion
Trigger generate
DAQ
Fake L1A
10Gb/s
PC
1Gb/s

## Slide 25: DEMO System
AMC13
MCH
uTCA Shelf
BE
FE
AMC13
fiber
PC
Net cable
Data Fiber
SC Fiber
Complete DEMO System FE/BE
  2 ixFP cards
    1 ixFP cards for slow control/processor
    1 ixFP cards for iRPC data source
  1 AMC13
    TTC/TTS
    Management
  1 MCH + 1 PC
    Slow control
    Management + data storage
Functions
  1. Emulation/Development System
  2. Hardware, GBT/GBT based
  3. Detector Simulator/data source
  4. Fast/Slow control, cluster finding, data saving on to disk

## Slide 26: Summary
Some Trigger and DAQ basics are introduced in order to monimize argument on triggerless idea
Some new and future ideas are perspected
A Proposal for TDAQ development is outlined
Tasks and roadmap are forseed
Comments and suggestions are welcome

## Slide 27
DAQ系统部署

## Slide 28: 信号处理与控制的通用仪器装置
模拟信号/数字信号的处理方框图
  Pre-Amplifier（前放）: 预放大微弱信号
  Main Amplifier（主放）: 小信号放大
  Digitizer（ADC/TDC）: 模拟信号转换为数字信号
  Trigger（触发）：是数字化工作
  Readout（读出）: 数据读出
  Processor（处理器）: data analysis and display数据分析与显示
Detectors
Weak Elec. Signals
FE Electronics
Amp. + Shaping
Digitizer
Trigger/Fast Control
Onl. Readout
Processing and Display
Phys. Process
粒子
Slow Control
Analog
Digital
Digital signal
standardization
模拟部分
模拟部分

## Slide 29: 趋势 1: 实验装置的小型化: 低电平／低功耗和快速数据传输
整个实验装置集成到一个小盒子
Detectors
Weak Elec. Signals
FE Electronics
Amp. + Shaping
Digitizer
Trigger/Fast Control
Onl. Readout
Processing and Display
Phys. Process
粒子
Slow Control
PMT(left),TOF( middle, right) exercise setup for RT School 2016

## Slide 30: 趋势 1: 实验装置的小型化: 低电平／低功耗和快速数据传输（续）
  甚至通过微电子芯片技术集成为手持系统
  ASICs: Application Specific Integrate Circuits专用集成电路
  FPGA:Field Programmable Gate Array现场可编程逻辑阵列
  System on Chip片上系统
  Experiment on Chip片上实验
粒子

## Slide 31: 趋势 2: 大规模实验的仪器装置（基于加速器）
海量的探测器单元和电子学通道(几十万),标准化设计
Detectors
Weak Elec. Signals
FE Electronics
Amp. + Shaping
Digitizer
Trigger/Fast Control
Onl. Readout
Offline Analysis
Data Storage
Phys. Process
粒子
Slow Control
Control and Data Readout
  Standardized Signal levels
  Standardized Crates
  Standardized Modules
Accelerators
Power/Control
Accelerators（BEPCII）
Detectors（BES III）
Electronics

## Slide 32: 高能所设计范例及应用(1)
AMC/ATCA
for PANDA