## Slide 1
R&D status for vertex detector prototype
Zhijun Liang (IHEP)

## Slide 2: MOST2 vertex detector R & D: Research Goal
Produce a world class vertex detector prototype
  Spatial resolution 3~5 μm (pixel detector)
  Radiation hard (>1 MRad)
Preliminary design of prototype
  Three layer, module ~1 cm × 12 cm2
Typical module
Typical tracker
ATLAS/CMS upgrade
（~15 μm）
Alice upgrade
（5~10 μm）
This project（3~5 μm）
Resolution
World
leading
Notes: General description highlighting major points and assessment indicators

## Slide 3: Overview of task2： vertex detector R & D
Can break down into sub-tasks:
  CMOS imaging sensor chip R & D
  Detector layout optimization, Ladder and vertex detector support structure R & D
  Detector assembly
  Data acquisition system R & D
CMOS imaging
sensor prototyping
Detector module (ladder)
Prototyping
Full size vertex detector Prototype
Beam test to
verify its spatial resolution
Notes: Full size vertex detector

## Slide 4: Achievement Presentation and Assessment Methods
Silicon Detector
Assessment index
  - Mid-term: produce 25*25 μm pixel size chip
  - Final : 3-5 μm resolution in Beam test
  - mid-term: verified by TCAD simulation
  - Final : Total ionization dose >1 Mrad
Spatial resolution
Radiation hardness

## Slide 5
3rd Year:
  3rd CMOS sensor fabricated and tested
     skipped , since 2nd MPW chip is working well
  Final support structure engineering design completed
  Fabricated support structure prototype for ladders
4th Year (2021.7 –2022.6) :
  Competed R & D full-size TaichuPix sensor
  Manufactured the support structure for whole detector
  Assembling and installing the detector prototype
  Completed DAQ system for whole detector
5th Year:
  Completed detector assembly and commissioning
  Test beam and data analysis
  Finish assembling of prototype
Overall plan of task2： Vertex detector R & D

## Slide 6: CMOS Sensor chip R & D
The existing CMOS monolithic pixel sensors can’t fully satisfy the requirement
Major Challenges for the CMOS sensor
    Small pixel size -> high resolution (3-5 μm)
    High readout speed (<500ns deadtime @40MHz at Z pole) -> for CEPC Z pole high lumi
    Radiation tolerance (per year): 1 MRad

## Slide 7: Sensor prototyping
Completed two round of sensor prototyping
  1st Multi-wafer project chip (Taichupix1)
    Submitted in June 2019, received in November 2019
  2nd Multi-wafer project chip(Taichupix2)
    Submitted in Feb 2020, received in July 2020
    Major bugs fixed in Taichupix1
    Radiation hard design (enclosed gate) in pixel analog
    A full functional pixel array (64×192 pixels)
    Periphery logics
      Fully integrated logics for the data-driven readout
      Fully digital control of the chip configuration
    Auxiliary blocks for standalone operation
      High speed data interface up to 4 Gbps
      On-chip bias generation
      Power management with LDOs
Taichupix2
Chip size：5mm×5mm
Pixel size：25μm×25μm
Taichupix1
Chip size：5mm×5mm
Pixel size：25μm×25μm
Taichupix2 on test board

## Slide 8: Laser test in last report (coarse scan)
Triggerless mode was used for the laser test  full readout chain verified
Measured positions from Taichupix is consistent with expected laser movements
Laser
(1064 nm)
TaichuPix-2
Light spot fitting for laser moving in y-direction with step of 200 µm

## Slide 9: Laser test （fine scan)
Improved laser setup
  Beam spot focused to few um
Study pixel internal structure
Study Uniformity of response
Designed diode window width : 9 um
Observed diode window width: 7~8 um
Scan direction

## Slide 10: TaichuPix2 test with 90Sr source
Digital readout (full chip)
Analog readout (debug mode for one row of pixel)
  High signal to noise ratio found in analog readout
More studies are on-going
Analog waveform in beta tests
typical waveform in beta tests

## Slide 11: TaichuPix2 test with 90Sr source (2)
exposure to 90Sr at different threshold (ITHR)
Finding a cluster for adjacent pixels
with a timestamp window of 100 ns
Mean cluster size around 3 for different ITHR
Hit map of TC2 exposure to 90Sr for 400 s
Cluster size distribution
<Mean Cluster size> VS Threshold

## Slide 12: Threshold tuning for TaichuPix2
For TC2, threshold current ITHR can not be set less than 5.4 nA
  unexpected from design (nominal design value 4.5 nA).
  Connected the internal ITHR to an IO-pad through FIB (Focused Ion beam) technology to provide an external ITHR voltage.
  Applying an external voltage @ Pad-A to tune the ITHR current
  ITHR can not as low as expected (min. ~7.8 nA) . Need more investigation.
TC2 chip with a Al connection by FIB
S-curve of one column with external ITHR

## Slide 13: DAC design in the full scale chip TC3
DAC was also modified by adding a optional 6-bit current DAC for the low current biasing
Original design suffers from the leakage current and the output range is too large
  LSB: 0.1nA
  Aiming at: 2~4nA
Modified design tuned the output range specifically for small current:
  Range: 0~8nA

## Slide 14: Simulations on DAC of Taichu3
TC2 includes two current DACs to provide ITHR
  One 8-bit DAC same as in TC2
  An optional 6-bit DAC (design LSB of 0.1nA, range of 0-8 nA )
  Simulation results indicate the parasitic resistance increases the DAC output current, and the parasitic extraction rule effects the value of R and then the simulation result. Have not been understood well.
Name | Input code | Output with Simu-sch. | Output with Parasitic R @extraction rule 1 | Output with Parasitic R @extraction rule 2
IBIAS | 1011 | 463.9 nA | 551.2 nA | 481.8 nA
ITHR_8bit | 101100 | 4.7 nA | 9.3 nA | 5.5 nA
ITHR_6bit | 100011 | 4.5 nA | 7.5 nA | ----
IDB | 11000 | 1.02 uA | 1.12 uA | 1.05 uA

## Slide 15: Full-size TaichuPix3 design (engineering run)
Full-size Taichu pixel design ready, passed review, ready for submission
  1024×512 Pixel array (25μm×25μm pixel size), Process: Towerjazz 180nm
  FE-I3 like Periphery digital readout , high speed data interface
    Time stamp precision: 25ns-50ns

## Slide 16
Completed preliminary version of detector module (ladder) design
  Detector module (ladder)= 10 sensors + support structure+ flexible PCB+ control board
  Sensors will be glued and wire bonded to the flexible PCB
  Flexible PCB will be supported by carbon fiber support structure
  Signal, clock, control , power, ground will be handled by control board through flexible PCB
3D model of the ladder
Detector module (ladder) R & D
Design of Flexible PCB prototype
Profile of flexible PCB
Schematic of ladder electronics

## Slide 17: New idea in Taichu pixel design – inter-chip connection
Inter-chip connection for slow controls through wire bonding
 Save some metal for PCB (reduce material budget)

## Slide 18
Completed preliminary version of detector engineering design
  3 double layer barrel design
  7 modules in inner layer, 22 modules in 2nd layer, 32 modules in outer layer
Physics simulation to optimize vertex detector layout design.
  The length of inner layer pixel should be the same as other two layers
  Inner pixel radium should be as close to beam pipe as possible
Old design
Vertex Detector Prototype R & D
Impact parameter resolution
Vs beam pipe radius
After optimization

## Slide 19
3~5um good position resolution require high assembly precision
Cooperate with domestic company on R & D Gantry automatic module assembly.
  Pattern recognition with high resolution camera
  Automatic chip pick-up and positioning
  Automatic Glue dispending
Gantry for vertex detector prototype assembly
Gantry system
automatic glue dispending
Pattern recognition

## Slide 20: Tooling Design for Barrels Assembling
3 sets of tooling for 3 layer of barrel assembling.
Tooling and special tool for inner and middle barrels assembling.

## Slide 21: Cooling design
Air cooling is baseline design for CEPC vertex detector
Sensor Power dissipation:
  Taichupix : ≤ 100 mW/cm2. (trigger mode) ; CEPC final goal : ≤ 50 mW/cm2
Cooling simulations of a single complete ladder with detailed FPC were done.
  Testbench setup has been designed and built for air cooling , vibration tests
Air flow
Test setup prototype for ladder cooling
Use compressed air for cooling
(See more from Jinyu’s talk)
The EMMI
(Emission Microscope)
For Taichupix2
Power consumption
Laser interferometer
Ladder support

## Slide 22: Plan for test beam
Expect to perform beam test in DESY(3 - 7GeV electron beams)
  IHEP test beam facility as backup plan (a few hundreds MeV - 2.5GeV electrons )
Enclosure for detector with air cooling is developed for beam test
  Beam is shooting at one sectors of vertex detectors
Beam
Install one sector of ladder in vertex detector
Beam
Beam

## Slide 23: Plan for test beam (2)
New opportunity in Beijing Synchrotron Radiation Facility (BSRF)
  High energy electron (0.2~2.5 GeV) leakage from BEPC
  High trigger rate (up to 50Hz/cm2)
  Need to filter low energy particles for vertex test beam
Energy spectrum measured
by calorimeter (by Yong Liu)

## Slide 24: Summary
Sensor:
  Completed two round of CMOS sensor prototyping, finalized full-size sensor design
  New readout architecture to reduce pixel size to 25μm*24μm
     Reach midterm Assessment index (实现中期指标）
  First irradiation test up to 30 Mrad >1Mrad total ionization dose radiation
Mechanics:
  Build the support structure prototype for ladder prototype
  Finalize the design for full vertex detector
 | Mid-term | Final goal | Status
Spatial resolution | Pixel size less than 25*25 μm | Spatial resolution 3~5 μm | Reach mid-term goal
Radiation hardness | > 1MRad in simulation | >1MRad In radiation test | First test up to 30 Mrad. Chip is still functional

## Slide 25: Outlook for the next year
  Competed R & D large area sensor
  Manufactured the support structure for whole detector
  Assembling and installing the detector prototype
  Completed DAQ system for whole detector

## Slide 26: Outlook for the next year
  Competed R & D large area sensor
  Manufactured the support structure for whole detector
  Assembling and installing the detector prototype
  Completed DAQ system for whole detector

## Slide 27: Backup : Preparation for the full size engineering run
df

## Slide 28: Backup : Preparation for the full size engineering run
df

## Slide 29: Backup: International collaboration
IFAE(Spain): very active in CMOS Sensor design and testing
Liverpool (UK): Tracker mechanical design,
Oxford(UK): CMOS sensor design validation, thermal design
RAL(UK): Pixel module design
Queen Mary(UK): module mechanical design (Zero mass concept)
Strasbourg (FR): CMOS sensor design, Tracker mechanical design
University of Massachusetts (US): Tracker mechanical design, thermal design
  In 2019, we have one engineer visited Oxford and Liverpool for 4 weeks, learned a lots about silicon.

## Slide 30: Main specs of the full size chip for high rate vertex detector
Bunch spacing
  CEPC Z+Higgs (240GeV): 680ns;
  WW threshold scan (160GeV): 210ns;
  CEPC Z pole runing (90GeV) Z: 25ns
High Hit density
  2.5hits/bunch/cm2 for Higgs/WW runs
  0.2hits/bunch/cm2 for Z pole running

## Slide 31: New proposed readout architecture in TaichuPix
df
New readout architecture
 reduce power consumption and reduce pixel size
CEPC readout time requirement:
  <500ns deadtime @40MHZ(Z pole)
Taichu-1 Column-drain readout
  Priority based data driven readout; time stamp at EOC
  Dead time: 2 CLK for each pixel (50ns @40MHz CLK)
  Two digital pixel designs: FEI3-like and ALPIDE-like design
2-level FIFO architecture
  L1: column level, to de-randomize injecting charge
  L2: chip level, to match in/out data rate between core and interface
Trigger readout:
  Coincidence by time stamp, matched event read out

## Slide 32: Pixel Analog design
CEPC time stamping precision requirement:
  25-100ns, better to time stamping each collision at Z pole
Taichu-1 pixel analog design:
  50ns~150ns (based one standard CMOS MAPS tech.)
  Consider to use depleted CMOS MAPS

## Slide 33: Backup: Ladder Mechanical testing
Detailed designs of platform and tooling for different test.
Static (different support and load cases)
Vibration and cooling + pressed air (different cases):
  Measure Deformation, temperature, air speed, flow rate, etc.
Goal: Measure vibration to 1μm level with air cooling with laser interferometer

## Slide 34: Data acquisition system
Preliminary design of data acquisition system(DAQ)
  Ladders are reader by readout boards
  All readout boards connected to computer through a switch
  User interface developed
  DAQ tested in five modules equipped with MIMOSA sensors
DAQ Tests with 5 MIMOSA chips
DAQ system data display
Tested with MIMOSA modules

## Slide 35: Main specs of the full size chip for high rate vertex detector
Bunch spacing
  CEPC Z+Higgs (240GeV): 680ns;
  WW threshold scan (160GeV): 210ns;
  CEPC Z pole runing (90GeV) Z: 25ns
High Hit density
  2.5hits/bunch/cm2 for Higgs/WW runs
  0.2hits/bunch/cm2 for Z pole running

## Slide 36: backup :
Preliminary
  Good chip function and noise performance proved to 2.5 Mrad,
pixel threshold vs. TID
Mean threshold of a column vs. TID
pixel noise vs. TID
Mean noise of column vs. TID

## Slide 37: Backup:
  The threshold was initially set at the minimum level. After ~1 Mrad, the pedestal level was shifted to see noise floor in S-curves, so the threshold level was set higher.
Probed pixel pedestal vs. TID
S-curve of pixel (7, 120) in S1
S-curve of pixel (40, 120) in S3
Probed pixel amplitude vs. TID

## Slide 38: Publications and International talks
International conference talks:
  Joao Guimaraes Da Costa, CepC phys/detectors, Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
  T. Wu , A full functional Monolithic Active Pixel Sensor prototype for the CEPC vertex detector, in proceeding of International Conference on Electronics Circuits and Systems, Nov. 27-29, 2019, Genova, Italy.
  Xiaomin Wei, High data-rate readout logic design for 1024*512 CMOS pixel array dedicated for CEPC experiment, International workshop on radiation imaging detectors, International workshop on radiation imaging detectors, July 2019, Crete, Greece
  Ying Zhang, Overview of the chip design for the MOST2 CEPC vertex project, Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
  Wei Wei, Full size pixel chip for high-rate CEPC Vertex Detector，Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
JINST 14 (2019) C12012
IEEE ICECS (doi: 10.1109/ICECS46596.2019.8965105.)
Publication:

## Slide 39: Task 2: Physics goal
Higgs precision measurement
  H → bb precise vertex reconstruction
  H → μμ (precise momentum measurement)
Main technology
  High spatial resolution technology → pixel detector
  Low-mass detector technology
  Radiation resistance technology
Need tracking detector with
high spatial resolution, low material

## Slide 40: Goal for the third year(2020.7 –2021.6)
Achieve the target in task book for the 3rd years
  Build the support structure prototype for ladder
  Finalize the full-size sensor design , and write a design report
  Complete the testing of 2nd MPW Taichu chip, write a testing report
  Complete initial design of readout electronics and DAQ for vertex detector prototype

## Slide 41: Electrical test
Electrical performance verified by injecting an external charge into pixel front-end
Analog output of a pixel @ Vin = 0.9 V

## Slide 42: Electrical test （2）
Four sectors with FEI3-like digital logic works well
and show similar noise performance for 4 different pixel design.
S1 sector design shows the minimum threshold.

## Slide 43: X ray tests and beta source tests
Analog output waveform agreed with the simulation
for the small signal, the S/N ratio was also good
Beta source Tests
X ray tube test

## Slide 44: CMOS Monolithic pixel sensor
CMOS Monolithic pixel (CIS process) is ideal for CEPC application
  low material budget (can be thin down to 50μm)
  This project use TowerJazz CIS 180nm technology
Hybrid pixel technology developed by ATLAS and CMS
  Thickness of sensor is about 200~300 μm
  Need to bump bonding with readout ASIC (ASIC thickness is about 300μm)
  Material budget about silicon sensor is about 10 times larger than CIS process
Hybrid pixel

## Slide 45: Research Team in task 2
课题2：IHEP - 中国科学院高能物理研究所
                SDU - 山东大学
                NJU - 南京大学
                NWU - 西北工业大学
4 institutes
Institutes | Tasks
IHEP | Full CMOS chip modeling, Pixel Analog, PLL block Detector module (ladder) prototyping Data acquisition system R & D Vertex detector assembly and commissioning
CCNU/IFAE | CMOS sensor chip: Pixel Digital
NWPU | CMOS sensor chip: Periphery Logic, LDO
SDU | CMOS sensor chip: Bias generation, TCAD simulation Sensor test board design
NJU | Irradiation, test beam organization
Notes: Total 51, average age is 39
Acc: 39=703/18
Silicon: 39=866/22
HCAL: 40=440/11
Total: 39

## Slide 46: TaichuPix radiation test
Completed two round of CMOS sensor prototyping
  First Radiation test up to 30Mrad at BSRF , TaichuPix2 is still functional
  TaichuPix-2 irradiated at BSRF 1W2B beamline (6 keV X-ray)
    Dose rate ~17.63 krad/min for the first 2.5 Mrad
    then 211.56 krad/min for 51 min, then 1.24 Mrad/min for 15 min
    Dose rates were calibrated with an ion chamber before test
Radiation test at BSRF for 2nd MPW chip

## Slide 47: TaichuPix radiation test (2)
  Good chip function and noise performance proved to 2.5 Mrad,
  no deterioration observed when TID up to 30 Mrad.

## Slide 48: TaichuPix radiation test (3)
Preliminary
Current [mA]
  No deterioration observed when TID up to 30 Mrad.