## Slide 1: Garfield simulation with different gas mixtures
Siman Liu, Linghui Wu, Guang Zhao, Shuiting Xin , Weimin Song
Cluster Counting Meeting
Sept 30th, 2021

## Slide 2: Outline
Introduction
Ionization
Drift velocity
Longitudinal diffusion
Summary

## Slide 3: Introduction
The choice of the gas mixture is essential. To improve reliability of the cluster counting, some characteristics would be expected
  Low cluster density to achieve high counting efficiency
  Low drift velocity helps to identify clusters in time
  Small longitudinal diffusion to avoid overcounting on the clusters with more than one electrons
A study with Garfield++ is performed to understand the property of different gas mixtures
  He + iC4H10
  He + C3H8
  He + C2H6
  He + CH4
In this talk , data on He+CH4 were added.

## Slide 4: Cluster density
Cluster density : (at the same ratio of He)
iC4H10 > C3H8 >C2H6>CH4
He ratio Cluster density
Incident particle: 10 GeV/c pion
Gas pressure: 1 atm

## Slide 5: Cluster size
Most clusters have only one electron (85~91%)
A few percent of clusters have more than two electrons

## Slide 6
Drift velocity vs E
Gas pressure: 1 atm
Increasing ratio of He helps to reduce the drift velocity

## Slide 7
Drift velocity vs E
With the same ratio of He, He+CH4 has the lower drift velocity
Gas pressure: 1 atm

## Slide 8: Simulation of drift time to distance relation and diffusion
Cell size: 2cm × 2cm
High voltage on sense wire: 2500V
Magnetic field : 3T
Gas pressure: 1 atm
Drift distance
Electron
Configurations:

## Slide 9: Drift time vs drift distance
Increasing ratio of He helps to reduce the drift velocity

## Slide 10: Drift time
When the ratio of He is 90%，
He+CH4 and He+C2H6 have the longer drift time
When the ratio of He is 80%，
He+C2H6 have the longer drift time

## Slide 11: Longitudinal diffusion vs drift distance
The higher ratio of He, the larger diffusion

## Slide 12: Longitudinal diffusion
With the same ratio of He, diffusion of gas with iC4H10 is smaller in most cases

## Slide 13: Summary
Comparison of ionization, drift velocity and diffusion between different gas mixtures performed
  Increasing the ratio of He
    helps to reduce the cluster density and drift velocity
    but causes the diffusion to be more serious
  With the same ratio of He
    diffusion of gas with iC4H10 is smaller in most cases
    the gas with CH4 has lower drift velocity and cluster density

## Slide 14: Thanks!

## Slide 15: Back up

## Slide 16
Drift velocity vs E
Gas pressure: 1 atm

## Slide 17
Drift velocity
E = 2000 V/cm | 
gas composition | Drift velocity (cm/μs)
He/IC4H10 (50/50) | 3.835
He/IC4H10 (60/40) | 3.693
He/IC4H10 (70/30) | 3.482
He/IC4H10 (80/20) | 3.139
He/IC4H10 (90/10) | 2.552
He/C3H8 (50/50) | 3.657
He/C3H8 (60/40) | 3.457
He/C3H8 (70/30) | 3.196
He/C3H8 (80/20) | 2.823
He/C3H8 (90/10) | 2.287
He/C2H6 (50/50) | 3.760
He/C2H6 (60/40) | 3.442
He/C2H6 (70/30) | 3.084
He/C2H6 (80/20) | 2.665
He/C2H6 (90/10) | 2.169
He/CH4 (50/50) | 4.364
He/CH4 (60/40) | 3.784
He/CH4 (70/30) | 3.201
He/CH4 (80/20) | 2.619
He/CH4 (90/10) | 2.073
E = 2000 V/cm | 
gas composition | Drift velocity (cm/μs)
He/IC4H10 (50/50) | 4.435
He/IC4H10 (60/40) | 4.176
He/IC4H10 (70/30) | 3.854
He/IC4H10 (80/20) | 3.460
He/IC4H10 (90/10) | 3.002
He/C3H8 (50/50) | 4.048
He/C3H8 (60/40) | 3.788
He/C3H8 (70/30) | 3.490
He/C3H8 (80/20) | 3.153
He/C3H8 (90/10) | 2.799
He/C2H6 (50/50) | 4.009
He/C2H6 (60/40) | 3.699
He/C2H6 (70/30) | 3.378
He/C2H6 (80/20) | 3.057
He/C2H6 (90/10) | 2.757
He/CH4 (50/50) | 4.199
He/CH4 (60/40) | 3.727
He/CH4 (70/30) | 3.316
He/CH4 (80/20) | 2.966
He/CH4 (90/10) | 2.704

## Slide 18: Drift time vs drift distance

## Slide 19: Drift time
Drift distance = 1.0 cm | 
gas composition | Drift time (ns)
He/IC4H10 (50/50) | 429.1
He/IC4H10 (60/40) | 423.9
He/IC4H10 (70/30) | 427
He/IC4H10 (80/20) | 445.2
He/IC4H10 (90/10) | 503.8
He/C3H8 (50/50) | 372.1
He/C3H8 (60/40) | 394.3
He/C3H8 (70/30) | 423.3
He/C3H8 (80/20) | 467.2
He/C3H8 (90/10) | 551.5
He/C2H6 (50/50) | 333.8
He/C2H6 (60/40) | 368.6
He/C2H6 (70/30) | 411.5
He/C2H6 (80/20) | 471.5
He/C2H6 (90/10) | 577.7
He/CH4 (50/50) | 285.8
He/CH4 (60/40) | 327.9
He/CH4 (70/30) | 378.8
He/CH4 (80/20) | 448.4
He/CH4 (90/10) | 572.4
Drift distance = 0.5 cm | 
gas composition | Drift time (ns)
He/IC4H10 (50/50) | 142.5
He/IC4H10 (60/40) | 146.3
He/IC4H10 (70/30) | 153.1
He/IC4H10 (80/20) | 165.8
He/IC4H10 (90/10) | 195.4
He/C3H8 (50/50) | 143.4
He/C3H8 (60/40) | 151.8
He/C3H8 (70/30) | 163.1
He/C3H8 (80/20) | 180.6
He/C3H8 (90/10) | 216.1
He/C2H6 (50/50) | 134.4
He/C2H6 (60/40) | 146.6
He/C2H6 (70/30) | 162.8
He/C2H6 (80/20) | 186.3
He/C2H6 (90/10) | 228.8
He/CH4 (50/50) | 114.5
He/CH4 (60/40) | 131
He/CH4 (70/30) | 151.9
He/CH4 (80/20) | 181.3
He/CH4 (90/10) | 234