## Slide 1
New idea of Crystal fan Ecal for CEPC
Huaqiao Zhang (IHEP)
With usefull discussion with Yong Liu, Gang Li, Qian Liu, Manqi, Shengsun, Jianbei, Jianchun,Joao et. al…

## Slide 2: Requirement of a CEPC Ecal
A PFA calorimeter
  Good Shower separation
    Small Moliere radius (Dense detector)
    High granularity/segmentation (~Moliere radius)
Good energy resolution
  Critical in some special process
Cost is key issue
  Crystal vs silicon vs others
  Less readout…
  Service and operation…
Overlap removal

## Slide 3: Exsiting options
Full silicon + Tunstan (Very popular in ILC/CEPC)
  Good position resolution
  Timing information
  Expensive
  Not good energy resolution at low E
Crystal
  Good Energy resolution
  Relative cheaper compared to Si. option
  Not good at granularity (3D postioning difficult)
Develeping:
  Crystal bar, dual readout…
2018 JINST 13 P03010

## Slide 4: Outline of this talk
New Idea of crystal fan (barrel only for the moment)
  Pure crystal fan option
    2D readout, 3D position information
    Preliminary simulation
  Improved Hybrid crystal fan with silicon layers option
    Improve near-by shower seperation， r-phi seperation
Summary

## Slide 5: Basical idea
Crystal not pointing back to IP(Z axis)
  Angle with inner det. radius is 𝛼
  𝛼 = 0; point to IP(Z axis)
  𝛼 <= 90 degrees
Segmentation along R
  Ex: N_l = 14 layers
Uniform along Z
  Ex: 1 cm each seg.
Total crystal volumme
  pi*(r2^2-r1^2) * Z
Use BGO as baseline
  ~20.5 radiation length
Each crystal has a readout at R2 surface
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼
CEPC: Z = 6.7 m
r1 = 1.8 m, r2 = 2.03 m
readout
Cylindrical coordinate system
（Z, R, phi）

## Slide 6: Some calculations
3 DoF. determined the full barrel design (For a given R1, R2)
  𝛼: [0,90] : pointing angle
  N_l:[1,2,3….]:
  Z: for the moment choose 1 cm segmentation, uniformly
Crystal length D = sqrt(r2^2 – r1^2*sin(𝛼)^2) – r1*cos𝛼
Crystal bar open phi angle ȹ = acos(r2^2 + r1^2 -D^2)/(2*r1*r2)
Phi segmentation = ȹ/N_l
Total number of crystal bars per Z segmentation: 2*pi*N_l/ȹ
Shower depth along r Sn at nth layer:
  Sn = Fn+1 – Fn
  Fn= r1* ( sin𝛼 /sin(𝛼 –n*ȹ/N_l) – 1 )
Crystal thickness xn:
  xn=Sn*sin(𝛼 –n*ȹ/N_l)

## Slide 7: Example configuration 1
Take 𝛼 = 0 degrees, transverse 1 layers
D=0.230 m
ȹ=0.0056 (0.32degree）
  Crystal: 23 cm *1cm * ~1cm
ȹ/N_l = 0.0056
Each z segmentation
  1130 crystals
BES III / CMS like
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼

## Slide 8: Example configuration 2 (more conf. in backup)
Take 𝛼 = 15 degrees, transverse 5 layers
D=0.237 m
ȹ=0.03 (1.7degree）
ȹ/N_l = 0.006
Each z segmentation
  1038 crystals
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼
Compared to configuration 1, Similar readouts, similar phi segmentation, 5 times more layers along r
Issue: possible confusion on phi/r

## Slide 9: A typical design
Take 𝛼 = 30 degrees, transverse 14 layers
D=0.260 m
ȹ=0.064 (3.7degree）
ȹ/N_l=0.0046
Each z segmentation
  1368 crystals
Crystal bar：261*7.4*10 mm3
CAD Credit: Xiao Zhao

## Slide 10: Simulation configuration
Configuarable Geometry already implemented into CEPCSW
Ecal dimension: R1 = 1.9 m; R2 = 2.135m; Z = 6.7 m;
Crystal(BGO) dimention: 26.2 cm * 1cm(Z) * ~0.75 cm (phi)
Alpha = 30 degree; R segementation = 13 -14
Phi segmentation: 1368; Z segmentation = 670
Thanks a lot for Chengdong Fu, super fast implementation

## Slide 11: Basical checks (1)
e- particle gun, theta = 90 degree, phi = 180 degree, 100 GeV
  40 simulated events, no energy threshold applied yet
occupancy
Energy weighted occupancy
Z segmentation
Phi

## Slide 12: Basical checks (2)
Particle pointing at crystal:
  phi ID = 684/685(w.o. correction of curvature in mag.); z ID = 335/336;
Occupancy: phi ID = 694.1 +- 14.6; z ID = 336 +- 12.5
Energy weighted: phi ID = 693.5 +- 3.14; z ID = 335.5 +- 1.5
Step of phi = 0.263 degree; Step of Z = 1 cm
Phi: +-2.6 cm; z +-1.5cm

## Slide 13: 4D Reconstruction
Very preliminary idea
  1: Find the shower cluster in Z-phi plane
  2: Use shower edge of phi define shower phi at inner circle (ȹ0, r1)
  3: Use phi distance to step 2 shower edge to calculate rn = r1 + Sn; the position of layer n is (ȹ0, rn)
  4: Z from Z axis index, energy from crystal bar readout
CAD Credit: Xiao Zhao
- | - | 1 | 2 | 3 | 4 | 5 | 6 | - | -
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 3 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 5 | 9 | 7 | 4 | 1 | 0 | 0
0 | 0 | 0 | 2 | 5 | 3 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
ȹ
Z
…4,3,2,1

## Slide 14: Cluster reco
Start: 688, due to electron curved in magnetic field (phi=180 degrees pointing between 684 and 685)
Ended at 700
All 13 layers have energy readout (above certain th)
40 events
1 event
(phi,r1)
140 events

## Slide 15: Crystal fan with silicion layers
Silicon layers: plate tiled by hexagon silicon module
Insert along Z axis, replace crystal bars with same phi
Provide r, phi information to reduce crystal r-phi amibigurity
CMS HGCal like Module
L= N*83mm, N=2,3,4…
CMS HGCal like module, 6.4mm thick, could fit alpha=30, 14 layer senario (7.17-7.4mm thick)
Slicon layer
CAD Credit: Xiao Zhao
SiPIN (or LGAD?) provide accurate 3D position
PCB
Z

## Slide 16: Current status and next steps
Still at proposal stage, many details need to pin down:
  Implemented a baseline crystal fan “geo” (Chengdong)
  Generate benchmark objects for performance study
    Step 1:
      3D segmentation (very preliminary shown here)
      Resolution (position, energy)
        Single electron sample: principle of 4D reco
        Z, R, Phi, E resolution
    Step 2: shower seperation
    Step 3: BMR
  Further Optimization
    Supporting, mounting, calibration, service….
  Prototying… (if feasible/worth to do… )

## Slide 17: Summary
Noval CEPC Crystal fan proposal
  Very uniform along Z and phi (Z-phi symetry)
  Fine segmentation of Z, Phi, r
  2D readout in Z, Phi plane, reduced readout electronics channels
  Readout SiPM+electronics behind Ecal crystal
  Pro.: Phi-R confusion, near by shower confusion…
Improved Hybrid Crystal fan proposal by insert silicon layers
  Help to reduce Phi-r confusion and near-by shower confusion
  Timing information
Performance study plan

## Slide 18: Bacup

## Slide 19: Typical crystals (From Ren-yuan Zhu’s slides)

## Slide 20: Example configure 3
Take 𝛼 = 15 degrees, transverse 10 layers
D=0.237 m
ȹ=0.03 (1.7degree）
ȹ/N_l = 0.003
Each z segmentation
  2077 crystals
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼

## Slide 21: Example configure 4
Take 𝛼 = 30 degrees, transverse 10 layers
D=0.261 m
ȹ=0.064 (3.7degree）
ȹ/N_l=0.0064
Each z segmentation
  977 crystals
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼

## Slide 22: Example configure 5
Take 𝛼 = 60 degrees, transverse 10 layers
D=0.400 m
ȹ=0.17 (9.8degree）
ȹ/N_l = 0.017
Each z segmentation
  366 crystals
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼