## Slide 1: The consideration and status of the Injection/Extraction hardware
Jinhui Chen, Lihua Huo , Yuwen Wu, Hua Shi , Guanjian Wu, Zilin Chen, Guanwen Wang, Lei Wang, X.H. Cui, D. Wang, Yiwei Wang
Injection group
2021-10-28
CEPC DAY 28 oct.2021

## Slide 2: Outline
1
Overview of CEPC Inj./Ext. systems
2
Lambertson magnet
3
Slotted-pipe kicker magnet
4
Ferrite core kicker magnet
5
Summary

## Slide 3
Overview of the CEPC injection and extraction systems

## Slide 4: Layout of the accelerator complex
The CEPC accelerator complex consists of a Linac, which including a small damping ring for positron beams, several transport lines, a booster ring and 2 storage rings, all of which are in a single tunnel.
1.2km
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring
Dump
Dump

## Slide 5: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
In CEPC accelerator complex, there are 9 injection and extraction sub-systems, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 6: Main types of inj.&ext. hardware
 | Sub-system | Kicker Type | Kicker waveform | Septa Type | Thickness of septum
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | Horizontal LMS | ф22/3.5mm
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal LMS | ф55/5.5mm
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф55/6mm
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/2mm
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф55/6mm
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical LMS | Ф55/6mm
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/6mm

## Slide 7: Hardware R&D plan
One team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping.
Hardware R&D activities:
  Lambertson septa magnets
    Outside vacuum magnet: Septum thickness ≥3.5 mm
    Half in vacuum magnet: Septum thickness =2 mm
  Kicker systems
    Strip-line kicker and super fast pulser（PW=10~50ns）
    Slotted-pipe kicker and fast pulser（PW=250~300ns）
    Ferrite core kicker （outside vacuum） and pusler
      Lumped parameter dipole kicker（PW=1.36us half-sine）
      Distributed parameter dipole kicker（ PW=440~2420ns trapezoid）
      Distributed parameter Nonlinear kicker（ PW=440~2420ns trapezoid）
Overlapping part

## Slide 8
Lambertson magnet

## Slide 9: LSM requirements
Parameters | Unit | DR-LSM | BST-LEI-LSM | CR-LSM-2
Quantity | - | 2 | 2 | 2×5
Energy | GeV | 1.1 | 10 | 120
Deflection angle | mrad | 120 | 22 | 0.35
Insertion length | m | 0.5 | 0.8 | 1.75
Magnetic field strength for injected/extracted beam | T | 0.883 | 0.9175 | 0.08
Min. Septum thickness（including septum board, inj./ext. beam pipe wall, installation gap) | mm | 3.5 | 5.5 | 2
Field uniformity | - | <±0.05% | <±0.02% | <±0.05%
Leakage field | - | ≤1×10-3 | ≤1×10-3 | ≤1×10-3
Clearance of stored beam at lambertson（HV） （refer to stored beam orbit） | mm | 36.422 | 3050 | -
Clearance of inj.&ext. beam at lambertson（HV）（refer to inj.&ext. beam orbit） | mm | 2211 | 1829 | -
Physical aperture of stored beam vacuum chamber | mm | 2222 | 5555 | 75x56

## Slide 10: DR and BST LE inj.
DR inj. & ext.
BST LE inj.
Septum=3.5mm
Stored beam
Inj. beam
11mm
5.5mm
11mm
Injected beam | X(mm) | Y(mm) | Z(mm)
LSM in | -30.0 | -23.75 | -500.0
LSM out | 0 | -20 | 0
x
z
Stored
beam
Injected
beam
Top view
-30.0
（mm）
y
z
Stored
beam
Injected
beam
septum
Side view
（mm）
Stored beam | X(mm) | Y(mm) | Z(mm)
LSM in | 0 | 0 | -500.0
LSM out | 0 | 0 | 0
Septum=5.5mm
Stored beam
Inj. beam
27.5mm
14mm
27.5mm
Injected beam | X(mm) | Y(mm) | Z(mm)
LSM in | -22.0 | -50 | -800.0
LSM out | 0 | -50 | 0
Stored beam | X(mm) | Y(mm) | Z(mm)
LSM in | 0 | 0 | -800.0
LSM out | 0 | 0 | 0
x
z
Stored
beam
Injected
beam
Top view
-22.0
（mm）
y
z
Stored
beam
Injected
beam
septum
Side view
（mm）
-50.0

## Slide 11: LSM physics design for DR
Stored beam chamber
(VP,FeCoV,1J22)
Injected beam chamber
(SS, 316L)
Yoke (DT4)
Winding (96T)
Stored beam
Inj. beam
Exit of LSM
Stored beam pipe(VP) inner
diameter= ø22mm,
Thickness=2mm
Injected beam pipe (SS):
W=41mm, H=19mm,
Thickness=1mm
Septum
Thickness=2+1+0.5=3.5mm
Magnet gap: 22mm
Winding:
W=70mm,H=105mm,T=96
Exciting current=166A
Inductance=0.0228H
700×344×268mm
Injected beam
Stored beam
Magnet pole
Installation margin
Yoke
1mm
2mm
0.5mm
3.5mm
Φ22mm
1J22
316L
41×19mm
Contributed By Yuwen Wu

## Slide 12: 3D simulation
Stored beam vacuum chamber:1J22
Center magnetic field intensity：8836Gauss
Magnet effective length：542mm
Vertical Leakage field：2.81E-04
Horizontal Leakage field：1.79E-06

## Slide 13: LSM physics design for BST LE-Inj.
Stored beam chamber
(VP,FeCoV,1J22)
Injected beam chamber
(SS, 316L)
Stored beam pipe(VP) inner
diameter= ø55mm,
Thickness=4mm
Injected beam pipe (SS):
inner diameter=ø29mm,
Thickness=1mm
Septum
Thickness=4+1+0.5=5.5mm
Magnet gap: 32mm
Winding:
W=70mm,H=140mm,T=128
Exciting current=188A
Inductance=0.0682H
Yoke (DT4)
Winding (96T)
Stored beam
Inj. beam
1000×383×343mm
Exit of LSM
Injected beam
Stored beam
Magnet pole
Installation margin
Yoke
1mm
4mm
0.5mm
5.5mm
Φ55mm
1J22
316L
Φ29mm
Contributed By Yuwen Wu

## Slide 14: 3D simulation
Stored beam vacuum chamber:1J22
Center magnetic field intensity：9200Gauss
Magnet effective length：849mm
Vertical Leakage field： 4.41E-04
Horizontal Leakage field： 1.56E-04

## Slide 15: LSM prototype for HEPS BST
FeCoV（1J22）
Fe（DT4）
Stainless Steel(304)
Stainless Steel(304)
Fe（DT4）
FeCoV（1J22）

## Slide 16
Slotted-pipe Kicker magnet

## Slide 17: DR inj./ext. kicker design parameters
parameter | Unit | DR-kicker
Quantity | - | 2
Type | - | Slotted-pipe kicker
Deflect direction | - | Vertical
Beam Energy | GeV | 1.1
Deflect angle | mrad | 10.7
Magnetic effective length | m | 1.4
Magnetic strength | T | 0.0281
Integral magnetic strength | T·m | 0.03934
Clearance region(H×V) | mm | 32.8×26.6
Good field region(H×V) | mm | 19.8×16
Field uniformity in good field region | - | ±1.5%
Repetition rate | Hz | 100
Amplitude repeatability | - | ±0.5%
Pulse jitter | ns | ≤5
Bottom width of half sine pulse(5%-5%) | ns | < 250

## Slide 18: Magnet physics design
2D simulation model
Max. voltage of coil: Umax=10622V
Max. exciting current: Imax=2400A
Magnet coil inductance=387nH
Good field region
19.8×16mm
x=±10, y=±8
Un.= -0.9%~1.5%
Good field region: 19.8×16mm
Field uniformity: -0.9%~1.5%
Contributed By Lihua Huo,Lei Wang

## Slide 19: Slotted-pipe kicker engineer design
Outer body (316L)
Busses (FOC)
insulation support (ceramic)
HV feedthrough
Cooling water pipe
+
-
To vacuum pump

## Slide 20: Prototype kicker for HEPS BST

## Slide 21: 250ns-fast kicker pulser design
Scheme: 20-stage inductive adder based on SiC-MOSFETs.
The co-axial transformer is configured as bipolar output.
The pulser is located outside tunnel and 10 50 Ω cables with length more than 30m are applied to connect with kicker.
Matching terminal resistor is 10Ω.
20-stage inductive adder

## Slide 22: First switching cell prototype test
VDS=1.62kV
VDS=1.2kV
Vout=-1.176kV
RL=0.5Ω

## Slide 23: Pulser prototype assembly

## Slide 24
Ferrite core kicker magnet

## Slide 25: BST EXT kicker design parameters
parameter | Unit | BST-EXT-kicker1 （for CR off-axis inj.） | BST-EXT-kicker2 （for CR on-axis inj.）
Quantity | - | 2 | 2
Type | - | In-air delay-line dipole kicker | In-air lumped parameter dipole kicker
Deflect direction | - | Horizontal | Horizontal
Beam Energy | GeV | 120 | 120
Deflect angle | mrad | 0.2 | 0.1
Magnetic effective length | m | 1.4 | 0.7
Magnetic strength | T | 0.06 | 0.06
Integral magnetic strength | T·m | 0.08 | 0.04
Clearance region(H×V) | mm | 55×55 | 55×55
Good field region(H×V) | mm | ? | ?
Field uniformity in good field region | - | ±1.5%？ | ±1.5%？
Repetition rate | Hz | 1k | 1k
Amplitude repeatability | - | ±0.5% | ±0.5%
Pulse jitter | ns | ≤5 | ≤5
Bottom width of pulse(5%-5%) | ns | Trapezoid：440~2420 | Half-sine：1360
Tr/Tf(5%-95%) | ns | <200 | <680
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 26: Kicker magnet physics design
h=64mm
W=68mm
55mm
4mm
L=
I=
U=I
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Ferrite core
Kicker magnet type | Pulse discharge mode | Magnetic field rise time Tr (5%-95%)
Lumped parameter | Shorted end | 3τ=561ns
Lumped parameter | Matching | 3τ/2=280.5ns
Delay-line | Matching | τ=187ns

## Slide 27
Lumped parameter dipole kicker system
Features:
Out-vacuum kicker with metallic coating ceramic vacuum chamber
<1360ns,1kHz
Ferrite core
Ceramic vacuum chamber
Eddy current Shielding plate
HV conductor

## Slide 28: Novel half-sine wave pulser
SIC 1200V SBD
IGBT
Inductive adder + LC resonance discharge circuit (IGBT+SBD)
Imax=2326.5A(2500A)
L=194nH(250nH)
C=25nF
Tw=π√LC=248.4ns
Z=√L/C=3.16Ω
U=7357V(8000V)
IGBT quantity=10*4=40
920mm
510mm
564mm

## Slide 29: Delay-line dipole kicker system
The structure of delay-line kicker is complicated, but helps to achieve ideal trapezoid waveform.
200ns
40~2000ns
200ns
1kHz
challenges
Pulser
Delay-line kicker
Lumped parameter kicker
PFN
Delay-line kicker magnet

## Slide 30: Dual-C type delay-line dipole kicker design
Ferrite core
Base
Ceramic support
Eddy current Shielding plate
Ceramic Vacuum chamber
Capacitor plate@
High potential
Capacitor plate @
Ground potential
HV conductor
High potential Lead
ground potential Lead

## Slide 31: Trapezoid wave pulser
Adjustable pulse width trapezoid waveform pulser based on SiC MOSFET
Energy storage component
  Capacitor ： Flat-top dropping compensate topology
  PFN ：low impedance
Power stacking topology
  inductive adder: not fit for long pulse
  Marx generator: hard to control structure impedance
PFN
Delay-line kicker magnet
200ns
40~2000ns
200ns
1kHz
Solid-state switches（SIC MOSFET）
Marx generator
Or
Cap.
challenges
Inductive adder

## Slide 32: Ceramic vacuum chamber
Chart: Wall thickness/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
octagon | 2.37 | 3.17 | 4.38 | 6.38 | 9.83 | 16.4 | 30.5 | 66.2 | 172
race track | 1.78 | 2.29 | 3.04 | 4.15 | 5.83 | 8.34 | 12 | 17.5 | 25.4
ellipse | 1.4 | 1.73 | 2.24 | 2.95 | 4.01 | 5.49 | 7.4 | 10.2 | 13.5
L=1.2m，thickness=5mm
ceramic vacuum chamber with special pattern metallic coating is key component for outside-vacuum kicker magnet.
ellipse
octagon
Race track
Ceramic material: 99% AL2O3
√
Integrated sintering

## Slide 33: Magnetron sputtering coating prepare
Movable solenoid
Solenoid coil
Inner diameter=208mm
Length =700mm
Good field region=500mm
According to the experience of coating, the cathode target discharge is unstable for long vacuum chamber more than 600mm and it is easy to cause ignition or local film formation failure.
So, sectional coating method by a movable solenoid is proposed for our 1.2m ceramic vacuum chamber. The coating experiment shows uniform coating achieved in one antechamber of 1m.
In order to obtain uniform coating inner racing track shape vacuum chamber, a horizontal movable cathode wire target solution is proposed.
The antechamber for HEPS
(inner aperture=6mm)
1m
Cathode wire
Moving track
view window
Cathode pole
Graduated bellows is used to adjust the horizontal position of cathode wire (compression at one end and tension at the other end)

## Slide 34: Film pattern study
Strip film
Mesh film
Ladder film
Spiral film
Comb film
Metallic coating on the inner wall of ceramic vacuum chamber is provided for beam mirror current as path .
The continuous uniform film on the wall of ceramic vacuum chamber can form large loop eddy current under fast pulse magnetic field, which has a great influence on the magnetic field.
An appropriate coating pattern can solve this contradiction at the same time.The design principles of coating pattern are as follows:
  The upstream and downstream of films are not connected to prevent the occurrence of large loop;
  The films shall cross to form a capacitor structure as far as possible to provide a path for high-frequency beam mirror current.
√
×

## Slide 35: Parts of simulation result
coil
ferrite
Ceramic vacuum chamber
Metallic film(spiral)
COMSOL 3D Model
Coil exciting current pulse
Central field deformation caused by different pattern films
the film square resistance is set to 0.2 Ω (equivalent to 86nm copper film or 1.1 μm TiN film)
Material conductivity is set to 5000S / m, and the corresponding thickness is 1mm.

## Slide 36: Delay-line Nonlinear Kicker (NLK)
Differential mode exciting
Common mode exciting
Injected bunch
stored bunch
Dipole field
Nonlinear field
Thinking about if the nonlinear kicker injection is possible for CEPC, after all this top-up injection scheme should loose the requirement of DA.

## Slide 37: Delay-line NLK preliminary design
Capacitor plate@
High potential
HV conductor
Ferrite core
Base
Capacitor plate @
Ground potential
Ceramic Vacuum chamber
ground potential Lead
High potential Lead
Eddy current Shielding plate
Ceramic support

## Slide 38: Summary
In CEPC accelerator complex，there are 9 inj. and ext. sub-systems. The types of all inj./ext. components are determined. The hardware designs towards TDR are being carried out.
One team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping.
The Lambertson septa with septum=3.5mm and slotted-pipe kicker system with 300ns half-sine wave for HEPS is on the way. R&D of delay-line kicker and ceramic chamber are just started.

## Slide 39
END
Thank you for attentions!!!

## Slide 40: abstract
The type of CEPC injection and extraction hardware including Lambertson septa，strip-line kicker，slotted-pipe kicker, Lumped parameter ferrite core kicker，and delay-line fast kicker.
The hardware designs towards TDR are being carried out. One team is in charge of both HEPS and CEPC inj. & ext. system. Some hardware R&D are overlapping.

## Slide 41
Backup slides

## Slide 42: Booster Ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 10 | 120 |  | 10 | 80 | 10 | 45.5
Function | Injection （both） | Extraction （off-axis） | Inj./Ext. （on-axis） | Injection （off-axis） | Extraction （off-axis） | Injection （off-axis） | Extraction （off-axis）
Bunch number | 242（in half ring） |  | 7（in half ring） | 1524（uniform） |  | 6000 | 
Min. bunch spacing （ns） | 680 |  | 23800 | 220 |  | 25 | 
Bunch number per train× train number | - |  | - | - | - | 80×75 | 
Train spacing （ns） | - |  | - | - | - | 2460 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 100 | 1000 |  | 100 | 1000 | 100 | 1000
Kicker pulse width (ns) | 1360 |  |  | 440 |  | 50 | <6900
Kicker flat top（ns） | - |  |  | - |  | - | >1980
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <25 | <2460
Timing delay(ns) | <680 |  | <23800 | <220 |  | <2460 | <4400
injection（extraction）period (s) | 2.42 | 0.242 | 0.007 | 15.24 | 1.5 | 60 | 0.075
Kick angle (mrad) | 0.11 | 0.2 | 0.1 | 0.11 | 0.2 | 0.11 | 0.2
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04 | 0.004 | 0.05 | 0.004 | 0.03
Beam pipe aperture Φ（mm） | 55 |  |  |  |  |  | 
Considering the compatibility of three operating modes:
Function | LE-Injection （both） | HE-Extraction （off-axis） | HE-Inj./Ext. （on-axis）
Kicker repetition rate (Hz) | 100 | 1000 | 1000
Kicker pulse width (ns) | 50 | 440~2420(Adjustable) | 1360
Kicker flat top（ns） | - | 0~1980(Adjustable) | -
Kicker rise（fall）time(ns) | <25 | <220 | <680
injection（extraction）period (s) | 60 | 1.5 | 0.007
Kick angle (mrad) | 0.11 | 0.2 | 0.1
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04
Beam pipe aperture Φ（mm） | 55 | 55 | 55
50ns,100Hz
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 43: Collider ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 120 |  |  | 80 |  | 45.5 | 
Function | Injection （off-axis） | Injection （on-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump）
Bunch number | 242（in half ring）- 7 |  |  | 1524（uniform） |  | 12000 | 
Min. bunch spacing （ns） | 680 |  |  | 220 |  | 25 | 
Bunch number per train× train number | - |  |  | - |  | 80×150 | 
Train spacing （ns） | - |  |  | - |  | 245 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Train by train | 
Kicker repetition rate (Hz) | 1000 |  |  | 1000 |  | 1000 | 
Kicker pulse width (ns) | 1360 |  |  | 440 |  | <2460 | 
Kicker flat top（ns） | - |  |  | - |  | >1980 | 
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <245 | 
Timing delay(ns) | <680 | <23800 | <680 | <220 |  | <4400 | 
injection（extraction）period (s) | 0.242 | 0.007 | 0.242 | 1.5 |  | 0.15 | 
Kick angle (mrad) | 0.1 | 0.2 | 0.2 | 0.1 | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.04 | 0.08 | 0.08 | 0.027 | 0.05 | 0.015 | 0.03
Beam pipe aperture HxV（mm） | 75×56 |  |  |  |  |  | 
Function | Injection （on-axis） | Injection （off-axis） | Extraction （dump）
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440~2420(Adjustable) | 440~2420(Adjustable)
Kicker flat top（ns） | - | 0~1980(Adjustable) | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <680 | <220 | <220
injection（extraction）period (s) | 0.007 | 1.5 | 1.5
Kick angle (mrad) | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.08 | 0.04 | 0.08
Beam pipe aperture HxV（mm） | 75×56 | 75×56 | 75×56
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Considering the compatibility of three operating modes:
200ns
40~2000ns
200ns
1kHz