## Slide 1
New idea of Crystal fan(晶扇) Ecal for CEPC
张华桥(IHEP, Beijing)
With usefull discussion with Yong Liu, Gang Li, Qian Liu, Manqi, Shengsun, Jianbei, Jianchun etc…

## Slide 2: Requirement of a PFA calorimeter
Good Shower separation
  Small Moliere radius (Dense detector)
  High lateral granularity (~Moliere radius)
High Granularity is crucial
  Dense lower power consume electronics
Energy resolution
  Could use sampling calorimeter
  Critical in some special process
Cost is key issue…
Overlap removal

## Slide 3: Exsiting options
Full silicon + Tunstan
  Very popular in ILC/CEPC
  Good position resolution
  Good logitudinal segmentation
  Expensive
  No good energy resolution at low E
Crystal
  Good Energy resolution
  Relative cheaper compared to Si. option
  Not good at granularity (3D postioning difficult)
Develeping: crystal bar, dual readout…
2018 JINST 13 P03010

## Slide 4: Outline
New Idea of crystal fan (barrel only for the moment)
  Pure crystal option
    2D readout, 3D position information
  Improved Hybrid crystal fan with silicon layers option
    Improve near-by shower seperation/phi seperation

## Slide 5: Basical idea (1)
Crystal not pointing back to IP(Z axis)
  Angle with inner det. radius is 𝛼
  𝛼 = 0; point to IP(Z axis)
  𝛼 <= 90 degrees
Transverse Segmentation
  Ex: N_l = 10 layers
Uniform along Z
  Ex: 1 cm each seg.
Total crystal volumme
  pi*(r2^2-r1^2) * Z
Use BGO as baseline
  ~20.5 radiation length
r1
r2
D
ȹ
𝛼=0
Crystal module
𝛼
r1 = 1.8 m, r2 = 2.03 m

## Slide 6: Some calculations
3 degree of freedom determined the full barrel design
  𝛼: [0,90]
  N_l: [1,2,3….]
  Z: for the moment choose 1 cm segmentation, uniformly
Crystal length D = sqrt(r2^2 – r1^2*sin(𝛼)^2) – r1*cos𝛼
Crystal bar open phi angle ȹ = acos(r2^2 + r1^2 -D^2)/(2*r1*r2)
  Ambiguity with Z
Phi segmentation = ȹ/N_l
Total number of crystal bars per Z segmentation: 2*pi*N_l/ȹ
Shower thickness(depth along r) Sn at inner layer starting point:
  Fn= r1* ( sin𝛼 /sin(𝛼 –n*ȹ/N_l) – 1 )
  Sn = Fn+1 - Fn
Crystal thickness xn:
  xn=Sn*sin(𝛼 –n*ȹ/N_l)

## Slide 7: Example configuration 1
Take 𝛼 = 0 degrees, transverse 1 layers
D=0.230 m
ȹ=0.0056 (0.32degree）
  Assume 1cm * 1cm
ȹ/N_l = 0.0056
Each z segmentation
  1130 crystals
r1
r2
D
ȹ
Pure crystal
Crystal module
𝛼

## Slide 8: Example configuration 2
Take 𝛼 = 15 degrees, transverse 5 layers
D=0.237 m
ȹ=0.03 (1.7degree）
ȹ/N_l = 0.006
Each z segmentation
  1038 crystals
r1
r2
D
ȹ
Pure crystal
Crystal module
𝛼
Similar readouts, similar phi segmentation, 5 times more layers along r
Issue: possible confusion on phi/r

## Slide 9: A typical design
Take 𝛼 = 30 degrees, transverse 14 layers
D=0.260 m
ȹ=0.064 (3.7degree）
ȹ/N_l=0.0046
Each z segmentation
  1368 crystals
Crystal bar：261*7.4*10 mm3
CAD Credit: Xiao Zhao

## Slide 10: 4D Reconstruction
Very preliminary idea
  1: Find the shower cluster in Z-phi plane
  2: Use shower edge of phi define shower phi at inner circle (ȹ0, r1)
  3: Use phi distance to step 2 edg to calculate r = r1 + Sn; (ȹ0, r )
  4: Z from Z axis index, energy from readout
CAD Credit: Xiao Zhao
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 3 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 5 | 9 | 7 | 4 | 1 | 0 | 0
0 | 0 | 0 | 2 | 5 | 3 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Still confusion with near by cluster yet to be check
ȹ
Z

## Slide 11: Design of silicion super layer
Silicon layers: plate tiled by hexagon silicon module
Insert along Z axis, replace crystal bars with same starting phi
Provide r, phi information to reduce crystal r-phi amibigurity
CMS HGCal like Module
L= N*83mm, N=2,3,4…
CMS HGCal layers, 6.4mm thick, could fit alpha=30, 14 layer senario(7.17-7.4mm thick)
Slicon layer
CAD Credit: Xiao Zhao

## Slide 12: Current status
Still at proposal stage, many details need to pin down:
  Implement a baseline crystal fan “geo” (Chengdong)
  Generate benchmark objects for performance study
    Step 1: 3D segmentation (very preliminary shown here)
    Step 2: shower seperation
    Step 3: BMR
  Further Optimization
    Supporting, mounting, calibration, service….
  Prototying… (if feasible/worth to do… )

## Slide 13: Summary
Noval CEPC Crystal fan proposal
  Very uniform along Z and phi (Z-phi symetry)
  Fine segmentation of Z, Phi, r
  2D readout in Z, Phi plane, reduced readout electronics channels
  Readout SiPM+electronics can safely hiden after Ecal
  Pro.: Phi-r confusion, near by shower confusion…
Hybrid Crystal fan proposal by insert silicon layers
  imporve 3D segmentation
  Help to reduce Phi-r confusion and near-by shower confusion
Inputs/discussion are very welcome

## Slide 14: Typical crystals (From Ren-yuan Zhu’s slides)

## Slide 15: Example configure 3
Take 𝛼 = 15 degrees, transverse 10 layers
D=0.237 m
ȹ=0.03 (1.7degree）
ȹ/N_l = 0.003
Each z segmentation
  2077 crystals
r1
r2
D
ȹ
Pure crystal
Crystal module
𝛼

## Slide 16: Example configure 4
Take 𝛼 = 30 degrees, transverse 10 layers
D=0.261 m
ȹ=0.064 (3.7degree）
ȹ/N_l=0.0064
Each z segmentation
  977 crystals
r1
r2
D
ȹ
Pure crystal
Crystal module
𝛼

## Slide 17: Example configure 5
Take 𝛼 = 60 degrees, transverse 10 layers
D=0.400 m
ȹ=0.17 (9.8degree）
ȹ/N_l = 0.017
Each z segmentation
  366 crystals
r1
r2
D
ȹ
Pure crystal
Crystal module
𝛼