## Slide 1
HCAL with Scintillating Glass:
first Geant4 simulation studies
Dejing Du, Yong Liu, Baohua Qi
November 3, 2021

## Slide 2: Scintillator HCAL: setup in Geant4 simulation
Transverse plane:
60 longitudinal layers, each with
Scintillator: 3mm
PCB: 2.1mm
Absorber (steel): 20mm
HCAL geometry
Scintillator materials
Plastic scintillator (polystyrene) as baseline reference
Scintillating glass: -------
References: https://doi.org/10.1016/j.jeurceramsoc.2021.05.064
1 GeV kaon0L
Note: HCAL with 40 layers in CEPC CDR as baseline.
Hereby use 60 layers to evaluate leakage effects

## Slide 3: HCAL with plastic scintillator tiles
Impact of Birks’ constant for energy resolution
Birks’ law included, with the Birks’ constant kB=0.126mm/MeV
Incident particle: kaon0L (1-100GeV)
Threshold: 0MIP
Note: Birks’ law generally describes
quenching effects in the scintillating
materials: lower light emission due to
higher density of energy deposition.

## Slide 4: HCAL: plastic scintillator vs scintillating glass
Preliminary performance comparison
Scintillating glass: better hadronic energy resolution in low energy region (<20GeV)
  Note that majority of hadrons in jets at CEPC are with low energy
Further issue: constant term
  To be further understood
  Could be due to the “non-compensation” effects
  “Software compensation” technique is ready to be applied

## Slide 5: Plastic Scintillator
Impact of energy threshold to hadronic energy resolution
Energy threshold: 0MIP, 0.05MIP, 0.1MIP, 0.25MIP, 0.5MIP
Incident particle: kaon0L (1-100 GeV)
Without birks’ constant
With birks’ constant

## Slide 6: Scintillating Glass
Impact of glass density to hadronic energy resolution
Density varying:
Incident particle : kaon0L
Birks’ constant not included
Fitting range: 1-100GeV
Fitting range: 10-100GeV

## Slide 7: Summary and prospects
A novel concept of PFA HCAL with heavy scintillating glass tiles
Major motivations
  Better hadronic energy resolution, especially in low energy regions
    Higher density provides higher energy sampling fraction
    Certain doping to enhance neutron capture: improve hadronic response
  More compact HCAL layout (given 4~5 nuclear interaction lengths in depth)
Geant4 full simulation established
  First studies show improvement of hadronic energy resolution with scintillating glass
  Essential to guide R&D activities of heavy scintillating glass
    Key properties: components (doping), intrinsic light yield, transmission, density, emission, decay time, etc.

## Slide 8
Simulation of Single Scintillating Glass Tile

## Slide 9: Setup in Geant4 simulation
Physical volume
Scintillating glass, Air gap, ESR wrapping,
Coupling agent: BC631
SiPM
Properties of scintillating glass
Component: :1
Density: 4.532 g/cm3
Refractive index: 1.65
Transmission: 74%
Emission peak: 394 nm
Light yield: 1000 ph/MeV
Scintillating glass
1*1*1
6mm
SiPM
BC631
mu-

## Slide 10: Experimental results
Sen Qian

## Slide 11: Experimental results
Zhehao Hua

## Slide 12: Simulation results
Primary particle: 1GeV muon
Light yield: 1000 ph/MeV
Light yield: 1000 ph/MeV
Light yield: 125 ph/MeV
Light yield: 125 ph/MeV

## Slide 13: Simulation results
Primary particle: 662keV gamma
Light yield: 1000 ph/MeV