## Slide 1: WaveDream Board by Gianluigi Chiarello
Credit to S. Ritt, Paul Sherrer Institute, Zurich, Switzerland

## Slide 2: DRS4 chip
Analog switched capacitor array: analog memory with a depth of 1024 sampling cells developed at PSI, perform a “sliding window” sampling.
500MSPS ↔ 5GSPS sampling speed with 11.5 bit signal-noise ratio
  8 analog channels + 1 clock-dedicated channel for sub 50ps time alignment
Pile-up rejection O(~10 ns)
Time measurement O(10 ps)
Charge measurement O(0.1%)
Shift Register
Clock
IN
Out
Storage
capacitors
Inverter “Domino” ring chain
0.2-2 ns
FADC
33 MHz

## Slide 3: WaveDREAM Board (WDB)
HV Board for SiPM
Preamp channel

## Slide 4: Preamp channel
Gain | BW3db (MHz) | Noise (mV)
1 | 940 | 0.37
10 | 880 | 0.40
100 | 300 | 1.2
100 | 500 | 1.7
100 | 800 | 3.3
Different compensations
LMH6629
LMH6629
PE4215
PE4215
ADC904
LTC6409

## Slide 5: WDB
HV Boards

## Slide 6: WDS
Server software using Mongoose C/C++ Framework
  Easy low level calls for fast DAQ operations
  Single executable with no need of dedicated http server
WDB interface is similar to the interface of an oscilloscope with 16 channels.
For each channel can:
  Select the gain
  Set a PZC
  HV for SIPM
Set different trigger patterns

## Slide 7: WDS: Examples event screen
4 trigger channels
6 tubes 1 cm cell size with typical event
3 tubes 2 cm cell size
Channel selection panel
Trigger selection pattern
Gain selection
Each data file has been saved in binary format and then converted in root files
2 tubes 3 cm cell size
typical event

## Slide 8: WDS: Binary format
Header relating to the board consisting of the words:
  DRS8
  TIME
  B#XXX (XXX represents the card number and changes according to the WDB, in this case 033)
  Calibration information
Header EVENT
  Serial. Number
  Time information
  Channel Information
The macro for converting binary files to root files is ready.

## Slide 9: WDS: Root signal

## Slide 10: WDS: Root signal