## Slide 1: Timing and bunch pattern compatibility study @High luminosity Z scheme
C. Meng, D. Wang, X. Cui, G. Lei, J. R. Zhang,
G. Li, J. Gao, Y. H. Li, X. P. Li, T. M. Xin, et al.
环形正负电子对撞机
Circular Electron Positron Collider
CEPC DAY Jan. 29 2022

## Slide 2: Outline
Background & Motivation
Basic Consideration
Linac scheme
Summary

## Slide 3: Background
CEPC is a 100km ring collider
  Revolution time = 100km/C = 0.333ms
  Revolution frequency frev = 3kHz
Linac repetition frequency is 100Hz or 200Hz
  RF interval is 10ms or 5ms, only about 30 or 15 revolution time
Harmonic number
  h= frf / frev
  Maximum bunch number
Frequency lock
  fcm as common frequency
  fLinac=m*fcm
  fBooster=n*fcm
  fRing=k*fcm

## Slide 4: Motivation
High luminosity Z scheme @30MW need more bunch number
  Minimum bunch number per second of Linac should be larger than 11920/((153-10)/2) ≈168, which is larger than the repetition frequency of Linac(100Hz)
  Need speed up the Linac injection
Requirement
 |  | ttbar |  | Higgs |  | W |  | Z | 
SR power /beam | MW | 30 | 50 | 30 | 50 | 30 | 50 | 30 | 50
Bunch number | / | 37 | 58 | 240 | 415 | 1230 | 2162 | 11920 | 19912
Train number | / | 37 | 58 | 240 | 415 | 1230 | 2162 | 149 | 152
Bunch number/train | / | 1 | 1 | 1 | 1 | 1 | 1 | 80 | 131
Interval for top up* | s | 65 |  | 38 |  | 155 |  | 153 | 
Bunch spacing | ns |  |  |  |  |  |  | 23.076 | 15.384
Bunch spacing (bucket number) |  |  |  |  |  |  |  | 15 | 10
* Beam current in collider decays by 3%.
168 280

## Slide 5: Motivation
In order to speed up the Linac injection, provide more bunches in the limit time, we can increase the repetition frequency or increase bunch number per pulse.
There are three schemes:
  S1: Increase the repetition frequency from 100Hz to 200Hz
    Power source, modulator and so on
  S2: Double-bunch acceleration scheme( two bunch per pulse @ 100Hz)
    To filling the required bucket pattern, the SHB frequency should be changed from 143MHz/572MHz to 119.17MHz/(476.76MHZ or 715.0MHz )
    Difficulties on BPM, LLRF, commissioning
  S3: The thermal electron gun and bunching system (ESBS) is replaced by RF gun
    More flexible injection scheme
    The Linac have better potential in terms of compatibility
Solution

## Slide 6
Consideration
Common frequency
Coincidence clock
RF pulse of the Linac

## Slide 7: Common frequency
RF frequency of the Linac, booster and ring is 2860MHz,1300MHz and 650MHz
  Greatest common divisor (GCD) is 130MHz
  All RF frequency is based on the common frequency
The circumference of the booster and the ring is same and the frequency of the ring is half of the booster, so all the following consideration is based on the ring frequency and parameters, such as bucket number, bunch interval, harmonic number et al.
The initial bucket in this article is denoted as a zero-numbered bucket, that is, the bucket number starts from 0.
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 200 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 1 |  | 76.9231 | ns
LINAC |  | 2860 | MHz | 22 |  | 0.3497 | ns
 |  | 5720 | MHz | 44 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 10 |  | 0.7692 | ns
Ring |  | 650 | MHz | 5 |  | 1.5385 | ns
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 200 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 1 |  | 76.9231 | ns
LINAC |  | 2860 | MHz | 22 |  | 0.3497 | ns
 |  | 5720 | MHz | 44 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 10 |  | 0.7692 | ns
Ring |  | 650 | MHz | 5 |  | 1.5385 | ns

## Slide 8: Scheme
Thermionic cathode electron gun + subharmonic buncher
  There are two SHB with different RF frequency
  More frequency should be considered for bunch frequency
    The bunch interval should be an integer multiple, n, of the time corresponding to the common frequency,
    SHB1 frequency is an integer multiple, m1, of bunch frequency,
    SHB2 frequency is an integer multiple, m2, of SHB1 frequency,
    Linac frequency is an integer multiple, m3, of SHB2 frequency,
     22*n=m3*m2*m1
RF gun
    The bunch interval should be an integer multiple, n, of the time corresponding to the common frequency,
    Linac frequency is an integer multiple, m3, of bunch frequency,
     22*n=m3

## Slide 9: Coincidence clock
Assuming the harmonic numbers of the booster and the colliding ring are hbooster and hring
The zero buckets of booster and ring should be aligned and need to be locked with the bunch frequency
Zero-bucket align frequency:
  is least common multiple
CEPC: hbooster =2 hring
All injection related time based on coincidence clock
  Should larger than the repetition frequency
Scheme1

## Slide 10: Injection scheme
Repetition frequency + Coincidence clock  zero bucket time, t1
Bucket section: delay M bucket time relative to the zero bucket, t2
  If t1+ t2 < trep, general injection
  If t1+ t2 > trep, specific injection, define the injection trigger train firstly

## Slide 11: Injection scheme
Repetition frequency + Coincidence clock  zero bucket time, t1
Bucket section: delay M bucket time relative to the zero bucket, t2
N is the number of turns

## Slide 12: RF pulse of Linac
CEPC is a 100km ring collider
  Revolution time = 100km/C = 0.333ms
Linac repetition frequency is 200Hz
  Interval is 5ms, only about 15 revolution time
Minimum RF pulse interval 1ms is possible ?
  So far yes !

## Slide 13
Linac Scheme
Based on thermionic cathode electron gun
  Scheme-1
  Scheme-2
Based on RF gun
  Scheme-3

## Slide 14: Scheme-1
The baseline scheme have two SHB with frequency as 143MHz/572MHz
  22*n=m3*m2*m1
  n=10，m1=11，m2=4，m3=5
  Bunch interval is 76.9ns, corresponding to 50 bucket, this scheme can increase repetition frequency (200Hz) and can’t be two-bunch acceleration.
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 200 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 10 |  | 76.9231 | ns
Bunch frequency |  | 13 | MHz | 1 |  | 76.9231 | ns
SHB1 |  | 143 | MHz | 11 |  | 6.9930 | ns
SHB2 |  | 572 | MHz | 44 |  | 1.7483 | ns
LINAC |  | 2860 | MHz | 220 |  | 0.3497 | ns
 |  | 5720 | MHz | 440 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 100 |  | 0.7692 | ns
Ring |  | 650 | MHz | 50 |  | 1.5385 | ns
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 200 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 10 |  | 76.9231 | ns
Bunch frequency |  | 13 | MHz | 1 |  | 76.9231 | ns
SHB1 |  | 143 | MHz | 11 |  | 6.9930 | ns
SHB2 |  | 572 | MHz | 44 |  | 1.7483 | ns
LINAC |  | 2860 | MHz | 220 |  | 0.3497 | ns
 |  | 5720 | MHz | 440 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 100 |  | 0.7692 | ns
Ring |  | 650 | MHz | 50 |  | 1.5385 | ns

## Slide 15: Scheme-1
To fill the bunch pattern, =5
  = 50* N + 5, 15, 35, 45
=216805
  C=99.995km
Minimum RF interval
  3 ms

## Slide 16: Scheme-1

## Slide 17: Scheme-2
If use two-bunch acceleration, we need change the SHB frequency
  22*n=m3*m2*m1
  n=12，m1=11，m2=4/6，m3=6/4
  Bunch interval is 92.3ns, corresponding to 60 bucket, can be two-bunch acceleration (100Hz)
    this scheme can increase repetition frequency (200Hz)
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 100 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 12 |  | 76.9231 | ns
Bunch frequency |  | 10.833 | MHz | 1 |  | 92.3077 | ns
SHB1 |  | 119.17 | MHz | 11 |  | 8.3916 | ns
SHB2 |  | 476.76/ 715.0 | MHz | 44/66 |  | 2.0979/ 1.3986 | ns
LINAC |  | 2860 | MHz | 264 |  | 0.3497 | ns
 |  | 5720 | MHz | 528 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 120 |  | 0.7692 | ns
Ring |  | 650 | MHz | 60 |  | 1.5385 | ns
 | frequency |  |  | Multiple | Period |  | 
Repetition frequency |  | 100 | Hz | / |  | 5.0 | ms
Common frequency |  | 130 | MHz | 12 |  | 76.9231 | ns
Bunch frequency |  | 10.833 | MHz | 1 |  | 92.3077 | ns
SHB1 |  | 119.17 | MHz | 11 |  | 8.3916 | ns
SHB2 |  | 476.76/ 715.0 | MHz | 44/66 |  | 2.0979/ 1.3986 | ns
LINAC |  | 2860 | MHz | 264 |  | 0.3497 | ns
 |  | 5720 | MHz | 528 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 120 |  | 0.7692 | ns
Ring |  | 650 | MHz | 60 |  | 1.5385 | ns

## Slide 18: Scheme-2
To fill the bunch pattern, =5 or 15
  = 60* N + 5, 15,25, 35, 45,55
=216845
  C=100.013km
Minimum RF interval
  7 ms

## Slide 19: Scheme-2

## Slide 20: Scheme-2
This scheme can increase repetition frequency (200Hz)
Minimum RF interval
  3 ms

## Slide 21: Scheme-2
200Hz + Two-bunch acceleration
Minimum RF interval
  3 ms

## Slide 22: Scheme-3
RF gun
  22*n=m3
  n=1
  Bunch interval is 7.69ns, corresponding to 5 bucket, can be two-bunch acceleration (100Hz)
    this scheme can increase repetition frequency (200Hz)
 | frequency |  |  | Multiple | Period |  | 
Common frequency |  | 130 | MHz | 1 |  | 7.6923 | ns
Bunch frequency |  | 130 | MHz | 1 |  | 7.6923 | ns
LINAC |  | 2860 | MHz | 22 |  | 0.3497 | ns
 |  | 5720 | MHz | 44 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 10 |  | 0.7692 | ns
Ring |  | 650 | MHz | 5 |  | 1.5385 | ns
 | frequency |  |  | Multiple | Period |  | 
Common frequency |  | 130 | MHz | 1 |  | 7.6923 | ns
Bunch frequency |  | 130 | MHz | 1 |  | 7.6923 | ns
LINAC |  | 2860 | MHz | 22 |  | 0.3497 | ns
 |  | 5720 | MHz | 44 |  | 0.1748 | ns
Booster |  | 1300 | MHz | 10 |  | 0.7692 | ns
Ring |  | 650 | MHz | 5 |  | 1.5385 | ns

## Slide 23: Scheme-3
To fill the bunch pattern, =1,2,3,4,5
  = 5* N + 1,2,3,4,5
=216845
  C=100.013km
Minimum RF interval
  4.67 ms
Suggested
  216844

## Slide 24: Scheme-3
200Hz
200Hz

## Slide 25: Scheme-3
Two-bunch acceleration@100Hz

## Slide 26: Scheme-3
Two-bunch acceleration@200Hz

## Slide 27: Summary
Baseline scheme with 200Hz scheme can meet the requirements of high luminosity Z scheme @ 30MW
Baseline scheme with two-bunch acceleration scheme can’t meet the requirements of high luminosity Z scheme @ 30MW, we should change the SHB frequency. In this case, all scheme can works.
RF gun scheme can meet the requirements of high luminosity Z scheme @ 30MW.
Only timing
 |  | High luminosity Z scheme @ 30MW |  |  |  | 
 |  | 200Hz | Two-bunch acceleration@100Hz | Two-bunch acceleration@200Hz | Harmonic number | comments
Based on thermionic cathode electron gun | Scheme1 | Yes | No | No | 216805 | Baseline SHB
 | Scheme2 | Yes | Yes | Yes | 216845 | Modified SHB
RF gun | Scheme3 | Yes | Yes | Yes | 216845 | 216844

## Slide 28: Summary
Considering compatibility, it is recommended:
  The baseline scheme update the bunch system design, using the new frequency SHBs
  Or develop the RF gun to replace the thermionic cathode electron gun
Only timing
 |  | High luminosity Z scheme @ 30MW |  |  |  | 
 |  | 200Hz | Two-bunch acceleration@100Hz | Two-bunch acceleration@200Hz | Harmonic number | comments
Based on thermionic cathode electron gun | Scheme1 | Yes | No | No | 216805 | Baseline SHB
 | Scheme2 | Yes | Yes | Yes | 216845 | Modified SHB
RF gun | Scheme3 | Yes | Yes | Yes | 216845 | 216844
Thank you for your attention!