## Slide 1: CPEC Vertex Detector Prototype Electronics & DAQ design status
JunHu, Hongyu Zhang, Jia Zhou
2022/4/13

## Slide 2: Readout structure
Flex board：Assembled with 10 TAICHU chips, Dual sides readout.
Interposer board：FMC mezzanine rigid and flex board
FPGA board：FMC carrier board
interposer
Sockets
FPGA
interposer
FPGA
Flex
Flex

## Slide 3: Flex board
External flex
(147.7 X 17.23)
Sensor area(257.6 X 17.23)
External flex
(147.7 X 17.23)
socket
socket
Left
Right
Socket signal definition
553mm length in total
500334-0800
54102-0804

## Slide 4: Layout topological
Independent signals（Bonding side）:
  CLK40M, SPI_CSB, DOUT_P, DOUT_N, SER_VALID
Shared signals（Bottom side）:
  APULSE, TRIGGER, VRESET, VHIGH, VLOW, 7 SPI signals
Power supply
  VDDD, VDDA, PWELL, GND
Bonding side
Bottom side
VDDA
VDDD

## Slide 5: 2 options
Option1
  2 layers + stiffener
  Inter-conn signal used
  worse signal integrity
    Noise
    Ground bounce
Thickness: ~0.2mm
Option2
  4 layers flex + stiffener
  Dedicated GND and power plane
  better signal integrity
Thickness: 0.38+/-0.08mm
Vdrop: 0.03Ω = (1mmX25.6mmX0.5oz)
  VDDD 6mm width, 0.21A * 0.03 / 6 *12.5 = 13mV
  VDDA 4mm width，0.21A * 0.03 / 4 * 12.5 = 20mV
  GND 2mm width， 0.42A * 0.03 / 2 *12.5 = 79mV

## Slide 6: Interposer board
7cm
DAC
LINEAR REGULATOR
REF
Voltage Regulator
10cm max
100X17.23
1.6cm
F
M
C
Top view
Side view
Flex
Sockets
power supply and filter are placed on rigid area
Socket

## Slide 7: Power supply
Requirement:
  1.8VDDA ≈ 0.21A
  1.8VDDD ≈ 0.21A
  PWELL (-6V – 0)
  VRESET, VHIGH, VLOW from DAC
LMZ12003
(3A)
+12V
+2.3V
ADP7158ARDZ-1.8(2A)
ADP7158ARDZ-1.8(2A)
1.8VD
1.8VA
LT1054ISW
(100mA)
PWELL
+12V
+3V3
DAC80004
VRESET, VHIGH, VLOW,

## Slide 8: FPGA board
FMC standard
  ASP-134606-01: 8.5mm height
1Gbps Ethernet to PC
  Data Readout：TCP/IP
  Configuration：UDP
FPGA board
To be defined
Data Format

## Slide 9: Architecture of CEPC Vertex Detector Prototype
Front End Electronics:
Readout Board: x12
  Readout Ladder electronics data
Clock Fan-out Board: x1
  Fan-out common clock signal to each readout board
Readout Control Board: x1
    Fan-out common reset / common start / common stop signals to each readout board
    Synchronize global timestamps of each readout board
Trigger Board: x1
    Provide timestamp of Scintillator trigger signal

## Slide 10: Schedule
Flex boards:
  Finished design
  In production ~ 2-3 weeks
Interposer board:
  Under design ~ 2 weeks
FPGA board and fanout board:
  18 FPGA boards and 2 fanout board are ready.