## Slide 1: Machine protection, beam dumps and other safety issues
Guangyi Tang, Haoyu Shi and Zhongjian Ma
IARC meeting, 2022

## Slide 2: outline
Introduction
Collider ring dump design
Synchrotron radiation shielding
Radionuclide productions
Linac hot spots and beam losses
Summary and outlook
Using FLUKA, Flair.

## Slide 3: Radiological impact
Main consideration aspects
Impact factors | Characteristics
Synchrotron radiation | Radiation damage to magnet coil; Over heat load to ventilation system; Formation of ozone and nitrogen oxides in the air; Slightly activation to the material around;
Random beam loss | Cause secondary radiation inside the tunnel; Determine the bulk shielding thickness;
Hot spots | MDI, Collimation locations, collider/linac dumps, injection/extraction points;
Radiological impact on environment | Dose from stray radiation emitted during machine running Radionuclides in the cooling water, underground water, tunnel air, soil. Radioactivity analysis for the solid components and waste
Machine protection | Active/passive protection

## Slide 4: Collider dump
A set of kicker magnets is used to dilute the beam horizontally and vertically.
The length of transfer tunnel is about 100m; the diameter is about 2m, considering the vacuum equipment, pipe installation.
The area of bunch distribution at dump entrance is optimized to be 6cm x 6cm for graphite core.
Dilution kicker requirement:
Vertical kicker should periodic oscillate 12.5 times in 300 us
From Xiaohao Cui
 |  | Extraction kicker | Septum | Dilution kickers
Length (m) |  | 2 | 20 | 10
Magnetic flux density (Gauss) | Z | 280 | 2600 | 40
 | WW | 493 | 4700 | 
 | Higgs | 740 | 7000 | 
 | ttbar | 1110 | 10500 | 

## Slide 5: Bunch distribution: 50MW
The bunch distributions at the dump entrance is simulated.
  Bunch size:
Simulate energy deposition in dump core.
Find the maximum energy deposition. And calculate maximum temperature rise.
Optimize dump dimensions
From Xiaohao Cui
Higgs
Higgs
WW
Z pole
ttbar
Dilution kicker requirement:
2. Horizontal kicker should reduce step by step from max. to min. in 300 us

## Slide 6: Max. temperature rise: 50MW
Example: graphite core
Max. temperature rise is smaller than graphite melting point.
Dimension (graphite + Iron): R~2.3m, L~8m; constrained by the condition that dose-eq is smaller than 5.5mSv.
Temperature rise @Z mode
Temperature rise @WW mode
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
Ne/bunch/ | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Max. temperature rise |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
 | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Max. temperature rise |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 

## Slide 7: Abort trigger
Abort request:
  Beam loss monitors
  Synchrotron oscillation phase monitor
  Hardware components
  Manual abort
Time interval
  Device request -> local control
  Local control -> central control
  Central control -> dump system
  Extract all beam.
Collider dump response time ~ 1ms.
SuperKEKB Design Report

## Slide 8: More issues
Abort beam in booster and collider
  For normal operations and machine tunning
Study feasibility to build extraction line from booster to dump.
Can be built around 4 straight sections. Number of dumps depends on machine requirement and reliability.
Need absorber to protect machine elements from incorrect extraction.
Will study reliability (or alternative design).
Response time ~ 1ms.
Need collimators to deal with beam losses faster than 1ms.
  fault cases.
Krainer, A. et.al., EPJ Techn Instrum 9, 3 (2022)
Straight sections
LHC design report Ch.17

## Slide 9: outline
Introduction
Collider ring dump system
Synchrotron radiation shielding
Radionuclide productions
Linac hot spots and beam losses
Summary and outlook

## Slide 10: Simulation setup
Tunnel geometry
Length: 100m;
  3 dipoles;
  2 quadrupoles;
  2 sextupoles;

## Slide 11: Simulation setup
Dipole
insulator, coils, lead
Insulator is added in the model.
In cross-section, area of lead:
Drift chamber
area of lead:

## Slide 12: Simulation setup
Quadrupole
insulator, coils, lead
Trim coils is added in the model.
area of lead :
Sextupole
area of lead :

## Slide 13: booster
dipole ->drift chamber ->quadrupole -> sextupole ->drift chamber ->dipole …
Magnets

## Slide 14: Parameters: 50MW
Collider
The ramping simulation is more critical than reality.
  Overestimate dose in booster
Booster
Ramping simulation: example @higgs
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
Ne/bunch/ | 14 | 13.5 | 14 | 20
Number of bunches | 415 | 2162 | 19918 | 58
Number of photons/114m | 4.7e18 | 1.6e19 | 8.4e19 | 1.4e18
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
 | 14 | 13.5 | 14 | 20
Number of bunches | 415 | 2162 | 19918 | 58
Number of photons/114m | 4.7e18 | 1.6e19 | 8.4e19 | 1.4e18
 | Higgs On | WW | Z | ttbar
Current(mA) | 1 | 2.69 | 14.4 | 0.12
Injection duration(s) | 32.8 | 39.3 | 134.7 | 30
Injection interval(s) | 38 | 155 | 153.5 | 65

## Slide 15: Dose in insulation
Dose value is equal in middle of magnet, not in both sides of magnet.
“Hot spots” in insulation because:
  The shielding between magnets are not matched very well.
  SR hits the iron close to beam pipe and bypasses lead.
Hot spots shielding will be considered in next stage.
Dose in uniform regions are summarized in the following pages.

## Slide 16: Dose vs lead thickness: 50MW
While running @Higgs/Z/WW (10 years),
  possible to reduce 2.5cm lead if no ttbar run;
Lead thickness is constrained by the operation plan.
While running @ttbar for 1 year,
  May run another 5 years for dipole and quadrupole, 2years for sextupole

## Slide 17: Dose in trim insulation: 50MW
While running Higgs/Z/WW (10 years),
Lead thickness is constrained by the operation plan.
While running @ttbar for 1 year,
  May run another 2 years for quadrupole trim coil

## Slide 18: dose in booster insulation: 50MW
While running Higgs/Z/WW (10 years),
  Carefully assesse dose in sextupole
Pay attention to sextupole. Simulate more precisely.
While running @ttbar for 1 year,
  May run another 5 years for booster dipole and quadrupole

## Slide 19: dose in the tunnel
In the arc section of the ring, the most important two radiation sources are from synchrotron radiation and random beam losses.
Radiation caused by synchrotron is more serious than beam losses
Secondary radiation components from random beam losses is harder and more liable to produce radioactivity in the material surrounded, Should be assessed.
Prompt radiation dose caused by random beam loss
Prompt radiation dose caused by synchrotron radiation

## Slide 20: Dose-EQ in the tunnel
In the arc section of the ring, the most important two radiation sources are from synchrotron radiation and random beam losses.
Radiation caused by synchrotron is more serious than beam losses
Secondary radiation components from random beam losses is harder and more liable to produce radioactivity in the material surrounded, Should be assessed.
Prompt radiation dose-eq caused by random beam loss
Prompt radiation dose-eq caused by synchrotron radiation

## Slide 21: radionuclides simulation
Beam losses & SR photon of energy >6MeV
FLUKA options
Wall material:
  Case1: water as wall
  Case2: rock as wall
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 50MW | 0.33 | 0.91 | 1.33 | 0.30
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 50MW | 0.33 | 0.91 | 1.33 | 0.30
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7

## Slide 22: Soil/rock
 |  | Soil | average components of different rocks
density |  | 1.6g/cm^3 | 1.2~3.3g/cm^3
Major element (wt%) | C | 1.0 | ---
 | N | 0.12 | ---
 | O | 34 | 30~70
 | Na | 0.50 | 0.1~2.9
 | Mg | 0.52 | 0.4~3.7
 | Al | 8.0 | 3.5~9.7
 | Si | 40 | 26~39
 | P | --- | 0.02~0.16
 | K | 2.36 | 1.8~3.7
 | Ca | 2.26 | 0.2~4.8
 | Ti | 1.0 | 0.09~0.8
 | Mn | 0.24 | 0.02~0.12
 | Fe | 9.6 | 0.8~6.3
In previous study, use soil as tunnel wall.
Now use average components of different kinds of rock.
Simulate productions of residual nuclei after 1 year running in:
  Cooling water
  Air in tunnel
  Water outside tunnel
  Rock (leachable isotopes)

## Slide 23: Radionuclides production
 |  | Half-life | Cooling water | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.44 | 10
 | C14 | 5700a | 3.5e-7 | 23
 | Be7 | 53d | 1.3e-2 | 34
 | H3 | 12a | 2.3e-6 | 22
SR @ttbar | None |  |  | 
 |  | Half-life | Air in tunnel | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.7e-4 | 52
 | C14 | 5700a | 7.7e-7 | 1
 | Be7 | 53d | 1.1e-5 | 57
 | H3 | 12a | 3.5e-9 | 32
 | P32 | 14d | --- | ---
 | P33 | 25d | 1.9e-8 | 100
 | Cl36 | 3e5a | --- | ---
 | Cl38 | 37m | --- | ---
 | Ar37 | 35d | 6.1e-9 | 59
 | Ar41 | 2h | 1.4e-3 | 12
SR @ttbar | C14 | 5700a | 6.5e-6 | 2
 | Ar41 | 2h | 1.5e-2 | 20
Densities of Long half-life isotopes are lower than mandatory standard, GB18871.

## Slide 24: Radionuclides production
Only leachable isotopes are listed:
  3H, 22Na, 45Ca, 54Mn
 |  | Half-life | Water wall | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2e-3 | 2
 | C14 | 5700a | 5e-10 | 4
 | Be7 | 53d | 3e-5 | 5
 | H3 | 12a | 6e-9 | 3
 | F18 | 2h | 5e-6 | 52
SR @ttbar | C14 | 5700a | 2e-12 | 99
 | H3 | 12a | 1e-10 | 71
 |  | Half-life | Rock wall | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | Mn54 | 312d | 6.94E-04 | 1.8
 | Ca45 | 163d | 5.49E-06 | 0.3
 | Na22 | 2.6y | 7.20E-04 | 1.4
 | H3 | 12a | 5.90E-09 | 0.9
SR @ttbar | H3 | 12a | 1e-10 | 71
Densities of Long half-life isotopes are lower than mandatory standard.
Should investigate if radionuclides would transport to drinking water.

## Slide 25: outline
Introduction
Collider ring dump system
Synchrotron radiation shielding
Radionuclide productions
Linac hot spots and beam losses
Summary and outlook

## Slide 26: CEPC linac
Length: 1215m; 7 dumps and 1 collimator;
Dump1
Dump2
Dump3 + Collimator
Dump4
Dump5
Dump6 + dump7

## Slide 27: Local shield design for hot spots
Carbon and iron is selected as the absorber material, surrounded by the polyethylene as local shielding.
5.5mSv/h is set as upper limit to decide the thickness of local shielding.
The thickness of shielding will be optimized combined with Linac tunnel geometry in the next stage.
Absorber geometry and local shielding:
Size for carbon and iron for different beam energy, adopt from other projects, is suitable but haven't been optimized.
Local size selection (20GeV dump as example):
2D map of dose distribution is obtained using FLUKA, the dose rate alone Z or R axis was averaged by 1x1cm^2 area, the shielding size can be selected by setting dose rate limit.
Preliminary design results for different beam energy analysis station:
Radiation level nearby each energy analysis station was figured out, also specify a roughly space for the future local shielding.
Beam energy | R/m | Length/m
60MeV | 0.7 | 1
4GeV | 1.2 | 2.6
250MeV | 0.55 | 1
1.1GeV | 0.85 | 1.7
6GeV | 1 | 2.5
20GeV | 1.2 | 3.8

## Slide 28: Linac beam losses assumptions
Angle of incidence 10mrad
Not consider EBTL & DR beam losses.
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | Number of particles [/s]
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 700m | 1.1~20GeV |  | 0.1 | 12.5
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | 
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 700m | 1.1~20GeV |  | 0.1 | 12.5

## Slide 29: Simulation setup
Beam pipes and concrete wall
Top/side view
Dose-eq distribution example: TAS
Thickness of Shielding wall according to upper limit 5.5mSv(left/right/bottom) /2.5uSv(top).
Wall thickness | FAS | SAS | TAS
Left | 0.3m | 1.9m | 0.3m
Right | 0.2m | 1.9m | 0.3m
Bottom | 0.3m | 2.1m | 0.3m
Top | 1.3m | 4.1m | 2m

## Slide 30: Summary & outlook
Preliminary dump design for collider is done.
Lead shielding seems well. Further optimize SR shielding design
  Unequal dose distribution in the insulation.
  Precise simulation for booster.
Radionuclides productions are studied. If necessary, all operation mode can be simulated.
  Precise beam losses model is need.
The dimensions for Linac hot spots and walls are designed.
Go on:
  Reliability study for dump.
  Activation transport assessment.
  Shielding around experiment hall (around MDI).
  Machine protection: fault cases.
Thank you

## Slide 31: backup

## Slide 32: Max. temperature rise
Example: aluminum core
Max. temperature rise @Z mode can decrease by increasing the bunch distance on the dump surface.
Max. temperature rise @Z mode
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 182.5
Ne/bunch/ | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Min. size (um^2) | 9261x56 | 9219x50 | 8538x49 | 9774x51
Max. temperature rise (50x28cm^2) |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 182.5
 | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Min. size (um^2) | 9261x56 | 9219x50 | 8538x49 | 9774x51
Max. temperature rise (50x28cm^2) |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 

## Slide 33: Max. temperature rise
Example: graphite core
Max. temperature rise @Z mode can decrease by increasing the bunch distance on the dump surface.
Max. temperature rise @Z mode
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Bunch number (50MW) |  | 415 | 2162 | 19918 | 58
Min. size of bunch (um^2) |  | 9261x56 | 9219x50 | 8538x49 | 9774x51
Max. temperature rise | 50x28cm^2 |  |  |  | 
 | 6x6cm^2 |  |  |  | 
Maximum temperature rise by one bunch |  |  |  |  | 
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Bunch number (50MW) |  | 415 | 2162 | 19918 | 58
Min. size of bunch (um^2) |  | 9261x56 | 9219x50 | 8538x49 | 9774x51
Max. temperature rise | 50x28cm^2 |  |  |  | 
 | 6x6cm^2 |  |  |  | 
Maximum temperature rise by one bunch |  |  |  |  | 

## Slide 34: Parameter
Collider
Booster
Ramping simulation
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Number of bunches | 30MW | 249 | 1297 | 11951 | 35
 | 50MW | 415 | 2162 | 19918 | 58
Number of photons/114m | 30MW | 2.8e18 | 9.2e18 | 5.0e19 | 8.4e17
 | 50MW | 4.6e18 | 1.5e19 | 8.4e19 | 1.4e18
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 30MW |  |  |  | 
 | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Number of bunches | 30MW | 249 | 1297 | 11951 | 35
 | 50MW | 415 | 2162 | 19918 | 58
Number of photons/114m | 30MW | 2.8e18 | 9.2e18 | 5.0e19 | 8.4e17
 | 50MW | 4.6e18 | 1.5e19 | 8.4e19 | 1.4e18
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 30MW |  |  |  | 
 | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 | Higgs On | WW | Z | ttbar
Current(mA) | 1 | 2.69 | 14.4 | 0.12
Injection duration(s) | 32.8 | 39.3 | 134.7 | 30
Injection interval(s) | 38 | 155 | 153.5 | 65

## Slide 35: hot spots inside Linac
Radiation hot spots, such as beam energy analysis stations, collimators, positron targets, dumps, should be shielded in order to protect equipment and people and minimize the thickness of the wall of Linac tunnel.
  Two kinds of prompt radiation inside Linac tunnel: radiation from hot spots and from beam loss
  Many hot spots inside Linac are used for beam energy analysis in different locations.
For 20GeV linac, there are more hot spots and will be updated soon.
No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | Charge/nC | Bunch populartion/
1 | Beam Energy Analysis | 60MeV | 2/1 | 1 | 10 | 6.3
2 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 10 | 6.3
3 | Beam Energy Analysis | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
4 | Positron target position | 4GeV | - | - | - | 6.0
5 | Dump for Linac beam | 11GeV | 0.5/0.5 | 1 | 3 | 1.9
No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | Charge/nC | 
1 | Beam Energy Analysis | 60MeV | 2/1 | 1 | 10 | 6.3
2 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 10 | 6.3
3 | Beam Energy Analysis | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
4 | Positron target position | 4GeV | - | - | - | 6.0
5 | Dump for Linac beam | 11GeV | 0.5/0.5 | 1 | 3 | 1.9

## Slide 36: Local shield design for hot spots
Carbon and iron is selected as the absorber material, surrounded by the concrete as local shielding.
5.5mSv/h dose-equivalent is set as upper limit to decide the thickness of local shielding .
The thickness of shielding will be optimized so that the dose-eq out of dumps is in the same order of dose-eq by beam loss.
Beam energy | Trans. Area / | Length/m
60MeV | 0.75*0.75 | 1.36
1.2GeV | 1.56*1.56 | 3.05
250MeV | 0.98*0.98 | 1.56
11GeV | 2.10*2.10 | 3.36
Beam energy |  | Length/m
60MeV | 0.75*0.75 | 1.36
1.2GeV | 1.56*1.56 | 3.05
250MeV | 0.98*0.98 | 1.56
11GeV | 2.10*2.10 | 3.36
Absorber geometry and local shielding:
Size for carbon and iron for different beam energy, adopt from other projects, is suitable but haven't been optimized.
Local size selection (11GeV dump as example):
2D map of dose distribution was simulated by FLUKA, the dose rate alone Z or X axis was averaged by 10*10cm^2 area, the shielding size can be selected by the setting dose rate limit.
Preliminary design results for different beam energy analysis station:
Radiation level nearby each energy analysis station was figured out, also specify a roughly space for the future local shielding.

## Slide 37
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | Charge/nC | Bunch populartion/
10GeV | 1 | Beam Energy Analysis | 60MeV | 2/1 | 1 | 10 | 6.3
 | 2 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 10 | 6.3
 | 3 | Beam Energy Analysis | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
 | 4 | Positron target position | 200MeV | 1.5/1.5 | 100 | - | 6.0
 | 5 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 3 | 
 | 6 | Beam Energy Analysis | 11GeV | 0.5/0.5 | 1 | 3 | 
 | 7 | Dump for Linac beam | 11GeV | 0.5/0.5 | 1 | 3 | 1.9
20GeV | 1 |  | 60MeV | 2/1 | 1 | 10 | 6.3
 | 2 |  | 4GeV | 0.5/0.5 | 1 | 10 | 6.3
 | 3 |  | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
 | 4 |  | 1.1 | 0.5/0.5 | 1 | 5 | 
 | 5 |  | 6 | 0.5/0.3 | 1 | 3 | 
 | 6 |  | 20GeV | 0.3/0.3 | 1 | 3 | 
 | 7 |  | 20GeV | 0.3/0.3 | 1 | 3 | 1.9
 | 8 |  | 250MeV | 1.5/1.5 | 100 | 5 | 
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | Charge/nC | 
10GeV | 1 | Beam Energy Analysis | 60MeV | 2/1 | 1 | 10 | 6.3
 | 2 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 10 | 6.3
 | 3 | Beam Energy Analysis | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
 | 4 | Positron target position | 200MeV | 1.5/1.5 | 100 | - | 6.0
 | 5 | Beam Energy Analysis | 1.2GeV | 0.5/0.5 | 1 | 3 | 
 | 6 | Beam Energy Analysis | 11GeV | 0.5/0.5 | 1 | 3 | 
 | 7 | Dump for Linac beam | 11GeV | 0.5/0.5 | 1 | 3 | 1.9
20GeV | 1 |  | 60MeV | 2/1 | 1 | 10 | 6.3
 | 2 |  | 4GeV | 0.5/0.5 | 1 | 10 | 6.3
 | 3 |  | 250MeV | 1.5/1.5 | 1 | 5 | 3.2
 | 4 |  | 1.1 | 0.5/0.5 | 1 | 5 | 
 | 5 |  | 6 | 0.5/0.3 | 1 | 3 | 
 | 6 |  | 20GeV | 0.3/0.3 | 1 | 3 | 
 | 7 |  | 20GeV | 0.3/0.3 | 1 | 3 | 1.9
 | 8 |  | 250MeV | 1.5/1.5 | 100 | 5 | 

## Slide 38
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | bunch charge/nC | Number of particles [/s] | Total energy[W] | CSDA range[g/cm^2]
TDR 20GeV | 1 |  | 60MeV | 2/1 | 2 | 10 | 12.5 | 1.2 | 26
 | 2 |  | 4GeV | 0.5/0.5 | 2 | 10 | 12.5 | 80 | 214
 | 3 |  | 250MeV | 1.5/1.5 | 2 | 5 | 6.3 | 2.5 | 64.7
 | 4 |  | 1.1GeV | 0.5/0.5 | 2 | 5 | 6.3 | 11 | 128
 | 5 |  | 6GeV | 0.5/0.3 | 2 | 3 | 3.7 | 36 | 248
 | 6 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120 | 383
 | 7 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120 | 383
 | 8 |  | 250MeV | 1.5/1.5 | 200 | 5（暂定） | 624 | 250 | 64.7
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | bunch charge/nC |  | Total energy[W] | CSDA range[g/cm^2]
TDR 20GeV | 1 |  | 60MeV | 2/1 | 2 | 10 | 12.5 | 1.2 | 26
 | 2 |  | 4GeV | 0.5/0.5 | 2 | 10 | 12.5 | 80 | 214
 | 3 |  | 250MeV | 1.5/1.5 | 2 | 5 | 6.3 | 2.5 | 64.7
 | 4 |  | 1.1GeV | 0.5/0.5 | 2 | 5 | 6.3 | 11 | 128
 | 5 |  | 6GeV | 0.5/0.3 | 2 | 3 | 3.7 | 36 | 248
 | 6 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120 | 383
 | 7 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120 | 383
 | 8 |  | 250MeV | 1.5/1.5 | 200 | 5（暂定） | 624 | 250 | 64.7
 | Beam energy | R/m | Length/m
1 | 60MeV | 0.7 | 1
2 | 4GeV | 1.2 | 2.6
3 | 250MeV | 0.55 | 1
4 | 1.1GeV | 0.85 | 1.7
5 | 6GeV | 1 | 2.5
6/7 | 20GeV | 1.2 | 3.8
8 | 250MeV | 1.3 | 1.8

## Slide 39: 直线dump和线损屏蔽
Dump 尺寸估计
线损屏蔽墙厚度估计

## Slide 40: dump点损参数
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | bunch charge/nC | Number of particles [/s] | Total energy[W]
TDR 20GeV | 1 |  | 60MeV | 2/1 | 2 | 10 | 12.5 | 1.2
 | 2 |  | 4GeV | 0.5/0.5 | 2 | 10 | 12.5 | 80
 | 3 |  | 250MeV | 1.5/1.5 | 2 | 5 | 6.3 | 2.5
 | 4 |  | 1.1GeV | 0.5/0.5 | 2 | 5 | 6.3 | 11
 | 5 |  | 6GeV | 0.5/0.3 | 2 | 3 | 3.7 | 36
 | 6 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120
 | 7 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120
 | 8 |  | 250MeV | 1.5/1.5 | 200 | 5（暂定） | 624 | 250
 | No. | Purpose of dumps | Beam energy | Bunch size/mm | Frequency/Hz | bunch charge/nC |  | Total energy[W]
TDR 20GeV | 1 |  | 60MeV | 2/1 | 2 | 10 | 12.5 | 1.2
 | 2 |  | 4GeV | 0.5/0.5 | 2 | 10 | 12.5 | 80
 | 3 |  | 250MeV | 1.5/1.5 | 2 | 5 | 6.3 | 2.5
 | 4 |  | 1.1GeV | 0.5/0.5 | 2 | 5 | 6.3 | 11
 | 5 |  | 6GeV | 0.5/0.3 | 2 | 3 | 3.7 | 36
 | 6 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120
 | 7 |  | 20GeV | 0.3/0.3 | 2 | 3 | 3.7 | 120
 | 8 |  | 250MeV | 1.5/1.5 | 200 | 5（暂定） | 624 | 250

## Slide 41: 直线dump结构
参考HEPS直线dump，采用三层圆柱（筒）结构
  中心圆柱：碳（石墨）；半径5cm，长度15cm~225cm。
  中层圆桶：铁；内径5cm，外径60cm~1.1m，长度80cm~3.7m。
  外层圆桶：聚乙烯；厚10cm~20cm。
为了抑制背散射剂量，铁圆桶和聚乙烯圆桶左端面相比碳靶左端面，向左侧超出若干距离，此距离未优化。 即图中碳圆柱左端面Z坐标为0，铁和聚乙烯左端面坐标为负值。
各dump半径和长度；长度从碳靶左端面（左图坐标原点，Z=0处）算起。
 | Beam energy | R/m | Length/m
1 | 60MeV | 0.7 | 1
2 | 4GeV | 1.2 | 2.6
3 | 250MeV | 0.55 | 1
4 | 1.1GeV | 0.85 | 1.7
5 | 6GeV | 1 | 2.5
6/7 | 20GeV | 1.2 | 3.8
8 | 250MeV | 1.3 | 1.8

## Slide 42: CEPC linac
Length: 1215m; 6 dumps and 1 collimator;
Dump1
Dump2
Dump3 + Collimator
Dump4
Dump5
Dump6

## Slide 43: Linac beam losses assumptions
Angle of incidence 10mrad
Not consider EBTL & DR beam losses.
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | Number of particles [/s]
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 700m | 1.1~20GeV |  | 0.1 | 12.5
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | 
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 700m | 1.1~20GeV |  | 0.1 | 12.5

## Slide 44: Simulation setup
俯视图
  隧道内只有束流管和部分bypass束流管
  混凝土墙
  长度参照前页直线示意图
有、无bypass部分的右视图

## Slide 45: Dose-eq: FAS
束流管所在水平面内剂量当量约1~100Sv/h
以5.5mSv限值（土壤中）估计，左/右/下侧混凝土墙厚度约30cm/20cm/30cm。
以2.5uSv限值（空气中）估计，顶部混凝土厚度1.3m。

## Slide 46: Dose-eq: PSPAS ~ SAS
束流管所在水平面内剂量当量约10~1000Sv/h
以5.5mSv限值（土壤中）估计，左/右/下侧混凝土墙厚度约1.9m/1.9m/2.1m。
以2.5uSv限值（空气中）估计，顶部混凝土厚度4.1m。

## Slide 47: Dose-eq: tAS
束流管所在水平面内剂量当量约2~100Sv/h
以5.5mSv限值（土壤中）估计，左/右/下侧混凝土墙厚度约30cm/30cm/30cm。
以2.5uSv限值（空气中）估计，顶部混凝土厚度2m。

## Slide 48: Dose-eq in Linac tunnel
Dose-eq inside Linac tunnel is important to determine the local shielding thickness.
Assume that leptons will be lost alone the beam-pipe. About 10% leptons with energy 10GeV is lost alone the beamline.
Dose-eq: total, gamma, neutron
Linac parameters
Linac simulation setup

## Slide 49: vacuum chamber: FCC-ee, two schemes
Absorbers (ABS)
CuCrZr alloy
Length: 30cm
5-6m distance
Angled surfaces for even power
Water cooled
25 ABS in each beam (MBs, MQs)
    (Design and initial placement by R. Kersevan)
Barbara Humann, FCC week 2021 talk
Continuous shielding
Equivalent to LEP layout
Continuous shielding around VC in MBs
  Due to space restrictions from yoke and coils respectively, no shielding in MQs and MSs.
Intermet180 (Tungsten alloy)
Shielding thickness:
  Top/bottom: 1cm
  Sides: 1.3cm

## Slide 50: deposited Energy
The energy deposited in air and wall is less than 5%.
Energy deposited in dipole and beam-pipe is quite large.
2cm-lead shielding
 | Z | WW | Higgs | ttbar
Beam pipe (Al) | 50.0% | 45.9% | 38.5% | 36.0%
Beam pipe (Cu) | 46.7% | 27.4% | 23.0% | 26.8%
Lead | 1.1% | 9.6% | 14.9% | 14.5%
Iron of dipole | 1.9% | 14.5% | 18.7% | 16.4%
Iron of quadrupole | 0.1% | 0.9% | 1.4% | 1.4%
Iron of sextupole | 0.1% | 0.6% | 0.9% | 0.8%
Air | 0.0005% | 0.01% | 0.03% | 0.04%
Wall | 0.0004% | 0.03% | 1.8% | 3.1%

## Slide 51: CEPC parameters
 | Higgs | WW | Z | Z (high lum.) | ttbar
Beam energy (GeV) | 120 | 80 | 45.5 |  | 182.5
SR loss/turn (GeV) | 1.73 | 0.34 | 0.036 |  | 9.15
Particles/bunch () | 15 | 12 | 8 | 15 | 20
Bunch number | 242 | 1524 | 12000 | 15000 | 35
Beam current (mA) | 17.4 | 87.9 | 461.0 | 1081.4 | 3.36
SR power/beam (MW) | 30 | 30 | 16.5 | 38 | 30
Bending radius (km) | 10.72 |  |  |  | 
Critical energy(keV) | 358 | 106 | 19 |  | 1258
Ave. energy/photon (keV) | 110.1 | 32.6 | 6.0 |  | 387.3
Photons/57.2m dipole |  |  |  |  | 
 | Higgs | WW | Z | Z (high lum.) | ttbar
Beam energy (GeV) | 120 | 80 | 45.5 |  | 182.5
SR loss/turn (GeV) | 1.73 | 0.34 | 0.036 |  | 9.15
 | 15 | 12 | 8 | 15 | 20
Bunch number | 242 | 1524 | 12000 | 15000 | 35
Beam current (mA) | 17.4 | 87.9 | 461.0 | 1081.4 | 3.36
SR power/beam (MW) | 30 | 30 | 16.5 | 38 | 30
Bending radius (km) | 10.72 |  |  |  | 
Critical energy(keV) | 358 | 106 | 19 |  | 1258
Ave. energy/photon (keV) | 110.1 | 32.6 | 6.0 |  | 387.3
Photons/57.2m dipole |  |  |  |  | 

## Slide 52: Hot points (2cm lead)
Quadrupole XY plane
Quadrupole : YZ plane
Dose hot points caused by particles bypassing lead shielding.
2D dose distribution on the surface of insulator

## Slide 53: Hot points (2cm lead)
Dose hot points caused by particles bypassing lead shielding.
2D dose distribution on the surface of insulator
Sextupole XY plane
Sextupole : YZ plane

## Slide 55: Dose around insulators
Lead thickness: 1.5cm
Dipole:
Quadrupole:
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Al |  |  |  | 
Cu |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Al |  |  |  | 
Cu |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Top right |  |  |  | 
Bottom right |  |  |  | 
Top left |  |  |  | 
Bottom left |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Top right |  |  |  | 
Bottom right |  |  |  | 
Top left |  |  |  | 
Bottom left |  |  |  | 

## Slide 56: Dose around insulators
 | Dipole | Quadrupole | Sextupole
Dose(Gy) |  |  | 
 | Dipole | Quadrupole | Sextupole
Lead thickness: 1.5cm
Sextupole:
Running schedule
Dose:
  10y H/Z/WW
  One year running ttbar
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Left |  |  |  | 
right |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Left |  |  |  | 
right |  |  |  | 
 | Higgs | Z | WW
Running time (yr) | 7 | 2 | 1
 | Dipole | Quadrupole | Sextupole
Dose(Gy) |  |  | 
 | Dipole | Quadrupole | Sextupole

## Slide 57: Dose around insulators
Lead thickness: 2.5cm
Dipole:
Quadrupole:
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Al |  |  |  | 
Cu |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Al |  |  |  | 
Cu |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Top right |  |  |  | 
Bottom right |  |  |  | 
Top left |  |  |  | 
Bottom left |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Top right |  |  |  | 
Bottom right |  |  |  | 
Top left |  |  |  | 
Bottom left |  |  |  | 

## Slide 58: Dose around insulators
 | Dipole | Quadrupole | Sextupole
Dose(Gy) |  |  | 
 | Dipole | Quadrupole | Sextupole
Lead thickness: 2.5cm
Sextupole:
Running schedule
Dose:
  10y H/Z/WW
  One year running ttbar
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Left |  |  |  | 
right |  |  |  | 
 | Dose(Gy/Ah) |  |  | 
 | Z | WW | Higgs | ttbar
Left |  |  |  | 
right |  |  |  | 
 | Higgs | Z | WW
Running time (yr) | 7 | 2 | 1
 | Dipole | Quadrupole | Sextupole
Dose(Gy) |  |  | 
 | Dipole | Quadrupole | Sextupole

## Slide 59: Temperature rise
Simulate only one bunch whose width is minimum
 |  | ttbar | Higgs | WW | Z(2T high lumi.)
Beam energy/GeV |  | 175 | 120 | 80 | 45.5
Ne/(bunch) |  | 24 | 17 | 12 | 15
Bunch number |  | 34 | 218 | 1569 | 15000
Total energy/MJ |  | 0.2 | 0.7 | 2.4 | 16.4
Maximum temperature rise | Fluka |  |  |  | 
 | One bunch |  |  |  | 
 |  | ttbar | Higgs | WW | Z(2T high lumi.)
Beam energy/GeV |  | 175 | 120 | 80 | 45.5
 |  | 24 | 17 | 12 | 15
Bunch number |  | 34 | 218 | 1569 | 15000
Total energy/MJ |  | 0.2 | 0.7 | 2.4 | 16.4
Maximum temperature rise | Fluka |  |  |  | 
 | One bunch |  |  |  | 

## Slide 60: dose Around insulators
In the arc section of the ring, the most important two radiation sources are from synchrotron radiation and random beam loss.
Around coils, dose caused by SR is more serious than by beam loss.
Prompt radiation dose caused by random beam loss
Prompt radiation dose caused by synchrotron radiation

## Slide 61: Number of Beam losses & SR
Beam losses & SR photon of energy >6MeV
FLUKA options
Wall material:
  Case1: water as wall
  Case2: rock as wall
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Number of bunches | 30MW | 249 | 1297 | 11951 | 35
 | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 30MW | 8e9 | 6e-8 | negligible | 8e14
 | 50MW | 1.4e10 | 1e-7 |  | 1.3e15
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 30MW |  |  |  | 
 | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Number of bunches | 30MW | 249 | 1297 | 11951 | 35
 | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 30MW | 8e9 | 6e-8 | negligible | 8e14
 | 50MW | 1.4e10 | 1e-7 |  | 1.3e15
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 30MW |  |  |  | 
 | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7

## Slide 62: Soil/rock
 |  | Soil 1 | Soil 2 | average components of 花岗岩、片麻岩、黄土、砂岩 | 长沙黑麋峰
density |  | 1.6g/cm^3 | 2.2g/cm^3 | 1.2~3.3g/cm^3 | ~2.9g/cm^3
Major element (wt%) | C | 1.0 | 5.1 | --- | ---
 | N | 0.12 | --- | --- | ---
 | O | 34 | 64 | 30~70 | 48.3
 | Na | 0.50 | 0.34 | 0.1~2.9 | 2.4
 | Mg | 0.52 | 3.8 | 0.4~3.7 | 0.2
 | Al | 8.0 | 2.4 | 3.5~9.7 | 7.8
 | Si | 40 | 14.5 | 26~39 | 34
 | P | --- | --- | 0.02~0.16 | 0.06
 | K | 2.36 | 0.81 | 1.8~3.7 | 4.2
 | Ca | 2.26 | 7.0 | 0.2~4.8 | 1.0
 | Ti | 1.0 | --- | 0.09~0.8 | 0.11
 | Mn | 0.24 | --- | 0.02~0.12 | 0.02
 | Fe | 9.6 | 1.1 | 0.8~6.3 | 1.1

## Slide 63: Number of Beam losses & SR
Beam losses & SR photon of energy >6MeV
FLUKA options
Wall material:
  Case1: water as wall
  Case2: rock as wall
One year running
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 30MW | 0.33 | 0.91 | 1.33 | 0.30
 | 50MW |  |  |  | 
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7

## Slide 64: Soil/rock
 |  | Soil | average components of 花岗岩、片麻岩、黄土、砂岩 | 长沙黑麋峰
density |  | 1.6g/cm^3 | 1.2~3.3g/cm^3 | ~2.9g/cm^3
Major element (wt%) | C | 1.0 | --- | ---
 | N | 0.12 | --- | ---
 | O | 34 | 30~70 | 48.3
 | Na | 0.50 | 0.1~2.9 | 2.4
 | Mg | 0.52 | 0.4~3.7 | 0.2
 | Al | 8.0 | 3.5~9.7 | 7.8
 | Si | 40 | 26~39 | 34
 | P | --- | 0.02~0.16 | 0.06
 | K | 2.36 | 1.8~3.7 | 4.2
 | Ca | 2.26 | 0.2~4.8 | 1.0
 | Ti | 1.0 | 0.09~0.8 | 0.11
 | Mn | 0.24 | 0.02~0.12 | 0.02
 | Fe | 9.6 | 0.8~6.3 | 1.1
In previous study, use soil as tunnel wall.
Now use average components of different kinds of rock.
Simulate residual nuclei in:
  Cooling water
  Air in tunnel
  Water outside tunnel
  Rock

## Slide 65: Cooling water
 |  | Half-life | Case 1 |  |  | Case 2 |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%) | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.44 | 2.76 | 10 | 2.37 | 2.67 | 3
 | C14 | 5700a | 3.5e-7 | 3.9e-3 | 23 | 3.4e-7 | 3.9e-3 | 9
 | Be7 | 53d | 1.3e-2 | 15.2 | 34 | 1.3e-2 | 14.4 | 12
 | H3 | 12a | 2.3e-6 | 2.6e-2 | 22 | 2.8e-6 | 3.2e-2 | 7
SR @ttbar | None |  |  |  |  |  |  | 

## Slide 66: Air in tunnel
Activation by beam losses
 |  | Half-life | Case 1 |  |  | Case 2 |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%) | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.7e-4 | 0.13 | 52 | 3.2e-4 | 0.15 | 17
 | C14 | 5700a | 7.7e-7 | 3.6 | 1 | 3.2e-7 | 1.5 | 0.5
 | Be7 | 53d | 1.1e-5 | 5.4 | 57 | 1.0e-5 | 4.8 | 27
 | H3 | 12a | 3.5e-9 | 1.7e-2 | 32 | 3.9e-9 | 1.8e-2 | 10
 | P32 | 14d | --- | --- | --- | 1.9e-7 | 9.0 | 100
 | P33 | 25d | 1.9e-8 | 9.0e-2 | 100 | 3.8e-9 | 1.8e-2 | 100
 | Cl36 | 3e5a | --- | --- | --- | 1.6e-14 | 7.7e-7 | 100
 | Cl38 | 37m | --- | --- | --- | 7.e-5 | 3.6 | 61
 | Ar37 | 35d | 6.1e-9 | 0.29 | 59 | 1.4e-9 | 6.5e-2 | 38
 | Ar41 | 2h | 1.4e-3 | 0.65 | 12 | 5.4e-4 | 0.26 | 6
SR @ttbar | C14 | 5700a | 6.5e-6 | 31 | 2 | 2.5e-6 | 11.7 | 3
 | Ar41 | 2h | 1.5e-2 | 7.2 | 20 | 3.3e-3 | 1.6 | 29

## Slide 67: Water outside tunnel
 |  | Half-life | Water in wall |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2e-3 | 39 | 2
 | C14 | 5700a | 5e-10 | 8e-3 | 4
 | Be7 | 53d | 3e-5 | 477 | 5
 | H3 | 12a | 6e-9 | 1 | 3
 | F18 | 2h | 5e-6 | 9 | 52
SR @ttbar | C14 | 5700a | 2e-12 | 3e-4 | 99
 | H3 | 12a | 1e-10 | 2e-2 | 71

## Slide 68: rock around tunnel
 |  | Half-life | Rock |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | Co60 | 5.3a | 8.92E-12 | 1.71E-04 | 99
 | Fe59 | 44d | 1.62E-03 | 3.11E+03 | 0.586
 | Ni59 | 7.6e4a | 2.08E-17 | 3.99E-10 | 72.617
 | Co58 | 71d | 7.13E-07 | 1.37E+00 | 70.563
 | Co57 | 272d | 1.09E-07 | 2.09E+00 | 47.979
 | Mn56 | 2.6h | 1.03E-01 | 1.98E+06 | 0.184
 | Co56 | 77d | 8.54E-06 | 1.64E+02 | 22.207
 | Fe55 | 3a | 1.24E-05 | 2.37E+04 | 0.166
 | Co55 | 18h | 1.70E-06 | 3.25E+00 | 50.501
 | Mn54 | 312d | 6.94E-04 | 1.33E+03 | 1.793
 | Mn53 | 3.8e6a | 1.98E-13 | 3.79E-07 | 2.116
 | Mn52 | 5.6d | 2.02E-04 | 3.87E+03 | 4.816
 | Fe52 | 8.3h | 7.45E-06 | 1.43E+01 | 23.642

## Slide 69: rock around tunnel
 |  | Half-life | Case 1 |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | Cr51 | 28d | 3.58E-06 | 6.86E+01 | 3.519
 | Mn51 | 46.2m | 3.46E-05 | 6.63E+02 | 11.289
 | Sc48 | 1.8d | 3.07E-05 | 5.88E+02 | 11.042
 | V48 | 16d | 8.87E-05 | 1.70E+03 | 7.25
 | Ca47 | 4.5d | 1.95E-05 | 3.74E+01 | 10.514
 | Sc47 | 3.3d | 1.41E-05 | 2.70E+02 | 5.303
 | Sc46 | 84d | 1.67E-04 | 3.20E+02 | 5.993
 | Ca45 | 163d | 5.49E-06 | 1.05E+03 | 0.279
 | K43 | 22h | 1.66E-05 | 3.18E+01 | 16.576
 | K42 | 12h | 4.55E-03 | 8.71E+04 | 0.201
 | Ar41 | 1.8h | 2.26E-06 | 4.33E-02 | 10.589
 | K40 | 1.2d9a | 4.66E-11 | 8.94E-04 | 0.108
 | Cl38 | 37m | 3.64E-05 | 6.97E+01 | 12.14

## Slide 70: rock around tunnel
 |  | Half-life | Case 1 |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | Ar37 | 35d | 4.45E-08 | 8.52E+01 | 0.697
 | Cl36 | 3e5a | 1.45E-11 | 2.77E-02 | 0.563
 | S35 | 87d | 9.35E-09 | 1.79E+00 | 6.826
 | P33 | 25d | 5.57E-09 | 1.07E+00 | 8.923
 | P32 | 14d | 1.44E-06 | 2.76E+03 | 5.557
 | Si31 | 2.6h | 6.82E-04 | 1.31E+05 | 0.123
 | Na24 | 15h | 3.26E-01 | 6.24E+06 | 0.113
 | Na22 | 2.6y | 7.20E-04 | 1.38E+03 | 1.322
 | F18 | 1.8h | 7.62E-04 | 1.46E+03 | 2.468
 | O15 | 122s | 1.34E-03 | 2.58E+01 | 0.694
 | C14 | 5700y | 3.47E-10 | 6.65E-02 | 1.337
 | Be7 | 53d | 2.09E-05 | 4.00E+02 | 1.632
 | H3 | 12a | 5.90E-09 | 1.13E+00 | 0.884

## Slide 71: rock around tunnel
 |  | Half-life | Case 1 |  | 
 |  |  | Specific activity/GB18871 | Activity/GB18871 | Stat. error (%)
SR @ttbar | C14 | 5700a | 1.5e-12 | 2.9e-4 | 99
 | H3 | 12a | 9.5e-11 | 1.8e-2 | 71

## Slide 72: Leachable radionuclides
H3, Na22, Ca45, Mn54, Cs134

## Slide 73: Production of toxic gases
Deposited energy by photons
Saturated concentrations of ozone and oxides of nitrogen. [Hoefert, 1986]
  smaller than limit values
 | Case 1 | Case 2
Beam losses | 2.1e13eV | 6.0e12eV
SR | 6.4e15eV | 1.6e15eV
 |  | O3 | NOx | HNO3
Number | Case 1 | 3.3e17 | 1.6e17 | 5.0e16
 | Case 2 | 9.3e16 | 4.5e16 | 1.4e16
Density (g/m^3) | Case 1 | 1.8e-10 | 8.6e-11 | 2.7e-11
 | Case 2 | 5.1e-11 | 2.4e-11 | 8.6e-12