## Slide 1: Beam-Beam Effects at CEPC
Yuan Zhang, Na Wang, Huiping Geng
CEPC Workshop
2022-Oct

## Slide 2: Outline
Update with New Longitudinal Impedance (ZL)
Simulation with Transverse Impedance (ZT)
Mitigation Scheme of Instability
+ Lattice (Higgs)
Summary

## Slide 3: Beam-Beam Related Issues
Beamstrahlung Effect (Luminosity, Lifetime)
Coherent head-tail instability (X-Z instability)
  Influenced by Potential Well Distortion due to longitudinal impedance (ZL)
TMCI-like instability in vertical direction with transverse impedance (ZT)
Combined effect of Beam-Beam Interaction and realistic lattice
…

## Slide 4: Higgs: versus Horizontal tune
Old Impedance
New Impedance
Stable tune area is too limited
Longitudinal impedance has been updated
= 0.33 m, Np = 14e10
Piwinski Angle: 6

## Slide 5: Higgs: =0.3 m, Np=13e10
Luminosity
versus Horizontal tune
Width of stable tune area: 0.006
Lum ~ 5e34
Beamstrahlung Liftime ~ 50min with MA=1.7%
Old: = 0.33 m, Np = 14e10

## Slide 6: W: versus Horizontal tune
Old Impedance
New Impedance
With stronger ZL, Stable tune area is still large enough
Piwinski Angle: 6

## Slide 7: Z: versus Horizontal tune
Old Impedance
New Impedance
Stable tune area is still large enough, even squeezed.
Piwinski Angle: 24

## Slide 8: Finite dispersion @ ZL
It is not found any clear effect from finite dispersion
Lum [Arbitrary Unit]
If the finite dispersion at ZL induce more synchro-betatron coupling? By K. Oide

## Slide 9: Frequency Analysis of Single Beam with Transverse Impedance (ZT)
IBB
Courtesy of Mauro Migliorati
PyHEADTAIL (only ZT)
Considering ZL,
the X threshold reduces from 22e10 to 18e10.
Considering ZL,
the Y threshold reduces from 24e10 to 18e10.
Considering ZL,
the X threshold reduces from 22e10 to 18e10.
Considering ZL,
the Y threshold reduces from 30e10 to 20e10.
Even though the tune shift reduces considering ZL, the instability threshold is lower!
PyHEADTAIL (only ZT)

## Slide 10: ttbar, w/ZT
No clear effect from transverse impedance.
Optimized Qx~0.570
Piwinski Angle: 1.2

## Slide 11: Higgs, w/ ZT
Only X-Z instability
Stable area width is reduced a little (ZT only applied 1 kick)

## Slide 12: W, w/ ZT
Only X-Z instability
stable region is large enought (ZT applied 1 kick)

## Slide 13: Z, w/ ZT
No stable working points
There exist very strong blowup in both X/Y direction

## Slide 14: CEPC Only Zx(+ZL)
Kick number of wake field affect the result
In horizontal direction, smooth distributed impedance nearly does not squeeze the stable tune area serious
A very local impedance may squeeze the stable area.
Simulation
Analysis, ZT kick applied at IP
Courtesy of Chuntao Lin and Na Wang
In horizontal direction, considering ZX
the instability growth rate is faster,
unstable tune area increases
Stable tune area is large enough (w/ZT)
Simulation and analysis agrees qualitatively.

## Slide 15: CEPC Only Zx(+ZL) @ Qx=0.562
X-Z instability is first excited
Bunch length is shorter
X-TMCI-like instability is then excited
Y is blowup due to stronger beam-beam interaction
It has been simulated that w/o BS (but keep same bunch length), the TMCI-like instability would not appear.
Behavior at unstable working point

## Slide 16: CEPC Only Zy(+ZL) Qx=0.567
Kick number of wake field affect the result
No stable tune area
Simulation
Analysis, ZT kick applied at IP
Courtesy of Chuntao Lin and Na Wang
  pure beam-beam is unstable due to ignorance of strong nonlinearity ?
  It is also found enhance of instability when considering ZY
No stable working point (w/ZT)
Simulation and analysis agrees qualitatively.

## Slide 17: CEPC Only Zy(+ZL) Qx=0.567
Y-TMCI-like instability is first excited
Bunch length is shorter
X-Z instability is excited
Stronger Y blowup due to strong beam-beam
It has been simulated that w/o BS (but keep same bunch length), the X-Z instability would not appear.
Behavior at unstable working point
mode

## Slide 18: Effect of Vertical Chromaticity (Lum & )
Qy’~10 could help suppress the strong TMCI-like instability induced by BB+ZT
ZX+ZY+ZL, Qx=0.567
Qy’=0
Qy’=5
Qy’=10

## Slide 19: Effect of different vertical tune (Qy+=0.610)
Qy’=0
Qy’=5
Qy Difference > 0.01 could help suppress instability with Qy’=5
Thanks: K. Oide, K. Ohmi

## Slide 20: Different Horizontal tune
Qx+=0.567
Asymmetric
Symmetric

## Slide 21: Higgs: Lifetime and equilibrium distribtuion
50k turns
w/o beambeam
@IP
@Injection point
@RF section
Realistic lattice w/o beam-beam
Huiping Geng and Yiwei Wang
K. Ohmi and F. Zimmermann, IPAC14

## Slide 22: Higgs:Lifetime w/ and w/o beambeam
50k turns, 1k macro-particles @injection point
Survival particles:
1000
Survival particles:
861
w/o bb
w/ bb
Huiping Geng and Yiwei Wang
Realistic lattice w/o and w/ beam-beam

## Slide 23: Higgs: Lifetime optimization
50k turns, 1k macro-particles @injection point
32 families of sextupoles in Arc
Survival particles:
962
Huiping Geng and Yiwei Wang
Realistic lattice w/ beam-beam
NIMA 959 (2020) 163517
Diffusion Map Analysis

## Slide 24: Summary
ZL: Updated longitudinal impedance is considered, machine parameter is optimized further
  Finite dispersion does not induce clear effect
The transverse impedance does not bring serious effect for ttbar/Higgs/W
Combined effect of beam-beam interaction and transverse impedance may induce strong head-tail instability in vertical direction at Z mode
In the presence of Beamstrahlung, X-Z instability may induce strong TMCI instability in horizontal direction with conventional impedance. TMCI instability in vertical direction could induce X-Z instability
The chromaticity could help mitigate the vertical TMCI instability induced by beam-beam with impedance
Asymmetric transverse tunes could help suppress the X-Z(horizontal) or TMCI (vertical) instability, since sigma-mode dominate

## Slide 25
backup

## Slide 26: Machine parameters of CEPC
 | Higgs | Z | W | ttbar
Number of IPs | 2 |  |  | 
Circumference [km] | 100.0 |  |  | 
SR power per beam [MW] | 30 |  |  | 
Half crossing angle at IP [mrad] | 16.5 |  |  | 
Bending radius [km] | 10.7 |  |  | 
Energy [GeV] | 120 | 45.5 | 80 | 180
Energy loss per turn [GeV] | 1.8 | 0.037 | 0.357 | 9.1
Piwinski angle | 5.94 | 24.68 | 6.08 | 1.21
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing [ns] | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population [10^10] | 13 | 14 | 13.5 | 20
Beam current [mA] | 16.7 | 803.5 | 84.1 | 3.3
Momentum compaction [10^-5] | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP (bx/by) [m/mm] | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance (ex/ey) [nm/pm] | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Beam size at IP (sigx/sigy) [um/nm] | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) [mm] | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) [%] | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) [%] | 1.6/2.2 | 1.3/1.7 | 1.2/2.5 | 2.3/2.6
Beam-beam parameters (ksix/ksiy) | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage [GV] | 2.2 | 0.12 | 0.7 | 10
RF frequency [MHz] | 650 | 650 | 650 | 650
Longitudinal tune Qs | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (bhabha/beamstrahlung)[min] | 39/40 | 80/18000 | 60/700 | 81/23
Beam lifetime [min] | 20 | 80 | 55 | 18
Hour glass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP[1e34/cm^2/s] | 5.0 | 115 | 16 | 0.5
by CEPC AP group, 2 June 2022