## Slide 1: CEPC booster and damping ring
Dou Wang (IHEP)
on behalf of CEPC AP group
The 2022 international workshop on the high energy Circular Electron-Positron Collider, October 24-28, 2022. IHEP & Nanjing University.

## Slide 2: outline
Design status for CEPC booster
Summary
Design status for CEPC positron damping ring

## Slide 3: CEPC injector chain
30 GeV linac provides electron and positron beams for booster.
Top up injection for collider ring ~ 3% current decay
Booster is in the same tunnel as collider ring, above the collider ring, bypass in IR.
Budget for transfer efficiency 90%: 95% for booster + 95% for transport lines.
Beam current threshold in booster is limited by RF system.
Feedback systems (Transverse & longitudinal) are need to damp the instability at low energy.
Injection energy: 30GeV
100km
30GeV
30180GeV

## Slide 4
Collider ring | Higgs (CDR) | Higgs (TDR)
Number of IPs | 2 | 2
Energy (GeV) | 120 | 120
Circumference (km) | 100 | 100
SR loss/turn (GeV) | 1.73 | 1.8
Half crossing angle (mrad) | 16.5 | 
Piwinski angle | 3.48 | 5.94
Ne/bunch (1010) | 15.0 | 13.0
Bunch number | 242 | 268
Beam current (mA) | 17.4 | 16.7
SR power /beam (MW) | 30 | 30
Bending radius (km) | 10.7 | 10.2
Momentum compaction (10-6) | 11.1 | 7.1
IP x/y (m) | 0.36/0.0015 | 0.3/0.001
Emittance x/y (nm) | 1.21/0.0024 | 0.64/0.0013
Transverse IP (um) | 20.9/0.06 | 14.0/0.036
x/y/IP | 0.018/0.109 | 0.015/0.11
VRF (GV) | 2.17 | 2.20
f RF (MHz) (harmonic) | 650 (216820) | 
Nature bunch length z (mm) | 2.72 | 2.3
Bunch length z (mm) | 4.4 | 4.1
Energy spread (%) (SR/BS) | 0.1/0.134 | 0.1/0.17
Energy acceptance requirement (%) | 1.35 | 1.6
Energy acceptance by RF (%) | 2.06 | 2.2
Lifetime due to beamstrahlung (min) | 80 | 40
Lifetime (min) | 25 | 20
F (hour glass) | 0.89 | 0.9
Lmax/IP (1034cm-2s-1) | 2.93 | 5.0
Requirement update for booster
Horizontal DA requirement of collider ring due to injection
X. H. Cui
Booster emittance @120 GeV <1.7nm (3.6nm in CDR)

## Slide 5: Booster TDR optics
TME like structure (cell length=78m)
Interleave sextupole scheme
Emittance@120GeV=1.26nm
D. Wang, C. H. Yu, Y. M. Peng…
Arc cell
Overall idea: uniform distribution for the Q
Combined magnet (B+S) scheme possible
Phase advance/cell: 100 (H) / 28 (V)
Dispersion sup.
Half ring

## Slide 6
Booster alternative optics
FODO structure (cell length=70m)
90/90 phase advance
Non-interleave sextupole scheme
Similar structure as CDR
FODO
=1.29nm
Emittance@120GeV=1.29nm
dis. supressor
straight section

## Slide 7
DA results @ 20GeV
Booster energy: 20GeV~180GeV
20GeV: BSCxy=(4xy+5mm)*2
Inj. emittance from Linac:10nm
Energy spread from Linac: 0.16%

## Slide 8
TME
DA results with errors and correction (w/o multipoles)
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | 100
Longitudinal shift Z (μm) | 100 | 150 | 100
Tilt about X/Y (mrad) | 0.2 | 0.2 | 0.2
Tilt about Z (mrad) | 0.1 | 0.2 | 0.2
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
D. H. Ji
error correction (w/o SR effect)
Orbit correction
Optics correction
FODO

## Slide 9
Multipole errors @ 20GeV
FODO
Multipole errors only
Multipole errors can not be corrected
TME is chosen as the baseline for TDR.
TME

## Slide 10: Injection energy change to 30GeV
30GeV injection is adopted for the cost saving in TDR.
The non-oriented silicon laminations for the iron dominated dipole magnet can be used at 30GeV.
Make a cost balance between Linac and booster
Linac parameters at 30GeV
- bunch length= 0.4mm, energy spread= 0.15%, emittance=6.5nm
Magnetic design: the quality of the dipole and sextupole fields meet the physical requirements.

## Slide 11
DA results with errors and correction
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | -
Longitudinal shift Z (μm) | 100 | 150 | -
Tilt about X/Y (mrad) | 0.2 | 0.2 | -
Tilt about Z (mrad) | 0.1 | 0.2 | -
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
D. H. Ji
dipole | quadrupole
B1/B0  210-4 | 
B2/B0  510-4 | B2/B1  310-4
B3/B0  210-5 | B3/B1  210-4
B4/B0  810-5 | B4/B1  110-4
B5/B0  210-5 | B5/B1  110-4
B6/B0  810-5 | B6/B1  510-5
B7/B0  210-5 | B7/B1  510-5
B8/B0  810-5 | B8/B1  510-5
B9/B0  210-5 | B9/B1  510-5
B10/B0  810-5 | B10/B1  510-5
Include multipole errors
(100 seeds)
(93 seeds)
DA track in AT w/o SR

## Slide 12
DA@30GeV
Tracking by SAD (1500 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
On axis injection from Linac to booster
BSC definition (inj=6.5nm):
Energy acceptance: 3*inj =0.45%
Dou Wang, Daheng Ji

## Slide 13
DA@45GeV
Tracking by SAD (1200 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
Off axis injection from booster to collider
BSC definition (x=0.18nm, y=x *1%):
Energy acceptance: 4* =0.15%
Dou Wang, Daheng Ji

## Slide 14
DA@80GeV
Tracking by SAD (500 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
Off axis injection from booster to collider
BSC definition (x=0.56nm, y=x *1%):
Energy acceptance: 4* =0.27%
Dou Wang, Daheng Ji

## Slide 15
DA@120GeV
Tracking by SAD (250 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (without taper)
Include SR damping & fluctuation
On axis injection from booster to collider
BSC definition (x=1.26nm, y=x *1%):
Energy acceptance: 5* =0.5%
Dou Wang, Daheng Ji

## Slide 16
DA@180GeV
Tracking by SAD (150 turns)
include errors (w. multipole errors)
Include SR sawtooth orbit (with taper)
Include SR damping & fluctuation
Keep possibility for on axis injection to collider
BSC definition (x=2.84nm, y=x *1%):
Energy acceptance: 4* =0.59%
--
--
Dou Wang, Daheng Ji

## Slide 17: Booster ramping scheme
3 cycles/beam
tt
Higgs
W
Z
1 cycles/beam
1 cycles/beam
1 cycles/beam
7.1s
7.1s
0.35s
4.3s
4.3s
2.7s
12.97s
2.4s
2.4s
19.9s
19.9s
19.9s
4.3s
4.3s
2.7s
4.7s damping
off-axis
on-axis
0.035s
0.27s
1.3s
0.05s
0.35s+7.1s+0.035s+7.1s=14.6s
2.7s+4.3s+4.7s+4.3s=16.0s
12.97s+2.4s+1.3s+2.4s=19.1s
(19.9s+1.0s+0.05s+1.0s)*3=65.9s
Dou Wang, Xiaohao Cui
1.0s
1.0s
1.0s
1.0s

## Slide 18: On-axis injection at Higgs energy
Swap-out injection
Current threshold in booster: 1A
Current decay for collider: 3% (top up mode)
4 damping times to merge the bunches in booster

## Slide 19: On-axis injection at Higgs energy (50MW upgrade)
Swap-out injection
Current threshold in booster: 1.4 A
Current decay for collider: 3% (top up mode)
Small upgrade for the RF power source

## Slide 20: Beam beam instability for on-axis injection
Collision stability check for on-axis injection scheme at 120GeV
• Emittance X = 1.26nm
• Energy spread = 0.1%
• Bunch length=1.85mm
• Coupling=1.0%
• Emittance X = 0.64nm
• Energy spread = 0.1%
• Bunch length=2.25mm
• Coupling=0.2%
e- (Ne=14×1010)
e+ (Ne=14×1010)
Yuan Zhang

## Slide 21: Injection scheme at Z pole
Booster threshold: 16mA
Bootstrapping from 220mA
Injection speed of Linac: double bunch@100Hz
Top-up injection
Full injection
Train num. @ booster = train num.@collider / 2
0.8h
Current drop: 3.0% (804mA in collider)
Booster current = 9mA
Train num. @ booster = train num.@collider / 3
Injection speed of Linac: double bunch@100Hz

## Slide 22
emittance
Beam parameter evolution
Injection emittance: 6.5nm @30GeV
Beam parameters reach balance after 45GeV.
energy
energy spread
bunch length
emit_x
emit_y

## Slide 23: Eddy current effect
Max K2=0.000029 (m-3)
Dedicated ramping curve to control the maximum K2.
K2 reaches max at 45GeV.
Dynamic chromaticity is not corrected.
- Sextupole field is attached to dipole
Al beam pipe (round shape)
- inner diameter: 55mm, thickness: 2mm
Analytical estimation for eddy effect*
*Yuan Chen et al., Analytical expression development for eddy ﬁeld and the beam dynamics eﬀect on the CEPC booster, IJMPA, Vol. 36, No. 22 (2021) 2142010
30 GeV injection weaken the eddy effect
Dou Wang, Yuemei Peng, Daheng Ji
Independent sext. (~100) — chromaticity adjustment

## Slide 24: RF ramping curve
Different RF ramping curve for each energy mode (constant s )
Max RF voltage @tt determined by longitudinal quantum lifetime & DA.
s for tt: 0.14
s for Higgs: 0.094
s for W & Z: 0.088
RF: ~ 12 
VRF (180GeV)=9.8GV
W &Z
Higgs
tt

## Slide 25: Longitudinal acceptance
180GeV
120GeV
30GeV
3 times of sigma for the longitudinal beam size

## Slide 26
Lattice | FODO 0 （CDR） | FODO 1 | TME (combine magnets)
Emittance X (nm) @120GeV | 3.57 | 1.29 | 1.26
Momentum compaction (×10-5) | 2.44 | 1.18 | 1.12
Tunes | [263.201/261.219] | [353.180/353.280] | [321.271/117.193]
Quad amount | 2110 | 2816 | 3458
Quad Strength (K1L rms） | 0.0383 | 0.0407 | 0.0259
Sext amount | 512 | 896 | 96
Sexts Strength (K2L rms) | 0.179 | 0.4091 | 0.0492
H Corrector | 1053 | 1408 | 1218
V Corrector | 1054 | 1408 | 2240
BPM | 2108 | 2816 | 3458
Power consumption of magnets@120GeV (MW) (max/average) | 15/6 |  | 12.1/4.8
Optics parameter comparison
Magnets’ cost of TME is lower than FODO 1
Less independent sextupole for TME
Quadrupole strength of TME is lower
D. H. Ji, W. Kang
TME is less sensitive to error effects
Weaker quad/sex strength
TME has lower magnets’ power consumption

## Slide 27: Booster TDR parameters
Injection
Extraction
*Diameter of beam pipe is 55mm for re-injection with high single bunch current @120GeV.
Injection energy: 10GeV  20GeV  30GeV
Max energy: 120GeV  180GeV
Lower emittance ─ new lattice (TME)

## Slide 28: Damping ring layout (CDR)
Linac repetition: 100Hz
Only for positron beam
Storage time: 20 ms
Emittance (norm.): 2500 530 mm.mrad
e +

## Slide 29: Comparison of damping ring design requirement
 | CDR | TDR | remark
Energy (GeV) | 1.1 | 1.1 | 
Inj. Emittance (mmmrad) | 2500 | 2500 | 
Ext. emittance (mmmrad) | 530 | <200 | 1) Linac lower emittance: 10nm@20GeV, 2)use C band acc. structure as early as possible
Storage time (ms) | 20 | 20 | 
Damping time (ms) | 15 | <13 | 1) Smaller ext. emittance with same storage time
Circumference (m) | 75 | ~150 | 1) Smaller nature emittance for DR
lower emittance collider  lower emittance booster  lower emittance linac

## Slide 30: DR parameters
 | DR V3.0
Energy (Gev) | 1.1
Circumference (m) | 147
Number of trains | 2 (4)
Number of bunches/trian | 2
Total current (mA) | 12.4 (24.8)
Bending radius (m) | 2.87
Dipole strength B0 (T) | 1.28
U0 (kev/turn) | 94.6
Damping time x/y/z (ms) | 11.4/11.4/5.7
Phase/cell (degree) | 60/60
Momentum compaction | 0.013
Storage time (ms) | 20 (40)
0 (%) | 0.056
0 (mm.mrad) | 94.4
injection z (mm) | 4.4
Extract z (mm) | 4.4
inj (mm.mrad) | 2500
ext x/y (mm.mrad) | 166(97)/75(3)
inj /ext (%) | 0.18 /0.056
Energy acceptance by RF(%) | 1.8
fRF (MHz) | 650
VRF (MV) | 2.5
Longitudinal tune | 0.0387
Damping with reversed bending magnet
4 (max. 8)-bunch storage, storage time:20 (40) ms
Emittance: 2500 166/75 (97/3) mm.mrad
Flexibility for extr. emittance

## Slide 31: DR time structure
Double bunch (Inj./Ext.: two by two)  at Z pole
tt/Higgs/W: 100Hz (Inj./Ext.: bunch by bunch)
Xiaohao Cui, Cai Meng, Gang Li, Ge Lei, Jinhui Chen…

## Slide 32
Phase/cell: 60/60
Interleave sextupole scheme
2 sex. families
DR optics
Arc
Straight
B=1.28T
Cell length: 3m
B=1.28T
r /0=0.355
-r
0

## Slide 33
DR DA results
Phase/cell: 60/60
Large trans. acceptance inj. efficiency
DA > 5 inj. beam size (inj=2500mm.mrad)
Energy acceptance =1.8% (RF)

## Slide 34
Transverse Mode Coupling Instability
The threshold for the TMCI is estimated by following analytical formula
Here,νs is he synchtron tune, βy is the,betraon function and κy is the transvers kicker factor which is decided by impedance and bunch length.
parameters | Phase/cell: 60/60
Energy | 1.1Gev
circumference | 147
Beta tune | 7.70/ 8.54
Bunch length | 4.4mm
Bunch number | 4 （2 train）
synchtron tune | 0.0387
Bunch current (mA) | 3.1
Bunch current threshold(mA) | 9.4
Yudong Liu
* Circular Al pipe with 30mm inner diameter

## Slide 35: Transport lines between DR and Linac
LinacDR | EC
E0 (Gev) | 1.1
0 (%) | 0.5
z0 (mm) | 1.5
fRF (MHz) | 2860
VRF (MV) | 16.5
Length of acc. Structure (m) | 1.0
RF (degree) | 87
R56 (m) | -0.83
Ef (Gev) | 1.1
f (%) | 0.18
zf (mm) | 4.4
DRLinac | BC
E0 (Gev) | 1.1
0 (%) | 0.056
z0 (mm) | 4.4
fRF (MHz) | 2860
VRF (MV) | 20.6
Length of acc. Structure (m) | 0.76
RF (degree) | 89.7
R56 (m) | -0.89
Ef (Gev) | 1.1
f (%) | 0.55
zf (mm) | 0.5
Dou Wang, Xiaohao Cui

## Slide 36
We optimized the RF voltage of EC based on the particle tracking with realistic distributions of particles from the target.
The injected energy spread at the entrance of DR is 0.185% (RMS).
RF acceptance of DR is enlarged by a higher RF voltage (1.8%).
Optimization of the EC design

## Slide 37: Particle tracking from Linac to DR (before ECS)
Track by SAD (real distribution)
Inj emittance: ~2500mm.mrad
0 :~1.5mm (RMS)
0 :~0.4% (RMS)

## Slide 38: Particle tracking from Linac to DR (after ECS)
Track by SAD (real distribution)
Transporting efficiency: 95%
f :~ 4 mm (RMS)
f :~0.18% (RMS)

## Slide 39: Primary design for the polarized damping ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.1 | 
Circumference (m) | 145 | 
Number of trains | 4 | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Bending radius (m) | 3.44 | 
Dipole strength B0 (T) | 1.07 | 
Wiggler strength B+ (T) | 1.8 | 
Wiggler cell length (m) | 1.5 | 
U0 (kev/turn) | 88.0 | 
Damping time x/y/z (ms) | 12.2/12.2/6.1 | 
Momentum compaction | 0.015 | 
Storage time | 20 ms | 10 min
0 (%) | 0.05 | 
0 (mm.mrad) | 45 | 
injection z (mm) | 6 | 
Extract z (mm) | 5.7 | 5.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 106/63 | 45/2
inj /ext (%) | 0.18 /0.05 | 
RF acceptance (%) | 1.8 | 
fRF (MHz) | 650 | 
VRF (MV) | 2.5 | 
Longitudinal tune | 0.032 | 
Produce polarized positron beam for the purpose of energy calibration @ Z & W*.
Compatible with standard top up operation
10 min storage  ~20% polarization
Asymmetric wigglers
B+=1.8T=5 B-
cell length=1.5m
* detail in Zhe Duan’ talk on this workshop
16 wigglers
Wiedemann, Particle Accelerator Physics, 4 Edition
Z. Duan, D. Wang

## Slide 40: Summary
Update booster design with smaller emittance in TDR─ support for CEPC high lum. scheme
TME structure with combined magnets (B+S)
DA with error effects fulfill the requirements
Booster parameters update ─ consistent with CEPC TDR parameters at 4 energy
Booster energy range is modified in TDR. (10GeV/120GeV  30GeV/180GeV)
Damping ring update is the requirement of higher luminosity goal for TDR.
Circumference: ~150m, energy: 1.1GeV
Reversed bending, extracted emittance=97~166 mmmrad (adjustable)
Damping time: 15ms (CDR)  11ms (new)
Polarized positron damping ring is under design.

## Slide 41
Thanks for your attention!

## Slide 42: Back up

## Slide 43: Booster power consumption @Higgs
The technical systems with changes are considered.
The power consumption of TDR is lower than CDR with much lower emittance.
Technical system | CDR [MW] |  | TDR [MW] |  | Budget increment [MW] | 
 | max | average | max | average | max | average
Magnet system | 15 | 6 | 12.1 | 4.8 | -2.9 | -1.2
Power supply | 10.04 | 4.02 | 6.62 | 2.65 | -3.42 | -1.37
RF system |  |  |  |  |  | 
RF power source | 3.95 | 0.15 | 4.45 | 1.44 | 0.5 | 1.29
Beam Instrumentation | 0.6 | 0.6 | 0.72 | 0.72 | 0.12 | 0.12
… |  |  |  |  |  | 
total |  | 20.97 |  | 19.81 | -5.7 | -1.16

## Slide 44: Booster power consumption @Z
The technical systems with changes are considered.
The power consumption of TDR almost same as CDR with much lower emittance.
Technical system | CDR [MW] |  | TDR [MW] |  | Budget increment [MW] | 
 | max | average | max | average | max | average
Magnet system | 2.14 | 1.28 | 1.72 | 0.69 | -0.42 | -0.59
Power supply | 2.48 | 0.99 | 1.88 | 0.75 | -0.6 | -0.24
RF system |  |  |  |  |  | 
RF power source | 0.5 | 0.04 | 1.13 | 0.084 | 0.63 | 0.044
Beam Instrumentation | 0.6 | 0.6 | 0.72 | 0.72 | 0.12 | 0.12
… |  |  |  |  |  | 
total |  | 9.7 |  | 9.034 | -0.27 | -0.666