## Slide 1
Rui Ge, Mei Li
On behalf of the CEPC cryogenic group
25th，Oct. 2022
CEPC Cryogenic System Design and R&D
The 2022 International Workshop on the High Energy Circular Electron Positron Collider
Notes: 1

## Slide 2
OUTLINE
Introduction
CEPC SRF cryogenic system
CEPC SC magnets cryogenic system
Key technology
  2K JT heat exchanger R&D and test
Summary
Notes: Well, The contents mainly include 4 parts, the first one is a brief introduction, then CEPC SRF cryogenic system; the third wone is CEPC SC magnets cryogenic system , and then talk about 2K JT heat exchanger R&D and test, lastly a short summary.

## Slide 3
CEPC Cryogenic System Brief Introduction
  Booster ring:
1.3 GHz 9-cell cavities, 96 cavities
12 cryomodules
3 cryomodules/each station
Temperature: 2K
  Collider ring:
650MHz 2-cell cavities, 240 cavities
40 cryomodules
10 cryomodules/each station
Temperature: 2K
  IR magnets:
4 IR magnets (4.5K), 32 Sextuple magnets (normal conducting)
4 cryostats
Temperature: 4.5K
Detectors:
2 detector magnets
Thermosiphon cooling
Layout of CEPC Double Ring
Inj(LSS8)
RF Cryo-station
Inj(LSS2)
Estr(LSS6)
RF Cryo-station
Ip_cc(LSS5)
Ip_cc(LSS1)
RF Station(LSS7)
RF Station(LSS3)
Estr(LSS4)
SC magnets Cryo-station
SC magnets Cryo-station
Notes: For the SRF side, there are four cryo-stations with the capacity of 15kW@4.5K for each. The working temperature is 2K. For the Booster ring, there are 12 cryomodules for 1.3GHz 9-cell cavities. And for the collider ring, there are 56 cryomodules for 650MHz 2-cell cavities.
For the IR SC magnets side, there are total 4 IR SC magnets working 4K in the MDI, and 32 sextupole magnets working in the room temperature. Besides, the detectors adopt thermosiphon cooling method.

## Slide 4
11000
11000
11000
5000
5000
Compressor group
Cold Box
Main Distribution
Valve Box
Dewar
11000
8000
5000
5000
6
Cryomodules
11000
11000
11000
117000
24000
2K valve boxes
10 cryomodules, 6×650MHZ 2-cell cavities each
Collider Ring
3 cryomodules, 8×1.3GHZ 9-cell cavities each
Booster Ring
gallery-tunnel
80000
Higgs 50MW
beam-tunnel
CEPC SRF cryogenic flow chart in CDR
Notes: In the previous conceptional design report (CDR), the cooling scheme is parallel for the SRF cryomodules. Each cryomodule has a separated valve box in the gallery tunnel.

## Slide 5
CEPC SRF cryogenic flow chart in TDR
3 cryomodules, 8×1.3GHZ 9-cell cavities each
Booster Ring
10 cryomodules, 6×650MHZ 2-cell cavities each
Collider Ring
11000
11000
11000
5000
5000
Compressor group
Cold Box
Main Distribution
Valve Box
Dewar
11000
8000
5000
5000
6
Cryomodules
11000
11000
11000
117000
24000
2K valve boxes
2K valve boxes
Higgs 50MW
Notes: In the previous conceptional design rate, the cooling scheme is parallel for the SRF cryomodules. That means each cryomodule has a separated valve box in the gallery tunnel. And the length of main TL is about 350meters. 4 Station means more than 2km. It’s very long.
Later, to improve the cavity performances and reduce the cost, the cooling scheme of both booster and collider cryomodules has been modified, from parallel to series. In this way, there will not have a lot number of small valve boxes in the tunnel, and we just use two big valve box to replace them. Besides,
the length of the TL is much reduced, and the process scheme looks more easier. Most importantly, much expenses and space will be saved.

## Slide 6: Estimated heat loads for SRF TDR Scheme
Higgs Mode 50MW | Unit | Collider |  |  | Booster |  | 
 |  | 40-80K | 5-8K | 2K | 40-80K | 5-8K | 2K
Predicted static heat load per cryomodule | W | 300 | 60 | 12 | 140 | 20 | 3
Cavity dynamic heat load per cryomodule | W | 300 | 60 | 118.2 | 0 | 0 | 44.8
HOM dynamic heat load per cryomodule | W | 20 | 12 | 2 | 20 | 6 | 1
Input coupler dynamic heat load per cryomodule | W | 60 | 40 | 6 | 40 | 3 | 0.4
Module dynamic heat load | W | 380 | 112 | 126.2 | 60 | 9 | 46.2
Each Module total heat load | W | 680 | 172 | 138.2 | 200 | 29 | 49.2
Cryomodule number | - | 40 | 40 | 40 | 12 | 12 | 12
EVB heat loss | W | 50 | 10 | 10 | 50 | 10 | 10
EVB number | - | 40 | 40 | 40 | 12 | 12 | 12
MDVB heat loss | W | 50 | 30 | 30 | 50 | 30 | 5
MDVB number | - | 4 | 4 | 4 | 4 | 4 | 4
Total cryogenic transfer line length | m | 1000 | 1000 | 1000 | 300 | 300 | 300
cryogenic transfer line heat loss per meter | W/m | 2 | 0.5 | 0.3 | 2 | 0.5 | 0.3
Total cryogenic transfer line heat loss | W | 2000 | 500 | 300 | 600 | 150 | 90
Total heat load | kW | 31.4 | 7.9 | 6.348 | 3.8 | 0.738 | 0.8204
Total predicted mass flow | g/s | 82.42 | 152.26 | 373.72 | 13.34 | 12.73 | 18.324
Overall net cryogenic capacity multiplier |  | 1.54 | 1.54 | 1.54 | 1.54 | 1.54 | 1.54
4.5K equiv. heat load with multiplier | kW | 3.63 | 11.01 | 31.29 | 0.44 | 1.03 | 4.05
4.5K equiv. heat load with multiplier | kW | 45.93 |  |  | 5.52 |  | 
Total 4.5K equiv. heat load with multiplier | kW | 51.45 |  |  |  |  | 
Four individual refrigerators (4 × 15kW@4.5K) will be employed for the CEPC cavity cryogenic system.
Notes: In the Higgs 50MW mode, the estimated heat loads at 4K is about 15kW@4.5K for each cryo-station. And four individual refrigerators will be employed.

## Slide 7
PAPS cryogenic system for RF cavity R&D
For the further improving the R&D status for SRF cryomodules, a test facility called PAPS has been successfully built, and passed the commissioning test last year. The cooling capacity is 300W@2K.
Notes: For the further improving the R&D status for SRF cryomodules, a cryogenic facility called PAPS has been successfully built, and it passed the commissioning test last year. The heat load at 2K is about 300W. This is the PFD of PAPS cryogenic system. This is refrigerator, main distribution valve box, and 6~7 test stands. The 2K production scheme adopts the combination of room temperature pumps and electrical heater.

## Slide 8
SRF building
Cryogenic building
Magnet building
Beam test building
X-ray building
Platform of advanced research facility
--Platform of Advanced Photon Source, PAPS

## Slide 9
cryogenic hall
PAPS cryogenic system for RF cavity R&D
RF hall
VT stands
Tanks zone
HT test stand
Beam test stand
Notes: There are some photos, respectively are the cryogenic hall, RF hall, tanks zone. The PAPS cryogenic system has three vertical test stands, two horizontal test stands, and a beam test stand,

## Slide 10
Cryomodule for 1.3GHz 9-cell cavities
XFEL / LCLS-II type Cryomodule for High Q Cavity
Design Goals:
Low heat loss
Fast cool down
Cryogenic Group in IHEP has manufactured 58 1.3GHz 9-cell Cryomodules for EXFEL cooperated with local companies.
It’s a good foundation for the optimization design for the CEPC cryomodules.
Notes: For the 1.3GHz cryomodules, we have manufactured 58 1.3GHz 9-cell Cryomodules for EXFEL cooperated with local companies, which lays a good foundation for the design.

## Slide 11
1.3GHz 9-cell cryomodule test in PAPS
Endcap
Cryomodule
Feedcap
2K valve box
2K valve box
2K horizontal test will be done in PAPS in the end of 2022.
Notes: These pictures are the mechanical 3D diagram of the cryomodule, this is 2K valve box, this feed cap, cryomodule, endcap. And a flat trolley will be used for easy loading and unloading for the cavities.

## Slide 12
Cryomodule for 1.3GHz 9-cell cavities
Assembly has been started in October.
So far, all of the key parts of the 1.3GHz Cryomodule have been almost finished.
Hope the end of the year the Cryomodule will be installed, and do the test.

## Slide 14
Including six 2-cell 650 MHz superconducting cavities, six high power couplers, six mechanical tuners and two HOM absorbers
Cryomodule performance |  | Specification
Number of leakage | He →insulation | 0
 | He →beam transfer line | 0
 | Insulation →coupler | 0
 | Insulation →beam transfer line | 0
 | Coupler →beam transfer line | 0
Alignment x/y inside (Cavities) |  | ±0.5mm
Alignment z inside |  | within 2 mm
Coupler antenna design z |  | within 2 mm
Six 2-cell Cavities Cryomodule | 
Overall length(flange to flange, m) | 8.0
Diameter of Vacuum vessel ,m | 1.3
Beamline height from floor, m | 1.5
Cryo-system working temperature, K | 2
Number of 200-POST | 6
Cryomodule for 650MHz 2-cell cavities
Notes: This diagram shows the cross diagram and parameters of the 650MHz 2-cell cavities cryomodule. Including six 2-cell cavities, high power couplers, mechanical tuners and Higher-Order-Mode (HOM) Absorbers.

## Slide 15
Cryomodule for 650MHz 2-cell cavities
The prototype cryomodule with two 2-cell 650 MHz superconducting cavities was operated in the PAPS system beam test stand last year.
Notes: A beam test cryomodule with two 2-cell 650 MHz superconducting cavities was operated in the PAPS system beam test stand last year.

## Slide 16
BTCM cooldown
BTCM: 100.7W@2K
Level
Pressure
Temperature
Mass flow
BTCM 2K stable operation
Pressure 31mbar±10Pa
Temperature 2K±0.02K
Cooling capacity test 300W@2K
Operation test for 650MHz 2-cell cavities
Notes: These pictures show the testing results, including cooldown curve and 2K stable operation.

## Slide 17
Advanced control strategy research status
We are now conducting the Advanced control strategy research, first of all, we have successfully designed and implemented automatic cool-down/warming-up procedure for SRF cavity cryomodule with Model Predict Control (MPC) method & Artificial Neural Network (ANN)
Module automatic cooldown research progress: the MPC control method has successfully tested in PAPS BTCM, It is verified that the MPC method has better control stability.
The foundation for a more intelligent automated control of future CEPC large cryogenic systems has been laid.
Team：Zhengze Chang、Mei Li、Keyu Zhu
300 to 150 K: < 10 K/hr. Cavity top and bottom ΔT < 20 K 150 to 4.5 K: rate > 2.4 K/min, fast cooldown
4.5 to 2 K
~34h
~24h
Former method:
Manual adjustment
Not stable
Improved method:
MPC; ANN
Stable
Fast cooldown
Efficiency increase a lot
Notes: In the former cooldown method, it relies on the human manual adjustment for the mixed temperature valves. It is not so stable, sometimes quick, sometime slow. Later, we conducted the advanced control strategy research, and we design and implemented automatic cool-down/warming-up procedure for SRF cavity cryomodule with Model Predict Control (MPC) method & Artificial Neural Network (ANN). As you can see, after using this automatic cooldown procedure, the cooldown curve is stable. Furthermore, it’s very safe, because the inlet pressure will be guarded all the time, and it was controlled less than the quench safety pressure.
And the foundation for a more intelligent automated control of future CEPC large cryogenic systems has been laid.

## Slide 18
OUTLINE
Introduction
CEPC SRF cryogenic system
CEPC SC magnets cryogenic system
Key technology
  2K JT heat exchanger R&D and test
Summary
Notes: Well, The contents mainly include 4 parts, the first one is a brief introduction, then CEPC SRF cryogenic system; the third wone is CEPC SC magnets cryogenic system , and then talk about 2K JT heat exchanger R&D and test, lastly a short summary.

## Slide 19
CEPC MDI SC Magnet Cryostat flow chart
Compressor
Cold box
Dewar
Main Distribution Valve Box
Helium circulating system 1
Helium circulating system 2
Cryostat 1
Cryostat 2
IP collision point
IR sextupoles have been changed from SC magnets to normal conducting ones and cryogenic system for sextupoles can be eliminated.
The requirement for IR sextupole magnets is updated.
The magnet bore and pole field is reduced.
Conventional sextupole magnet technology can be used (FeCoV pole). Max strength 3886T/m2 is achieved with bore aperture 42 mm. Max current < 200A.

## Slide 20: Estimated heat loads for SC IR magnets-updated
 |  | 4.5K main loop |  |  | Thermal Shielding 40~80K | 
Name | Unit | No. | Heat load for each | Heat load | Heat load for each | Heat load
IR SC sextupole magnet | W | 32 | 10 | 320 | 68 | 2176
Valve Box of IR SC sextupole magnet | W | 32 | 20 | 640 | 20 | 640
Current lead of IR SC sextupole magnet | g/s | 32 | 0.1 | 3.2 | 0.1 | 3.2
IR SC magnet | W | 4 | 30 | 120 | 180 | 720
Valve Box of IR SC magnet | W | 4 | 30 | 120 | 30 | 120
Current lead of IR SC magnet | g/s | 4 | 0.5 | 2 | 0.5 | 2
Main distribution valve box | W | 4 | 50 | 100 | 50 | 200
Cryogenic transfer-line | W | 4000 | 0.3 | 1200 | 2 | 8000
Total equiv. heat load @4.5K | W | 14356 |  |  |  | 
Total equiv. heat load @4.5K | W | 14356W+10.4g/s |  |  |  | 
Total equiv. heat load @4.5K | W | 14478 |  |  |  | 
Total equiv. heat load @4.5K with multiplier 1.5 | W | 21717 |  |  |  | 
Cooling capacity of refrigerator@4.5K | W | 2 | 12kW@4.5K | 24kW@4.5K |  | 
Installed power (COP 300W/1W) | MW |  |  |  |  | 
 |  | 4.5K main loop |  |  | Thermal Shielding 40~80K |  | 
Name | Unit | No. | Heat load for each | Heat load | No. | Heat load for each | Heat load
IR SC magnet | W | 4 | 30 | 120 |  |  | 
Valve Box of IR SC magnet | W | 4 | 30 | 120 |  |  | 
Current lead of IR SC magnet | g/s | 4 | 0.8 | 3.2 |  |  | 
Main distribution valve box | W | 4 | 50 | 100 |  |  | 
Cryogenic transfer-line | W | 100 | 0.3 | 30 | 100 | 1.5 | 150
Total heat load @4.5K | W |  |  | 370 |  |  | 150
Total heat load @4.5K including current lead | W |  |  | 370W+3.2g/s |  |  | 150
Total heat load @4.5K | W |  |  | 432 |  |  | 150
Coefficient |  |  |  | 1 |  |  | 0.05
Total heat load @4.5K | W |  |  | 432 |  |  | 7.5
Total equiv. heat load @4.5K | W | 439 |  |  |  |  | 
Total equiv. heat load @4.5K with multiplier 1.5 | W | 659 |  |  |  |  | 
Notes: This sheet gives the estimated heat loads for the SC magnets side. And Two individual refrigerators with the capacity of 4kW@4.5K will be employed.

## Slide 21
Refrigerator selection | 
Liquefaction | 430L/h
Refrigeration | 2×1.5kW@4.5K
Liquefaction/Refrigeration | 1kW@4.5K & 150L/h
Zhu Zian，Wang Meifen
Heat loads and layout for detector magnet
layout for detector magnet
Therefore, two individual refrigerators
(2 x 2/2.5kW@4.5K) will be employed for the CEPC SC magnets cryogenic system (including IR SC magnets and detector).
Notes: This slide shows the heat loads, layout of the detector. And two individual refrigerators (2 x 1.5kW@4.5K) will be employed.

## Slide 22
The total weight of cryostat is about 2.5 T, length 6.7m.
Mechanical design, stress analysis and thermal simulation have been finished.
Find funds for manufacturing.
CEPC MDI Cryostat
Notes: And according to the mechanical design, the total weight of cryostat is about 2.5 Tones.

## Slide 23
OUTLINE
Introduction and Layout
CEPC SRF cryogenic system
CEPC SC magnets cryogenic system
Key technology
  2K JT heat exchanger R&D and test
Summary
Notes: Next, I will introduce the key technologies, mainly the 2K JT HX.

## Slide 24
2K JT heat exchanger R&D and test
In larger flow rate condition, Plate Fin Heat Exchanger (PFHE) has many advantages, such as relative impact sizes, high heat transfer coefficient, and low pressure drop.
2K heat exchangers of large flow rate need to be designed and developed for the 4 sets of 2-3kW cryogenic system of CEPC, so their design flow rate would be about 100-120g/s.
But the design calculation and the manufacture are more difficult than the traditional Coiled Finned-Tube HX (CFHX).
Coil Finned Tube HX
(≤10g/s)
Plant-Fin HX
(≥5g/s)
2K JT Heat Exchanger Flowchart

## Slide 25
2K JT heat exchanger R&D and test
Special difficulties in the development of large flow PFHE
Flow distribution problem in large flow heat exchanger.
Build accurate and efficient numerical models for different fin structures.
Multi-objective optimization problem considering pressure drop, heat exchange efficiency and volume.
Using the similarity principle to complete high precision and high reliability test.
Similarity Principle
The actual working conditions of 50-120g/s flow can not be obtained(25-30g/s now).
In order to ensure the validity of the test, the key dimensionless parameters in the flow and heat transfer processes need to be the same.
Including:
Re= Nu= Gr= …….
The existing test conditions of PAPS can ensure that the boundary conditions, physical principle and dimensionless parameters are the same except for different flow rates, so the validity of the test results can be guaranteed.

## Slide 26
2K JT heat exchanger R&D and test
Previous works (-2022.01)
Design, optimization and test of 5g/s and 10g/s HX
5g/s CFHE
10g/s CFHE
10g/s PFHE
CFD simulation for PFHE

## Slide 27
2K JT heat exchanger R&D and test
Previous works (-2022.01)
Test Flowchart
(≤10g/s)
Test Platform
Test result of 10g/s double layer CFHE

## Slide 28
2K JT heat exchanger R&D and test
Process design of the new test platform based on PAPS 2K system
(≤30g/s)
Design, optimization and test of 25g/s and 50g/s PFHE
Recent works (2022.01-2022.09)

## Slide 29
2K JT heat exchanger R&D and test
Result of the first round of design and optimization
Optimal design of 50g/s PFHE
 | Fin type |  | Total length/mm | Total width/mm | Total thickness/mm | effectiveness | Low pressure side ΔP/Pa
1 | High pressure side | Serrated | 1240 | 375 | 240 | 88.91% | 103.49
 | Low pressure side | Wavy |  |  |  |  | 
2 | High pressure side | Serrated | 1020 | 375 | 240 | 88.88% | 167.00
 | Low pressure side | Serrated |  |  |  |  | 
Optimal design of 25g/s PFHE
 | Fin type |  | Total length/mm | Total width/mm | Total thickness/mm | effectiveness | Low pressure side ΔP/Pa
1 | High pressure side | Serrated | 1280 | 525 | 80 | 91.47% | 81.50
 | Low pressure side | Serrated |  |  |  |  | 
2 | High pressure side | Serrated | 1130 | 270 | 180 | 88.68% | 63.06
 | Low pressure side | Perforated |  |  |  |  | 
The design and calculation of the PFHE nearly finished, manufacturing will be started from next month.

## Slide 30
Summary
Previous CDR and TDR works have laid a good foundation for the further design.
For the CEPC cryogenic system TDR design, relevant aspects have been considered , including process scheme, layout, and key equipment design.
We still need to work together to greatly push forward the work, and complete the TDR design on time.
Notes: Lastly, a short summary.

## Slide 31
Thanks for Your Attention！