## Slide 1: CEPC Injection/extraction system studies
Jinhui Chen, Guanjian Wu, Zilin Chen, Xinzhe Zhai, Guanwen Wang,
Lei Wang，Lihua Huo , Yuwen Wu, Hua Shi
Injection group
2022-10-25
The 2022 international workshop on the high energy Circular Electron-Positron Collider
Oct.24-28,2022, Online

## Slide 2: Outline
1
Overview of CEPC Inj./Ext. systems
2
Lambertson magnets
3
Slotted-pipe kicker system
4
Ferrite core kicker magnet
5
Summary

## Slide 3
Overview of the CEPC injection and extraction systems

## Slide 4: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
In CEPC accelerator complex, there are 9 injection and extraction sub-systems, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 5: Main types of inj. & ext. hardware
 | Sub-system | Kicker |  | Septa | 
 |  | Kicker Type | Kicker waveform | Septa Type | Stored beam pipe aperture /Thickness of septum
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine or trapezoid/250ns | Horizontal in air LMS | ф22/3.5mm
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal in air LMS | ф55/5.5mm
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical in air LMS | Ф55/6mm
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical in vacuum LMS | Ф75x56/2mm
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical in air LMS | Ф55/6mm
6 | Booster HE inj. for CR on-axis inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical in air LMS | Ф55/6mm
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical in air LMS | Ф75x56/6mm
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical in air LMS | Ф75x56/6mm
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical in air LMS | Ф75x56/6mm

## Slide 6: Hardware R&D plans
One team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping. HEPS project started on 29th June, 2019. Some hardware prototypes are completed and some are in final assembling progress. These hardware R&D experiences should be shared for CEPC.
Hardware R&D activities:
  Lambertson septa magnets
    Outside vacuum magnet: Septum thickness ≥3.5 mm
    Half in vacuum magnet: Septum thickness =2 mm
  Kicker systems
    Strip-line kicker and super fast pulser（PW=10~50ns）
    Slotted-pipe kicker and fast pulser（PW=250~300ns）
    Ferrite core kicker （in-air with metallic coated ceramic vacuum chamber) and pusler
      Lumped parameter dipole kicker（PW=1.36us half-sine）
      Distributed parameter (delay-line) dipole kicker（ PW=440~2420ns trapezoid）
      Distributed parameter (delay-line) Nonlinear kicker（ PW=440~2420ns trapezoid）
Overlapping part

## Slide 7
Lambertson magnet

## Slide 8: Typical requirements for CEPC LSM
Parameters | Unit | DR-LSM | BST-LEI-LSM | CR-LSM-2
Quantity | - | 2 | 2 | 2×5
Energy | GeV | 1.1 | 10 | 120
Deflection angle | mrad | 120 | 22 | 0.35
Insertion length | m | 0.5 | 0.8 | 1.75
Magnetic field strength for injected/extracted beam | T | 0.883 | 0.9175 | 0.08
Min. Septum thickness（including septum board, wall of beam pipes, installation gap) | mm | 3.5 | 5.5 | 2
Field uniformity | - | <±0.05% | <±0.02% | <±0.05%
Leakage field | - | ≤1×10-3 | ≤1×10-3 | ≤1×10-3
Clearance of stored beam at lambertson（HV） （refer to stored beam orbit） | mm | 36.422 | 3050 | -
Clearance of inj.&ext. beam at lambertson（HV）（refer to inj.&ext. beam orbit） | mm | 2211 | 1829 | -
Physical aperture of stored beam vacuum chamber | mm | 2222 | 5555 | 75x56
In-air
Half in vacuum

## Slide 9: Lambertson Magnet Design Considerations
In order to decrease the septum thickness, 2 novel structures of magnet were proposed:
  half-in-vacuum (for 2mm septum)
  embedded thin-wall vacuum chamber (for 3.5mm septum)
Injected bunch
Stored bunch
Magnet pole
Installation margin
Yoke
Injected bunch
Magnet pole
Installation margin
Yoke
Stored bunch
Injected bunch
Magnet pole
Installation margin
Installation margin
Yoke
Stored bunch
SS
Iron or
VP(FeCoV，1J22)
Traditional LSM
SS
Half in-vacuum
in-air
Septum
thickness
Wall of stored beam pipe
+
Wall of injected beam pipe
+
Iron septum
+
installation margins
=

## Slide 10: Lambertson Magnet Design Considerations
In order to decrease the absolute values of leakage field with thinner septum, Vanadium Permendur (FeCoV： iron50% cobalt 48% vanadium 2%, domestic brand 1J22 ） is adopted for septum board.
    Higher Bs (Saturation magnetic density)
    Higher μr(Relative permeability)

## Slide 11: Lambertson Magnet Design Considerations
In order to decrease the integrate leakage field, the upstream end of the stored beam chamber is located under the side leg of the yoke to create a leakage field that is opposite in sign.

## Slide 12: Lambertson Magnet Design Considerations
In order to further reduce the integrate leakage field, The shielding plate design at the end of Lambertson magnet also plays an important role. With the shield plate, the leakage field in the opposite direction to the main field will be generated at the end of the magnet to cancel the leakage field in the body of magnet.

## Slide 13: Half in-vacuum LSM R&D for HEPS SR
Full size prototype:
  Started in 2021
  All the mechanical component processing was completed
  The biggest challenge is magnetic shielding block machining because the VP is hard and brittle. Although it can be segmented processing by EDM, but annealing deformation is hard to control.
Vacuum chamber
DT4 Yoke
1J22 Magnetic shielding block
Half cu Beam pipe
1J22 with cu coating
DT4 with Ni coating
Upper iorn yoke
1J22: hard and brittle
Machining by EDM
But annealing deformation hard to control
Full size prototype

## Slide 14: Half in-vacuum LSM prototype for HEPS
  Latest progress: Final assembling and vacuum testing was completed
  Vacuum pressure: 5.0×10-8pa（vacuum chamber）, 2.2×10-7pa（Transition section）
  Next plan: magnetic field measurement

## Slide 15: In-air LSM R&D for HEPS BST
Because FeCoV（1J22，Co50）is hard to machine, the magnetic shielding blocks must segmented processing by EDM . And that, the embedded thin wall SST vacuum chamber for stored beam is needed.
The gap at the joint of magnetic poles has a great influence on the leakage field and the main field distribution.
Feature：magnet is located in the air; total septum thickness=3.5mm， Length=1.6m

## Slide 16: In-air LSM R&D for HEPS BST
  The latest progress: the prototypes are being in magnetic measurement
  Preliminary result：the leakage field is good enough for HEPS requirements

## Slide 17
Slotted-pipe Kicker system

## Slide 18: DR inj./ext. kicker design parameters
parameter | Unit | DR-kicker
Quantity | - | 2
Type | - | Slotted-pipe kicker
Deflect direction | - | Vertical
Beam Energy | GeV | 1.1
Deflect angle | mrad | 10.7
Magnetic effective length | m | 1.4
Magnetic strength | T | 0.0281
Integral magnetic strength | T·m | 0.03934
Clearance region(H×V) | mm | 32.8×26.6
Good field region(H×V) | mm | 19.8×16
Field uniformity in good field region | - | ±1.5%
Repetition rate | Hz | 100
Amplitude repeatability | - | ±0.5%
Pulse jitter | ns | ≤5
Bottom width of pulse(5%-5%) | ns | < 250

## Slide 19: CEPC DR kicker Magnet physics design
2D simulation model
Max. voltage of coil: Umax=10622V
Max. exciting current: Imax=2400A
Magnet coil inductance=387nH
Good field region
19.8×16mm
x=±10, y=±8
Un.= -0.9%~1.5%
Good field region: 19.8×16mm
Field uniformity: -0.9%~1.5%
Contributed By Lihua Huo,Lei Wang

## Slide 20: CEPC DR kicker engineer design
Outer body (316L)
Busses (FOC)
insulation support (ceramic)
HV feedthrough
Cooling water pipe
+
-
To vacuum pump
It’s the CEPC DR kicker engineer design, which is very similar to HEPS booster injection kicker.

## Slide 21: Prototype kicker for HEPS BST
  The latest progress: the kicker prototype is pass the vacuum assembling test and the magnetic field measurement have completed. The field distribute performance meet the requirements.

## Slide 22: 250ns-fast kicker pulser design
Scheme: 20-stage inductive adder based on SiC-MOSFETs.
The co-axial transformer is configured as bipolar output.
The pulser is located outside tunnel and 10 50 Ω cables with length more than 30m are applied to connect with kicker.
Matching terminal resistor is 10Ω.
20-stage inductive adder

## Slide 23: Pulser prototype for HEPS
Progress：Single stage and double stages full power test has been completed（1400V into 0.5Ω）
Final version
Mass production and test

## Slide 24: Pulser prototype for HEPS
Latest Progress：18-stage inductive adder was tested（DC HV=800V, output pulse voltage is 14.2kV into 10Ω）.
Due to the existence of parasitic inductance outside the adder, a reverse voltage spike with high amplitude will be induced at the tail of the pulse when MOSFET is turned off, which must be suppressed by the reverse peak absorption circuit composed of high-speed diodes, Otherwise, MOSFET overvoltage breakdown will be caused.

## Slide 25
Ferrite core kicker magnet

## Slide 26: BST EXT kicker design parameters
parameter | Unit | BST-EXT-kicker1 （for CR off-axis inj.） | BST-EXT-kicker2 （for CR on-axis inj.）
Quantity | - | 2 | 2
Type | - | In-air delay-line dipole kicker | In-air lumped parameter dipole kicker
Deflect direction | - | Horizontal | Horizontal
Beam Energy | GeV | 120 | 120
Deflect angle | mrad | 0.2 | 0.1
Magnetic effective length | m | 1.4 | 0.7
Magnetic strength | T | 0.06 | 0.06
Integral magnetic strength | T·m | 0.08 | 0.04
Clearance region(H×V) | mm | 55×55 | 55×55
Good field region(H×V) | mm | ? | ?
Field uniformity in good field region | - | ±1.5%？ | ±1.5%？
Repetition rate | Hz | 1k | 1k
Amplitude repeatability | - | ±0.5% | ±0.5%
Pulse jitter | ns | ≤5 | ≤5
Bottom width of pulse(5%-5%) | ns | Trapezoid：440~2420 | Half-sine：1360
Tr/Tf(5%-95%) | ns | <200 | <680
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 27
Lumped parameter dipole kicker system
Features:
Out-vacuum kicker with metallic coating ceramic vacuum chamber
<1360ns,1kHz
Ferrite core
Ceramic vacuum chamber
Eddy current Shielding plate
HV conductor
For 1.3us half-sine kicker, a Lumped parameter dipole kicker is fit.

## Slide 28: Delay-line dipole kicker system
For trapezoid kicker system, a delay-line dipole kicker is preferred, because it can helps to achieve ideal trapezoid waveform. While, its structure is complicated.
200ns
40~2000ns
200ns
1kHz
challenges
Pulser
Delay-line kicker
Lumped parameter kicker
PFN
Delay-line kicker magnet

## Slide 29: Dual-C type delay-line dipole kicker R&D
Latest progress: We have finished a dual-C delay-line kicker prototype engineer design. The R&D was initiated at the end of last year.

## Slide 30: Delay-line Nonlinear Kicker (NLK)
Differential mode exciting
Common mode exciting
Injected bunch
stored bunch
Dipole field
Nonlinear field
Thinking about if the nonlinear kicker injection is possible for CEPC, after all this top-up injection scheme should loose the requirement of DA.

## Slide 31: Delay-line NLK preliminary design
Capacitor plate@
High potential
HV conductor
Ferrite core
Base
Capacitor plate @
Ground potential
Ceramic Vacuum chamber
ground potential Lead
High potential Lead
Eddy current Shielding plate
Ceramic support

## Slide 32: Ferrite core for delay-line kicker prototype
Investigating the domestic ferrite core manufacturers
L(uH)/μr | 100Hz | 1kHz | 10kHz | 100kHz
200mV | 421.7/1841 | 275.4/1202 | 279.28/1279 | 262.98/1148
400mV | 609.7/2662 | 280.85/1226 | 280.17/1223 | 260.17/1136
600mV | 871.9/3806 | 283.18/1236 | 278.73/1217 | 259.02/1131
800mV | 1139.4/4974 | 287.91/1257 | 281.26/1228 | 259/1131
1000mV | 1290.7/5635 | 295.22/1289 | 280.5/1225 | 259.92/1135
Ni-zn ferrite sample core test

## Slide 33: Ceramic vacuum chamber R&D
Chart: Wall thickness/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
octagon | 2.37 | 3.17 | 4.38 | 6.38 | 9.83 | 16.4 | 30.5 | 66.2 | 172
race track | 1.78 | 2.29 | 3.04 | 4.15 | 5.83 | 8.34 | 12 | 17.5 | 25.4
ellipse | 1.4 | 1.73 | 2.24 | 2.95 | 4.01 | 5.49 | 7.4 | 10.2 | 13.5
L=1.2m，thickness=5mm
ceramic vacuum chamber with special pattern metallic coating is key component for outside-vacuum kicker magnet.
Latest progress: the prototype is in fabrication phase
ellipse
octagon
Race track
Ceramic material: 99% AL2O3
√
Integrated sintering

## Slide 34: Magnetron sputtering coating prepare
Movable solenoid
Solenoid coil
Inner diameter=208mm
Length =700mm
Good field region=500mm
Horizontal coating system have been setup. It can support 700mm long pipe coating one-time or 1400mm long pipe sectional coating.
In order to obtain uniform coating inner racing track shape vacuum chamber, a horizontal movable cathode wire target solution is proposed.
The antechamber for HEPS
(inner aperture=6mm)
1m
Cathode wire
Moving track
view window
Cathode pole
Graduated bellows is used to adjust the horizontal position of cathode wire (compression at one end and tension at the other end)
As for metallic coating, a set of magnetron sputtering coating platform was set up.

## Slide 35: TiN coating test
And we have achieved TiN (Titanium nitride) film sample on a shorter ceramic vacuum chamber.
Cathode wire discharge during coating (200mA)
cathode wire discharge curve
TiN coating
SEM section test diagram
EDS test results
Four probe conductivity test bench
the conductivity of TiN film is about 5.4 × 104 S/m (ρ=0.0018 Ω·cm)

## Slide 36: Film pattern study
Strip film
Mesh film
Ladder film
Spiral film
Comb film
√
×
the film square resistance is set to 0.2 Ω (equivalent to 86nm copper film or 1.1 μm TiN film)
Material conductivity is set to 5000S / m, and the corresponding thickness is 1mm.
coil
ferrite
Ceramic vacuum chamber
Metallic film(spiral)
COMSOL 3D Model
Coil exciting current pulse
Central field deformation caused by different pattern films
The coating pattern on PCB research by Vector network analyzer(VNA).
The film pattern study by PCB is ongoing.

## Slide 37: Summary
The types of all inj./ext. components are determined. The hardware designs towards TDR are being carried out. One team is in charge of both HEPS and CEPC inj. & ext. system. A part of hardware R&D for 2 projects are overlapping.
The latest progress of the Lambertson magnet prototypes for HEPS are in magnetic measurement stage.
The slotted-pipe kicker prototype for HEPS BST has completed. The pulser of 18 stage inductive adder is being test. The reverse peak absorption circuit composed of high-speed diodes has to been designed to avoid MOSFET overvoltage breakdown.
R&D of delay-line kicker including ceramic chamber with TiN coating has started this year and the prototypes will be finished in May 2023.

## Slide 38
END
Thank you for attentions!!!