## Slide 1: CEPC mechanical system
Minxian Li, Haijing Wang, Peng Zhang
The 2022 international workshop on CEPC
October 26th, 2022

## Slide 2: Outline
Progress on MDI mechanics
Progress on collimators
Supports for regular magnets

## Slide 3: MDI layouts
The devices at MDI are integrated together.
  Detective angle: acos0.99
  IP chamber:-700mm~700mm
  Detector York length: 9620mm

## Slide 4: MDI layouts
All the devices are within the detective angle, acos0.99.
IP
Be-Al chamber
Z: -700~700mm
Remote Vacuum Connector
Z: 700~783mm
IP BPMs
Z: 855~950mm
Y chamber
Z: 783~855mm
Lumical body
Z: 940-1100mm
Q1a Q1b
Z: 1855~4440mm

## Slide 5: SC magnet support system
The superconducting quadruples for TDR are longer, and the structure of cryostat and SCQ has been updated.
The cryostat is about 5.6m long. The cantilever length is 5283mm.
SC quadruples become 3 parts:Q1a,Q1b,Q2.
Vacuum vessel
Helium vessel
Support rods
Q1a
Q2
Anti-solenoid
Q1b
Thermal shield

## Slide 6: SC magnet support system
Magnets to helium vessels
  Skeleton with outer ring support can minimize weight and reducing deformation.
Helium vessel to vacuum vessel
  Support blocks, 60mm x 20mm.
Aim: minimize the SC magnets deformation, enhance stability.
Sketch of skeleton support
Sketch of support blocks
Models | materials
Q1a/Q1b/Q2 | Nb-Ti alloy+ SS + FeCoV
Anti-solenoid | SS + Cu + AL
Vessels | SS
Magnet supports | SS
Vacuum chamber | SS

## Slide 7: SC magnet support system
G
Fz1
Fz2
Fz3
Magnet support | uneven deformation in Q1a (um) |  | uneven deformation in Q1b (um) |  | uneven deformation in Q2 (um) |  | Max. displacement of cryostat (mm) | 
 | Vertical | Horizontal | Vertical | Horizontal | Vertical | Horizontal | Vertical | Horizontal
TDR s-o support | 5 | 1.2 | 15 | 3.5 | 14 | 4 | 1.79 | 0.08
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.

## Slide 8: SC magnet support system
G
Fz1
Fz2
Fz3
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.
Future work
  Continue to optimize the structure of the magnet support
  Integral simulation with thermal contraction and support/adjustment components

## Slide 9
Modification suggestion of vacuum chamber for the collider ring，Liu Yu Dong for CEPC accelerator physical group，2021/3/25
37.5mm
28mm
28mm
28mm
The synchrotron radiation load reduced from 9.3KW to 7.5KW
The inclination of block ramp smaller.
The thermal power density decreases
Beam loss reduced
reduce the temperature
reduce stress
The diameter in the X direction smaller
The cross section of the vacuum pipe is changed from ellipse to circle, and the collimator is adjusted accordingly.
Collimators
From Peng Zhang

## Slide 10: Simulation results of block
183℃ （original version, i.e. ellipse vacuum pipe） → 147℃
129.31MPa (original version) → 89.7MPa
1.89mm (original version)→ 1.53mm
From Peng Zhang

## Slide 11: Simulation results of vacuum chamber
141℃ (original version) → 124℃
132MPa (original version) → 110MPa
From Peng Zhang

## Slide 12: Supports for regular magnets
Over 80% of the length is covered by magnets of about 138 types.
Adjustment Ranges of magnets |  |  | 
X | ≥±20 mm | Δθx | ≥±10 mrad
Y | ≥±30 mm | Δθy | ≥±10 mrad
Z | ≥±20 mm | Δθz | ≥±10 mrad
Booster
Collider

## Slide 13: Supports for regular magnets
Transportation and coarse location of magnets in Collider
Transportation and coarse location of magnets in Booster
Flexible load support for “long” devices and “short” devices
  * Cooperate with Beijing North Vehicle Group Corporation.

## Slide 14: Supports for regular magnets
The magnet girders will be renewed too.
  Simple & flexible structure.
  Small deformation & good stability
  Low cost
  Detailed structure for typical supports are under design.
According to the lattice design, the layout of one cell of collider and booster has been updated.

## Slide 15: Conclusion
We have updated the cryostat and MDI layout.
The SC magnet supports inside the cryostat are under design and optimization. Integral FEA with thermal contraction will be studied next step.
The structure of the collimator was optimized according to the modification of the vacuum chamber, and the temperature, stress and deformation were simulated.
The layout of one cell of collider and booster has been updated. Preliminary design for typical regular magnet supports are undergoing, more detailed work will be done.

## Slide 16
Thanks for your attention!