## Slide 1
Heat transfer analysis
of CEPC beampipe
Feng jie
Oct.28.2022

## Slide 2
Contents
1.Introduction
2. Change of model(Thermal loads and structures)
3. Heat transfer analysis of beampipe
4.Summary

## Slide 3
1. Introduction
Beam pipe:
High-order mode heat
Uniformly distributed
Total heat load：
910.834W@Z.
85mm
95mm
475mm
45mm
half model
455.417W
Extending AL pipe
Be pipe
Be pipe transition

## Slide 4
Transition pipe(AL):
Total area：53726mm2
Z: 680.25W(2.45W/cm2)
Be pipe transition(AL)：
Area：7477mm2
Z: 68.79W(2.45W/cm2)
Be pipe ：
Area：10556mm2
Z: 97.12W(0.92W/cm2)
April.8.2021
From Liu Yudong‘Impedance and HOM Heating in IR region of MDI for CEPC_2021-4-8’
2.1 Change of heat source(half model) (Φ20mm)
Previous
Transition pipe(AL):
Total area：
Z:341.56W(0.83W/cm2)
Be pipe ：
Area：
Z:55.295W(1.35W/cm2)
Be pipe transition(AL)：
Area：
Z: 29.28W(0.491W/cm2)
Transition (AL):
Total area：
Z:29.28W(0.701W/cm2)
Now
Sep.23.2022
1692W
910.834W
The total heat drop

## Slide 5
2.2 Change of structrue (Extending AL pipe)
Conical pipe
Runway and conical pipe
Previous
Now

## Slide 6
Heat transfer requirement：
The detector requires that the temperature difference between the two ends of the outer beryllium tube is less than 10 degrees.
The smaller the mass, the better.
3.1 Basic structure of beampipe
Be pipe
Extending AL pipe
O inlet
O outlet
Oil inlet
Oil outlet
Coolant: O
Inlet temperature: 20℃
Flow rate: 1.7L/min
Coolant: oil
Inlet temperature:20℃
Flow rate: 0.8L/min
Critical dimension:
Be Length:170mm
Outer Be pipe: 0.15mm
Inner Be pipe: 0.2mm
Cooling channel: 0.35mm
Viscous model: Laminar
The gap between the two layers of beryllium tubes
gap

## Slide 7
(1) Results of oil cooling in Be pipe
3.2 Heat transfer of Be pipe and extending AL pipe (Φ20mm)
Max.t of outer Be: 29.5℃ (Figure 2)
Max.t of inner Be: 39.4℃ (Figure 1)
Max.t of ends AL: 22.5℃
(Figure 1)
(Figure 2)
Paraffin flow parameters:
Flow rate: 0.8L/min
Inlet velocity: 0.0108kg/s
Inlet temperature: 20℃
Heat flux density of inner Be:13500W/m2
Heat flux density of Be pipe transition:
4190W/m2
Δt of two ends of outer Be: 7.4℃<10℃
meet the cooling requirements

## Slide 8
(1) Results of water cooling for in AL
3.3 Heat transfer of Be pipe and extending AL pipe (Φ20mm)
Max.t of transition AL: 35.5℃ (Figure 3)
Max.t of expending AL: 22.5℃
(Figure 3)
(Figure 4)
O flow parameters:
Flow rate: 1.7L/min
Inlet velocity: 0.02826kg/s
Inlet temperature: 20℃
Heat flux density of transition AL:
8300W/m2
Heat flux density of expending AL:
7010W/m2
Max.t of Be pipe transition: 36.3℃ (Figure 4)

## Slide 9
Heat transfer requirement：
Meet the pressure requirements.
The detector requires that the temperature difference between the two ends of the outer beryllium tube is less than 10 degrees.
The smaller the mass, the better.
3.4 Basic structure of beampipe
Be pipe
Extending AL pipe
O inlet
O outlet
O inlet
O outlet
Coolant: O
Inlet temperature: 20℃
Flow rate: 1.7L/min
Coolant: O
Inlet temperature:20℃
Flow rate: 0.8L/min
Critical dimension:
Be Length:170mm
Outer Be pipe: 0.15mm
Inner Be pipe: 0.2mm
Cooling channel: 0.35mm
Viscous model: Laminar

## Slide 10
(1) Results of O cooling in Be pipe
3.5 Heat transfer of Be pipe and extending AL pipe (Φ20mm)
Max.t of outer Be: 23.8℃ (Figure 2)
Max.t of inner Be:26.8℃ (Figure 1)
Max.t of ends AL: 22.4℃
(Figure 1)
(Figure 2)
O flow parameters:
Flow rate: 0.8L/min
Inlet velocity: 0.0108kg/s
Inlet temperature: 20℃
Heat flux density of inner Be:13500W/m2
Heat flux density of Be pipe transition:
4190W/m2
Δt of two ends of outer Be: 3.1℃<10℃
meet the cooling requirements
Max.t of transition AL: 30.1℃

## Slide 11
(1) Results of oil cooling in Be pipe
3.6 Compare the two cooling media
The maximum temperature is in inner Be(39.4℃)
(2) Results of O cooling in Be pipe
The maximum temperature is in transition AL(30.1℃)
Cause analysis:
The use of water medium cooling at the Be pipe makes the effect significantly improved, and the temperature of the inner beryllium pipe drops, so after using water cooling in beryllium, the maximum temperature is not on the beryllium tube but on the aluminum tube.
Compare the results:
After using water cooling, the temperature drops.Mainly at beryllium tubes, and at the transition between beryllium tubes and aluminum tubes.

## Slide 12
4. Summary
(1)Be pipe
Z mode: Safety!
Compare conclusions:Water cools better than oil. Therefore, water cooling may be required, but the corrosion of Beryllium by water needs to be studied.
(2)Future research prospects
Vertex detector
The first vertex detector is close to the outer beryllium tube and receives heat from the outer beryllium tube,
the heat transfer between the two will be analyzed.

## Slide 13
Thanks for your attention and guidance!