## Slide 1: SDHCAL Status and future
I. Laktineh
For
Gent, CIEMAT,GWNU, IP2I, LPC, OMEGA, SJTU, Tunis. U.

## Slide 2
Status:
SDHCAL technological prototype
Short description
Energy reconstruction method
Improvement with PID techniques
Further improvements on energy reconstruction
Future:
SDHCAL @Linear Collider
SDHCAL @Circular Collider
Summary
Outline

## Slide 3
Philosophy of the PFA-based detectors
Detectors should be precision and discovery
tools beyond the LHC scope.
Relevant Physics phenomena in the TeV
energy range are associated to multi jet
final states  Jet energy measurement
is the most important item.
Particle Flow Algorithm Construction of individual
particles and estimation of their energy/momentum
in the most appropriate sub-detector.
PFA requires the different sub-detectors including calorimeters to be highly granular.
PFA uses their granularity to separate neutral from charged contributions and exploits
the tracking system to measure with precision the energy/momentum of charged particles.

## Slide 4
The structure proposed for the SDHCAL :
is very compact with negligible dead zones
Eliminates projective cracks
Minimizes barrel / endcap separation
(services leaving from the outer radius)
SDHCAL
The SDHCAL concept is based on exploiting Gaseous Detectors high granularity potential
G.D are equipped with semi-digital, power-pulsed electronics readout and placed
in self-supporting mechanical structure to serve as absorber as well.
SDHCAL Technological Prototype should
be as much as possible similar to the ILD module
and able to study hadronic showers
Challenges
-Homogeneity for large surfaces
-Thickness of only few mms
-Lateral segmentation of 1 cm X 1 cm
-Services from one side
-Embedded power-cycled electronics
-Self-supporting mechanical structure

## Slide 5
48 layers (-6λI)
1 cm X 1 cm granularity
3-threshold, 500000 channels
Power-Pulsed
Triggerless DAQ system
Self-supporting mechanical structure
Published: JINST 10 (2015) P10039
Completed in 2011 and tested in 2012

## Slide 6
SDHCAL prototype was exposed to beam particles
at CERN PS, SPS in 2012, 2015, 2017 and 2018
Electron rejection: shower starting after the fourth layer (6 radiation length)

## Slide 7
SDHCAL prototype was exposed to beam particles
at CERN PS, SPS in 2012, 2015, 2017 and 2018
Muon rejection: average number of hits/layer < 2

## Slide 8
Energy reconstruction
Erec = α (Ntot) N1 + β (Ntot) N2 + γ (Ntot) N3
Ntot = N1 + N2 + N3
α , β , γ are quadratic functions of
They are computed by minimizing :
χ2= (Ebeam-Erec)2/Ebeam
N1= Nb. of pads with first threshold <signal < second threshold
N2 = Nb. of pads with second threshold <signal < third threshold
N3 = Nb. of pads with signal> third threshold
Track segments reconstruction using 3D-Hough Transform helps to apply different treatment to the hits of these segments.
JINST 11 (2016) P04001
Ntot = N’1 + N’2 + N’3+ NHT
Hough-Transform
JINST 12 (2017) P05009
Erec = α (Ntot) N’1 + β (Ntot) N’2 + γ (Ntot) N’3 + c NHT

## Slide 9
PFA
It helps to optimize the connection of hits belonging to the same shower by using first the topology and then the energy information
ArborPFA, April algorithms:
It connect hits and then their clusters using distance and orientation information
then correct using tracker information (momentum)
CALICE note CAN054
Efficiency
Purity
ΔE
1 neutral of 10 GeV
1 neutral of 10 GeV
1 neutral of 10 GeV

## Slide 10
Particle Identification
Due to the absence of Cerenkov detectors in front of the SDHCAL, the use of an electron selection (shower starting > d= 6 XI) was rather powerful but led to an important loss of hadrons (d= 1 ll).
To reject electrons and muons without losing hadrons we use the excellent granularity of SDHCAL to discriminate the three species. Several discriminatory variables were selected:
1- First layer of the shower (begin)
2- Number of tracks in the shower (trackMultiplicity)
3- Ratio of shower layers over total fired layers (nSHowerLayer/Nlayers)
4- Shower density (density)
5- Shower radius (radius)
6- Maximum shower position (length)
7- Ratio of N3/Ntot
8- Average number of clusters
….
BDT technique was used.
Simulated events of electrons, muons and pions were used for training/validation before to apply to data.
To avoid a possible bias due to discrepancy between data/simulation of electrons showers in the SDHCAL, pure electrons and muons data events were also used

## Slide 11
JINST 15 (2020) P10009

## Slide 12
Electron and muon rejection > 99%
JINST 15 (2020) P10009

## Slide 13
The BDT-based PID technique was also applied to the PS (3-80 GeV) samples
Linearity
Resolution
arXiv:2202.09684
Accepted to be published in JINST
Particle Identification & Energy reconstruction

## Slide 14
Further improvements on the energy reconstruction
Detector homogeneity
The homogeneity of the detector response is important to achieve better energy reconstruction
A new calibration method based on varying the thresholds rather than the electronic gain was found to be powerful. Muon runs with different thresholds Thr1: 0.1-0.42 pC, Thr2: 0.4-5, Thr3:4.7-24) and efficiency and multiplicity were measured for each value. The values of the three thresholds of each ASIC were fixed to obtain same multiplicity (first threshold) and the same efficiency for thr2 and thr3.
H2/2018
CALICE SDHCAL Preliminary
CALICE SDHCAL Preliminary
CALICE SDHCAL Preliminary
CALICE SDHCAL Preliminary
CALICE SDHCAL Preliminary

## Slide 15
Detector homogeneity
The homogeneity of the detector response is important to achieve better energy reconstruction
A new calibration method based on varying the thresholds rather than the electronic gain was found to be powerful. Muon runs with different thresholds Thr1: 0.1-0.42 pC, Thr2: 0.4-5, Thr3:4.7-24) and efficiency and multiplicity were measured for each value. The values of the three thresholds of each ASIC were fixed to obtain same multiplicity (first threshold) and the same efficiency for thr2 and thr3.
Further improvements on the energy reconstruction
H2/2018
CALICE SDHCAL Preliminary

## Slide 16
Detector homogeneity
The homogeneity of the detector response is important to achieve better energy reconstruction
Further improvements on the energy reconstruction
H2/2018
H2/2018
CALICE SDHCAL Preliminary
CALICE SDHCAL Preliminary

## Slide 17
Detector homogeneity
The homogeneity of the detector response is important to achieve better energy reconstruction
Before
After
We will apply the new method to the data to be collected in 2022
Further improvements on the energy reconstruction
H2/2018
CALICE SDHCAL Preliminary
3.9%
1.4%

## Slide 18
Several MVT methods (NN and BDT) were used to exploit, in addition to N1, N2 and N3, the hadronic shower shape information related to its energy thanks to the high granularity of the SDHCAL
Further improvements on the energy reconstruction
Multi-Variate Techniques

## Slide 19
Several MVT methods were used to exploit in addition to N1, N2 and N3 the shape information that is related to the shower energy thanks to yhe high granularity of SDHCAL. Simulated pion events within SDHCAL were used for this study.
MLP seems to perform better
JINST 14, 2019, P10033
Further improvements on the energy reconstruction
Simulation
Simulation

## Slide 20
Hadron identification
The energy reconstruction method was applied to hadron events.
No distinction was made between pions and protons or others.
Hadronic showers of pions and protons are not identical.
Better construction can be made if one can identify the nature f the hadron.
2022 beam test will be dedicated to study pion vs proton and kaon showers using Cerenkov detectors. Then BDT technique will be used to develop hadron PID and then energy construction algorithm with different (a, b, g) parameters could be used.
Further improvements on PID energy reconstruction
Simulation
Simulation
Simulation
Simulation
Simulation
This is one of the goals of the TB at CERN in September 2022

## Slide 21
SDHCAL@LC

## Slide 22
SDHCAL R&D towards ILD@ILC
Detectors as large as 3m X 1m need to be built
Electronic readout should be the most robust with
minimal intervention during operation.
DAQ system should be robust and efficient
Mechanical structure to be similar to the final one
Envisage new features such timing, etc..
Goal: to build new prototype with few but large GRPC with the new components
 ILD Module0
SDHCAL
ILD Module
GRPC
Glass Resistive Plate Chambers

## Slide 23
2 m
1 m
inlet
outlet
Prototype circulation system
New circulation system
Detector conception
Construction and operation of large GRPC necessitate some improvements with respect to the present scenario.
Gas distribution : new scheme is proposed
Cassette conception to ensure good contact between the detector and electronics is to be improved

## Slide 24
DIF #1
DIF #2
DIF #3
144 ASICs= 9216 channels/1m2
USB
HDMI
ASU1
3072 ch
ASU2
DIF
100 cm
33 cm
HADROC chip
(ASIC)
1m2 board  6 ASUs hosting 24 ASICs
Electronics readout for the 1m3 prototipo
1 DIF (detector InterFace) for 2 ASU (Active Sensor Unit.- PCB+ASICs)  3 DIFs for ONE 1m2 GRPC detector
Electronics readout for the final detector
Only 1 DIF per GRPC (any size) with small dimensions to fit in the small space available at the ILD detector
DIF dimensions
New electronics
Uo to 9

## Slide 25
HARDROCR3 main features:
  Independent channels
  Zero suppress
  Extended dynamic range (up to 50 pC)
  I2C link with triple voting for slow control parameters
  packaging in QFP208, die size ~30 mm2
  Consumption increase (internal PLL, I2C)
6,3 mm
4,7 mm
H3B TESTED : 786, Yield : 83.3 %
New electronics: ASIC

## Slide 26: HARDROC3: Analog linearity
FSB0
FSB0: 5σ noise limit= 15 fC
Up to 10 pC
Up to 50 pC
Fast shaper outputs (mV) vs Qinj (fC)
50% trig. Eff. (DAC units) vs Qinj (fC)
Dynamic range: 15fC - 50 pC
FSB1
FSB2

## Slide 27: ASU (Active Sensor Unit)
An important challenge is to build a PCB up to 1m length with good planarity to have a homogeneous contact of pads with RPCs in order to guarantee an uniform response along all the detector.
A company was found and 1x0.33 m2 with 13 layer ASUs have been built.
ASU
PCB
HR3
ASICs
The ASU-ASU (= ASU-DIF) connections also produced

## Slide 28
DIF sends DAQ commands (config, clock, trigger) to front-end and transfer their signal data to DAQ. It controls also the ASIC power pulsing
• Only one DIF per plane (instead of three)
• DIF handle up to 432 HR3 chips (vs 48 HR2 in previous DIF)
• HR3 slow control through I2C bus (12 IC2 buses).
Keeps also 2 of the old slow control buses as backup &
redundancy.
• Data transmission to/from DAQ by Ethernet
• Clock and synchronization by TTC (already used in LHC)
• 93W Peak power supply with super-capacitors
(vs 8.6 W in previous DIF)
• Spare I/O connectors to the FPGA (i.e. for GBT links)
• Upgrade USB 1.1 to USB 2.0
FPGA XC7A35TFGG484
TEXAS TM4C1294U
POWER
POWER
POWER
New electronics : DIF

## Slide 29
100 cm
33 cm
New readout electronics is being tested
All functionalities seem ok

## Slide 30
To synchronize several DIFs, a new DAQ board was developed. It contains:
-1 FPGA (cyclone10LP) with 12x5 LVDS links
-Microprocessor (PIC32MZ) interfaced with TCP/IP and with the FPGA for
high level operations ( calibrations..etc)
New electronics : DCC

## Slide 31
SDHCAL@CC

## Slide 32
Strategy followed by the SDHCAL groups
Three important aspects were studied to cope with the constraint of CEPC:
SDHCAL depth
SDHCAL power consumption and active cooling
SDHCAL timing
Rate capabilities

## Slide 33
Due to L* constraint from CEPC the detector radius is smaller than the one for ILC. This leads to that fact that the depth of the HCAL is smaller than that of ILD@ILC.
The option to reduce the number of SDHCAL layers by 4 and 8 and 12 layers was studied on the simulation and on the data collected at TB@CERN.
Reducing by 4 layers seem to have small effects but one can still be efficient with
40 layers
SDHCAL depth

## Slide 34
SDHCAL power consumption and cooling
The duty cycle of CEPC is different from that of ILC and no power pulsing is possible.
The power consumption is therefore increased by a factor of 100-200 with respect to ILC and active cooling is needed.
Lyon and Shanghai groups worked on a simple cooling system for SDHCAL based on using water circulating into copper pipes
108 chips
Rectangular section tubes : 2x1 mm
Copper plate over: 1.5 mm
PCB plate under: 1.4 mm
symmetry
1.5 m
0.5 m
Flow in
Flow out
0.8 mW/chips with power pulsing, 80 mW/chips without power pulsing

## Slide 35
SDHCAL power consumption and cooling
The duty cycle of CEPC is different from that of ILC and no power pulsing is possible.
The power consumption is therefore increased by a factor of 100-200 with respect to ILC and active cooling is needed.
Lyon and Shanghai groups worked on a simple cooling system for SDHCAL based on using water circulating into copper pipes
0.8 mW/chips with power pulsing, 80 mW/chips without power pulsing

## Slide 36
SDHCAL power consumption and cooling
Other solution is to use the new scheme developed by Lyon group (woven strips) to read out RPC for which a reduction of a factor higher than 30 can be obtained.
Caveat: This is ok for muon detectors and tail catchers. For SDHCAL a simulation is needed to validate

## Slide 37
SDHCAL power consumption and cooling
Other solution is to use the new scheme developed by Lyon group (woven strips) to read out RPC for which a reduction of a factor higher than 30 can be obtained.
Caveat: This is ok for muon detectors and tail catchers. However to be used in SDHCAL
a simulation is needed to validate the concept.
With four PCBs
With 10 PCBs
Preliminary results: Efficiency > 85%

## Slide 38
Timing is an important factor to identify delayed neutrons and better reconstruct their energy
Timing can help to separate close-by showers and reduce the confusion for a better PFA application. Example: pi-(20 GeV), K-(10 GeV) separated by 15 cm.
1 ns resolution
100 ps resolution
Y
Y
Z
X
Y
X
X
First step towards transforming SDHCAL into T-SDHCAL

## Slide 39
Including time information in the simulation to separate hadronic showers ( 10 GeV neutral particle from 30 GeV charged particle) using techniques similar to ARBOR’s ones.
Master work of C Devanne
First step towards transforming SDHCAL into T-SDHCAL

## Slide 40
How to achieve an excellent time resolution:
An ASIC with a fast preamplifier, precise discriminator and excellent TDC
is needed
PETIROC 32-channel, high bandwidth preamp (GBWP> 10 GHz), <3 mW/ch, dual time and charge measurement (Q>50 fC)
jitter < 20 ps rms @ Q>0.3 pC
TDC either internal or external (delay-line, Vernier,.etc on FPGA as for iRPC CMS upgrade project)
A fast-time DETECTOR
MultiGAP RPC is an excellent candidate.
4-5 gaps of 250 µm each can provide 100 ps tim resolution
First step towards transforming SDHCAL into T-SDHCAL

## Slide 41
Front-End Electronics for MRPC readout with high timing resolution
The system includes a front-end board (FEB), a detector interface card (DIF) and a data acquisition system(DAQ) based on ZCU102.
Test System and Setup
First step towards transforming SDHCAL into T-SDHCAL
Some noise was observed because of external power lines

## Slide 42
New version of PETIROC front-end board
Improving power rail design
Better isolation between sensitive analog signals and digital signals
Its power rails have been tested and verified.
Si5345 – used to generate clocks for Petiroc
Output clocks have been successfully tested

## Slide 43
New and easy way of construction MRPC
Board with 8 (could be extended to 12) Petircoc2B ASICs
Pads 2cm x 2cm, 256 channels
Local FPGA (Xilinx Spartan-6 TQFP) embedded on board
Top view
Bttom view
Using thin spacers made of mylar+double face
Large timing PCB
First step towards transforming SDHCAL into T-SDHCAL

## Slide 44
SDHCAL rate capability
GRPC have low rate detection capability (a few hundreds of Hz/cm2)
This is ok for ILC.
For CEPC with 1.5 MHz cycle duty (Higgs factory) this is still ok since the probability to have the same pad fired in one BC (0.7 µs) is about 10-5 and the probability to be fired once again before the electric field of the GRPC has reached its full value after a depletion is still small.
In case of Z-run the rate may be a problem, in particular at high eta.
Several scenarios are proposed:
Replace glass by other low resistivity electrodes leading to higher rate
(a factor of 100-1000 higer) PEEK doped with nanoparticle

## Slide 45
SDHCAL rate capability
GRPC have low rate detection capability (a few hundreds of Hz/cm2)
This is ok for ILC.
For CEPC with 1.5 MHz cycle duty (Higgs factory) this is still ok since the probability to have the same pad fired in one BC (0.7 µs) is about 10-5 and the probability to be fired once again before the electric field of the GRPC has reached its full value after a depletion is still small.
In case of Z-run the rate may be a problem, in particular at high eta.
Another possible scenario is to use resistive MPGD such as GEM, MICROMEGAS or µWell in the forward region and RPC in the barrel region.
Tests using MM in the SDHCAL along the RPC has already been successfully done.

## Slide 46
4 units of SDHCAL-MM, 1m x 1m each were produced, tested in a muon beam
CNRS-LAPP
SDHCAL rate capability

## Slide 47
The 4 units of SDHCAL-MM were then inserted in the SDHCAL-RPC prototype replacing the RPC units #10, 20, 35 and 50
Additional development with Resistive Micromegas has started to render the SDHCAL-Micromegas more robust against discharges that may happen in the core of the shower.
Similar activities with Thick GEM replacing MM could be initiated.
SDHCAL rate capability

## Slide 48
SDHCAL rate capability
GRPC have low rate detection capability (a few hundreds of Hz/cm2)
This is ok for ILC.
For CEPC with 1.5 MHz cycle duty (Higgs factory) this is still ok since the probability to have the same pad fired in one BC (0.7 µs) is about 10-5 and the probability to be fired once again before the electric field of the GRPC has reached its full value after a depletion is still small.
In case of Z-run the rate may be a problem, in particular at high eta.
Another possible scenario is to use resistive MPGD such as GEM, MICROMEGAS or µWell in the forward region and RPC in the barrel region.
Tests using MM in the SDHCAL along the RPC has already been successfully done. Similar tests with µWell is being discussed with colleagues from Wiseman Institute.
Still the use of MPGD will not allow to reach excellent time resolution as in the case of MRPC.

## Slide 49
Summary
SDHCAL concept with its high granularity provides an excellent tool not only to apply PFA by separating nearby showers but also to measure their energy.
Different techniques were used to measure hadronic shower energy
excellent linearity and very good resolution are obtained
The exploitation of the hadronic shower shape thanks to the high granularity is an excellent asset to identify particles and then better measure their energy.
In the future SDHCAL will exploit precise time information using MRPC. The time information will improve on energy reconstruction by separating delayed neutrons contribution and better estimating it.

## Slide 51
Time correction

## Slide 52
SDHCAL High-granularity impact
Hough Transform is an example to extract tracks within hadronic showers and to use them to control the calorimeter in situ
ρxz = z sin(θ) + x cos(θ)
Excellent agreement with efficiency/multiplicity results obtained with cosmic and beam-muons. Excellent agreement data/MC

## Slide 53
Gas recycling is necessary to reduce cost :
-Goal: reduce the gas consumption to reduce the cost.
-Gas renewal of 5-10% rather than 100%
-Conceived by the CERN gas group
Gas system