## Slide 1: Intrinsic resonance in CEPC Booster 2022-6-14 ChenTao

## Slide 2: Spin motion in Synchrotron
Tomas-BMT equation:
Use the motion parameter to replace the magnetic field
Use wave function to express the equation in which
Solve for one revolution around the accelerator

## Slide 3: Spin motion in Synchrotron
In perfect planar ring:
  No transverse motion;
  ;
  ;
  Polarization on vertical direction preserved.
In real ring:
  , the off-diagonal element is the source of depolarization
Choose a certain K , the equation can be solved :
Compare the 2 terms we can get
We can conclude: only when K close to , the spin closed orbit obviously deviate from vertical direction,
Thus the depolarization terms with different K can be treat separately .They are so-called spin resonances ,
K is the location of spin resonance.

## Slide 4: Analytical analysis of intrinsic resonance
B
QF
QD
B
…
Straight section
1 FODO Cell
M * FODO Cell
Assume bending angle angle of each FODO cell is , betatron phase advance is
1/P of the ring

## Slide 5: Analytical analysis of intrinsic resonance
Calculate the sum:
+
Enhancement factor: ;

## Slide 6: Intrinsic resonance structure in CEPC Booster
In CEPC Booster: , Calculated by DEPOL

## Slide 7: RESONANCE FREE DESIGN
Intrinsic spin resonance : The strongest intrinsic resonance at
P is the periodicity of the lattice, and is the vertical betatron tune
When , the first two important intrinsic spin resonances occur at and at .
At 18GeV ,
Choose this constrains the integer part of the vertical betatron tune to be
In the EIC design ,
Imperfection resonance: in the design the strongest imperfection resonance will be at ]
REF: PHYSICAL REVIEW ACCELERATORS AND BEAMS 21, 111003 (2018)
45.5GeV
120GeV
80GeV
Intrinsic resonance in CEPC Booster

## Slide 8: K=199.21
K=198.79,energy=8.75967e10,strength= 0.00002270
K=199.21 ,Energy =8.77818 e10 eV ,strength= 0.01775020
K=200.79,energy=8.8478e10,strength= 0.00002104
electron; CEPC Booster; K=199.21 ; normalized emittance = 10mmmrad
DEPOL计算结果：0.0177502
BMAD计算：共振强度
理论公式计算结果：0.01695（不包含直线节贡献）
升能模拟结果：
(取最终Sy=0.98)

## Slide 9: 多粒子跟踪结果-ZMode
45.5GeV
200个粒子

## Slide 10: 多粒子跟踪结果-HMode
120GeV
200个粒子