## Slide 1: Peak finding using ML with partial-label dataset
Guang Zhao, Shuiting Xin
zhaog@ihep.ac.cn

## Slide 2: Peak finding with ML
Advantage of ML:
Can learn internal signal/background characteristics automatically, and make full use of the information
Peak finding with ML:
Supervised binary classification with slicing window samples
Architecture: RNN based network
Signal
Noise
RNN
“Memory” structure for sequence data

## Slide 3: Dataset: Full labelled MC
Labelled MC samples
  ~20 primary ionizations per waveform
  Tuned based-on beam test waveforms: noise model, amplitude, peak rising-time
Beam-test data
MC

## Slide 4: Peak finding with ML/derivative
Neural Network
Derivative
The NN can find the peaks more effective!

## Slide 5: ROC comparison
Note: ROC curve is a standard tool for evaluation binary classifiers. ROC curve with larger area-under-curve (AUC) is better
RNN is a better binary classifier than the derivative method

## Slide 6: Challenge for data
(MC waveform for demonstration)
Supervised learning requires labels in good quality
There is no “truth” information for labelling in data

## Slide 7: Adding partial labels
(MC waveform for demonstration)
Some labels can still be added with human knowledge
Signal with large confidence:
  Big “local maxima“
Background with large confidence:
  “Marginal” bins

## Slide 8: Strategy for data
Partial labelled train dataset
Supervised model
Test dataset
Train
Apply
Due to the discrepancy between data/MC, try to train the model with data.
In the development stage:
Using MC sample for the whole process (assuming partial label)
Easy for performance evaluation

## Slide 9: Preprocessing
Intuitive idea:
  Remove possible biases for the partial labelled samples
Preprocessing procedures
  Slicing window size: 15 -> 6
    To reduce the contamination from the overlapping (due to partial labeling, overlapping cannot be effectively learned)
  Baseline subtraction
    Simple linear baseline subtraction for each slicing sample (improve noise detection for noise superposing on the signal)
  Height shifting
    Shift the absolute height to around 0 (removing the possible bias introduced by the training sample, because noises are always with low height in the partial labelled samples)

## Slide 10: Peak finding results (partial labels)
TPR = 0.452
FPR = 0.019

## Slide 11: Peak finding results (full labels)
TPR = 0.616
FPR = 0.004

## Slide 12: Conclusion
Have tried to train the peak finding classifier with partial-label datasets
The peak finding performance with MC sample looks okay
To perform further optimize the model and to apply the method with beam test data