## Slide 1: Demo system of Belle2link
Sun Dehui , Zhao Jingzhou ,Liu zhen’an
Trigger Lab
IHEP

## Slide 2: Outline
Belle2Link
Demo system
  Hardware
  Firmware
  Driver and Software
Implementation of slow control
Discussion

## Slide 3: Belle2Link
d
SVD FEE
COPPER
Belle2Link
RF ClocK
CDC FEE
………
PID
KLM
TTC
I/F_FE
I/F_TTC
I/F_COPPER
Slow control
Data
Belle2Link is a unified high speed link which connect Front-End Electronics (FEE) and Trigger and DAQ system for signal and data transmission. For system simplicity and reliability, It features as:
  unification in hardware design
  unification in firmware design
  provides electrical isolation
  provides high speed transmission rate
  can work at different input data rate
  home brew transmission protocol

## Slide 4: Demo system
Hardware
  COPPER board
  High Speed Link Board (Plugged to COPPER)
  FEE boards, such as CDC board (Linked to HSLBs with optic fibers)
  Server PC (file system server)
HSLB
COPPER board
COPPER plugged in VME crate with a File server
CDC board linked to HSLB

## Slide 6: Demo system
Firmware
  HSLB
    Virtex 5 Firmware ( Belle2link in HSLB board)
    CPLD Firmware ( online downloading )
  FEE
    Belle2Link in FEE

## Slide 7: Demo system Firmware —Structure of HSLB firmware
Slow Control module
  Receive or transfer the slow control message from Local bus
Data Link module
  Receive the data of FEE, transmit the data and the clock to the COPPER FIFO
Protocol
  Receive the package from GTP module
  Check the packages and unpack them
  Separate the data and transfer them to slow control module or data link module

## Slide 8: Demo system Firmware —Structure of Belle2lin firmware in FEE
Slow Control module
  Configure or read the slow control message from FEE register
Data Link module
  Receive the data from FEE. Pack the data
Protocol
  Receive the package from GTP module, check the packages and unpack them
  Transfer the data form FEE, and arbitrate the priority between slow control module and data link module

## Slide 9: Demo system
Software
  Data processing
    readhslb : read the data of FEE from the COPPER;
  Slow control
    paraconf : read or configure the register of HSLB and FEE
    fileconf : transfer file to FEE, such as a DSP ROM file
Driver
  Inherit from Higuchi-san’ Finesse general driver

## Slide 10: Implementation of Slow Control
General Consideration
  Task for Belle2link
    Parameter setting only
  Aim
    Unification suitable for all systems, not system dependent
    Easy implementation for FEE as was with Belle FINESSE
    Provide CDC implementation as an example for FEE

## Slide 11: Local Bus Interface
Difficulties
  Larger parameter data size(>128byte) needed
  How to make the belle2link transparent to FEE and local buss
New scheme has to be defined

## Slide 12: How to transfer a file
HSLB/FINESSE side(Two approaches)
First approach
  Large stream(>128B)
  Address 0X00: for this approach
  Length up to the maximum allowed
  Address/Data meaning definition by system
  The data will also be written to the address 0x00 on the interface between the FEE and Belle2link

## Slide 13: How to configure register
HSLB/FINESSE side(Two approaches)
Second approach
  Large stream(<128B or individual setting )
  Address 0X00-0x74: Length up to 127B
  Address/Data meaning definition by system
  Control module synchronies the control signal and control the reading or writing of the RAMs.
  One RAM records the value from system, used for configuration .
  Another Ram records the value form FEE, used for read-back.
  TWO CSRs are used as signal of acknowledge ,reading ,configuration.

## Slide 14: Implement on FEE side
FEE side(Parameter Bus)
  Keep the definition of local bus of COPPER.
    AB0-AB6 Local address bus.
    DB0-DB7 Local data bus.
    LWR Read/write direction indicator.
    EN ready signal.
  If COPPER write a value on address 0x41 of the Local bus, the value will be send to the same address on FEE after a few nanoseconds.
  If a ROM file is transferred , the file will be written on address 0x00 on front end serially. There are no buffer in Belle2Link .
  The Belle2link is transparent to the COPPER and FEE register.

## Slide 15: Parameter bus: Timing Chart
At least One cycle
One cycle
At least 1 cycle
AB0-AB6
RW
EN
DB0-DB7
At least
3 cycles
At least
4 cycles
one cycle
AB0-AB6
RW
EN
read cycle
write cycle
DB0-DB7
0 ns

## Slide 16: How to read
How to read the register is not so straightforward.
The program must inform the HSLB which register to be read, and wait for some time until the value was sent to the local bus interface from the FEE.
A CSR is used as acknowledge signal. When the value of the FEE register come , the value of CSR will be set to 0x11 .
Slow control message and the data from FEE are both transferred by fiber with different package.

## Slide 17: How to read
PMC CPU
Bridge
local bus
PCI bus
COPPER
Protocol
GTP
Optic Fiber
HSLBS
Parameters
Config
Para bus
FEE
Protocol
GTP
HSLBR
The program must inform the HSLB which register to be read and wait.
The HSLBS sends the address to FEE through Belle2Link
The FEE receives the address , read the value and send the address and the value back.
A CSR is used as acknowledge signal. When the HSLBS read the value of the FEE register completely , the value of CSR will be set to 0x11 .
Program check the CSR, and print the result on screen.

## Slide 18: New Sending link layer state machine
Belle2link need to transfer the data and the slow control message at the same time . So priority level is necessary .
New link layer protocol was designed
reset
Priority 1
priority 2
Send
slow control
message
Send
FEE Data
Priority 3
FEE data buffer almost full
CRC
Slow control buffer not empty
FEE Data buffer not empty

## Slide 19: New receiving link layer state machine
The receiving protocol must separate the slow control message and the FEE data.
reset
idile
Unpack the data and
Transfer to Datalink module
Unpack the data and
Transfer to SC module
SOP = 0x95FB
SOP = 0x951c
EOP = 0x95FD
Check error
EOP = 0x95FD

## Slide 20: Conclusion
Slow Control over Belle2link is predefined for CDC and works
For other system, we provide the design between the local bus and the FEE parameter Bus and the examples of the Linux program and configuration module .
Unification on SC in consideration and need further discussion

## Slide 21: Discussion
Upper-left: Belle
Lower-right: Belle II
  HSLB/Finesse info need to be defined
  FEE side also need to be defined
  Not fully discussed yet, latest at the coming workshop
Address | Description | Note
0x00-0x74 | User defined | 
0x75 | HSLB CSR | 
0x76 | FEE FW Ver. # | Mandatory
0x77 | FEE HW Ver. # | Mandatory
0x78 | FEE Type | Mandatory
0x79 | Belle2link FEE FW ver. # | Mandatory
0x7a | HSLB Download Flag2 | 
0x7b | HSLB Download Flag1 | 
0x7c | Belle2link HSLB CPLD Ver. | 
0x7d | Belle2link HSLB FW ver. # | Mandatory
0x7e | Belle2link HSLB HW ver. # | Mandatory
0x7f | Reserved | mandatory