## Slide 1
Possible MRPC detector for CEPC-TOF
王义
清华大学工程物理系

## Slide 2
PID of CEPC
Gent4 simulation:
TPC resolution: <2.5%
TOF: <50ps
PID of K: >98%
From Manqi’s summary @ 2022 CEPC workshop

## Slide 3
Application in nuclear physics experiments
Application in industry（Muon tomography)
Application in medicine（TOF-PET）
Read out
Read out
Insulator
Carbon
Insulator
Resistive
plate
MRPC application：
MRPC structure
Standard parameters:
Resistivity of glass: ~1012 Ω.cm
Working gas: 90%Freon+5%iso-butane+5% SF6
Time resolution <100ps
Efficiency >95%
Charge: a few PC
Dark current: a few nA
Noise ~1Hz/cm2
Rate <100 Hz/cm2
Large area, low cost
A good choice-MRPC

## Slide 4
 | ALICE | STAR | FOPI | BESIII | CBM | SoLID
Active area per detector (cm) | 120 x 13 | 22 x 8.4 | 90 x 4.6 | 0.5x(9.2+14.8)x32.8 | 33 x 27.6 | --
Total active area (m2) | 141 | 50 | 5 | 1.33 | 120 | 10
Pad size (cm) | 3.7 x 2.5 | 6.3 x 3.1 | 90 x 0.3 | (9.1~14.1) x 2.4 | 27 x 1.0 | (16~28) x 2.5
Gap×thickness(mm) | 10 x 0.25 | 6 x 0.22 | 6 x 0.3 | 12 x 0.22 | 10 x 0.25 | 32 x 0.128
Gas mixtures (C2H2F4/ C4H10/SF6) | 90/5/5 | 95/5/0 | 85/5/10 | 90/5/5 | 90/5/5 | 90/5/5
Operating field (kV/cm) | 96 | 107 | 110 | 109 | 110 | 150
Efficiency | 99.9% | 95-97% | 97±3% | 99% | 97% | 98%
Time resolution(ps) | 40 | 60 | 73±5 | 60 | 60 | 20 ps
Max rate (Hz/cm2) | 50 | 10 | 50 | 50 | 30k | 20k
higher counting rate and time precision.
MRPC in TOF system

## Slide 5
low-resistive glass control the voltage drop (efficiency loss) when incident flux goes up by Decrease the resistivity of the electrodes
Low-resistive glass has been operating at FAIR-Phase 0 programs like STAR-eTOF and mCBM
It will be applied in CBM-ToF Wall
Beam test result:
93%, 80ps ,70kHz/cm2
Specifications of low resistive glass
Low resistive glass for high rate detector

## Slide 6
Gas flow
Gas inlet
Gas outlet
Sealed pad spacer MRPC for CBM-TOF
Sealed pad spacer MRPC
Speed up gas exchange and can reduce to 1sccm/m2 flush rate at cosmic experiment!
Prevent creepage on fishing line at high rate (>7kHz/cm2)
Save working gas and environmentally friendly.

## Slide 7
TOF <20 ps， the intrinsic resolution of narrow gaps MRPC is around 15ps，so the time jitter of readout electronics <13~15 ps。
Simulation indicates proper ways to design the gap thickness and arrange the stacks
Narrower gap thickness required
MRPC <20 ps，the gas gap: <0.18mm
gap number: >16
20ps MRPC for SoLID-TOF

## Slide 8
Waveform sampling
Based on DRS4
Sampling freq=5 GS/s
Fast amplifier
Bandwidth=1.4GHz
 | MRPC prototype
gas gap thickness | 128 μm
number of gas gaps | 4 chambers × 8 gaps
glass material | low resistivity glass
glass thickness | 400
readout strips | 5 mm in width (2 mm clearance)
MRPC and electronics

## Slide 9
Total time resolution
MRPC + fast amplifier + DRS4
Timing：CFD
Event choose：Vertical cosmic ray
Test results

## Slide 10
桶部：
绕筒圆周方向两层tower overlap，每层16个tower，每个tower包含1个module-A和2个module-B，覆盖角度为360°，沿筒轴向放置tower（tower长4.9m）。
Module-A、Module-B中两相邻的MRPC之间2条读出条重叠，读出条为10+2.5mm，4室6气隙单个探测器厚3.02cm。
端部：
一端共24个module，分两层overlap；每个module中有5个探测器，两相邻的MRPC之间1-2条读出条重叠，每个探测器有24个读出条，读出条为10+3.5mm
CEPC-TOF总体构造
性能：
1、时间分辨：<35ps
2、PID of /k: 2.5GeV @3
3、TOF面积：~77m2
4、电子学道数：37632
5、电子学功耗：17mW/道
6、造价估算：3420万RMB (MRPC 784万元）

## Slide 11
Figure 1.1 Main sizes of the TOF barrel.

## Slide 12
Figure 1.2 Arrangement of MRPCs inside the box along the beam direction.

## Slide 13
Figure 1.3 Arrangement of MRPCs inside the box in the End-cap.
Figure 1.4 Diagram of the End-cap.

## Slide 14
电子学通道设计：

## Slide 15
MRPC采用4室6气隙结构，气隙厚度0.14mm，单个探测器厚3.02cm

## Slide 16
能量损失
谢谢！