## Slide 1
Qian LIU
University of Chinese Academy of Sciences
2023.7.5
CloverS: Coherent eLastic neutrinO-nucleus scatteRing at CSNS
progress report

## Slide 2
Science of CENS
Neutrino from CSNS
The Cryogenic undoped CsI detector
Background investigation
Expected output and schedules
Outline

## Slide 3
CEνNS coherent elastic neutrino-nucleus scattering
CEνNS : neutrino scatter on a nucleus via exchange of a Z boson.
CEνNS cross section is well calculable in the SM
Coherent up to
Nuclear form factor correction, important at
High order corrections <5%
CEνNS cross section is large!

## Slide 4
Motivation
COHERENT Collaboration Result
  First Detection at 2017------CsI(Na)： significance， agreement with SM
  2020-------LAr：
  significance, agreement with SM
  Verification at 2021------CsI(Na): significance, agreement with SM
Independent Experiment Verification is Important!

## Slide 5
Motivation
5
CSNS
Any deviation from N2 prediction can be a signature of beyond-the-SM physics

## Slide 6
Proposal: Cryogenic pure CsI crystal @ CSNS
At liquid nitrogen temperature ，CsI + R11065，33.5pe/keVee
The light yield is 2.5 times higher than that of COHERENT
EPJC(2020)80:1146
CsI+R11065 PMT
@ 77K
CsI(Na) @ RT
COHERENT

## Slide 7
China Spallation Neutron Source CSNS
7
Guangdong Province
1.5 hours to CSNS

## Slide 8
CSNS Top platform of the target station
Pros
Significantly shorten the distance
& increase the neutrino flux
The collision point is located 7.7 meters below the platform
Cons
beam-related neutron backgrounds
shielding is needed
Bonar Sphere detector

## Slide 9
Neutrino flux @ CSNS
Detector Location
  Neutrino Flux: per flavor @ 10.5 m (7.7m + 2.3m shield + offset)
Huang, Ming-Yang Chinese Physics C 40.6 (2016): 063002.
Neutrino production
  Neutrinos via Pion Decay-at-Rest(DAR)
  0.17/proton/flavor or higher!
Red: rector neutrino
Blue: CSNS neutrino
9
Det. With Shielding

## Slide 10
CSNS vs. SNS
 | CSNS | SNS
Beam Powe(MW) | 0.14 (will upgrade to 0.15 in the near future) | 1.4
Proton Energy(GeV) | 1.6 | ~1.0
Target | W | Hg
Target size(cm3) | 5×15×60 | 39.9×10.4×50.0
Repetition rate(Hz) | 25 | 60
Neutrino production | 0.17/proton/flavor | 0.08/proton/flavor
Neutrino Flux ( |  | 
Distance to IP | 10.5 | 19.3
 | CSNS | SNS
Beam Powe(MW) | 0.14 (will upgrade to 0.15 in the near future) | 1.4
Proton Energy(GeV) | 1.6 | ~1.0
Target | W | Hg
Target size(cm3) | 5×15×60 | 39.9×10.4×50.0
Repetition rate(Hz) | 25 | 60
Neutrino production | 0.17/proton/flavor | 0.08/proton/flavor
 | 10.5 | 19.3

## Slide 11
Experiment Design
R11065 PMT
double side readout
CsI: 3kg × 4
Dewar
LN2
PTFE
Detector is ~10.5m from Target
(Shielding～2.3m)
CSNS beam provides trigger signal
Cosmic ray anti-coincidence system provides veto
Flash ADC data taking at 8 channel
50μs data taking window and waveform analysis
N
Photons
Photons
~1.2m

## Slide 12
CEνNS Signal Spectrum
The following processes have been considered: Cross section, nuclear recoil energy, scintillation due to nuclear deposition, light collection, and converting into detector signals
The preliminary criteria：Npe ∈ [2,100],
The number of signal events per year：𝜈_𝜇 (134), 𝜈_𝑒 (154), 𝜈 ̅_𝜇 (197)
preliminary
preliminary

## Slide 13
Background Investigation
  Radioactive background
  Environmental gamma
  Beam related neutron
  Cosmic ray
  Neutrino induced neutron
  PMT dark count & Cherenkov light
80 cm HDPE
5 cm PS
60 cm Lead
30 cm HDPE
60cm
150cm
Not to scale
To be optimized

## Slide 14
 | K40 | Ra226 | Ra228 | Th228 | U238 | Ac228 | Bi214 | Pb212 | Pb214 | Th234 | Tl208 | Th232 | Pb210 | Ar39 | Co60 | Cs137 | Cs134 | Rb87 | Mass
PTFE | 0.343 | 0.12 | 0.11 | 0.065 | 1.96 | - | - | - | - | - | - | - | - | - | - | 0.17 | - | - | 32
Fe | 60 | - | - | - | - | 70 | 25 | 70 | 25 | 200 | 70 | - | - | - | 17 | 6 | - | - | 60
HDPE | 43.3 | - | - | - | 19.8 | - | - | - | - | - | - | 12.2 | - | - | - | - | - | - | 194
PMT | 37.1 | - | - | - | 5.2 | - | - | - | - | - | - | 13.4 | - | - | - | - | - | - | 9
Roman Lead | 1.3 | 0.3 | - | 0.3 | - | - | - | - | - | - | - | - | 120 | - | - | - | - | - | 2100
Modern Lead | - | 3 | - | 1 | 0.12 | - | - | - | - | - | - | - | 240000 | - | - | - | - | - | 7600
Liquid Nitrogen | - | - | - | - | - | - | - | - | - | - | - | - | - | 0.01 | - | - | - | - | 86
CsI | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | 150 | 50 | 8.7 | 12
Radioactive background
Radioactive isotopes from detector materials
Unit: mBq/kg
Mass:kg
14
COHERENT measured the radioactive background of CsI(Na) to be 10mBq/kg
KIM measure it to be typically 200mBq/kg，take KIMS’s result as a conservative estimation

## Slide 15
Radioactive background
15
CsI dominate, stainless steel and PMT follows.
After event selection，radioactive background events that surviving all cuts within [0.12 - 3] keVee，is ～23/year.
We can also try to measure the 661keV gamma peak of Cs137 to do a in-situ monitor of Cs137 background

## Slide 16
Environmental Gamma
16
After shielding，contribution from environmental gamma is ~ 0.1/year
Environmental gamma background
Accumulated spectrum for half an year
Energy deposition spectrum in CsI after the shielding
Environmental gamma rate

## Slide 17
Beam related neutrons (BRN)
17
Triggered by CSNS beam, only fast neutrons can reach CsI within our time window
After event selection, BRN rate ~2500/year with the shielding.
preliminary
preliminary
Energy deposition spectrum in CsI

## Slide 18
PMT dark count and Cherenkov background
PMT dark count rate has been measured to be (110Hz)
Coincidence of the dark count from two PMTs
| |<10，T0 = min()
  &
Dark count rate ~300/year@Npe
18
Experiment measured PMT dark count spectrum@77K
preliminary
PMT dark count rate
preliminary
Time spectrum of PMT dark count
preliminary

## Slide 19
Threshold
19
NPE threshold taken as 4，Equivalently～2.6keVnr threshold
Potential to further down to 3。Background dominated by PMT dark count coincidence.
Contribution from PMT dark count
cut
Selection Efficiency

## Slide 20
Background Investigation
20
Background type | Number of event sin 1 year | MC simulated | Event rate after cut (per year)
Radioactive background |  |  | 16
Environmental gamma |  |  | 0.1
Beam related neutrons |  |  | ～2500
PMT dark count |  |  | ～300
Neutrino induced neutrons | - | - | negligible
Comic ray induced radioactive isotopes | - | - | negligible
Background type | Number of event sin 1 year | MC simulated | Event rate after cut (per year)
Radioactive background |  |  | 16
Environmental gamma |  |  | 0.1
Beam related neutrons |  |  | ～2500
PMT dark count |  |  | ～300
Neutrino induced neutrons | - | - | negligible
Comic ray induced radioactive isotopes | - | - | negligible

## Slide 21
Expected sensitivity
21
12kg undoped CsI crystall，33.5p.e./keVee; 1 year data taking, significance～5.2σ
at low momentum transfer. Statistical error~16%

## Slide 22
Experiment：PMT R11065
22
R11065
RMS 1.07%
PMT dark count rate @ 77K: ～110Hz
PMT gain @ 77K: ～8.3E6，and stable

## Slide 23
Prototype test
23
R11065
77K big CsI crystal light yield test～15.8p.e/keVee
The light yield can be further improved by enhancing the optical coupling and employing wavelength shifters, etc.

## Slide 24
BRN measurement-LS detector
24
R11065
EJ301
PMT
-HV(1950V)
DT5751
PC
Calibrated EJ301 Liquid Scintillator detector
Remote controlled HV unit.
DT5751 ADC
Signal triggered by CSNS beam
System controlled by a PC
net
交换机
Use LS capable of N/ discrimination to measure the BRN
Beam
Trigger
Detector size: mm mm

## Slide 25
LS detector calibration
25
Good Linearity!
SN08
SN15
SN01

## Slide 26
PSD Algorithm N-γ discrimination
26
Rejection rate to gamma > 99.5%；
Pink Line: Gamma border
Right side of Red Line:
      Gamma and Neutron selection efficiency ~ 100%
Left side of Red Line:
  Neutron selection efficiency < 100%

## Slide 27
BRN measurement at CSNS
The dual bunch structure with time interval ~ 410ns of the CSNS proton beam is clearly observed.
27
X-axis : m
Y-axis ：m
Beam
Scanning the neuron counting rate at different positions in CSNS
(1.2, 0) selected to be the detector site
Shielding designed to be 2.4m wide and 1.8m high
ns
counts

## Slide 28
CSNS BRN rate monitoring
SN01: 5’’, （1,0）
LS01: 2‘’, (-1.2, 0)
LS02: 2‘’, (-3, 0)
28
Beam Power / kW

## Slide 29
CSNS BRN rate distribution on the platform
2.4m
Normalized to beam power 135kW
Near (1.2，0), the neutron background situation is quite similar,
Around 25-50neutrons/h.
This includes the neutron detection efficiency of the LS detector.
(0,0)
(1.2,0)
29

## Slide 30
BRN rate measurement plan
30
Building three different thickness settings of shielding and measuring the BRN rate.
Simulating the response matrix for each thickness setting of shielding, deconvolving it to obtain the neutron energy spectrum.
Approximately 100,000 events need to be accumulated for each setup, and the testing is estimated to take 2 weeks, with an additional week for installation.

## Slide 31
CloverS Experiment Schedule
31
R11065
2022
On site background study
Detector assembly fabrication
2023
2025
Accumulate the first year data
Start commissioning
2024
Start data taking

## Slide 32
Summary
32
The detection of Coherent Elastic Neutrino-Nucleus Scattering (CEνNS) involving neutrinos and nucleons is a significant frontier topic in particle physics. It holds great scientific importance for testing the Standard Model at low-energy scales and accurately measuring weak mixing angles.
The experimental setup at the China Spallation Neutron Source (CSNS) allows for placing the detector at a distance of 10.5 meters from the collision point. This greatly enhances the neutrino flux, making CEνNS detection feasible at CSNS.
Utilizing neutrinos from CSNS and employing a pure CsI scintillation crystal detector at liquid nitrogen temperature, the proposed detection scheme offers advantages such as high light yield and low detector dark noise. This effectively lowers the threshold for measuring nuclear recoil energy and thus enhances the sensitivity for CEνNS detection.
Some initial experimental demonstrations have been completed, and further refinement of the experimental plan will be carried out.

## Slide 34
87Rb
34
10 ppb is taken

## Slide 35
Unfolding Algorithm is implemented to extract BRN spectrum from LS data
Neutron spectrum with shielding is used to estimate the high energy neutron flux at CSNS. Lead will convert GeV neutrons into MeV neutrons can be measured by LS
BRN spectrum measurement
10cmHDPE+10cmPb
10cmHDPE
10cmPb
LS
Response matrix of 10cmHDPE+10cmPb

## Slide 36
Combine the spectrum W/WO the shielding, consider the effect of the shielding, we can estimate the energy spectrum of BRN to 1GeV
BRN spectrum measurement
10cmHDPE+10cmPb
10cmHDPE
10cmPb
LS
Unfolded Neutron Spectrum
Basically consistent with the Bonar result, uncertainty can be improved