## Slide 1
Preliminary waveform selection and charge analysis of beam test data
Yaxin Shen,Mingyi Dong,Guang Zhao, Linghui Wu
Cluster Counting Meeting
Nov 24,2022

## Slide 2
Introduction
Waveform selection
Charge distribution
  Charge distribution of each channel
  Fitted to Landau distribution
Maximum amplitude distribution

## Slide 3
Experiment condition: Gas : 80/20
Sampling rate: 1.5Ghz
Angle: 0
Data file:tbdata_29

## Slide 4: Waveform selection
Find all the local max of the waveform (>0.015mV)
For each local maximum points, find the nearest early point, whose slope starts to decrease (inflection point)
The Amplitude distance between the local maximum and the inflection points is recorded as the rising edge.
The points marked in the figure are local maximum points and inflection points
Amplitude (mV)
Time (ns)
Select good waveforms for peak finding analysis

## Slide 5: waveform selection
Valid： with maximum amplitude>0.03
Case Ⅰ： good waveforms with multi-peaks(number of rising edges between 0.01 and 0.03mV more than 6).
Time (ns)
Amplitude (mV)
Amplitude (mV)
Time (ns)
Total entries | 10000
Valid entries | 2791
Case Ⅰ | 877
Case Ⅱ | 1914
Case Ⅱ：number of rising edges between 0.01 and 0.03mv not more than 6
Case Ⅰ
Case Ⅱ
Tube：HV 23

## Slide 6
Waveform selection
Charge distribution: add the amplitude values for each point
Time from 50ns to 800ns
Maximum distribution:
The highest point of each waveform amplitude
(marked in red)

## Slide 7
channel0
channel1
channel2
channel3
channel4
channel5
channel6
channel7
channel8
channel9
channel10
channel11
Charge distribution:fitted to Landau distribution
This includes all valid entries(2791).

## Slide 8
Maximum amplitude distribution: include all value entries(2791).
Channel 0
Channel 1
Channel 2
Channel 3
Channel 4
Channel 5
Channel 6
Channel 7
Channel 8
Channel 9
Channel 10
Channel 11

## Slide 9
Gains of channel7 and 11 are much higher than that of others
dE/dx vs tube
q
Amplitude (mV)
Maximum amplitude vs tube

## Slide 10
Select a channel with a large mean for drawing waveform(root29,channel11)：
find that some waveforms have more than one big peak
Discussion:

## Slide 11
Summary
Preliminary waveform selection performed
Charge distribution and maximum amplitude distribution obtained.
It seems that the gains of channel 7 and 11 are much higher
To do:
  Future analysis with peak finding algorithm