## Slide 1: Preliminary peak finding results with derivative method for beam test data
Shuaiyi Liu, Yaxin Shen, Guang Zhao, Siman Liu, Linghui Wu, Mingyi Dong

## Slide 2: Data sets
The using data sets are from the result of the beam test at CERN SPS, July 2022.
Data of run 10, 11, 41, 44, 45, 46, 47, 49 are used in the slides
  Data of run 10, 11, 47, 49 with gas mixture 90/10, 4 runs in same HV and momentum, each run is in different angle
  Data of run 41, 44, 45, 46 with gas mixture 80/20, 4 runs in same HV and momentum, each run is in different angle
Gas 80/20 | Run | ch | angle
 | 41 | 4 | 45
 | 44 | 4 | 0
 | 45 | 4 | 30
 | 46 | 4 | 60
Gas 90/10 | Run | ch | angle
 | 10 | 4 | 45
 | 11 | 4 | 0
 | 47 | 4 | 60
 | 49 | 4 | 30
All 8 runs’ sampling rate are 2G

## Slide 3: Peak finding algorithm
Low pass filter
  Filter out high frequency noises in the waveforms to improve the S/N ratio
  Moving average(MA) filter: .
  When MA=1, , which means no filter.
Derivative
  First derivative(D1): D1[i] = y[i] – y[i-G]
  Second derivative (D2): D2[i] = D1[i] – D1[i-G]
Parameter
  Derivative: D2 threshold for hit detection(Th)
  Filter: Moving average steps(MA)

## Slide 4: Peak finding algorithm
Use second derivative instead of first derivative
For first derivative, pile-up on the falling edge is easier to recover, but it is not easy on the rising edge.

## Slide 5: Peak finding algorithm: amplitude cut
In the RMS distribution, take the low RMS events as noises
Using 0.004 (4 times noises RMS mean value) as an amplitude cut
One noise example waveform

## Slide 6: Peak finding algorithm: amplitude cut
The aera where amplitude lower than 0.004 will not be used in peak finding
Without cut
With cut
The example waveform in peak finding with and without the amplitude cut

## Slide 7: Scan Threshold (keep MA=1, means no MA)
When threshold is larger than 0.003, there are too many peaks not found, so we only use threshold smaller than 0.003 later.
Th=0.003
Th=0.004
Threshold | ncount
0.001 | 124
0.002 | 78
0.003 | 55
0.004 | 45
0.005 | 35
0.006 | 29
0.007 | 27
0.008 | 21

## Slide 8: Scan MA: MA effect in a waveform example Th=0.001, MA =1~3
Th=0.001
MA=1
MA=3
MA=2
MA=1 means without filter

## Slide 9: Scan MA: MA effect in a waveform example Th=0.002, MA =1~3
Th=0.002
MA=1
MA=3
MA=2

## Slide 10: Scan MA: MA effect in a waveform example Th=0.003, MA =1~3
Th=0.003
MA=1
MA=3
MA=2

## Slide 11: Ncount in one channel’s data
Too many noises involved
Apply the cut ncount>1 to select out the noise events.
Checked one channel’s waveforms with ncount<=1 by eyes, almost noises(>99%)
Run44 ch4
Noise event examples

## Slide 12: Peak finding with different Th and MA
gas:80/20 δ=18 size = 1cm α=0
Th=0.001,MA=1
Th=0.001,MA=2
Th=0.002,MA=1
Th=0.003,MA=1
Run44 ch4
Run44 ch4 ncount mean value |  |  | 
Th\MA | 1 | 2 | 3
0.001 | 19.77 | 10.78 | 8.50
0.002 | 12.44 | 6.59 | 5.76
0.003 | 8.71 | 5.10 | 4.79

## Slide 13: Expected number of electron peaks
Get from Brunella’s talk at Feb18 2022
Run44 ch4 ncount mean value |  |  | 
Th\MA | 1 | 2 | 3
0.001 | 19.77 | 10.78 | 8.50
0.002 | 12.44 | 6.59 | 5.76
0.003 | 8.71 | 5.10 | 4.79
gas:80/20 δ=18 size=1cm α=0
Npeak(Expected)=18*0.8*1.3*1.6*1=29.952
The group with Th=0.001 and MA=1 is closest to the expected number

## Slide 14: Compare count numbers in different gas mixture and angle
For gas 80/20:
  Run 41,44,45,46
  same HV and momentum
  different angles(0, 30, 45, 60).
Gas 80/20 | Run | ch | angle
 | 41 | 4 | 45
 | 44 | 4 | 0
 | 45 | 4 | 30
 | 46 | 4 | 60
Gas 90/10 | Run | ch | angle
 | 10 | 4 | 45
 | 11 | 4 | 0
 | 47 | 4 | 60
 | 49 | 4 | 30
For gas 90/10:
  Run10,11,47,49
  same HV and momentum
  different angles(0, 30, 45, 60).

## Slide 15: Comparison between different angles
Run 41,44,45,46 ch4 (gas 80/20, 1cm, same HV & momentum, different angle)
MA=1 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 19.77 | 34.64 | 47.67 | 55.90
0.002 | 12.44 | 20.47 | 28.27 | 35.60
0.003 | 8.71 | 13.27 | 18.46 | 25.03
MA=2 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 10.78 | 18.72 | 25.24 | 29.80
0.002 | 6.59 | 10.46 | 14.12 | 18.21
0.003 | 5.10 | 7.09 | 9.59 | 13.17
MA=3 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 8.50 | 13.95 | 18.61 | 22.90
0.002 | 5.76 | 8.50 | 11.32 | 15.10
0.003 | 4.79 | 6.14 | 8.20 | 11.44
Dataset Gas 80/20 | Run | ch | angle | Expected number
 | 44 | 4 | 0 | 29.95
 | 45 | 4 | 30 | 34.59
 | 41 | 4 | 45 | 42.36
 | 46 | 4 | 60 | 59.90
MA Th , Ncount
Angle , Ncount

## Slide 16: Comparison between different angle
Run 10,11,47,49 ch4 (gas 90/10, 1cm, same HV & momentum, different angle)
MA=1 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 36.71 | 48.74 | 60.04 | 63.25
0.002 | 15.33 | 20.60 | 26.48 | 30.64
0.003 | 8.27 | 10.95 | 13.12 | 17.29
MA=2 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 14.64 | 20.03 | 24.98 | 27.78
0.002 | 5.37 | 7.44 | 8.54 | 11.56
0.003 | 3.56 | 4.64 | 4.80 | 6.93
MA=3 |  |  |  | 
Th\Angles | 0 | 30 | 45 | 60
0.001 | 8.93 | 12.49 | 15.10 | 19.00
0.002 | 4.69 | 6.29 | 6.74 | 9.79
0.003 | 3.38 | 4.39 | 4.38 | 6.46
Dataset Gas 90/10 | Run | ch | angle | Expected number
 | 11 | 4 | 0 | 19.97
 | 49 | 4 | 30 | 23.06
 | 10 | 4 | 45 | 28.24
 | 47 | 4 | 60 | 39.94
Count number in gas 90/10 group is larger than gas 80/20 group
But not the case in the expected number

## Slide 17: Summary and outlook
Apply peak finding algorithm with derivative method to beam test data analysis
Scaning threshold and MA shows:
  For gas 80/20 group, Th=0.001 & MA=1 has closest number with expected
  For gas 90/10 group, Th=0.002 & MA=1 has closest number with expected
  Number of found peaks increase with larger angle
To optimize the derivative algorithm
To apply the ML algorithm (currently tuning MC simulation based on data)

## Slide 18: Backup

## Slide 21: Threshold test (Run44 ch4 80/20gas 1cm)
Th=0.001
Th=0.002
Th=0.003
Th=0.004

## Slide 22: Threshold test (Run44 ch4 80/20gas 1cm)
Th=0.005
Th=0.006
Th=0.007
Th=0.008

## Slide 23: Run41 ch4 waveform Th0.001~0.003&MA1~3

## Slide 32: 4 Runs counting numbers compare
Run 41,44,45,46 ch4 (gas 80/20, 1cm, same HV & momentum, different angle)
Run 41 ch4 45°
Run 45 ch4 30°
Run 46 ch4 60°
Run 44 ch4 0°
The showed number is the mean value of number of found peaks

## Slide 33: 4 Runs counting numbers compare
Run 10,11,47,49 ch4 (gas 90/10, 1cm, same HV & momentum, different angle)
Run 10 ch4 45°
Run 47 ch4 60°
Run 49 ch4 30°
Run 11 ch4 0°

## Slide 34: 4 Runs counting numbers compare
Run 47,49,52,53 ch4 (gas 90/10, 1cm, same HV & momentum, different angle) 0° & 45° have sampling rate 1.0, while 30° & 60° have sampling rate 2.0
Run 47 ch4 60°
Run 52 ch4 0°
Run 53 ch4 45°
Run 49 ch4 30°

## Slide 35: 4 Runs counting numbers compare(ncount>1)
Run 47,49,52,53 ch4 (gas 90/10, 1cm, same HV & momentum, different angle) 0° & 45° have sampling rate 1.0, while 30° & 60° have sampling rate 2.0
Run 47 ch4 60°
Run 52 ch4 0°
Run 53 ch4 45°
Run 49 ch4 30°