## Slide 1: CEPC Collider ring lattice design
Yiwei Wang
for the CEPC Accelerator Physics Group
The Institute of High Energy Physics, Chinese Academy of Sciences
The 2023 CEPC MDI workshop
30 March-1 April 2023, USC, Hengyang

## Slide 2: Overall design requirement of the CEPC collider ring
SR power per beam 30 MW (50 MW upgradable), 100 km, 2 interaction points
Compatible modes for H/Z/W/runnig: provide high quality beam energy from 45.5 to 180 GeV
Compatible with SPPC: two machines share the most tunnels except the IP1-IP4
CEPC detectors
Tunnel in the arc regions
CEPC+SPPC complex

## Slide 3: Lattice design of the CEPC collider ring
*ref: CEPC-CDR; CEPC pre-CDR; K. Oide, arXiv:1610.07170; M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010); A. Milanese, PRAB 19, 112401 (2016);
Basically 2 folded symmetry
8 arc sections
  dual aperture dipole and quadrupole magnets
  non-interleaved sextupoles
4 short straight section
  on/off axis injection regions for different modes
  beam dumping
2 interaction regions
  crab waist collision
  local chromaticity correction for the interaction region
  asymmetric interaction region
2 RF acceleration regions
  shared cavities for two beam @ ttbar, Higgs
  flexible switching between compatible modes
Correction of sawtooth orbit
CEPC complex
CEPC collider layout

## Slide 4: Machine parameters of CEPC
*CEPC AP group, TDR draft ch 4.1
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 266/267 | 266/266 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.3/1.7 | 1.2/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (Bhabha/beamstrahlung) (min) | 39/40 | 80/18000 | 60/700 | 81/23
Beam lifetime (min) | 20 | 80 | 55 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 266/267 | 266/266 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.3/1.7 | 1.2/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (Bhabha/beamstrahlung) (min) | 39/40 | 80/18000 | 60/700 | 81/23
Beam lifetime (min) | 20 | 80 | 55 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5

## Slide 5
CEPC TDR luminosity checked by
beam-beam simulations
Higgs : 5*10^34/cm^2/s (BB Simulation)
5*10^34/cm^2/s (Parameter table)
W-pole : 18*10^34/cm^2/s (BB Simulation)
16*10^34/cm^2/s (Parameter table)
Y. Zhang
ttbar: 0.55* 10^34/cm^2/s (BB Simulation)
0.5*10^34/cm^2/s (Parameter table)
ttbar
Higgs
W
Z
Z-pole : 125*10^34/cm^2/s (BB Simulation)
115*10^34/cm^2/s (Parameter table)
Qx
Qx
Qx
Qx

## Slide 6: Interaction region for all modes
Crab waist collision, local chromaticity correction, asymmetric interaction region
*ref: Y. Cai, IAS2016, HKUST; K. Oide, arXiv:1610.07170;
P. Raimondi, Proc. of the 2nd SuperB Workshop, Frascati, March 2006；M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010);
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
 | QD | QF
Z | Q1A | Q1B
W/H | Q1A+Q1B | Q2
ttbar | Q1A+Q1B+Q2 | add quad Q3A and Q3B
Strength of other modes doesn’t exceeded the one of Higgs mode.
 | L* [m] | LQ1 [m] | LQ2 [m] | GQ1 [T/m] | GQ2 [T/m] | d [m]
CDR | 2.2 | 2.0 | 1.5 | -136 | 111 | 0.3
TDR | 1.9 | 1.22/ 1.22 | 1.5 | -141/ -85 | +95 | 0.3
ttbar
Q1AIRU
Q1BIRU
Q2IRU
Q3AIRU
Q3BIRU
Q1AIRD
Q1BIRD
Q2IRD
Q3AIRD
Q3BIRD

## Slide 7: Interaction region for all modes (cont.)
Crab waist collision, local chromaticity correction, asymmetric interaction region
ttbar
Q1AIRU
Q1BIRU
Q2IRU
Q3AIRU
Q3BIRU
Q1AIRD
Q1BIRD
Q2IRD
Q3AIRD
Q3BIRD
CW
CCX
CCY
FT
beam
a pair of chromatic sextupoles in CCY
*ref: Y. Cai, IAS2016, HKUST; K. Oide, arXiv:1610.07170;
P. Raimondi, Proc. of the 2nd SuperB Workshop, Frascati, March 2006；M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010);
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
 | QD | QF
Z | Q1A | Q1B
W/H | Q1A+Q1B | Q2
ttbar | Q1A+Q1B+Q2 | add quad Q3A and Q3B
Strength of other modes doesn’t exceeded the one of Higgs mode.
 | L* [m] | LQ1 [m] | LQ2 [m] | GQ1 [T/m] | GQ2 [T/m] | d [m]
CDR | 2.2 | 2.0 | 1.5 | -136 | 111 | 0.3
TDR | 1.9 | 1.22/ 1.22 | 1.5 | -141/ -85 | +95 | 0.3

## Slide 8: CEPC TDR RF Layout
Lumi/IP[10^34/cm^2/s] | Higgs | Z | W | ttbar
Stage 1 | 8.3 | 38(10MW limit) | 26.7 | -
Stage 2 | 8.3 | 192 | 26.7 | -
Stage 3 | 8.3 | 192 | 26.7 | 0.83
Peak luminosity at different stages with SR power up to 50MW/beam
Stage 1
：
H/W/LL
-
Z (and HL
-
H/W upgrade)
Stage 2
：
HL
-
H/W/Z (HL
-
Z upgrade)
Stage 3
：
HL
-
H/W/Z/ttbar (ttbar
-
upgrade)
H
650 MHz 2
-
cell cavity
6 cavities in 1 CM
Z
650 MHz 1
-
cell cavity
1 cavity in 1 CM
ttbar
650 MHz 5
-
cell cavity
4 cavities in 1 CM
ttbar
Inner Ring
Outer Ring
H
H
Z
Z
Inner Ring
Outer Ring
H
H
Inner Ring
Outer Ring
H
H
Z
Z
1st priority of the Higgs running and flexible switching
Low cost at early stage
Get high luminosity for all modes
Stage 1 (H/W run)
Layout and parameters are same with CDR except longer central part
Medium or low luminosity at Z
Stage 2 (HL-Z upgrade)
Move Higgs cavities to center and add high current Z cavities.
By-pass low current H cavities.
Stage 3(ttbar upgrade)：
Add ttbar cavities (low current, high gradient, high Q)
Nb3Sn@4.2 K or others to significant reducing the cost of cryo-system and AC power.
Jiyuan Zhai, Yiwei Wang

## Slide 9: ARC region for all modes
Z and W modes need larger momentum compaction factor p and thus larger emittance εx, Qs
  To suppress the impedance induced instability at Z mode
  To increase stable tune area if considering beam-beam effect and impedance consistently at W and Z modes
stable tune area with both beam-beam and impedance (Z mode 90/90)
Yuan Zhang
Microwave instability
  Phase advance reduced from 90 to 60 for W and Z modes
Na Wang,
CEPC Day, March 2020
    H/ttbar mode 90/ 90
    W/Z mode 60/ 60

## Slide 10: Optimization of ARC aberration for Higgs/ttbar modes
2nd order chromaticity is a main aberration for the optimization of momentum acceptance with one –I sextupole pair scheme.
  In previous versions, 2nd order chromaticity generated in the ARC region are corrected with IR knobs (phase advance or K1).
  However, the IR knobs will generate distortions at IP (beta, alfa and dispersion) especially for the horizontal plane.
A lattice with four –I sextupole pairs scheme for Higgs & ttbar modes
  much less 2nd order chromaticity for the horizontal plane
Q’’=313, 410
Q’’=9, 145
Scheme with one –I sextupole pair
Proposed by K. Oide
Scheme with four –I sextupole pairs
Proposed by Tianjian Bian

## Slide 11
The distribution of sextupoles for Higgs & ttbar mode allowed to select –I sextupole pairs for W &Z mode.
  6*6=36 cases for 23 cells
  There are much more combinations if choose different cases in each arc section (184 cells)
1st pair | 2nd pair |  | 
(1A, 2A) | (2B,3B) | (3A,4A) | (3B,4B)
(1B, 2B) | - | (3A,4A) | (3B,4B)
(2A, 3A) | - | - | (3B,4B)
SF
1A
SF
1B
SF
2A
SF
2B
SF3A
SF
3B
SF
4A
SF
4B
SD
1A
SD
1B
SD
2A
SD
2B
SD3A
SD
3B
SD
4A
SD
4B
-I
-I
-I
-I
@ dp/p=1%
2nd and 3rd order dQ@dp/p=1% in x, y
  Optimization of ARC aberration for
  W/Z modes

## Slide 12
+
case {3,4}
case {4,3}+{3,4}
case {4,3}
Cancellation of main aberration has period of 23*3 cells.
  Optimization of ARC aberration for
  W/Z modes (cont.)

## Slide 13: Lattice design of the CEPC half ring
ttbar: εx=1.4nm, β=1.04m/2.7mm
Higgs: εx=0.64nm, β=0.30m/1mm
W: εx=0.87nm, β=0.21m/1mm
Z: εx=0.27nm, β=0.13m/0.9mm
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 14: Dynamic aperture requirement
DA requirement | ttbar | Higgs | W | Z
with on-axis injection | - | 1.6% | - | -
with off-axis injection | 2.0% | 1.6% | 1.2% | 1.3%
DA requirement | ttbar | Higgs | W | Z
with on-axis injection | - |  | - | -
with off-axis injection |  |  |  | 
 | ttbar | Higgs | W | Z
Horizontal Emittance in collider/booster [nm] | / 2.83 | / 1.26 | / 0.56 | / 0.19
DA requirement from injection | off axis | off axis on axis | off axis | off axis
Beam lifetime (mainly bhabha and beamstrahlung) [min] | 18 | 20 | 55 | 80
Energy acceptance requirement from beam lifetime [%] | 2.0 | 1.6 | 1.2 | 1.3
 | ttbar | Higgs | W | Z
Horizontal Emittance in collider/booster [nm] |  |  |  | 
DA requirement from injection |  |  |  | 
Beam lifetime (mainly bhabha and beamstrahlung) [min] | 18 | 20 | 55 | 80
Energy acceptance requirement from beam lifetime [%] | 2.0 | 1.6 | 1.2 | 1.3
by Y. Zhang, X. H. Cui, Y. W. Wang
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 15: Dynamic aperture @ Higgs and ttbar
Tracking to get DA without errors, with turns for one transvers damping time, with 4 initial phases
DA optimized with 84 variables (64 arc sextupoles + 8 IR sextupoles + 4 multipoles + 8 phase advance)
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
ttbar
Higgs
1.6 %
1.6 %
2.3 %
2.3 %
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 16: Dynamic aperture @ Z and W
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
Tracking to get DA without errors, with turns for one transvers damping time, with 4 initial phases
DA optimized with 116 variables (96 arc sextupole families + 8 IR sextupoles + 4 multipoles + 8 phase advance)
W
Z
1.3 %
1.3 %
1.2 %
1.2 %
Notes: Though the current injection schemes for W and Z modes are both transverse injection, it’s worthy to further improve the momentum acceptance for exploring the longitudinal injection scheme and leaving more margins for the error effects. The dynamic aperture at the W and Z energies has been optimized with 116 variables (96 arc sextupole families + 8 IR sextupoles + 4 multipoles + 8 phase advance). The current momentum acceptance of W and Z energies achieved 1.2% and 1.3% respectively which fulfill the requirement from the beam-beam effect and injection, shown in the following figure. Further optimization with 160 more arc families is undergoing to increase the on-momentum dynamic aperture.
11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 17: Dynamic aperture with errors @ Higgs
Component | x (mm) | y (mm) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.02%
IR Quadrupole | 0.10 | 0.10 | 0.10 | 0.02%
Sextupole | 0.10* | 0.10* | 0.10 | 
*reduced to 10 um by turn on sextupole gradually or movers
w/o misalignment of the girder, main field errors of the sextupole
Higgs
1000 and 500 lattices with errors are corrected for Higgs and Z respectively.
The DA with error correction are tracked and satisfy the on-axis injection requirement for Higgs and off-axis injection requirement for Z.
—DA w/o error
—mean value
—statistic errors
—requirement
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
Bin Wang,
Yuanyuan Wei,
Yiwei Wang
Z

## Slide 18: Summary
  The lattice of CEPC collider ring was designed with luminosity goal 5e34/cm^2/s/IP @ Higgs with 30 MW/beam.
  RF region: 1st priority of the Higgs running and flexible switching
  ARC: New aberration correction scheme in ARC region. The distribution of sextupoles for Higgs & ttbar modes (90 deg cell) allowed to select –I sextupole pairs for W &Z modes (60 deg cell) .
  IR: Crab waist collision, local chromaticity correction, asymmetric interaction region
Dynamic aperture w/o error for four modes achieve the requirement of energy acceptance.
Dynamic aperture w/ main errors for Higgs and Z modes achieve the requirements.

## Slide 19: backup

## Slide 20: Location of the dumping system
Dumping system for collider ring
  Seems not necessary to be close to IP
    Active machine protection for the beam loss with time larger than multi turns
  Located at STR1 and STR2 or STR2 and STR3
    At least one dump for each collider ring
    STR4 for future option of ep collision
  Inner side of tunnel
    SPPC will locates outer side of CEPC
    Maintenance of the dump
Dumping system for booster ring
  Low charge bunches can be dumped by collimator
  Dumping for bunches of on axis injection can share the dump with collider ring
STR1
STR2
STR4
STR3