## Slide 1: MDI accelerator mechanics
Haijing Wang
On behalf of CEPC mechanics group
The 2022 CEPC MDI Workshop
30th Mar-1st Apr, 2023

## Slide 2: Outline
Integration of the MDI devices
Remote vacuum connector
SC magnet support system in cryostat
Movable collimators

## Slide 3: Integration of the MDI devices
The devices at MDI are integrated together.
  Detective angle: acos0.99
  IP chamber:-700mm~700mm
  Detector York length: 9620mm

## Slide 4: Integration of the MDI devices
All the devices are within the detective angle, acos0.99.
IP
Be-Al chamber
Z: -700~700mm
With 1 BPM inside
Remote Vacuum Connector
Z: 700~783mm
IP BPMs
Z: 855~950mm
Y chamber
Z: 783~855mm
Lumical body
Z: 940-1100mm
Q1a Q1b
Z: 1855~4440mm

## Slide 5: Integration of the MDI devices
Distance to detective angle
  IP chamber flange: 5.34mm
  RVC: 19.65 14.91mm
  Cryostat:26.49mm
Pressure tube of RVC has been added
IP chamber flange
RVC
BPM & cable
Lumical& support
Cryostat
Pressure tube of RVC

## Slide 6: Integration of the MDI devices
Vacuum layout
  Inner diameter at IP: 28 mm20mm
  Y-chamber cross section: circle (d40 mm)  racetrack (35mm-20mm)
Be
Al
Cu
IP chamber
Y chamber
Cryostat chamber
IP
IP BPM
Lumical
Water cooled
RVC
No forced cooling
RF bellows
Water cooled
Paraffin cooled

## Slide 7: Remote vacuum connector
Improved inflatable seal
Two layers of edge sealing
Replace the sealing membranes by two layers of edge sealing.
RF finger
Dimensions:
Transversal: Max. ϕ174mm
Longitudinal: ~83mm
Low vacuum

## Slide 8: Remote vacuum connector
Difficulties:
  Space limitation, leak rate, thermal dissipation…
  For sealings with the same F/L
  Decrease roughness A
  Perimeter L: determined by layout
  Decrease gasket hardness copper instead of SS
  Decrease the seal width : knife-edge seal
Demonstrated by J-PARC
Picture from Roth Alexander, Vacuum technology
The leak rate is estimated in theory in the TDR stage. No prototype has been developed.
  Can endure a heat flux of 1 W/cm2, the HOM power is acceptable.

## Slide 9: SC magnet support system
The cryostat is about 5.6m long. The cantilever length is 5283mm.
  Movement mechanism: has high precision rails, motion range 6 m.
  Support bed: steel bed with ribs inside.
  Adjusting mechanism: Auto driven wedge jacks for adjusting.
The resolution requirement of the adjusting mechanism < 5 μm.
Key points
  Stability (static and modal)
  Accuracy
  Easy-operating
  Dimensions

## Slide 10: SC magnet support system
Vacuum vessel
Helium vessel
Support rods
Q1a
Q2
Anti-solenoid
Q1b
Thermal shield
After the optimization of the supports in the cryostat, the total weight of the cryostat and the devices inside is 2790 Kg.
Material | Density (kg/m3) | Specific stiffness (Nm/kg 103)
Stainless steel | 8000 | 25
Ti-6Al-4V | 4430 | 25.7
A6061 (Al) | 2700 | 25.5
Copper (Cu) | 8960 | 12.3
Material | Density (kg/m3) | 
Stainless steel | 8000 | 25
Ti-6Al-4V | 4430 | 25.7
A6061 (Al) | 2700 | 25.5
Copper (Cu) | 8960 | 12.3
Candidate materials for supports inside

## Slide 11: SC magnet support system
Magnets to helium vessels
  Skeleton with outer ring support can minimize weight and reducing deformation.
Helium vessel to vacuum vessel
  Support blocks, 60mm x 20mm.
Aim: minimize the SC magnets deformation, enhance stability.
Sketch of skeleton support
Sketch of support blocks
Models | materials
Q1a/Q1b/Q2 | Nb-Ti alloy+ SS + FeCoV
Anti-solenoid | SS + Cu + AL
Vessels | SS
Magnet supports | SS
Vacuum chamber | SS

## Slide 12: SC magnet support system
G
Fz1
Fz2
Fz3
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.

## Slide 13: SC magnet support system
Magnet support | uneven deformation in Q1a (um) |  | uneven deformation in Q1b (um) |  | uneven deformation in Q2 (um) |  | Max. displacement of cryostat (mm) | 
 | Vertical | Horizontal | Vertical | Horizontal | Vertical | Horizontal | Vertical | Horizontal
TDR s-o support | 5 | 1.2 | 15 | 3.5 | 14 | 4 | 1.79 | 0.08
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.
Requirements:
  The alignment accuracy of SC magnets: ≤100 μm.

## Slide 14: SC magnet support system
No. of order | Frequency (Hz) | Mode
1 | 14.5 | Integral vertical sway
2 | 14.9 | Integral horizontal sway
3 | 51.7 | Integral vertical wave
4 | 53.7 | Integral horizontal wave
5 | 89.7 | Vertical wave of helium vessel
6 | 91.4 | Horizon wave of helium vessel

## Slide 15: SC magnet support system
Auxiliary support of cryostat
  Auxiliary constraint: V groove, translational in beam direction
  Range: 4 m to 5.9 m from IP (on inner wall of detector yoke)
  Can decrease the uneven deformation as well as enhance natural frequency largely.
Harmonic response
  Frequency 1~50 Hz.
  The auxiliary support can reduce the response amplitude largely.
Natural frequency VS support location
Uneven deformation VS support location
* Not for the latest magnet version. Updates are undergoing.

## Slide 16
Modification suggestion of vacuum chamber for the collider ring，Liu Yu Dong for CEPC accelerator physical group，2021/3/25
37.5mm
28mm
28mm
28mm
The synchrotron radiation load reduced from 9.3KW to 7.5KW
The inclination of block ramp smaller.
The thermal power density decreases
Beam loss reduced
reduce the temperature
reduce stress
The diameter in the X direction smaller
The cross section of the vacuum pipe is changed from ellipse to circle, and the collimator is adjusted accordingly.
Movable collimators
Collimators for background decreasing

## Slide 17
183℃ （original version, i.e. ellipse vacuum pipe） → 147℃
129.31MPa (original version) → 89.7MPa
1.89mm (original version)→ 1.53mm
Movable collimators

## Slide 18
141℃ (original version) → 124℃
132MPa (original version) → 110MPa
Movable collimators

## Slide 19: Conclusion
We have updated the cryostat and MDI layout.
  The SC magnet supports inside the cryostat are under design and optimization.
  The stability of the TDR cryostat is being studied.
  Integral FEA with thermal contraction and adjustment components will be studied next step.
  Structure design and thermal-mechanics analyses of movable collimators for background decreasing have been done.

## Slide 20
Thanks for your attention!