## Slide 1: Cluster Timing Analysis for Beam Test data
Shuaiyi Liu, Yaxin Shen, Guang Zhao, Linghui Wu, Mingyi Dong

## Slide 2: Content
Event Selection
Timing Analysis
  First Cluster Time Distribution
  First Cluster Time & Difference between First and Last Cluster Time 2D Histogram

## Slide 3: Definition of Q and RMS
Q=,
  a[i] means the amplitude of i-th bin
  The first and last several bins are removed due to abnormal values
RMS=
Run10, Ch5, gas90/10, 45°
RMS distribution
Q distribution

## Slide 4: Event Selection Via RMS&Q 2D Histogram
Almost noises
Validated event by event
Almost signals
Validated event by event
Q>2.5 can be used to remove noise
Run10, Ch5, gas90/10, 45°
RMS vs Q
RMS vs Q
(events with RMS<0.004 removed)

## Slide 5: Event Selection with Q
Run10, Ch5, gas 90/10, 45°
ncount distribution of noises
(Q<2.5)
ncount distribution of signals
(Q>2.5)

## Slide 6: Timing Analysis: First Cluster Time ,0°
Blue arrow: track
Brown square: tube
Run11, Ch5, gas90/10, 0°
Peaks with t<t0 could be recognized as noises
Time distribution of the first peak (TFirst)

## Slide 7: Timing Analysis: Ncount vs TFirst, angle=0
Ncount vs TFirst
Slope: -0.128
Run11, Ch5, gas90/10, 0°, 2.0G, low statistics
Profile of Ncount vs TFirst
TFirst (ns)
TFirst (ns)
Ncount
Ncount

## Slide 8: Timing Analysis: Ncount vs TFirst, angle=0
Run13 Ch5 gas90/10 0°, 1.5G, low statistics
Ncount vs TFirst
Profile of Ncount vs TFirst
TFirst (ns)
TFirst (ns)
Ncount
Ncount
Might be related with cluster density (next page)

## Slide 9: Timing Analysis: TLast-TFirst vs TFirst, angle=0
Run11, Ch5, gas90/10, 0°
ΔT vs TFirst (ΔT = TLast – TFirst)
TFirst (ns)
ΔT (ns)
ΔT (ns)
For the track with drift distance = d
  The drift distance of the first cluster: dF = d
  The drift distance of the first cluster: dL = sqrt(d2+R2)
  Cluster density in time is related with Δd (=dL-dF)
Δd gets smaller as d increases, i.e. cluster density increases as d increases
R
Δd vs d

## Slide 10: TFirst distribution with angle=45
Blue arrow: track
Brown square: tube
Run10, Ch5, gas90/10, 45°
Distribution of TFirst

## Slide 11: Ncount vs TFirst with angle=45
Slope: -0.068
Run10, Ch5, gas90/10, 45°
Ncount vs TFirst
Profile of Ncount vs TFirst
TFirst (ns)
TFirst (ns)
Ncount
Ncount

## Slide 12: Timing Analysis: TLast-TFirst vs TFirst, angle=45
Run10 Ch5 gas90/10 45°
ΔT vs TFirst (ΔT = TLast – TFirst)

## Slide 13: Summary
Event Selection with Q>2.5 can be used to select good signals
Timing Analysis:
  Variation in Ncount over time of 1st cluster observed
    For angle=0, possible related with cluster density and need further study
    For angle=45, the correction on track length should be taken into account
Next
  Correction on track length and drift distance in the analysis
Discussion
  Calibration on drift distance and incident angle is important to improve the dN/dx performance. Tracking information is helpful
  A multi-layer DC prototype would benefit the data analysis in the test

## Slide 14: Backup

## Slide 15: BackUp: Run10 Ch5 TimePlot 0

## Slide 16: High Event Timeplot
Blue arrow: track
Brown square: tube
Run13 Ch5 gas90/10 0° 1cm sampling rate=1.5

## Slide 17: High Event Timeplot
Run13 Ch5 gas90/10 0° 1cm