## Slide 1
Beam-Beam Effects in CEPC
Yuan Zhang
12-16. June. 2023, Hongkong, CEPC Accelerator TDR International Review
Contributors:
Na Wang, Yiwei Wang, Dou Wang, Huiping Geng, Zhiyuan Li (IHEP)
Kazuhito Ohmi(KEK), Chuntao Lin (IASF), Demin Zhou(KEK)
M. Zobov(INFN/LNF)
Thanks:
D. Shatilov, K. Oide, M. Migliorati

## Slide 2: Content
Introduction
Pure Beam-Beam Interaction
Combined effect with Impedance
Combined effect with Lattice
Summary

## Slide 3
Introduction
This talk is about Beam-Beam Interaction (sec4.2.2)
This talk relates to the TDR sec4.1, sec4.2.1, sec4.2.3
The content relates to the “charge letter” item
  Are the accelerator system design goals well defined? Have the goals been reached in the TDR?
  Are the accelerator physics issues adequately addressed?

## Slide 4
Design Parameters
 | Higgs | Z | W | ttbar
Beam Energy [GeV] | 120 | 45.5 | 80 | 180
Damping Decrement (x/y/z, SR) | 0.75/0.75/1.5 [] | 4/4/8 [] | 2.2/2.2/4.4 [] | 2.5/2.5/5 []
[m/mm] | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
[nm/pm] | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
(SR/BS) [mm] | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
(SR/BS) [%] | 0.1/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.2
 | 1.2 | 2.5 | 1.2 | 1.2
Piwinski Angle | 4.88 | 24.23 | 5.98 | 1.23
 | 0.0049 | 0.035 | 0.062 | 0.078
Bunch Population [] | 13 | 14 | 13.5 | 20
 | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
Bunch Number | 268 | 11934 | 1297 | 35
Luminosity/IP [] | 5 | 115 | 16 | 0.5
 | Higgs | Z | W | ttbar
Beam Energy [GeV] | 120 | 45.5 | 80 | 180
Damping Decrement (x/y/z, SR) |  |  |  | 
 | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
 | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
 | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
 | 0.1/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.2
 | 1.2 | 2.5 | 1.2 | 1.2
Piwinski Angle | 4.88 | 24.23 | 5.98 | 1.23
 | 0.0049 | 0.035 | 0.062 | 0.078
 | 13 | 14 | 13.5 | 20
 | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
Bunch Number | 268 | 11934 | 1297 | 35
 | 5 | 115 | 16 | 0.5
2 IPs, 2x16.5 mrad
100 km

## Slide 5
R. Assmann and K. Cornelis, EPAC’00
CEPC-Z
CEPC-W
CEPC-H
CEPC-ttbar

## Slide 6: Crab-waist collision
P. Raimondi , 2nd SuperB Workshop, March 2006
M. Zobov et al., PRL 104, 174801 (2010)

## Slide 7: Beamstrahlung Effect & 3D flip-flop
Synchrotron radiation during beam-beam interaction
High energy photon -> Momentum acceptance -> Lifetime
Longer bunch length and Higher energy spread
Asymmetrical beam blowup: 3D flip-flop
V. I. Telnov, PRL 110, 114801 (2013)
A. Bogomyagkov et al., Phys. Rev. ST Accel. Beams 17, 041004 (2014)
D. Shatilov, ICFA Beam Dyn. Newslett. 72, 30 (2017).

## Slide 8: Simulation Tool
Linear Arc Map with SR radiation
One turn map including general chromaticity
Horizontal crossing angle: Lorentz boost map
Bunch slice number is about 10 times Piwinski angle
Slice-Slice collision: Synchro-beam mapping method (or PIC)
Synchrotron radiation during collision
Longitudinal wakefield
Transverse wakefield
IBB
K. Hirata et al., PA 40, 205-228 (1993)
K. Hirata, PRL, 74, 2228 (1995)
Y. Zhang et al., PRST-AB, 8, 074402 (2005)
Y. Seimiya et al., PTP 127, 1099 (2012)
K. Ohmi, IPAC16
Y. Zhang et al., PRAB 23, 104402, (2020)

## Slide 9: Luminosity versus horizontal tune
ttbar
Higgs
W
Z
The design luminosity could be achieved in the pure beam-beam simulation.

## Slide 10: Beamstrahlung Lifetime vs Momentum Acceptance
* If particles exceed the momentum acceptance are checked just after collision.
Z
W
higgs
ttbar
K. Ohmi, etal., IPAC 14
The pure beam-beam simulation presents a goal value for Lattice optimization.

## Slide 11: Beam-Beam Performance & Beamstrahlung lifetime vs bunch population (higgs/ttbar)
The beam-beam parameter does not stature at design bunch population
The beamstrahlung lifetime evaluation shows that it is very sensitive to the bunch population
* If particles exceed the momentum acceptance are checked just after collsion.

## Slide 12: Beam-Beam Performance vs bunch population （W/Z）
The beam-beam parameter does not stature at design bunch population

## Slide 13: Asymmetric Collision: Higgs/ttbar
Lifetime
Luminosity
ttbar
ttbar
Higgs
Higgs
* If particles exceed the momentum acceptance are checked just after collision.
The weak beam’s lifetime would be about only half with collision between 100% vs 90% bunch population. (design 100% vs 97%: ~20% lifetime reduction)
The luminosity scale linearly with the weak beam’s bunch population

## Slide 14: Asymmetric Collision: Z/W
Z
Z
W
W
The beamstrahlung lifetime induced by pure beam-beam interaction would not be a serious issue.
The luminosity scale linearly with the weak beam’s bunch population
Lifetime
Luminosity

## Slide 15: Horizontal Coherent Beam-Beam Instability (X-Z instability)
1. In the collision scheme with Crab Waist and Large Piwinski Angle the luminosity and tune shifts strongly depend on the bunch length
2. For the future circular colliders with extreme beam parameters in collision several new effects become important such as beamstrahlung, coherent X-Z instability and 3D flip-flop. The longitudinal beam dynamics plays an essential role for these effects
K. Ohmi, Int. J. Mod. Phys. A, 31, 1644014 (2016).
K. Ohmi and et al., PRL 119, 134801 (2017)
N. Kuroo et al, PHYS. REV. ACCEL. BEAMS 21, 031002 (2018)
K. Ohmi, eeFACT 2018

## Slide 16: Combined effect of beamstrahlung and longitudinal impedance in stable tune areas
Semi-analytical calculations are in reasonable
agreement with numerical modeling
Bunch length
Energy spread
Longitudinal Impedance induces
Longer bunch length
Lower energy spread
Lower incoherent synchrotron tune
D.Leshenok and et al. PRAB 23, 101003 (2020)
Y. Zhang et al., PRAB 23, 104402, (2020)

## Slide 17: X-Z instability with and without beam coupling impedance
After the horizontal beta function reduction from 0.2 m down to 0.15 m
By including the impedance stable areas become narrower and are shifted
(CEPC-CDR-Z)
17
w/o ZL
w/ ZL, mode
Y. Zhang etal., PRAB 23, 104402, (2020)
C. Lin etal.,, PRAB 25, 011001 (2022)

## Slide 18: Parameter Optimization for X-Z instability
Different modes of CEPC has been well optimized to mitigate the X-Z instability
Courtesy of D. Shatilov
Larger is preferred
K. Oide， IPAC2017
D. Shatilov, ICFA Beam Dyn.Newslett. 72 (2017) 30-41
Y. Zhang et al., PRAB 23, 104402, (2020)
Courtesy of D. Shatilov

## Slide 19: w/ transverse impedance (ZT): Higgs/ttbar
ttbar:
No clear effect from transverse impedance.
Higgs:
Only X-Z instability
Stable area width is reduced a little (ZT only applied 1 kick)

## Slide 20: w/ transverse impedance (ZT): Z/W
W:
Only X-Z instability
stable area is large enough
Z:
No stable working points.
There exist very strong blowup in both X/Y direction

## Slide 21: Z: Only horizontal impedance (+ZL)
Simulation
Analysis, ZT kick applied at IP
Courtesy of Chuntao Lin and Na Wang
In horizontal direction, considering ZX
the instability growth rate is faster,
unstable tune area increases
Stable tune area is large enough (w/ZX)
Simulation and analysis agree well.
Kick number of wake field affect the result
In horizontal direction, smooth distributed impedance nearly does not squeeze the stable tune area serious
A very local impedance may squeeze the stable area.

## Slide 22: Vertical mode coupling with ZT(-mode)
TMCI threshold is reduced from about 21e10 to 11e10
Accepted by PRAB

## Slide 23: Mitigation of Vertical TMCI (BB+ZT)
Growth rate of vertical centroid versus tune with different vertical chromaticity. Both transverse and longitudinal
impedance are considered.
vertical beam size versus asymmetric vertical tunes with different vertical chromaticity. Both transverse and longitudinal impedance are considered. One beam’s vertical working point is fixed at 0.610.
Chromaticity
Asymmetrical Tunes + Chromaticity
Accepted by PRAB

## Slide 24: More measures to suppress vertical TMCI
Hourglass effect
  (K. Ohmi)
Courtesy of K. Ohmi
Feedback + Chromaticity
Resistive feedback, damp rate=0.05 + Qy’=10
np=21e10 is stable with 1.5 times higher transverse impedance
Y. Zhang, HK-IAS, 2023
K. Ohmi et al., submitted to PRAB

## Slide 25: Combined effect considering realistic lattice
Case (a) has a larger DA but a shorter beam lifetime,
while case (b) is opposite.
lattice nonlinearity
strong synchrotron radiation
Beam-beam interaction
beamstrahlung effect
Diffussion Map:
Better Lifetime
Better Lifetime
Diffussion Map Analysis of Four Cases
J. Wu et al., NIMA 959 (2020) 163517

## Slide 26: A lifetime optimization sample
w/o BB and BS
Survival particles:
861
w/ BB and BS
Survival particles:
1000
Survival particles:
962
50k turns, 1k macro-particles @injection point
w/ BB and BS
32 families of sextupoles in Arc
Optimization of diffusion
Huiping Geng, Yiwei Wang

## Slide 27: Code development for future work
Tracking with realistic lattice + Strong Beam-Beam
Based on SAD,
  Supports element: DRIFT, BEND, QUAD, SEXT, MULT, SOL, CAVIT, APERT
  Support lattice generated by SAD
  Lattice error could be included
CPU and GPU.
  MPI or CUDA to parallelize multi-particle tracking
Collective effects (MPI) could be included
GPU:NVIDIA A100 FP64：9.746 TFLOPS (1:2)
CPU: Intel(R) Xeon(R) Gold 6348 CPU @ 2.60GHz
SuperKEKB lattice was used:
The acceleration ratio for particle tracking：
GPU /CPU(single core) ≈ 250
Some initial benchmark comparing with SAD has been done
SKEKB LER/HER lattice + Strong-Strong Collision
Zhiyuan Li, K. Ohmi and Demin Zhou

## Slide 28: Summary
Machine parameters are evaluated by strong-strong simulation
X-Z instability is well suppressed even considering longitudinal impedance
Strong vertical instability exist at Z with transverse impedance. Simulation and analysis has helped understanding the physics. Mitigation schemes have been studied.
Disagreement between dynamic aperture and lifetime have been found. Diffusion analysis method is presented to optimize the lifetime. (lattice+beambeam+beamstrahlung)
More self-consistent simulation code is being developed for future study
Error effects and necessary luminosity tuning knob are still not yet studied.

## Slide 29
BACKUP

## Slide 30
Main Parameters

## Slide 31: Lifetime evaluation (pure beam-beam interaction)
Watch Point before vs after IP

## Slide 32: Crab Waist strength
ttbar
Higgs

## Slide 33: Different Horizontal tune
Qx+=0.567
Asymmetric
Symmetric

## Slide 34: CEPC Only Zx(+ZL) @ Qx=0.562
X-Z instability is first excited
Bunch length is shorter
X-TMCI-like instability is then excited
Y is blowup due to stronger beam-beam interaction
It has been simulated that w/o BS (but keep same bunch length), the TMCI-like instability would not appear.
Behavior at unstable working point

## Slide 35: CEPC Only Zy(+ZL) Qx=0.567
Y-TMCI-like instability is first excited
Bunch length is shorter
X-Z instability is excited
Stronger Y blowup due to strong beam-beam
It has been simulated that w/o BS (but keep same bunch length), the X-Z instability would not appear.
Behavior at unstable working point
mode