## Slide 1
CEPC collective instabilities in collider ring, booster and damping ring
Na Wang
12-16. June. 2023, Hongkong, CEPC Accelerator TDR International Review
Contributors:
Yuan Zhang, Yudong Liu, Haisheng Xu, Saike Tian, Yuting Wang, Sen Yue, Jintao Li (IHEP)
Chuntao Lin (IASF)

## Slide 2
Introduction
This talk is about impedance and collective effects evaluations in the accelerator physics design.
This talk relates to the TDR chapters:
  Ch 4.2.3 Beam Instability and Beam Lifetime
  Ch 5.2.2 Beam Instability
  Ch 6.2.2.4 Impedance and Beam Instability
The content relates to the “charge letter” item:
  2. Are the accelerator physics issues adequately addressed?

## Slide 3
Accelerator Complex
Booster
Circ: 100km
Ek: 30 180GeV
I0: 10.5 0.1mA
Np: 4.9 127109
Damping ring
Circ: 147m
Ek: 1.1GeV
I0: 12.4 mA
Np: 0.951010
Collider rings
Circ: 100km
Ek: 45.5 180GeV
I0: 804 3.3mA
Np: 13  201010
Motivations:
Beam stable reach the design bunch population and beam current.
Beam quality degradation acceptable for the design luminosity.
Avoid hardware damage due to parasitic heat loss from the beam.

## Slide 4: Content
Collider Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Bunch lengthening, MWI, TMCI, Coupled bunch instabilities, Beam ion, Electron cloud
Booster Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Single/Coupled bunch instabilities, CSR
Damping Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Single bunch instabilities

## Slide 5: Content
Collider Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Bunch lengthening, MWI, TMCI, Coupled bunch instabilities, Beam ion, Electron cloud
Booster Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Single/Coupled bunch instabilities, CSR
Damping Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Single bunch instabilities

## Slide 6: Main beam parameters (30MW)
Parameter [unit] | Higgs | Z | W | tt
Beam energy Ek [GeV] | 120 | 45.5 | 80 | 180
Lmax/IP (1034cm-2s-1) | 5 | 115 | 16 | 0.5
Emittance (H/V) [nm/pm] | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Beam current [mA] | 16.7 | 803.5 | 84.1 | 3.3
Bunch number | 268 | 11934 | 1297 | 35
Bunch Population [1010] | 13 | 14 | 13.5 | 20
Momentum compaction p [10-5] | 0.71 | 1.43 | 1.43 | 0.71
Bunch length z (natural/total) [mm] | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) [10-4] | 10/17 | 4/13 | 7/14 | 15/20
Betatron tune x/y | 445.10/445.22 | 317.10/317.22 | 317.10/317.22 | 445.10/445.22
Synchrotron tune | 0.049 | 0.035 | 0.062 | 0.078
Radiation damping [ms] | 44/44/22 | 816/816/408 | 150/150/75 | 14/14/7
Design queries
Small p
Short natural z
Slow damping at low Ek

## Slide 7: Impedance modeling
Impedance modeling of the key vacuum components has been performed since the beginning of the project.
Resistive wall impedance
  Generated from finite conductivity of the vacuum chambers
  Calculated with theoretical formulas considering the NEG coating
Geometrical impedance
  Generated by the discontinuity of the vacuum chambers
  Calculated individually with 2D/3D simulation codes

## Slide 8: Impedance updates since release of CDR
Impedance model is updated regarding the change of the chamber cross section
elliptical  circular
DC value of the quadrupolar impedance dominates
Multilayer elliptical RW impedance model is derived to study influence of NEG coating [Y.T. Wang, NIM-A 1037, 166928 (2022)]
Incoherent tune shift due to the quadrupolar impedance is derived from beam oscillation equations [Y.T. Wang, NIM-A 1029, 166414 (2022)]
[y]frev
0.1Hz
Incoherent tune shift ~0.2 @Z

## Slide 9: Resistive wall impedance
Simplified formulas are derived for coated metallic chamber:
Multilayer formula from field matching:
Typical vacuum chamber: Cylindrical copper beam pipe with radius of 28mm and NEG (Non-Evaporable Getter) coating on its inner surface.
Multi-layer analytical formula is used [N. Wang, PRST-AB 10, 111003 (2007)].
NEG coating thickness of 0.2 m has been chosen to control their impedance contributions.

## Slide 10: Geometrical impedance
Main vacuum components considered in the impedance model.
RF cavity
Flange
Bellows
Pumping port
BPM
Gate Valve
Electro separator
Collimator

## Slide 11: Impedance model
ReZL
ImZL
ReZy
ImZy
The longitudinal broadband impedance is dominated by the RW, flanges and bellows.
The transverse impedance is dominated by the RW, flanges, bellows and collimators.
The impedance contributed by Inj./ext. elements, feedback kickers, absorbers, masks and collimators outside the IR region are not included.

## Slide 12: Impedance budget @z=3mm
Components | Number | Z¦¦/n, mΩ | L, nH | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.2 | 329.2 | 363.7 | 11.3
RF cavities | 60 | 0.5 | 24.8 | 101.2 | 0.5
Flanges | 37714 | 5.2 | 276.1 | 37.3 | 5.2
BPMs | 1808 | 0.04 | 2.0 | 9.5 | 0.2
Bellows | 15949 | 2.9 | 154.6 | 87.4 | 3.9
Gate Valves | 500 | 0.2 | 11.4 | 14.5 | 0.4
Pumping ports | 5316 | 0.3 | 18.4 | 2.3 | 0.2
Collimators | 16 | 0.04 | 1.7 | 23.4 | 0.6
IP chambers | 2 | 0.004 | 0.2 | 0.3 | 0.05
Electro-separators | 20 | -0.1 | -5.4 | 34.5 | 0.1
Taper transitions | 48 | 0.04 | 2.3 | 2.5 | 0.09
Total |  | 15.3 | 815.3 | 676.6 | 22.5

## Slide 13: Collective instabilities in the collider rings
Rough estimations of the instability threshold based on analytical criterions.
Impedance budget | 
Z¦¦/n, mΩ | 15.3
ky, kV/pC/m | 22.5
 | Higgs | W | Z | ttbar
Single bunch threshold (Long) Z¦¦/n [m] | 6.5 | 4.1 | 0.7 | 14.4
Single bunch threshold (Trans) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8
Multi-bunch SR threshold (Long) [GHzG] | 4.5 | 0.1 | 6.5E-4 | 171.2
Multi-bunch SR threshold (Trans) [G/m] | 3.0 | 0.08 | 8.9E-4 | 72.7
 | Higgs | W | Z | ttbar
Single bunch threshold (Long) Z¦¦/n [m] | 6.5 | 4.1 | 0.7 | 14.4
Single bunch threshold (Trans) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8
 | 4.5 | 0.1 | 6.5E-4 | 171.2
 | 3.0 | 0.08 | 8.9E-4 | 72.7
Although the criterion usually underestimates the threshold, we do observed its influence on the beam-beam interaction
[PRAB 23, 104402 (2020); PRAB 25, 011001 (2022)].
TMCI unstable
Tight narrowband impedance requirements for Z (at least ~two orders higher for the other energies)

## Slide 14: Bunch lengthening and microwave instability
Considering single beam, variations of bunch length and beam energy spread with bunch intensity are calculated by particle tracking simulations.
Higgs:
Instability threshold is around 701010 far above the design bunch current.
At the design bunch intensity, the bunch will be lengthened by ~30% due to the impedance.
Z:
Instability threshold is about half of the design bunch intensity.
At the design bunch current, the bunch length and the beam energy spread are increased by ~140% and ~35%, respectively.
Higgs
Higgs
Z
Z
141010
141010
131010
131010

## Slide 15: Other influences of longitudinal impedance
Longitudinal impedance (ZL) will induce incoherent synchrotron tune spread and bunch distortion.
Influence transverse single beam dynamics
Cross talk with beam-beam
Beamstrahlung significantly lengthen the bunch  mitigate the effect of the ZL on beam dynamics.
ZL shrinks and shifts the stable beam-beam interaction region More details discussed in Yuan Zhang’s talk (the design luminosity can be reached with careful parameter tuning).

## Slide 16: Transverse mode coupling instability (TMCI)
Transverse impedance (ZT) can induce fast instability through mode coupling, usually resulting in beam losses  Main constraint on single bunch current.
The instability @Z is investigated in three different ways
  Analytical estimation with classical Vlasov solver
    Mode analysis with and without impedance induced bunch lengthening
  Macro particle simulations and mitigations
    Study the transverse beam dynamics more consistently including the longitudinal impedance
  Analytical estimation considering the longitudinal perturbations
    Mode analysis with perturbations from ZL, as well as lengthened bunch from beamstrahlung.
Impedance budget | 
ky, kV/pC/m | 22.5
 | Higgs | W | Z | tt
Single bunch threshold (Trans) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8

## Slide 17: TMCI – Classical Vlasov solver
Analytical estimations show that threshold current will increase when consider impedance bunch lengthening. The instability is supposed to be further detuned if consider further bunch lengthening due to the beamstrahlung. However ….
Design
141010
W/O ZL bunch lengthening
Design
141010
W/ ZL bunch lengthening

## Slide 18: TMCI – Consistent macroparticle simulations
Particle tracking simulations performed with Elegant shows that the TMCI get more unstable when including the longitudinal impedance
  Without ZL: TMCI threshold91010 (consistent between simulation and theory)
  With ZL: TMCI threshold  61010 (much lower than the theoretical estimation only with bunch lengthening: 191010, shift of the mode 0 below the threshold still consistent)
W/O ZL
W/ ZL

## Slide 19: TMCI – Possible mitigations
Positive chromaticity  – negative effect
  Head-tail phase shift over the bunch <1, high order TMCI modes could be excited with large 
Lower longitudinal perturbations – limited increase of the threshold
  With only RW or ZL/2, the TMCI threshold is increased from 10nC to 11.5nC
Transverse bunch-by-bunch feedback – effective
Beamsstrahlung bunch lengthening – effective
Threshold beam current decreases with increase of chromaticity
Longitudinal impedance reduced by a factor of 2, and transverse impedance unchanged
Ith: 10nC->11.5nC
Feedback kick=-dp/2p=0.05, =10
Np=21e10 is stable with 1.5 ZT

## Slide 20: TMCI – Mode analysis with long. perturbations
Considering longer bunch with beamstrahlung
  TMCI threshold without ZL is increased to 221010 due to lengthened bunch;
  Including ZL, the higher order modes shift to mode 0 with wider bandwidth, and TMCI threshold is decreased to 191010  TMCI stable with beamstrahlung (Consistent study of ZT and beam-beam was discussed in Yuan Zhang’s talk)
W/O ZL
W/ ZL
[C.T. Lin, PRAB 25, 011001 (2022)]
N0=251010

## Slide 21: Coupled bunch instabilities
Transverse resistive wall instability
 Dominant due to large circumference
Other narrowband impedances
 High order modes of the RF cavities
 Impedances of flanges, bellows, gate valves, and BPMs are well below the SR threshold
 Impedance of the electro separators and the IP chambers requires further investigations
 | Higgs | W | Z | tt
Multi-bunch SR threshold (Long) [GHzG] | 4.5 | 0.1 | 6.5E-4 | 171.2
Multi-bunch SR threshold (Trans) [G/m] | 3.0 | 0.08 | 8.9E-4 | 72.7
 | Higgs | W | Z | tt
 | 4.5 | 0.1 | 6.5E-4 | 171.2
 | 3.0 | 0.08 | 8.9E-4 | 72.7

## Slide 22: Transverse resistive wall instability
Mainly determined by the zero-frequency resonance of the transverse RW impedance
n=11616
n=11615
n=11617
n=11618
f [kHz] | Mode index | Growth t [ms]
-2.338 | 11616 | 2.2 (7 turns)
-5.335 | 11615 | 3.2 (10 turns)
-8.332 | 11614 | 4.0 (12 turns)
-11.330 | 11613 | 4.6 (14 turns)
Tough requirement on feedback damping (broadband feedback + mode feedback)
First few unstable modes for Z:
 [ms] | Higgs | Z | W | tt
instability growth time | 400 | 2 | 38 | 3060
SR damping time | 44 | 816 | 150 | 14

## Slide 23: RF HOMs
For the operation modes of Higgs, W and low luminosity Z (with total beam power of 10 MW), the 2-cell 650MHz RF cavities will be adopted.
  The Qe of the longitudinal and transverse HOMs below the cutoff frequency are measured.
  The impedance is above the SR threshold for Z in both longitudinal and transverse planes. In the resonant case, the instability has a growth rate of 114 ms and 19 ms, respectively.
  The W operation mode will also be unstable in transverse when consider only SR damping. In the resonant case, the instability has a growth rate of 105 ms.

## Slide 24: RF HOMs (cont.)
For the high luminosity Z, the RF cavities will be replaced by the 1-cell cavities.
  HOMs can be well damped (loaded Q of 100 has been considered) below the threshold that determined by the SR damping.

## Slide 25: Beam ion effects
Trapped ions can induce bunch centroid oscillation and emittance growth.
The possibility of ion trapping and fast beam ion instability are investigated.
With vacuum pressure of 1nTorr, and CO+ has been considered as the only ion species
Consider multi bunch train filling pattern, the instability growth calculated by the analytical theory for W and Z are faster than SR damping
Build-up of ions along the bunch train
Parameters | Higgs | Z | W | tt
Lsepion/c0 | 6.2 | 0.7 | 2.4 | 14.7
ion, ave[e11 m-3] | 0.6 | 4.1 | 0.8 | 0.1
e [ms] | 7.9 | 0.1 | 1.9 | 105.4
H [ms] | 44.1 | 4.3 | 24.3 | 220.5
SR damping [ms] | 44 | 850 | 156 | 14
FB damping [ms] | 1.0 |  |  | 
y | 0.0006 | 0.02 | 0.002 | 0.0001

## Slide 26: Ion trapping for Z
Linear theory indicates that ions with relative molecular mass larger than the critical mass Ax,y will be trapped.
With vacuum pressure of 1 nTorr and uniform bunch filling:
  Only CO2+ will be trapped at the locations around IP with large beta function y.
  The total percentage of the region with trapped ions is less than 0.1%.

## Slide 27: Macro-particle simulations for Z
With uniform filling pattern, ion instability is checked at different locations.
  Both H and V beam centroid oscillation amplitude increased to larger than 0.1 in few turns, then saturate at around the scale of beam size.
Horizontal
Vertical
x/y=69/96m
Horizontal
Vertical
x/y=151/4.4km
Horizontal
Vertical
x/y=0.13/9E-4m

## Slide 28: Macro-particle simulations for Z (cont.)
Filling pattern: 144 bunch trains, each train contains 83 bunches with spacing of 23ns
Multi-train filling is effective in mitigating the beam ion instability. Transverse beam size is almost unchanged, but with some small oscillations  bunch by bunch feedback could suppress the betatron oscillations if needed.
x/y=69/96m
Horizontal
Vertical
Beam centroid oscillation amplitude
Transverse beam size

## Slide 29: Electron cloud effects
Influence on the machine performance
  Single bunch fast head-tail instability – coherent motion of a bunch and local electrons
  Coupled bunch instabilities – Coherent motion of bunch train and electron cloud
Parameters |  | Higgs | Z | W | tt
Beam line density | beam [1013 m-1] | 2.3 | 2.2 | 2.2 | 3.6
Beam size | x/y [m] | 151/6.8 | 116/8.3 | 209/9.2 | 224/13.0
RMs bunch length | z [mm] | 2.3 | 2.5 | 2.5 | 2.2
Synchrotron tune | s | 0.049 | 0.035 | 0.062 | 0.078
Electron osc. period | ez/c | 17.7 | 19.4 | 13.7 | 12.7
Threshold electron density | e, th [1011 m-3] | 7.3 | 1.4 | 4.4 | 17.4
Coupled bunch instability growth time (SEY=1.2) |  [ms] | >300 | 3 | / | /
[K. Ohmi, PRE 65, 016502 (2001)]
[F. Zimmerman, IPAC 2001]

## Slide 30: Electron cloud build-up
The coating to SEY<1.3 is necessary for the restriction on ECI
Higgs mode ()
Z mode: Lsep=23ns
Secondary electron yield
Density
Higgs mode: Lsep=591ns

## Slide 31: Measurements on SEY with NEG coating
Experimental apparatus
  applicable for both normal or cryogenic environment
Y.D. Liu, talk in ECLOUD2022
Cu with TiZrV coating
Cu with TiZrHfV coating
The SEY of NEG coating (thickness: 200~400nm) can be decreased to 1.2 by backing treatments at 300℃ for an hour.

## Slide 32: Summary on the Collider
Impedance model has been developed for the collective effects studies.
Potential restrictions from the collective effects and their mitigations are investigated  no apparent show stoppers for Higgs, W and tt
 Important restriction for Z – performance can be reached with the mitigations
:
Instability mechanism | Status and mitigation strategies
Microwave instability | 71010 <=141010, ZL is coupled with beam-beam brightness degradation for some working point  mitigations: careful parameter tuning.
Transverse mode coupling instability | 61010 <=141010, ZY is coupled with beam-beam Restrict bunch current and beam-beam unstable  mitigations: Bootstrapping injection, bunch-by-bunch feedback with positive , larger emittance.
Transverse resistive wall instability |  = 2ms << SR damping  Restrict total beam current  mitigations: bunch-by-bunch feedback (damping time ~1ms)
CBI due to the RF HOMs |  = 19ms, ¦¦ = 114ms, << SR damping  Restrict total beam current  mitigations: bunch-by-bunch feedback, HOM damper, 1-cell cavities for high luminosity Z
Beam ion effects |  = 4ms  Beam size blow-up, transverse tune shift  mitigations: multi-bunch train filling pattern, bunch-by-bunch feedback
Electron cloud |  = 3ms << SR damping  Beam size blow-up, transverse tune shift, restrict beam current  mitigations: bunch-by-bunch feedback, low SEY with NEG coating
Instability mechanism | Status and mitigation strategies
Microwave instability | 
Transverse mode coupling instability | 
Transverse resistive wall instability |  = 2ms << SR damping  Restrict total beam current  mitigations: bunch-by-bunch feedback (damping time ~1ms)
CBI due to the RF HOMs |  = 19ms, ¦¦ = 114ms, << SR damping  Restrict total beam current  mitigations: bunch-by-bunch feedback, HOM damper, 1-cell cavities for high luminosity Z
Beam ion effects |  = 4ms  Beam size blow-up, transverse tune shift  mitigations: multi-bunch train filling pattern, bunch-by-bunch feedback
Electron cloud |  = 3ms << SR damping  Beam size blow-up, transverse tune shift, restrict beam current  mitigations: bunch-by-bunch feedback, low SEY with NEG coating

## Slide 33: Discussions – Impedance evolving
The impedance model will be continuously updated along with the development of the hardware designs  impedance increase is expected with more contributors included.
Main constraints from impedance are focused on Z, enough safety margin is reserved for other energies.
Considering the elements been missing, a larger increment is expected in the transverse plane, while less influence in longitudinal.
TMCI restriction could be met
Better understanding of the physics and further mitigations: bunch-by-bunch feedback, positive , larger emittance
Limited influence on the transverse resistive wall instability
 Instability growth time from 2.2ms1.7ms with more detailed chamber material, collimators have little contribution
n=11616
n=11615
n=11617
n=11618

## Slide 34: Content
Collider Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Bunch lengthening, MWI, TMCI, Coupled bunch instabilities, Beam ion, Electron cloud
Booster Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Single/Coupled bunch instabilities, CSR
Damping Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Single bunch instabilities

## Slide 35: Impedance modeling
Resistive wall impedance
  radius=28mm, thick=2mm, Aluminum
Geometrical impedance
  Same as in the collider ring, excluding the components related to collision
Longitudinal impedance
Transverse impedance
ReZL
ImZL
ReZy
ImZy

## Slide 36: Collective instabilities in Booster
Instabilities are checked for both injection and extraction energies.
Single bunch effects
  Injection: Ek=30GeV, Max bunch population of 6.9109 @tt
  Extraction: Ek depends on operation mode, Max bunch population of 1.3 1011 @Higgs
Components | Z¦¦/n [mΩ] | kloss [kV/pC] | ky [kV/pC/m]
Resistive wall | 1.9/3.6 | 6.8/1.0 | 27.0/14.4
Geometrical | 0.1/8.1 | 12.2/1.0 | 28.2/16.0
Total | 2.0/11.7 | 19.0/2.0 | 55.2/30.4
Impedance budget @z=0.5mm/1.8mm
Threshold value | Injection @z=0.5mm | Extraction @z=1.8mm
Single bunch (longitudinal) Z¦¦/n [m] | >14 | >3.4
Single bunch (transverse) ky [kV/pC/m] | >190 | >36
Impedance threshold
  Some safety margin is reserved for TMCI
  Bunch lengthening is expected
RW and dominant geometrical impedance (bellows and flanges) extends to 200 GHz

## Slide 37: Coupled bunch instabilities
Transverse resistive wall instability
HOMs
  Much more relaxed compare to the collider ring at Z mode
Bunch-by-bunch feedback system is required.
 | Injection | Extraction | Collider-Z
Multi-bunch SR (longitudinal) [GHzM] | >5.7 | >113 | 0.7
Multi-bunch SR (transverse) [M/m] | >0.9 | >18 | 0.9
 | Injection | Extraction | Collider-Z
 | >5.7 | >113 | 0.7
 | >0.9 | >18 | 0.9
Growth time [ms] | Higgs | Z | W | tt
Injection | 1060 | 62 | 211 | 5865
Extraction | 2685 | 105 | 614 | 38397
SR damping at injection | 3100 |  |  | 
SR damping at extraction | 47.6 | 879 | 160 | 14.2

## Slide 38: CSR effect
CSR impedance and its induced MWI threshold are calculated, considering the quite short bunch length of ~0.5mm.
CSR impedance << resistive wall impedance.
MWI threshold due to the CSR effect are estimated analytically.
  K. Bane et al. (PRST-AB 13, 104402 (2010))
 | Inj. (linac beam: z0=0.4mm, =1.5E-3) | Inj. (equilibrium: z0=0.3mm, =2.5E-4) | Extraction
Threshold value | >7Ib, design | >0.8Ib, design | >9Ib, design
Extraction enough safety margin is reserved concerning CSR effect
Injection
  With injection beam parameters  threshold >> design current
  With equivalent beam parameters  the lowest threshold is comparable to the design current (only degrade beam quality during energy ramping + MWI is self-limiting  less critical)

## Slide 39: Content
Collider Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Bunch lengthening, MWI, TMCI, Coupled bunch instabilities, Beam ion, Electron cloud
Booster Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Collective instabilities
    Single/Coupled bunch instabilities, CSR
Damping Ring
  Impedance modeling
    Resistive wall, geometrical impedance
  Single bunch instabilities

## Slide 40: Impedance modeling
Resistive wall impedance
  radius=15mm, thick=2mm, Aluminum
Geometrical impedance
  Scaled from the collider ring (excluding the components related to collision)
  ZL*(28mm/15mm)*147m/100km, ZY *(28mm/15mm)3*147m/100km
Longitudinal impedance
Transverse impedance
ReZL
ImZL
ReZy
ImZy

## Slide 41: Single bunch effects
Impedance budget
Single bunch instabilities
  Enough safety margin reserved for TMCI
  Bunch lengthen is increased by 2%
@z=4.4mm
Threshold on Z¦¦/n [m] | 680
Threshold on ky [kV/pC/m] | 90
Components | Z¦¦/n, mΩ | kloss, V/pC | ky, kV/pC/m
Resistive wall | 10.2 | 0.7 | 0.2
Geometrical | 17.3 | 0.3 | 0.1
Total | 27.5 | 1.0 | 0.3
Meet the Requirements on the beam quality
  Increase on the bunch length, beam energy spread and emittance should be less than 20%

## Slide 42: Summary on Booster and Damping ring
Impedance model, including a rough geometrical impedance, has been developed and used for the instability studies in both booster and damping ring.
The Booster show no apparent constraints from single bunch effects, as well as CSR, however, bunch-by-bunch feedback is required to damp the transverse resistive wall instability.
No constraints observed from the Damping ring, and the impedance will lengthen the bunch by ~2%, which still meet the requirement from injections.

## Slide 43: Thank you!

## Slide 44: Backup slides

## Slide 45: Booster main beam parameters-Injection
Parameter [unit] | Higgs | Z | W | tt
Beam energy Ek [GeV] | 30 | 30 | 30 | 30
Beam current [mA] | 0.62 | 10.5 | 3.1 | 0.12
Bunch number | 268 | 3978 | 1297 | 35
Bunch Population [109] | 4.9 | 5.4 | 5.1 | 6.9
Momentum compaction p [10-5] | 1.12 | 1.12 | 1.12 | 1.12
Bunch length z (from Linac) [mm] | 0.4 | 0.4 | 0.4 | 0.4
Energy spread (from Linac) [10-4] | 15 | 15 | 15 | 15
Bunch length z (equilibrium) [mm] | 0.5 | 0.5 | 0.5 | 0.3
Energy spread (equilibrium) [10-4] | 2.5 |  |  | 
Betatron tune x/y | 321.23/117.18 |  |  | 
Synchrotron tune | 0.0943 | 0.0879 | 0.0879 | 0.14
Radiation damping x/y/z [s] | 3.1/3.1/1.5 |  |  | 

## Slide 46: Booster main beam parameters-Extraction
Parameter [unit] | Higgs | Z | W | tt
Beam energy Ek [GeV] | 120 | 45.5 | 80 | 180
Beam current [mA] | 0.56/0.98 | 9.5 | 2.85 | 0.11
Bunch number | 268 | 3978 | 1297 | 35
Bunch Population [109] | 4.4/127 | 5.0 | 4.6 | 6.2
Momentum compaction p [10-5] | 1.12 | 1.12 | 1.12 | 1.12
Bunch length z [mm] | 1.85 | 0.75 | 1.3 | 1.8
Energy spread [10-4] | 9.9 | 3.7 | 6.6 | 15
Betatron tune x/y | 321.27/117.19 | 321.27/117.19 | 321.27/117.19 | 321.27/117.19
Synchrotron tune | 0.0943 | 0.0879 | 0.0879 | 0.14
Radiation damping x/y/z [ms] | 47.6/47.6/23.8 | 879/879/440 | 160/160/80 | 14.2/14.2/7.1

## Slide 47: Damping ring main beam parameters
Parameter [unit] | Value
Beam energy Ek [GeV] | 1.1
Circumference [m] | 147
Beam current [mA] | 12.4 (24.8)
Bunch number | 4 (8)
Bunch Population [109] | 9.5
Momentum compaction p | 0.013
Bunch length z [mm] | 4.4
Energy spread [10-4] | 5.6
Betatron tune x/y | 7.70/8.54
Synchrotron tune | 0.0387
Radiation damping x/y/z [ms] | 11.4/11.4/5.7