## Slide 1
CEPC instrumentation and beam diagnostics development
Yanfeng Sui
On behalf of CEPC BI group
12-16. June. 2023, Hongkong, CEPC Accelerator TDR International Review

## Slide 2: Content
The design of CEPC beam instrumentation
  Booster and collider ring beam instrumentation
  Linac and damping ring beam instrumentation
The related R&D of beam instrumentation in IHEP
  Beam position monitor
  Feedback system
  Tune monitor
  ……
Summary

## Slide 3
Introduction
This talk is about CEPC beam instrumentation system
This talk relates to the TDR ch4.3.7, ch5.3.6, ch6.3.8 and ch6.4.6
The content relates to the “charge letter” item 3 and 6
  3. Are the accelerator complex design, the key technologies adopted, and the conventional facilities effective for achieving the performance goals?
  6.Regarding the key technology research and development, are critical technologies and components of the CEPC accelerator ready or will they be ready before 2026, through the R&D program being carried out, or achieved with the Light Source project undertaken by IHEP, for the eventual realization of the CEPC?
  …

## Slide 4
Item |  | Method | Parameter | Amounts
Beam position monitor | Closed orbit | Button electrode BPM | Measurement area (x  y)：±20mm×±10mm Resolution：<1um Measurement time of COD：< 4 s | 4252
 | Bunch by bunch | Button electrode BPM | Measurement area (x  y)：±40mm×±20mm Resolution：0.1mm | 
Bunch current |  | BCM | Measurement range：10mA / per bunch Relatively precision：1/4095 | 2
Average current |  | DCCT | Dynamic measurement range：0.0~1A Linearity：0.1 % Zero drift: <0.05mA | 2
Beam size |  | Double slit interferometer x ray pin hole | Resolution:0.2 µm | 4
Bunch length |  | Streak camera Two photon intensity interferometer | Resolution:1ps@10ps | 2
Tune measurement |  | Frequency sweeping method | Resolution:0.001 | 2
 |  | DDD | Resolution:0.001 | 
Beam loss monitor |  | PIN-diode | Dynamic range:120 dB Maximum counting rates≥10 MHz | 5800
Feedback system |  | TFB | Damping time<=1ms | 4
 |  | LFB | Damping time<=12ms | 4
Requirement List of the Collider Beam Instrumentation

## Slide 5
Requirement List of the Booster Beam Instrumentation
Item | Method | Parameter | Amounts
Beam position monitor | Button electrode BPM | Measurement area (x  y)：±20mm×±10mm Resolution：<20um(turn by turn) | 2408
Bunch current | BCM | Measurement range：10mA / per bunch Relatively precision：1/4095 | 2
Average current | DCCT | Dynamic measurement range：0.0~1A Resolution:50uA@0.6-8mA Linearity：0.1 % Zero drift: <0.05mA | 2
Beam size | Double slit interferometer x ray pin hole | Resolution:0.2 µm | 2
Bunch length | Streak camera Two photon intensity interferometer | Resolution:1 ps | 2
Tune measurement | Frequency sweeping method | Resolution:0.001 | 2
 | DDD | Resolution:0.001 | 
Beam loss monitor | Optical fiber | Space resolution:0.6m | 670
Feedback system | TFB | Damping time<=3ms | 2
Feedback system | LFB | Damping time<=35ms（50ms） | 2

## Slide 6: CEPC BST and collider beam instrumentation design
Beam position monitor
Beam current monitor
Synchrotron radiation based beam diagnostics
  Beam size and bunch length
Feedback system
Tune measurement
Beam loss monitor
Other systems

## Slide 7: Beam position monitor
With one Beam Position Monitor (BPM) near each quadruple, there will be 4252 BPMs in collider ring and 2408 BPMs in the booster
The best solution is a capacitive monitor with a button-like electrode. The four buttons will be mounted on a machined block of stainless steel welded into vacuum chamber.
The booster beam position monitors are the same as those of collider.
 | ttbar |  | Higgs |  | W |  | Z | 
 | Real | CST | Real | CST | Real | CST | Real | CST
Charge | 20e10 | 32 nC | 14e10 | 22.4 nC | 13.5e10 | 21.6 nC | 14e10 | 22.4 nC
Bunch length | 2.2/2.9 | 3 mm | 2.3/3.9 | 4 mm | 2.5/4.9 | 5 mm | 2.5/8.7 | 8.7 mm
Vpp | 635V |  | 359V |  | 295V |  | 179V | 
Z_500M | 0.22Ω |  | 0.22Ω |  | 0.22Ω |  | 0.22Ω | 
P_500M | -7.3dBm/320mA |  | -12.8dBm/170mA |  | -10.6dBm/216mA |  | -10.4dBm/224mA | 
Kx=Ky | 19.9mm |  | 19.9mm |  | 19.9mm |  | 19.9mm | 
Parameters |  | 
Bunch | Length | 4.1 mm
 | Charge | 1 nC
Mechanical | rb | 3 mm
 | tb | 4 mm
 | gb | 0.25 mm
 | b | 28 mm

## Slide 8: Beam position monitor
The BPM electronics can be categorized into two main parts: the Analog Front-End (AFE) for radio frequency signal conditioning and the Digital signal processing part (DFE).
The AFE consists of the RF signal conditioning module, ADC analog-to-digital conversion module, clock processing module, and pilot signal generation module. On the other hand, DFE includes the BPM signal acquisition module, signal conditioning module, data acquisition and transfer module, EPICS IOC module, and CSS control module.
About 6600 BPM electronics are required in CEPC and will installed in auxiliary tunnels.
Radiation-tolerant design of the electronics, the ADC and FPGA should be radiation resistant.

## Slide 9: Beam position monitor
50 stations along the storage ring in auxiliary tunnel and connecting with PC sever station with the star topology fiber optic network.

## Slide 10: Beam current monitor
Two types of beam current measurement systems are utilized: average beam current measurement and bunch current measurement.
The average current monitor employs Bergoz type DCCT (Direct-current current transformer) sensors.
Bunch by bunch electronics are used for measuring each bunch current.
Bergoz NPCT senor and front-end electronics
 | ttbar | Higgs | W | Z
Energy [GeV] | 180 | 120 | 80 | 45.5
Beam current [mA] | 3.3 | 16.7 | 84.1 | 803.5

## Slide 11: Beam current monitor
The ceramic gap functions as a capacitor to cut off wall current. The capacitor determines the cut-off frequency, restricting high-frequency signals through the sensor.
Loss factor and longitudinal impedance are simulated by CST Particle Studio for different gap sizes.
The simulation reveals that a 2 mm gap results in low impedance at around 0.3 GHz, while a 10 mm gap produces high impedance at about 1 GHz. In this case, 2mm gap is chosen for the structure.
Structure of DCCT vacuum chamber and longitudinal wake impedance of the structure

## Slide 12: Beam current monitor
A bunch current monitor equipped with a fast ADC sampling BPM sum signal is utilized to measure the bunch current and share the data with the injection control system for bucket selection.
To improve the luminosity, it is necessary to accurately measure and control the charge of each bunch, ensuring that the charge of each bunch in the storage ring is equal.
The core part of the AFE is its high-speed ADC. The front-end circuit receives the sum signal from BPM. The signal is sampled at a frequency of 650MHz. The digitized data is instantly transferred to the DFE.

## Slide 13: Beam size measurement
For a storage ring with high beam energy and a long bending radius, it can be challenging to separate SR light from the beam over a long distance. This makes it difficult to place diagnostic elements close enough to the source point. To overcome this challenge, the X-ray double slit interferometer is considered the best option for beam size measurement.
In the booster, beam sizes ranging from several hundreds of microns up to millimeters in both x and y directions. A visible light beam line will be constructed for beam size measurement
X ray energy：12keV
Light spot size：x 40e-6m y 5e-6m
Slits：Distance: d=200µm Width: a=8µm
Distance from source to slit: R=100m
Distance between observation point to slit 75m
Configuration for double slit X-ray interferometer
Typical interferogram and the intensity distribution curve in vertical direction
The synchrotron light diagnostic beamlines
SLDB-E
SLDB-P

## Slide 14: Bunch length measurement
Bunch by bunch measurement system to monitor the bunch length and its lengthening. Visible SR beam line should be necessary.
Resolution about 1ps（~10% of bunch length）, streak camera based on visible light will be used.
In order to protect the extraction mirror from the incidence SR power, only half upper visible light is reflected
The distance from the mirror to the dipole source is about 98m.
 | ttbar | Higgs | W | Z
Energy [GeV] | 180 | 120 | 80 | 45.5
Bunch length (SR/total) [mm] | 2.2/2.9 | 2.3/4.1 | 2.5/4.9 | 2.7/10.6

## Slide 15
Feedback system
Bunch by bunch system including frontend/backend electronics, digital signal processing electronics, amplifier and kicker. There are 3-directions feedback system in storage ring and booster.
Frontend electronics are frequency down-convert electronics to fit ADC. And back end electronics are frequency up-convert electronics to fit LFB kicker.
Schematic diagram of Feedback system

## Slide 16: Feedback system
The basic structure of transverse feedback kicker
Reflection parameter S11 of the TFB kicker
Transverse shunt impedance versus frequency. ~140KΩ@25MHz

## Slide 17: The power of transverse feedback
Parameter | Higgs | Z
Energy（GeV） | 120 | 45.5
Beta functions at pickup (m) | 250 | 250
Beta function at kicker（m） | 250 | 250
Number of kickers | 4 | 4
Revolution time（ms） | 0.33 | 0.33
RF frequency（MHz） | 650 | 650
Kicker shunt impedance（kΩ） | 140 | 140
Amplitude of oscillation（mm） | 0.2 | 0.2
Damping time（ms） | - | 1.0
Power(w) | - | 1460

## Slide 18: Feedback system
Parameter | Value | Parameter | Value
Beampipe radius R | 28 mm | Back cavity length | 27.44 mm
Back cavity radius | 56 mm | Cavity length | 303 mm
Ridge radius | 82 mm | Port angle | 15.3 deg
Pillbox cavity radius | 90 mm | Port base angle | 6.7 deg
Cavity gap | 91 mm | Barrier angle | 61 deg
Distance of feedthrough | 5 mm | Nose cone radius | 6 mm
Ridge length | 53.56 mm | Nose cone length | 7 mm
The schematic of the longitudinal feedback kicker
The reflection parameter S11 of the LFB kicker
The shunt impedance of the LFB kicker

## Slide 19
The power of longitudinal feedback
Parameter | Higgs | Z
Energy（GeV） | 120 | 45.5
Momentum compaction（） | 0.71 | 1.43
Longitudinal tune（m） | 0.049 | 0.035
Phase acceptance（mrad) | 1.7 | 1.7
RF frequency（MHz） | 650 | 650
Kicker shunt impedance（kΩ） | 2.6 | 2.6
Number of kicker | 4 | 4
Damping time（ms） | - | 65
Power(w) | - | 7720
Parameter | Higgs | Z
Energy（GeV） | 120 | 45.5
 | 0.71 | 1.43
Longitudinal tune（m） | 0.049 | 0.035
Phase acceptance（mrad) | 1.7 | 1.7
RF frequency（MHz） | 650 | 650
Kicker shunt impedance（kΩ） | 2.6 | 2.6
Number of kicker | 4 | 4
Damping time（ms） | - | 65
Power(w) | - | 7720

## Slide 20: Feedback system in the booster
As the beam pipe in booster has same size as it in collider, the design of TFB kicker for booster is the same as for collider. The required working bandwidth of feedback kicker is 20MHz, and the minimum shunt impedance within bandwidth is roughly 150kΩ.
Parameter | Value (z-injection) | Value (z-extraction)
Energy（GeV） | 30 | 45.5
Beta functions at pickup (m) | 120 | 120
Beta function at kicker（m） | 120 | 120
Number of kickers | 2 | 2
Revolution time（ms） | 0.33 | 0.33
RF frequency（MHz） | 650 | 650
Kicker shunt impedance（kΩ） | 150 | 150
Amplitude of oscillation（mm） | 0.3 | 0.3
Damping time（ms） | 10 | 10
Power(w) | 81.7 | 188

## Slide 21: Feedback system in the booster
After optimization, the longitudinal shunt impedance within the required bandwidth of 1.615~1.635GHz for the RF frequency of 1.3GHz in the booster is approximately 1800Ω, with a central frequency of 1.625GHz
Parameter | Value (z-injection) | Value (z-extraction)
Energy（GeV） | 30 | 45.5
momentum compaction（） | 1.12 | 1.12
Longitudinal tune(m) | 0.0879 | 0.0879
Phase acceptance（mrad） | 1.7 | 1.7
RF frequency（MHz） | 1300 | 1300
Kicker shunt impedance（kΩ） | 1.8 | 1.8
Damping time（ms） | 200 | 200
Number of kicker | 4 | 4
Power(w) | 1320 | 3030
Parameter | Value (z-injection) | Value (z-extraction)
Energy（GeV） | 30 | 45.5
 | 1.12 | 1.12
Longitudinal tune(m) | 0.0879 | 0.0879
Phase acceptance（mrad） | 1.7 | 1.7
RF frequency（MHz） | 1300 | 1300
Kicker shunt impedance（kΩ） | 1.8 | 1.8
Damping time（ms） | 200 | 200
Number of kicker | 4 | 4
Power(w) | 1320 | 3030

## Slide 22: Beam loss monitor
This system can be used to study the beam loss and to understand the beam behavior.
The following important factors are focused for selecting the right type of BLM for a specific application in CEPC: intrinsic sensitivity, dynamic range, radiation hardness, response time and sensitivity to synchrotron radiation (SR).
The improved PIN-photodiode in storage ring and the Quartz Fiber in booster for large range of beam energy

## Slide 23: Tune monitor
Direct Diode Detection method invented by Marek Gasior will be taken.
Sub-micrometer oscillation will be detected.
Pilot bunch exciting method will also be used to measure the tune.
One method is to change the phase in Bunch by bunch feedback filter.
The other is to kick the appointed bunch to get the tune.
Frequency sweeping method with gated pulse or FFT analyzing to the data from the digital BPM.
The BPM monitor, signal processing unit and the kicker form the entire system.
Direct Diode Detection（3D）is another choice for tune monitor

## Slide 24: Other systems
Vacuum Chamber Displacement Measurement
  Due to heat effects caused by synchrotron radiation and beam loss, the vacuum chamber will be displaced. In order to calibrate the BPMs, the displacement need to be measured.
  The entire system includes Linear Variable Differential Transformer (LVDT), signal processing unit, computer and network.
  Relevant research has been carried out on BEPCII. The displacement detector uses the DL6230 of Micro with dynamic range 500 μ m and accuracy 1 nm.
  Beam test has been carried out in BEPCII
BPM reading Δ40μm ~ displacement sensor reading Δ 15 μm ~ Temperature 0.5 ℃
Shut down
Re-injection
Notes: The temperature difference with /without beam is 2 ℃, the difference is much smaller for different current, the position difference is 15 μm in a run (150~250 mA)

## Slide 25: The beam instrumentation in CEPC Linac
 | Item | Method | Parameter | Amounts
Linac | Beam position | Stripline BPM | Resolution ：30um | 140
 | Beam current | ICT | 2.5%@1nC-10nC | 42
 | Beam profile | YAG/OTR | Resolution: 30um | 80
 | Beam emittance | Q+PR | 10% | 3
 | Beam energy & spread | AM+PR | 0.1% | 3
Damping ring | Average current | DCCT | Resolution :50uA@0.1mA-30mA | 1
 | Beam position | Button BPM | Resolution : 20um @ 5mA TBT | 40
 | Tune measurement | Frequency sweeping | Resolution:0.001 | 1

## Slide 26: Beam position monitor
There are a total of 150 stripline BPMs in the Linac and its transport lines, which are divided into two groups based on the size of the beam-stay-clear area. The beam-stay-clear area with a diameter of 30 mm and 20 mm.
BPM electronics hardware is the same as that of collider ring，but the algorithm is specifically tailored for Linac. Bunch by bunch electronics is adopted for double-bunch acceleration

## Slide 27: Beam current measurement
In total, there are 42 ICTs installed in the Linac to monitor beam intensity and calculate transmission efficiency.
An in-house signal processing electronics system is designed to adjust the signal from the ICT, performing the functions of filtering and amplification.
The sensitivity of the ICT sensor must take into account the attenuation caused by the transmission cable to ensure accurate measurement results. For this reason, an on-line functional examination and re-calibration can be carried out using the Cali-winding within the sensor.
ICT （Tunnel）
BCM electronics
A/D
（Local station）
Data base

## Slide 28: Beam Profile Measurement
The beam profile monitor is designed with three position screens for testing. a YAG:Ce crystal plate for low current commissioning, 100 nm aluminum(OTR) for high energy and calibration screen .
The control system software for the beam profile monitors is based on EPICS
Beam emittance and beam energy & spread measurement are both based beam profile measurement

## Slide 29: Beam instrumentation related R&D
The R&D activities based on lepton accelerator beam measurement mainly include the following three aspects.
  The design and fabrication of HEPS beam instrumentation
  The maintenance and upgrade of BEPCII beam instrumentation
  The R&D of CEPC beam instrumentation

## Slide 30: Beam instrumentation related R&D
We designed, manufactured, and calibrated the whole beam diagnostics system for HEPS, including the linac, booster, and storage ring.
In particular, we performed a detailed analysis of factors affecting the resolution of beam position monitor, and through various measures, we achieved the design goals for HEPS BPM, which are higher than those for CEPC.

## Slide 31: Beam instrumentation related R&D
We have developed button pick-ups BPM for HEPS.
Goubau line based wire calibration system were set to check BPM PU

## Slide 32: Digital Front End Board (DFE)
4 SFP +
Gigabit Ethernet
RS-232-C
JTAG
+12V Power Input
ADF Interface
2 Gbytes DDR3
SD Card
InterLock IN
InterLock OUT
Machine Clk
Trigger IN
SYNC
ZYNQ 7Z100
Features:
Xilinx ZYNQ FPGA (XZ7100)
  Hard dual-core ARM A9 processor
  Beam signal processing with DDC+CIC+FIR
  Runs standard Debian based Linux Operating System
  Embedded IOC
Boot via 32Gbyte micro SD-Card
Gigabit Ethernet
2Gbyte DDR3 Memory (SO-DIMM Module)
  Four 6.6Gbps SFP modules
  Embedded Event Receiver
  Fast Orbit Feedback
32Mbit FLASH memory

## Slide 33: Analog Front End Board (AFE)
Performance Features
P1dB = +18.5dBm (at ADC Input)
IP3 = +39 dBm (at ADC input)
NF =6.0dB (LPF and SAW Filter)
Channel to Channel Isolation > 40dB
Phase difference < 10°
Amplitude difference < 5%
-3dB Bandwidth ≈ 20MHz
Receiver S-Parameter Characterization
A
B
C
D
Pilot Tone
Cross-switch
Machine Clk

## Slide 34: Analog Front End Board (AFE)
A
B
C
D
Pilot Tone
Cross-switch
Machine Clk
Hole space: S ≈ 4D to 10D
More than 2 rows Ground Via needed;
Vias on Adjacent rows are interlaced placed;
Less λ /4 Via to Via space in one row.
Clock Power Supply factors cannot be ignored！
Rms jitter = 174fs
(10Hz-10MHz)

## Slide 35: Digital Signal Processing Block
LFSR: Linear Feed-back Shift-Register
FIR filter : Finite Impulse Response filter
CIC filter : Cascaded Integrator-Comb filter
DDS : Direct Digital Synthesis
RAW
ADC
×
DDS
IQ Data
FIR Filter
Bandpass
CIC Filter
Decimator
Compensating
FIR Filter
CORDIC
CIC Filter
Decimator
Compensating
FIR Filter
Programmable
FIR Filter
CIC Filter
Decimator
Compensating
FIR Filter
Programmable
FIR Filter
LFSR
BPM Calc.
BPM Calc.
BPM Calc.
TBT Data
220 kHz
FA Data
22 kHz
SA Data
10 Hz
COD BPM block
DDC BPM block
The DDC algorithm module mainly consists of modules such as NCO, CIC, and FIR. In the first stage, a BPF is used to remove the baseline of ADC data and reduce the difference between the four channels of data. The algorithm module mainly generates TbT, FA, and SA data. The digital signal filtering mainly consists of an extraction filter composed of CIC and FIR
 | DBPM@BEPCII | DBPM@HEPS
TbT Data | 1.2621MHz | 220kHz
FA data | 10kHz | 22kHz
COD data(SA) | 10Hz | 10Hz

## Slide 36: Data Acquisition Module
Data Acquisition function block.
  EPICS Device Driver
  Linux Kernel Driver
  Data Acquisition DMA/FIFO
  Data base logic
  Graphical User Interface
EPICS BPMApp IOC
EPICS Device Driver
Linux Kernel Driver
DMA
ADC RawData
EPICS Device Driver
Linux Kernel Driver
FIFO
TBT Data
EPICS Device Driver
Linux Kernel Driver
FIFO
FA Data
EPICS Device Driver
Linux Kernel Driver
FIFO
SA Data

## Slide 37: ADC Performance Analysis
 | SNR | ENOB | SFDR | SINAD | THD
ADC | 60.3 | 12.2 | 75.5 | 52.2 | -56.1
A
B
C
D
ADC histogram
ADC SNR vs Input Frequency vs Clock Jitter
ADC test results
Raw ADC FFT

## Slide 38: BPM electronics test in Lab
TBT RMS (X=767nm,y=786nm)
SA RMS(X=30nm,Y=38nm) 10points STD
FA RMS (X=103nm,y=98nm)
Performance
TBT data rms xpos ≈767nm, ypos ≈786nm;
FA data rms xpos ≈103nm, ypos ≈98nm;
SA data rms xpos ≈30nm, ypos ≈38nm;
Kx=Ky=8.26mm;

## Slide 39: BPM Processor Performance Testing
** BPM electronics
IHEP BPM electronics
40nm
40nm
40nm
35nm
(IHEP&&commercial products)

## Slide 40: Real beam test in BEPCII
BPM 1O_03 (IHEP&&commercial products)
** BPM electronics
IHEP BPM electronics
70nm
90nm
80nm
70nm

## Slide 41: BPM electronics application
We successfully solved the issue of mass production of BPM electronics and the home-made BPM electronics were used in BEPCII collider ring operation and HEPS linac commissioning
There will be ~600 sets self-developed BPM electronics in HEPS storage ring.

## Slide 42: Beam instrumentation related R&D
Optical fiber based BLM test in BEPCII
Bunch by bunch electronics are used to measure beam oscillation
The 3D tune measurement system beam test in BEPCII

## Slide 43: Beam instrumentation related R&D
Multi-feedback systems can be used to improve the performance of particle accelerators. At BEPCII, the double feedback technique was successfully implemented, and the results showed that the damping times are almost equal to the sum of the two feedback systems. This demonstrates the effectiveness of multi-feedback systems in improving the stability and performance of particle accelerators in one direction.
The damping time of two TFBs

## Slide 44: Beam instrumentation related R&D
Study of feedback system kicker
Resonant strip-line type longitudinal kicker

## Slide 45: Summary
We have reviewed and improved the design report of the system based on the latest parameters and suggestions from IARC
We have thoroughly understood the measurement requirements of CEPC and conducted extensive research on key technologies.
Through our research and development activities, we have trained our personnel and mastered the necessary technology, which has prepared us for the construction of the project.
Thank you for attention！