## Slide 1
CEPC mechanics system
Haijing Wang
12-16. June. 2023, Hongkong, CEPC Accelerator TDR International Review

## Slide 2
Introduction
This talk is about the mechanics system of CEPC, including the supports for regular magnets, the MDI mechanics, the movable collimators for background decreasing.
This talk relates to the TDR Ch 4.3.10, Ch 5.3.9, Ch 6.3.10 and Ch 6.4.9.
The content relates to the “charge letter” items:
  1. Are the accelerator system design goals well defined? Have the goals been reached in the TDR?
  6. Regarding the key technology research and development, are critical technologies and components of the CEPC accelerator ready or will they be ready before 2026, through the R&D program being carried out, or achieved with the Light Source project undertaken by IHEP, for the eventual realization of the CEPC?
  7. What are the primary technical risks and their potential impacts on the CEPC? What are the mitigation measures that should be taken?
  8. Will the CEPC accelerator be ready for construction, after the completion of the outlined R&D program, and industrial and engineering preparation, as well as issues identified in item 7 above be properly addressed in due time?
  9. Any other issues you notice or any improvements you may suggest.

## Slide 3: Content
Supports for regular magnets
MDI mechanics
Movable collimators
Summary

## Slide 4: Content
Supports for regular magnets
  Supports in Collider
  Supports in Booster
  Supports in Linac and Damping Ring
MDI mechanics
Moveable Collimators
Summary

## Slide 5: Supports for regular magnets
Over 90% of the 100 km ring is covered by magnets.
Booster
Collider
Requirements
  Stability with large time constants to avoid creep and fatigue deformation,
  Simple and reliable structures for safe mounting and easy alignment.
  Good vibration performance.
Direction | Ranges | Direction | Ranges
X | ≥±20 mm | Δθx | ≥±10 mrad
Y | ≥±30 mm | Δθy | ≥±10 mrad
Z | ≥±20 mm | Δθz | ≥±10 mrad
Adjustment ranges of magnets in Collider, Booster, Linac, Damping Ring and transport lines

## Slide 6: Supports for regular magnets
Quantities of magnets and their supports in the collider
Magnet type | Quantity | Magnet length (mm) | Core number per magnet | No. of supports per core
Dipole (13250 magnet cores) | 1024 | 19743 (twin-aperture) | 4 | 4
 | 1920 | 23142(twin-aperture) | 4 | 4
 | 64 | 21700(twin-aperture) | 5 | 4
 | 162 | 28450~93378 (single aperture) | 5~17 | 4
Quadrupole | 3008 | 3000(twin-aperture) | 1 | 3
 | 8 | 1500 (twin-aperture) | 1 | 2
 | 1124 | 500~3500 (single aperture) | 1 | 1~3
Sextupole | 3072 | 1400 | 1 | 3 in common girder
 | 104 | 300~1000 | 1 | 1
Corrector | 7088 | 875 | 1 | 1

## Slide 7: Supports in Collider
Dipole supports
  To form a magnet unit for the majority of dipoles, four magnet cores with lengths of 4,738 mm or 5,594 mm are connected.
  Each core is supported by four supports, two Y supports, one XY support and one XYZ support.

## Slide 8: Supports in Collider
Deformation optimization
  Methods: theoretical derivation & Workbench Response surface
  The maximum uneven deformation of the 5,594 mm long dipole core is 7μm, induced by gravity and support.
L
Number of supports | 3 | 4 | 5
Max. deformation (µm) | 19 | 7 | 5

## Slide 9: Supports in Collider
No. of order | Frequency (Hz) | Mode
1 | 50.2 | Z translation
2 | 51.3 | X translation
3 | 59.7 | Yaw rotation
4 | 89.0 | Bend in XZ plane
5 | 117.2 | 1st order bend YZ plane
6 | 123.8 | 2nd order bend YZ plane
Dynamic stability
  Assume the natural frequency of the pedestals is above 150 Hz according to the experience of HEPS.
  The 1st natural frequency is 50.2 Hz.

## Slide 10: Supports in Collider
Quadrupole Support
  Similar to dipole supports
  Three supports for the majority of quadrupoles 3000 mm long.
No. of order | Frequency (Hz) | Mode
1 | 27.3 | X translation
2 | 31.5 | Z translation
3 | 33.2 | Yaw rotation
4 | 65.8 | Pitch rotation
5 | 67.3 | Y translation
6 | 80.4 | Roll rotation
Dynamic stability
  Similar method as Dipole magnet and support.
  The 1st natural frequency is 27.3 Hz.

## Slide 11: Supports in Collider
Sextupole support
  Common girder for the adjacent three sextupoles.
  Magnet length: 1.4 m; girder length: 3 m.
  Needs pre-alignment.

## Slide 12: Supports in Booster
Support structures are similar to those of the Collider, with the exception that its pedestal is made of steel frames attached to the tunnel ceiling.
Magnet type | Quantity | Core length (mm) | No. of supports per core
Dipole | 14226 | 4700 | 4
 | 640 | 2350 | 2
Quadrupole | 2314 | 1000/700 | 2 (common frame)
 | 1144 | 2000 | 2
Corrector | 1200 | 583 | 1
Quantities of magnets and their supports in the Booster

## Slide 13: Supports in Booster
Topology optimization
  To design the supporting location in the XY plane.
  Constraint: volume; Objective function: structure compliance.
  Applicable to all types of magnet supports hanged to the ceiling.
  Vertical steel frames with horizontal ribs are adopted to achieve a simple structure and a better appearance.
Tunnel ceiling
Magnet
Selected elements for support
Angular coordinate of 1st support point
Angular coordinate of 2nd support point

## Slide 14: Supports in Booster
Similar design for longitudinal locations
Similar design for adjusting structures
Hanged on the ceiling by steel frames
No. of order | Frequency (Hz) | Mode
1 | 24.2 | X translation
2 | 26.6 | Yaw rotation
3 | 28.9 | Z translation
4 | 79.0 | Bend in XZ plane
5 | 117.4 | Roll rotation
6 | 122.2 | Pitch rotation
Modal analyses of Booster dipole and support

## Slide 15: Supports in Linac and Damping Ring
Supports | Quantity (set) | Remarks
Bunching system support | 1 | Supports of subharmonic buncher, buncher, accelerating structure, solenoid and instruments
EBTL support | 2 | 
Positron accelerating structure support | 1 | Supports of positron source, solenoid, accelerating structure and positron acceleration section
Triplet support unit | 104 | Support of the quadruples, correctors and instruments in the triple unit
Dipole support | 19 | Supports of 6 kinds of dipoles
Accelerating structure support | 579 | Supports of S band and C band accelerating structures
Mechanical supports in the Linac

## Slide 16: Supports in Linac and Damping Ring
Linac：Similar to the Linac support of HEPS
Bunching system support
Accelerating structure support
Triplet unit support

## Slide 17: Supports in Linac and Damping Ring
Supports | Quantity (set) | Remarks
Quadrupole & sextuple support | 72 | Common girder for one quadrupole and one sextuple
Quadrupole support | 32 | Supports of 2 kinds of quadrupoles
Dipole support | 80 | Supports of 2 kinds of dipoles
Lambertson support | 2 | 
Kicker support | 2 | 
Damping Ring: Similar to the transport line supports of HEPS
Mechanical supports in the Damping Ring
Support of adjcent quadrupole and sextupole
Individual support of quadrupole magnet
Individual support of dipole magnet

## Slide 18: Content
Supports for regular magnets
MDI mechanics
  MDI Layouts
  SC magnet support system
  Remote vacuum connector
Movable Collimators
Summary

## Slide 19: MDI layouts
Detective angle: acos0.99
IP chamber:-700mm~700mm
Detector York length: 9620mm

## Slide 20: MDI layouts
All the devices are within the detective angle, acos0.99.
IP
Be-Al chamber
Z: -700~700mm
Remote Vacuum Connector
Z: 700~783mm
IP BPMs
Z: 855~950mm
Y chamber
Z: 783~855mm
Lumical body
Z: 940-1100mm
Q1a Q1b
Z: 1855~4440mm

## Slide 21: MDI layouts
Distance to detective angle
  IP chamber flange: 5.34mm
  RVC: 14.91mm (pressure tube)
  Shielding outside cryostat: 16.49mm
IP chamber flange
RVC
BPM & cable
Lumical& support
Cryostat
Pressure tube of RVC
Tungsten shielding

## Slide 22: MDI layouts
Vacuum vessel
Helium vessel
Anti solenoid
Skeleton supports
Cross section at Q1a
SKEKB experience is greatly helpful for the integration

## Slide 23: SC magnet support system
Key points
  Stability (static and dynamic)
  Accuracy
  Easy-operating
  Dimensions
Alignment requirements: ≤100 μm.
  High resolution: ≤ 5 μm
  Small uneven deformation
Cryostat length: ~5.6 m

## Slide 24: SC magnet support system
Magnets to helium vessels
  Skeleton support has been adopted based on optimization.
Helium vessel to vacuum vessel
  Support rods.
Aim: minimize the SC magnets deformation, enhance stability.
Models | materials | 
QD0/QF1 | Fe-Co-V | 
Anti-solenoid | Fe | 
Anti-solenoid inner pipe | Ti-6Al-4V | Based on material optimization
Vessels | SS | 
Magnet supports | Ti-6Al-4V | 

## Slide 25: SC magnet support system
For cylinder cantilever under gravity
For concentric cylindrical cantilever under gravity
  Shape factors: ; material factors: /, /
The goal is to minimize the uneven deformation of the SC magnets.
After the optimization, the total weight of the cryostat and the devices inside is 2790 Kg.
Material | Density (kg/m3) | Specific stiffness (Nm/kg 103)
Stainless steel | 8000 | 25
Ti-6Al-4V | 4430 | 25.7
A6061 (Al) | 2700 | 25.5
Copper (Cu) | 8960 | 12.3
Material | Density (kg/m3) | 
Stainless steel | 8000 | 25
Ti-6Al-4V | 4430 | 25.7
A6061 (Al) | 2700 | 25.5
Copper (Cu) | 8960 | 12.3
equivalent density of inside cylinder

## Slide 26: SC magnet support system
G
Fz1
Fz2
Fz3
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.
Max. displacement in Y direction is 1.79 mm.

## Slide 27: SC magnet support system
Integral FEA
  Loads：gravity, Lorentz force Fz with detector solenoid operation
  Alignment cannot based on the displacement.
  To pre-align the magnet to compensate the absolute displacement.
Alignment requirements: ≤100 μm.
  Maximum uneven deformation in Y direction (max-min): 31 μm in Q1b, doesn’t change with temperature
  Thermal expansions are assumed constants for this estimation.
Temperature | uneven deformation in Y direction (um) |  |  | Displacement in Z direction (mm) |  | 
 | Q1a | Q1b | Q2 | Q1a | Q1b | Q2
295K | 5 | 31 | 14 | 0.3 | 0.26 | 0.24
4.2K | 7 | 30 | 12 | Contract with temperature |  | 

## Slide 28: SC magnet support system
No. of order | Frequency (Hz) | Mode
1 | 14.5 | Integral vertical sway
2 | 14.9 | Integral horizontal sway
3 | 51.7 | Integral vertical wave
4 | 53.7 | Integral horizontal wave
5 | 89.7 | Vertical wave of helium vessel
6 | 91.4 | Horizon wave of helium vessel
Dynamic stability
  Assume the cryostat is fixed at the end.
  The 1st natural frequency is 14.5 Hz.

## Slide 29: SC magnet support system
Enhancing the natural frequency is an effective method to decrease vibration.
Ground vibration decreases with increase in frequency :
  Displacement PSD ~ f-4
  Spectral displacement ~ f-2
HEPS site
Mechanical dynamic stability (vibration)
  Ground vibration
  Magnet-support assembly
  Damping devices
  Slab and pedestal

## Slide 30: SC magnet support system
Auxiliary support of cryostat
  Auxiliary constraint: V groove, translational in beam direction
  1st natural frequency: 1429 Hz
  Harmonic response (1-50 Hz) , the response amplitude decreased largely.
  Can decrease the cryostat deformation as well.
Uneven deformation VS support location

## Slide 31: SC magnet support system
In the FEA, the adjusting mechanism, support bed and movement mechanism are assumed to be fixed right now. The real condition is assumed worse than the FEA case.
FEA based hammer method was proposed for HEPS, which can be used for the stiffness estimation.
[M1,k1,Q1]
[M2,k2,Q2]
Joint

## Slide 32: Remote vacuum connector
Used to connect the IP chamber and the vacuum tubes of accelerator.
Leak rate requirement: 2.7 10–11 Pa·m3/s
Leak rate:
  Decrease the pressure difference .
  Decrease the conductance
Anti-radiation
Limited operation space
High leak rate requirement
Remote connection
All-metal sealing
Improve C and
Special location
High safety and reliability
Difficulties
Solutions

## Slide 33: Remote vacuum connector
    Decrease (experience from CSNS)
  Single-layer  double layer, leak rate can be improved from 1e-6 Pa.m3/s to 8.5e-10 Pa.m3/s.
    Decrease conductance C
  For sealings with the same F/L
  Decrease roughness A, demonstrated by J-PARC
  Decease the perimeter L almost determined by layout
  Decrease the hardness of gasket materialsusing copper
  Decrease the seal width knife-edge seal
Inflatable seal
Roughness and conductance, J-PARC

## Slide 34: Remote vacuum connector
    Leak rate estimation
  Leak rate obtained in CSNS: 3.9e-10 Pa.m3/s (inner diameter 320mm)
  It is possible to obtain the requirement of 2.7e-11Pa.m3/s (inner dimensions 35-20mm, racetrack)
    Can endure a heat flux of 1 W/cm2, the HOM power is acceptable.
temperature
Heat flux

## Slide 35: Content
Supports for regular magnets
MDI mechanics
Moveable Collimators
Summary

## Slide 36: Movable collimators
5 horizontal collimators and 4 vertical collimators per IP per ring for background decreasing.
name | Position | Distance to IP/m | Beta function/m | Horizontal Dispersion/m | Phase | BSC/2/m | Range of half width allowed/mm
APTX1 | D1I.785 | 44611 | 20.7 | 0.12 | 164.00 | 0.006 | 1~6
APTX2 | D1I.788 | 44680 | 20.7 | 0.12 | 164.25 | 0.006 | 1~6
APTY1 | D1I.791 | 44745 | 105.37 | 0.12 | 165.18 | 0.0036 | 0.156~3.6
APTY2 | D1I.794 | 44817 | 113.83 | 0.12 | 165.43 | 0.0036 | 0.156~3.6
APTX3 | D1O.5 | 1729.66 | 20.7 | 0.06 | 6.85 | 0.00182 | 1~6
APTX4 | D1O.8 | 1798.24 | 20.7 | 0.12 | 7.10 | 0.00182 | 1~6
APTY3 | D1O.10 | 1832.52 | 20.7 | 0.25 | 7.22 | 0.00182 | 0.069~3.3
APTY4 | D1O.14 | 1901.1 | 20.7 | 0.25 | 7.47 | 0.00182 | 0.069~3.3
APTX5 | DMBV01IRU0 | 56.3 | 196.59 | 0 | 362.86 | 0.01178 | 2.9~11.78

## Slide 37: Movable collimators
Horizontal movable collimator
  To minimize RF losses, the inner profile is gradually altered from a circular to a rectangle.
  Material of vacuum vessel and the jaws is GlidCopAl-15， and SS for flanges.
  Half aperture 4mm for normal operation.
  Open-loop accuracy 10 µm (can be obtained for HEPS).

## Slide 38: Movable collimators
Structure Optimization
  Impedance varies with the offset of the tip.
  About 70% of the synchrotron radiation energy (7.5 kW @ 30MW Higgs) is deposited in the block.

## Slide 39: Movable collimators
Thermal mechanical analyses @30MW Higgs
  Jaw: highest temperature 147 ℃，Maximum von Mises stress89.7 MPa
  Vacuum chamber: highest temperature 124 ℃，Maximum von Mises stress 110.4 MPa

## Slide 40: Movable collimators
Beam Impact
  Nominal operating: heating power 21.2 W, temperature increase 1.3 ℃。
  Accident: assuming all beam bunches impact on the jaw. σx = 165 µm, σy = 35.7 µm. Copper will melt when the thickness exceeds about 0.026 mm. Carbon will melt when the thickness exceeds 1 mm.
  Additional machine protection strategies need to be considered, which will be studied in further stage.

## Slide 41: Summary
The magnet supports for the majority of magnets in Collider, Booster, Linac and Damping Ring have been designed and analyzed. Other support should have similar structure.
The MDI layout can fulfill the space requirements. The general support structure design and analyses have been done for the SC magnets and cryostat. The adjusting resolution and uneven deformation of magnets can fulfill the alignment requirement. The structure design and leak rate estimation have been done for the remote vacuum connector.
Structure design and analyses have been done for the horizontal movable collimators used for background decreasing.

## Slide 42
Thanks for your attention!

## Slide 43: Back up

## Slide 44: Back up

## Slide 45: Back up
Transportation and coarse location of magnets in Collider
Transportation and coarse location of magnets in Booster
Flexible load support for “long” devices and “short” devices
  * Cooperate with Beijing North Vehicle Group Corporation.

## Slide 46: Back up

## Slide 47: Back up
Bellows
Spline flange
flange
Pneumatic annular
Long tools
Support
Spline gear
Locking gear
Flange
Screw thread
Limit pin
Spline flange
Spline gear
RVC Design
Dimensions:
Transversal: Max. ϕ264mm
Longitudinal: ~223mm
  * Cooperate with Shenyang Huiyu vacuum technics co., Ltd.

## Slide 48: Back up
Flange
Flange
Sealing membrane
bellows
Guiderods and limits
Tubes
Flange
Inflatable seal design
Dimensions:
Transversal: Max. ϕ112mm
Longitudinal: ~120mm
  Experience from CSNS: leak rate ~10-10 Pa.m3/s level, one level higher then CEPC requirement.