## Slide 1
CEPC Beam Polarization Study
Zhe Duan
12-16. June. 2023, Hongkong, CEPC Accelerator TDR International Review
Contributors:
S. H. Chen, T. Chen, D. H. Ji, X. P. Li, W. H. Xia, B. Wang, D. Wang, Y. W. Wang,
D. P. Barber (DESY&UNM),
S. Nikitin (BINP)
Acknowledgement:
E. Forest & D. Sagan on help with Bmad/PTC code.

## Slide 2: Content
Introduction
Longitudinally polarized colliding beams at Z-pole
Resonant depolarization
Radiative depolarization at ultra-high energies
A preliminary study of Compton Polarimeter
Summary

## Slide 3
Introduction
This talk is about the design study of beam polarization aspects of CEPC
This talk relates to the TDR Appendix 8 Beam Polarization
The contents are based on the CEPC CDR lattices and parameters, and shall be considered as an exploratory study independent from the main trunk of the CEPC TDR at this stage, while the results can be implemented into the CEPC design later.

## Slide 4: Motivation of CEPC polarized beam program
Vertically polarized beams in the arc
  Beam energy calibration via the resonant depolarization technique
  Essential for precision measurements of Z and W properties
  At least 5% ~ 10% vertical polarization, for both e+ and e- beams
Longitudinally polarized beams at IPs
  Beneficial to colliding beam physics programs at Z, W and Higgs
  Figure of merit: Luminosity * f( Pe+, Pe- )
  ~50% or more longitudinal polarization is desired, for one beam, or both beams
Supported by National Key R&D Program 2018-2023 to design longitudinally polarized colliding beams at Z-pole.
L. Arnaudon, et al., Z. Phys. C 66, 45-62 (1995).

## Slide 5: Beam polarization in the collider rings
Colliding bunches: top-up injection
Non-colliding “pilot” bunches: decay mode
time
Polarization
Bunch charge
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
Polarization build-up time w/o radiative depolarization (hour) | 253 | 15.2 | 2.0
Beam lifetime (hour) | 2.5 | 1.4 | 0.43
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
 | 253 | 15.2 | 2.0
 | 2.5 | 1.4 | 0.43
  If , then
Self-polarization can be utilized for RD measurements using pilot bunches
  Employ asymmetric wigglers to reduce the polarization time @Z [1]
To achieve a high-level polarization for colliding bunches without significantly sacrificing luminosity [2]
  Injection of polarized beams is mandatory
[1] The FCC-ee Energy and Polarization Working Group, arXiv:1909.12245v1, 2019.
[2] Zhe Duan, talk on 2nd FCC EPOL Workshop, Sep 29, 2022

## Slide 6: Content
Introduction
Longitudinally polarized colliding beams at Z-pole
Resonant depolarization
Radiative depolarization at ultra-high energies
A preliminary study of Compton Polarimeter
Summary

## Slide 7: Preparation and injection of polarized electron beam
Compton polarimeter
Compton polarimeter
Assumption: Polarized e- vs. unpolarized e+
State-of-the-art polarized e+ source cannot meet the requirements of top-up injection for CEPC [1]
The design is applicable to e+ when the polarized e+ source becomes technically ready.
[1] P. Musumeci et al., Positron Sources for Future High Energy Physics Colliders, ArXiv:2204.13245 Phys. (2022).

## Slide 8: Polarized electron source
Polarized electron gun
Wien filter
Mott polarimeter
Main linac
Photocathode DC gun @ PAPS
Using state-of-the-art technology, polarized electron gun can supply > 85% polarization and satisfy injection requirements of CEPC.
Photocathode DC gun @ PAPS can provide a basis for R&D of polarized electron beam generation.
bend
Unpolarized electron gun
bend

## Slide 9: Polarization transmission in the linac & transport lines
Booster to ring transport line
Linac to booster transport line
  Depolarization in the linac is expected to be negligible[1,2].
  Transport lines (polarization loss < 10%)
    non-interleaved horizontal bending & vertical bending
    Typical errors without trajectory correction
[1] G. Moortgat-Pick, et al., Polarized positrons and electrons at the linear collider, Physics Reports 460 (2008) 131-243.
[2] M. Woods, The polarized electron beam for the SLAC Linear Collider, arXiv:heps-ex/9611006v1, 1996
Mismatch at injection
rms vertical trajectory set to 2mm

## Slide 10: Depolarization in the booster
The spin tune changes and could cross spin resonances
  The spin resonances are spaced by 440 MeV for e+/e-
The non-adiabatic crossing could vary and lead to depolarization [1]
  Spin resonance strength ε
  Acceleration rate [km]
  Δ|P| < 1% in the regimes of fast crossing & slow crossing
Previous studies suggested using Siberian snakes to maintain polarization for future 100km-scale boosters[7]
[1] Froissart and Stora, NIM 7, 297 (1960) [2] A. K. Barladyan, et al., PRAB 22, 112804, (2019)
[3] S. Nakamura, et al., NIM A 411, 93 (1998) [4] T. Khoe et al., Part. Accel. 6, 213 (1975)
[5] Configuration Manual: Polarized Proton Collider at RHIC, 2006 [6] V. Ranjbar, et al., PRAB 21, 111003 (2018)
[7] I. Koop et al., Phys. Part. Nucl. Lett. 13. 7 (2016); S. Nikitin, IJMPA 34, 1940004(2019); IJMPA 35, 2041001 (2020).
Fast crossing
Slow crossing
Spin precession
Orbit motion in a helical snake @ RHIC
Data from Ref [2-6]

## Slide 11: Setup of CEPC booster lattice
Arc region covers ~ 80% of circumference
General structure of the CEPC booster lattice (an alternative design)
  8 arcs each containing 140 FODO cells
  interleaved with 8 straight sections
60 imperfection lattice seeds
  Misalignment error & field error, scan BPM offset
  Closed orbit correction & tune correction
Multi-particle tracking in Bmad
  Energy and RF ramping in the whole process
  Element-by-element tracking with radiation damping & quantum excitation
[1] T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).

## Slide 12: Spin resonance structure
Intrinsic resonances:
Super strong resonances:
Imperfection resonances:
Super strong resonances:
Strength of intrinsic & imperfection resonances can be approximated by[1]
Enhancement occurs near , νB is the total νy in all standard arc cells [2]
Resonances at K<< νB tend to be weak due to cancellation [2]
due to P superperiods
due to M identical FODOs in each arc
[1] S. Y. Lee, Spin dynamics and snakes in synchrotrons (World Scientific, 1997).
[2] T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).

## Slide 13: Depolarization effects: simulation vs. estimation
Z-mode
W-mode
H-mode
In the acceleration to Z & W
  The spin resonances are generally weak
  Polarization is mostly maintained
  Estimations agree fairly well with simulations
In the acceleration to H
  The spin resonances become stronger at higher energies
  Severe depolarization occurs
  Mitigation methods to be explored
[1] T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).
This study supports injecting highly polarized beams into the collider rings as a very attractive solution, for applications @ Z & W.

## Slide 14: Spin rotators in the collider ring at Z-pole
Solenoid-based spin rotator + anti-symmetric arrangement [1,2,3,4]
[1] D. Barber, et al., A solenoid spin rotator for large electron storage rings. Part. Accel. 17 (1985) 243. [2] I. Koop, Longitudinally polarized electron in SuperB, eeFACT’08 [3] S. Nikitin, Opportunities to obtain polarization at CEPC, IJMPA, 34, 194004 (2019) [4] W. Xia et al., Radiat. Det. Tech. Meth. 6:490 (2022).
two modules: ~100 m
2.65 mrad
1.39mrad
solenoids: 240 T m, Lsol = 40m @ 6T

## Slide 15: Performance evaluation: orbital motion
Changes in optics parameters
  Increase of circumference ~ 2.8 km, can be optimized.
  Increase of integer betatron tunes by 18 units
Moderate reduction in dynamic aperture and local momentum acceptance
Further optimization using more sextupole families could help recover
[1]W. Xia et al., Radiat. Det. Tech. Meth. 6:490 (2022).

## Slide 16: Performance evaluation: polarization
Bmad/PTC simulations show:
Weak dependence of over energy in the working energy range
Errors in solenoid sections only
  Rms relative field error of 5e-4 for solenoids & quadrupoles, roll error of 1e-4 for quadrupoles.
More complete machine imperfections
  W/ closed orbit correction, but w/o optics correction (pessimistic)
w/ errors in solenoid sections
w/ more complete imperfections and closed orbit correction
[1]W. Xia et al., Radiat. Det. Tech. Meth. 6:490 (2022).

## Slide 17: Time-averaged polarization for colliding bunches
Polarized e- source
Polarization >85%
Ref: ILC, EIC
Linac and transport lines
Polarization loss < 10%
Ref: SLC, ILC
Booster
Polarization loss < 5%
Collider
Pinj > 70% after considering these factors
Polarization transmission
For colliding bunches in top-up injection, time-averaged beam polarization
> 50% if
 | =1hour | =2hour | =3hour
Pinj = 70% | >0.9% | >1.8% | >2.7%
Pinj = 75% | >0.7% | >1.4% | >2.1%
Pinj = 80% | >0.6% | >1.2% | >1.8%
Pinj = 70% |  |  | 
Pinj = 75% |  |  | 
Pinj = 80% |  |  | 
> 70% for the simulated cases with PDK > 70% at [aγ] = 0.5
Maintaining a beam polarization > 50% still reserves a large safe margin for effects not yet considered
  More realistic error sources & detector solenoids
  Beam-beam depolarization

## Slide 18: Content
Introduction
Longitudinally polarized Colliding beams at Z-pole
Resonant depolarization
Radiative depolarization at ultra-high energies
A preliminary study of Compton Polarimeter
Summary

## Slide 19: Polarized beams for Resonant Depolarization at Z-pole
Scenario 1: Self-polarization enhanced by asymmetric wigglers [1]
[1] The FCC-ee Energy and Polarization Working Group, arXiv:1909.12245v1, 2019.
Implementation of the asymmetric wigglers into the CDR lattice w/ spin rotators
The lifetime limited by the dynamic aperture is not an issue for the above wiggler settings

## Slide 20: Polarized beams for Resonant Depolarization at Z-pole
Scenario 2: Injecting polarized e+/e- beams [2]
[1] The FCC-ee Energy and Polarization Working Group, arXiv:1909.12245v1, 2019.
[2] Zhe Duan et al., Proc. eeFACT 2022, Proc. IPAC 23.
Scenarios |  | Self-polarization in the collider[1] | Injection of polarized beams[2]
Hardware | Polarized electron gun | None | Yes
 | Asymmetric wigglers | In the colliders | In the e+ damping ring
Polarization level |  | 5% ~ 10% | > 70% for e-, > 20% e+
Dead time for physics |  | Initial 1~2 hours in each fill | None
Frequency of RD measurements |  | Every ~10 min per beam | More frequent for e- beam
RD on colliding beams |  | None | Possible at lower bunch charge

## Slide 21: e+ damping/polarizing ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.542 | 
Circumference (m) | 144.2 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Bending radius (m) | 3.44 | 
Dipole strength B0 (T) | 1.07 | 
Wiggler strength B+ (T) | 1.8 | 
Wiggler cell length (m) | 1.5 | 
U0 (kev/turn) | 190.9 | 
Damping time x/y/z (ms) | 7.77/7.77/3.89 | 
Momentum compaction | 0.015 | 
Storage time | 20 ms | 10 min
0 (%) | 0.072 | 
0 (mm.mrad) | 138 | 
injection z (mm) | 6 | 
Extract z (mm) | 5.7 | 5.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 151/15 | 138/14
inj /ext (%) | 0.18 /0.072 | 
RF acceptance (%) | 1.8 | 
fRF (MHz) | 650 | 
VRF (MV) | 3.95 | 
Longitudinal tune | 0.044 | 
Asymmetric wigglers
B+=1.8T=-5 B-
cell length=1.5m
16 such cells
+1(2)
[1] Z. Duan et al., eeFACT 2022, IPAC 2023

## Slide 22: Some preliminary simulations of the RD process
Simulations of the RD process for different operation modes [1].
RD experiments planned at BEPCII & HEPS booster.
CEPC-Z pilot bunch
CEPC-Z colliding bunch
CEPC-W pilot bunch
[1] I. Koop, EPOL Workshop 2017, eeFACT 2018, HKIAS mini workshop 2020, FCC Week 2022
Cases | Z pilot bunch | Z colliding bunch | W pilot bunch
ag0 | 103.4921 | 103.4921 | 181.5123
sd | 3.847e-4 | 1.3e-3 | 6.79e-4
nz | 0.03448 | 0.03448 | 0.062
Modulation index | 1.15 | 3.9 | 2.0

## Slide 23: Content
Introduction
Longitudinally polarized Colliding beams at Z-pole
Resonant depolarization
Radiative depolarization at ultra-high energies
A preliminary study of Compton Polarimeter
Summary

## Slide 24: Radiative depolarization in electron storage rings
The SPEAR electron polarization for different beam energies[1]
[1] J. R. Johnson, et al., Nucl. Instrum. Meth 204, 261 (1983).
[2] R. Assmann, et al., AIP Conference Proceeding, 570, 169 (2001).
Electron polarization measurements in different machines [2]
  ,
Radiative depolarization characterized by exhibits two phenomenon in previous measurements:
  Dips near spin resonances
  More difficult to achieve a high polarization at higher energies
    Stronger first-order spin resonances
    Enhanced higher-order synchrotron-sideband resonances

## Slide 25: Radiative depolarization in ultra-high-energy storage rings
Two distinct spin diffusion mechanisms were proposed in [1] in 1970s, regarding the regimes of spin resonance crossing, in the combined effects of synchrotron oscillation and synchrotron radiation
Regime | Correlated regime (consistent with existing measurements) | Uncorrelated regime (not yet confirmed by experiments)
Condition |  | is violated and
Theory | Non-resonant spin diffusion & perturbative treatment of | Resonant spin diffusion
Depolarization effect | Higher-order synchrotron sideband spin resonances | No dependence on , weaker depolarization
Regime | Correlated regime (consistent with existing measurements) | Uncorrelated regime (not yet confirmed by experiments)
Condition |  | 
Theory |  | Resonant spin diffusion
Depolarization effect | Higher-order synchrotron sideband spin resonances | 
Monte-Carlo simulations were compared with these theories in the energy range of CEPC [2]
  showing a gradual evolution from the correlated regime to the uncorrelated regime in parameter scan
Z
Higgs
Case A: dependence on beam energy
Case B: influence of harmonic RF cavity
optimal lengthening condition
Scan harmonic RF voltage
[1] Derbenev, Kondrantenko and Skrinsky, Part. Accel. 9, 247 (1979)
[2] W. H. Xia, Z. Duan, D. P. Barber, Y. W. Wang, B. Wang, J. Gao, accepted by Phys. Rev. Accel. Beams.
This study suggests existing theories are incomplete, requiring further development

## Slide 26: Content
Introduction
Longitudinally polarized Colliding beams at Z-pole
Resonant depolarization
Radiative depolarization at ultra-high energies
A preliminary study of Compton Polarimeter
Summary

## Slide 27: Study of a Laser Compton polarimeter
[1] S. H. Chen, Y. S. Huang, et al., JINST 17 P08005, (2022)
Simulation studies of a Compton polarimeter that measures the spatial distribution of scattered electrons.
Will be extended to measure 3D polarization components.
Vertical distribution asymmetry on the detector reveals vertical beam polarization.
Some systematic errors
Analyzing power

## Slide 28: Summary
We’ve studied the approach of preparation of polarized beam from the source, transmission in the injector and injection into the collider ring, which promises high-level injected beam polarization for applications.
Longitudinally polarized colliding beams at Z-pole have been designed for CEPC CDR lattice and parameters.
Two different scenarios of polarized beam generation for RD measurements have been investigated.
Some theoretical and simulation studies of depolarization effects in booster & collider rings.
Preliminary simulation study of a laser-Compton polarimeter.

## Slide 29: Future work
For the longitudinally polarized colliding beams:
  Implement the spin rotator design into future iterations of CEPC lattice, include more comprehensive error modeling and corrections.
  Extend the spin rotator design to cover higher beam energies.
For the resonant depolarization measurements:
  Continue simulation studies of the RD process and the analysis of the errors in beam energy calibration.
  Carry out RD experiments at BEPCII & HEPS booster

## Slide 30
Your comments and suggestions are highly appreciated!