## Slide 1
WR: a high precise synchronize Ethernet and the applications
International workshop on the CEPC, Oct.24 2023
Guanghua Gong , Hao Chu, Jianmeng Dong, Yimeng Ye, Hongming Li,
Dept. of Engineering Physics, Tsinghua University

## Slide 2: Outline
WR applications
WR @ LHAASO
Summary
WR standardization
WR introduction

## Slide 3: Outline
WR introduction

## Slide 4: WR introduction
  CERN and GSI initiative for control and timing
  Sub-ns synchronization
  Thousands nodes, links to tens km
  Based on well established standards
    Ethernet + PTP + SyncE + DDMTD
  IEEE1588-2019 as high accuracy
Notes: 由于之前时钟同步技术的种种局限，因此发展出基于以太网扩展增强的WR技术。
WR技术实现了频率源广播及亚纳秒时间同步，同时提高了确定、可靠、低延时的数据传输能力。
有望成为下一代网络同步标准PTPv3

## Slide 5: WR introduction

## Slide 6: WR technology
Clock Data Recovery
Bi-directional frequency transmission
Digital Dual Mixer Time Difference for phase synchronization
Improved precision time protocol for time tick synchronization
Sync-E
DMTD
PTPv2

## Slide 7: Precise time protocol (IEEE 1588)
PTP as IEEE 1588
Frame based synchronization protocol
Simple calculations
Link delay
Offset correction
Master
Slave
t1
t2
t3
t4
Sync. package
Follow-up
Delay response
Delay request

## Slide 8: From PTP to WR
Devices have free-running oscialtors (±100PPM) that accumulates time drift that requires periodic message exchange
Symmetry medium assumation
Limeted timestanps resolution(8ns for Gigibit ethernet）
Layer 1 syntonisation among all devices
Link delay model to correct link asymmetries
Digital Dual Mixer Time Difference to measure the precise phase difference

## Slide 9: Layer 1 syntonisation
  Clock is encoded in the Ethernet carrier and recovered by the receiver (CDR)
  All network devices use the same physical layer clock
  Clock loopback allows phase detection to enhance precision of timestamps

## Slide 10
Digital Dual Mixer Time Difference (DDMTD)
Precise phase measurements in FPGA
Performed on both the master and slave sides
WR parameters:
  clkin = 62.5 MHz
  clkDDMTD = 62.496185 MHz (N=14)
  clkout = 3.814 kHz
Theoretical resolution of 0.977 ps
Notes: 它实际上就是将被测相位放大了N+1倍，因此也将鉴相器的时间分辨提高了N+1倍

## Slide 11: WR link delay model
single fiber with WDM to avoid physical link length difference
Asymmetry sources:
  Variable delays
    Chromatic dispersion in fibers
  Fixed delays：
    PCB trace
    FPGA
    SFP modules
Pre-calibration needed
  Chromatic dispersion calibrated as alpha
  Fixed delay of each node

## Slide 12: WR network and components
WR Switch
WR Nodes
Optical fibers
Freq. and Time reference

## Slide 13: WR Switch

## Slide 14: WR node (carrier mode)
PCIe carrier
PXIe Carrier
VME Carrier
AMC Carrier

## Slide 15
Mini-WR
Cute-WR-A7
WR node (mezzanine mode)
Cute-WR-A7 in SHINE time node
Mini-WR in JUNO timing/trigger devices

## Slide 16: WR node (IP mode)
WR as IP core with external support circuit
WR_NEM: WR external support circuit
WR_NEM in LHAASO MD elec.

## Slide 17: WR performance

## Slide 18: Outline
WR @ LHAASO

## Slide 19: Large High Altitude Air Shower Observatory
29o21’ 27.6” N, 100o08’19.6” E
4410 m a.s.l.
Full operation since 2021-June.
Chinese National Major Science and Technology Infrastructure
YaDing airport
Notes: Location: Haizishan(Lakes Mountain), Sichuan Province， 8 km to Daocheng Airport, the world’s highest civilian airport

## Slide 20
LHAASO timing system
High reliability
Large Scale
1.3Km2 area
~8000 detectors
High Precision
Accuracy： <500ps
Jitter： <20ps
4410 a.s.l altitude
wild field deployment
Notes: LHAASO-KM2A实验需求主要包括以下三点：
大规模探测节点
能量越高的宇宙线探测需要越大的探测面积，KM2A在平方公里地面部署了5195个ED探测器和1171个MD探测器
数千探测器的规模要求节点采用集成技术，单节点成本尽可能低，能实现时钟同步与数据网络复用
2. 高精度时间同步：
阵列式探测器需要全局统一时钟才能完成原始粒子入射径迹重建，为了实现入射角分辨小于0.5度，要求各探测器节点时间测量精度<2ns，时钟全局同步精度<500ps
3. 系统高可靠运行：
大气对粒子衰减严重，为提高探测效率LHAASO选择在高海拔野外区域建设，设备工作环境复杂，温度变化大，在这类工作环境下要求系统：时钟同步可靠性高、阵列的时钟同步标定

## Slide 21: Structure
WRS
ADC
TDC
FPGA
Memory
FMC connector
WRS
WRS
WRS
Ru.OSC
GM
WRS-L1
x3
WRS-L2
x30
WRS
L3 x 450
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
WRS
ADC
TDC
FPGA
Memory
FMC connector
WRS
~600m
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
WRS
ADC
TDC
FPGA
Memory
FMC connector
WRS
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
ADC
TDC
FPGA
Memory
FMC connector
~600m
~600m
1# Elec_HUT
Detector elec.
X 6800
GPS
DAQ SERVER
Computer Room
Distributed in field

## Slide 22
Improved heat dissipation, without FAN
Improved device temp. range to -20 ~ 70
Improved low jitter clock circuit
Improved kernel board placement
Optical Management port for fiber connection
18 WR ports with light guide
Software/Firmware compatible with standard WRS-18
https://www.ohwr.org/projects/wrs-fl-hw/wiki
WR Switch improvement

## Slide 23: Mass production for LHAASO
550 WRS-FL produced, 500 installed in field

## Slide 24: WR deployment
L3 WRS in the rack
Detector
(FEE inside)
Outdoor Rack
WR nodes are embedded inside the detector
photoelectric composite cables used for detector
  220V AC power + 3 fiber (1used, 2 spare)
4-core fiber from L3 WRS to 1#HUT
  1 used for WR Uplink (port1)
  1 used for Management
  2 spare

## Slide 25: WR in 1#HUT
SYS rack
MNG rack
ODF rack
WRS-A
Cable tray for inter-connection
WRS-B

## Slide 26: WR integrated in detector FEE
WRPC intergraded inside the detector electronics
  Save the cost for additional connector and FPGA
  Simplify the interface and protocol
  Calibration required when the detector logic changes
  Additional constrains added for the project
ED electronics
MD electronics
WR support circuit

## Slide 27: Outline
WR applications

## Slide 28: WR applications in HEP
SKA
LHC
Einstein telescope
KM3NET
JUNO
SHINE

## Slide 29: WR application in PET instrument
MR-compatible brain PET insert with DOI and TOF capability.
Full digitized front-end
WR based coincidence
FEB
ADB
DPB
CUTE-WR
PWB
BMB

## Slide 30: WR potential applications
Science
  Time and frequency, metrology
  Radio astronomy，incoherent scattering radar，VLBI
  Fast trigger and control
Military
  Electronics warfare, beam forming
  Multi-static radar ， synthetic aperture radar
  Adaptive antenna array
Industry
  Distributed base stations, 5G BBU&RRU
  3D mapping, 3D imaging
  Stereo vision，radio positioning
  Power grid synchronization
  Finance, data center, stock exchange
  Time based control and measurement

## Slide 31: Outline
WR standardization

## Slide 32: IEEE1588 standard revision
New IEEE-1588 standard published in mid-2019
WR became High Accuracy profile of IEEE1588-2019

## Slide 33
Q&A
Thank You !