## Slide 1
23-27. Oct. 2023，Nanjing，CEPC Workshop
CEPC Injection Delay-line Kicker Magnet R&D
Guanjian Wu
From injection & extraction team
Contributors：Jinhui Chen, Lei Wang, Xinzhe Zhai, Zilin Chen, Sen Yue, Lihua Huo, Hua Shi

## Slide 2: Content
1
Research background
3
Delay-line kicker magnet R&D
2
The task of research
4
Summary
① Delay-line dipole kicker magnet for pulsed local bump injection scheme
② Delay-line nonlinear kicker(DNLK) magnet for NLK injection scheme

## Slide 3
1. Research background

## Slide 4: Layout of the inj.&ext. systems in CEPC
Linac
DR
Booster
Collider
120GeV
1.1GeV
30~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤
⑩
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
Booster beam dump system(e+,e-)
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Overall layout of the CEPC
Composition of CEPC injection and extraction system
The CEPC complex consists of 4 circular accelerators：
1 damping ring (1.1Gev/147m)
1 booster ring (30 ~ 120GeV/100km)
2 storage rings (120GeV/100km)
there are 10 injection and extraction sub-systems, including:

## Slide 5: Off-axis injection system of CEPC collider ring
Collider operating mode | Higgs | W | Z
Beam energy (GeV) | 120 | 80 | 45.5
Function | Injection（off-axis） | Injection（off-axis） | Injectio（off-axis）
Bunch number | 242（in half ring ) -7 | 1524（uniform） | 12000
Min. bunch spacing (ns) | 680 | 220 | 25
Bunch number per train×train number | - | - | 80×150
Train spacing (ns) | - | - | 245
Injection(extraction) mode | Bunch by bunch | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440 | <2460
Kicker flat top (ns) | - | - | >1980
Kicker rise(fall) time (ns) | <680 | <220 | <245
Timing delay (ns) | <680 | <220 | <4400
Injection(extraction) period (s) | 0.242 | 1.5 | 0.15
Kick angle (mrad) | 0.1 | 0.1 | 0.1
Kick Integral field strength (Tm) | 0.04 | 0.027 | 0.015
DA_x（mm） | 13.32 | 17.82 | 13.11
DA_y（mm） | 0.4 | 0.54 | 0.74
Beam pipe aperture HxV (mm) | 75×56 |  | 
Function | Injection（off-axis）
Kicker repetition rate (Hz) | 1000
Kicker pulse width (ns) | 440~2420(Adjustable)
Kicker flat top（ns） | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <220
injection（extraction）period (s) | 1.5
Kick angle (mrad) | 0.1
Kick Integral field strength (Tm) | 0.04
Beam pipe aperture HxV（mm） | 75×56
Pulse waveform | 
Injection physics parameter of CEPC collider ring
The requirements of the CEPC collier ring injection kicker magnet system
Higgs Energy Mode：
Smaller beam dynamic aperture(DA) →On-axis swap-out injection scheme.
W&Z Energy Mode：
Enough large dynamic aperture (DA) → Off-axis injection scheme.
In order to be compatible with the two kind operation energy modes, the kicker magnet system must be a trapezoidal wave pulse discharge system with steep edges, adjustable pulse amplitude and width.
notes：beam pipe aperture of TDR is Φ56mm

## Slide 6: Trapezoidal wave kicker magnet system
Simulation result comparison of distributed parameter kicker and lumped parameter kicker system
lumped parameter kicker
Delay-line kicker
Strip-line kicker
Typical trapezoidal wave kicker magnet system
dump switch
terminating
resistor
kicker magnet
main switch
coaxial cable
RCPS
single-way delay
PFN or PFL
pulser
lumped parameter
distributed parameter
dump
resistor
Z
 | lumped inductance short circuit discharge | lumped inductance matching discharge | Delay-line kicker | Strip-line kicker
Rise Time of pulsed magnetic field （5%-95%） |  |  |  | 
The amplitude of the pulse current |  |  |  | 
 | lumped inductance short circuit discharge | lumped inductance matching discharge | Delay-line kicker | Strip-line kicker
The amplitude of the pulse current |  |  |  | 
Performance Comparison of Trapezoidal Wave Kicker Magnet System
For a trapezoid-wave kicker system, the delay-line kicker has better dynamic response characteristics than the lumped parameter kicker. The delay-line kicker better meets the requirements of trapezoid pulse magnetic field with steep edges. More importantly, the delay-line kicker in the trapezoid-wave discharge system is equivalent to a transmission line with impedance matching, which is conducive to generating and transmitting regular trapezoidal wave pulses.

## Slide 7: Two ways for off-axis injection system
Nonlinear kicker injection has the following advantages:
Reduce the number of injection components, thereby reducing the cost of construction, while reducing the beam impedance of the ring;
Reduce the disturbance to the stored beam during the injection process and achieve a more "transparent" Top-Up injection to improve the brightness of the collision integral.
Reduce the requirement of machine DA, relax the requirements of accelerator lattice optimization constraintsand and installation errors of equipment such as accelerator magnets.
Nonlinear field distribution
Local pulse bump injection
Nonlinear kicker injection
A physical image of the off-axis injection process in phase space
Comparison of two off-axis injection methods for DA
The position of the injection point in phase space

## Slide 8
2. The Task of Research

## Slide 9: The task of research
Delay-line nonlinear kicker(DNLK) magnet for NLK injection scheme
On the basis of delay-line dipole kicker magnet, we introduce nonlinear structure, design and develop the performance prototype of DNLK.
Physical design：
Kicker magnet aperture；
Kicker magnet unit；
Capacitor plate；
Electromagnetic parameter ；
Simulation and verification：
simulation of magnetic field space distribution(OPERA)；
simulation of magnetic field time distribution(PSpice)；
Preliminary mechanical design：
Establish the 3D model of the delay-line dipole kicker magnet ；
Delay-line dipole kicker magnet for pulsed local bump injection scheme
CEPC TDR adopts this scheme as the base-line scheme, we need to explore the design process of the delay-line dipole kicker magnet.
Physical design：
Eddy current shielding plate；
Kicker magnet aperture；
Kicker magnet unit；
Capacitor plate；
Electromagnetic parameter ；
Simulation and verification：
Magnetic field space distribution；
Eddy current shielding action；
Magnetic field time distribution；
Thermal power deposition of eddy current shielding plate；
Mechanical design, machining and assembly：
Ceramic vacuum chamber；
Ferrite core；
Overall mechanical structure；
Establish the 3D model；
Draw engineering drawings；
Kicker magnet parts machining；
Prototype assembly and debugging；
Performance prototype test and analysis：
Build the characteristic impedance measurement platform；
Characteristic impedance measurement ；
Build long coil magnetic field measurement platform；
Integrated magnetic field measurement；

## Slide 10
3. Delay-line kicker magnet R&D

## Slide 11: 3.1 Delay-line dipole kicker magnet
Parameters | Unit | Value
Core construction | — | Dual-C type
Integral magnetic strength | T•m | 0.04
Pulse waveform | — | Trapezoid
System rise/fall time | ns | 200
Power supply rise/fall time | ns | 80
Kicker rise/fall time | ns | 120
Pulse flat top | ns | 0~1980（adjustable）
Beam pipe aperture（H×V） | mm | 75×56
Kicker aperture（H×V） | mm | 100×80
Good field region（H×V） | mm | 20×20
Field uniformity | — | ±1.5%
Repetition rate | Hz | 1k
Typical performance of the MOSFET and IGBT
Parameter of CEPC collider ring off-axis injection dipole kicker system
Schematic diagram of delay-line dipole kicker magnet structure
Cross sectional diagram of delay-line kicker magnet
Equivalent circuit of delay-line kicker magnet

## Slide 12: Main parameters design and initial 3D model of delay-line dipole kicker
Main parameters of delay-line dipole kicker
Sectional view of delay-line dipole kicker magnet 3D model
Overall View of delay-line dipole kicker magnet 3D model
Parameters | Value
Aperture of magnet（mm） | 100×80
Longitudinal length of magnet cell（mm） | 36
Cell number of magnet | 26
Differential impedance of magnet（Ω） | 12.5
Length of magnet（mm） | 942
Total mechanical Length of magnet（mm） | 1018
Inductance of magnet cell（nH） | 56.6
Total inductance of magnet（nH） | 1471.6
Capacitance of magnet cell（pF） | 362
Total capacitance of magnet（nF） | 9.412
Magnetic strength （Gs） | 425
Exciting current of magnet（A） | 2703
Differential voltage of magnet（V） | 33791

## Slide 13: Simulation and verification of delay-line dipole kicker
Chart: X/mm
Opera 2D model of delay-line dipole kicker
x axial magnetic field distribution
Good field region magnetic field distribution
Circuit model of delay-line dipole kicker system
Time distribution of magnetic field pulse
Magnetic flux density distribution

## Slide 14: Comparison of design requirements with simulation results
Summary of performance indicators for delay-line dipole kicker magnet
Parameters | Unit | Design requirements | Simulation results
Integral magnetic strength | T•m | 0.04 | 0.04
Total rising time | ns | 200 | 193
Total falling time | ns | 200 | 191
Pulse width | ns | 440~2420（adjustable） | Determined by the pulse generator
Beam pipe aperture（H×V） | mm | 75×56 | 75×56
Kicker aperture（H×V） | mm | 100×80 | 100×80
Magnetic field strength | Gs | 425 | 421
Good field region（H×V） | mm | 20×20 | 20×20
Field uniformity | — | ±1.5% | ±0.2%
Max. flux density | Gs | ＜3000 | 740

## Slide 15: 3.2 Evolution from dipole kicker to non-linear kicker
Comparison of dipole kicker and NLK
Evolution from pulsed Multipole to NLK (red: +direction, blue: -direction)
Evolution from dipole kicker to NLK
The NLK with ferrite core has more advantages:
simpler winding structure;
smaller magnet inductance;
more excitation efficiency;
lower requirements for the shape and position errors of the electrodes.
Bunch size and DA of the colliders in different energy mode
Parameter | tt | H | W | Z
Emittance | 2.4 | 1.21 | 0.54 | 0.18
Coupling | 0.3% | 0.2% | 0.3% | 2.2%
s_x | 2.08mm | 1.48mm | 0.99mm | 0.57mm
s_y | 0.042mm | 0.025mm | 0.02mm | 0.032mm
DA_x | 20.8mm | 13.32mm | 17.82mm | 13.11mm
DA_y | 1.09mm | 0.4mm | 0.54mm | 0.74mm

## Slide 16: Main parameters design of delay-line NLK
Chart: X/mm
| -20 | -19 | -18 | -17 | -16 | -15 | -14 | -13 | -12 | -11 | -10 | -9 | -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0
R6D3L4 | 477.6653 | 483.1293 | 489.1096 | 497.1343 | 505.4754 | 515.6601 | 526.8451 | 537.9137 | 547.995 | 553.032 | 542.4448 | 477.944 | 342.9936 | 183.1838 | 79.0654 | 38.4816 | 17.002 | 7.0377 | 3.5443 | 1.4389 | 0.03086
R4D3L4 | 465.8936 | 470.8284 | 475.8401 | 482.2433 | 489.2007 | 497.4083 | 506.552 | 516.0407 | 526.3244 | 535.5431 | 539.6935 | 526.6004 | 476.4782 | 350.7443 | 190.1336 | 88.5055 | 38.6292 | 16.4126 | 7.0059 | 2.743 | -0.00088
R4D2L4 | 456.1403 | 459.3484 | 463.3329 | 468.2331 | 473.1333 | 479.9704 | 486.9878 | 495.0148 | 503.3143 | 513.053 | 521.7423 | 525.5622 | 513.1353 | 460.6379 | 341.7905 | 185.1872 | 83.3153 | 35.249 | 15.1641 | 5.9628 | -0.07279
R4D2L3 | 449.9835 | 453.0548 | 457.4798 | 461.9347 | 467.3994 | 473.9642 | 481.8295 | 490.227 | 501.1612 | 511.7431 | 525.7736 | 537.0055 | 538.6288 | 501.0707 | 346.4038 | 147.5337 | 51.7646 | 16.6491 | 6.2383 | 2.3207 | -0.00071
R3D2L3 | 446.5818 | 449.3537 | 452.1431 | 455.6522 | 459.5131 | 464.2375 | 469.9904 | 476.6364 | 484.698 | 493.363 | 503.8762 | 515.0215 | 526.5419 | 530.2387 | 494.2618 | 341.7726 | 148.4861 | 50.5052 | 15.9554 | 5.0851 | -0.00681
Comparison of field distribution of arc shielding plates with different sizes
shape | Circular arc
radius | 4mm
width | 12mm
height | 6mm
thickness | 2mm
spacing | 3mm
material | copper
The profile and parameters of the eddy current shielding plate
Parameter | value
Aperture of magnet (mm) | 100×80
Longitudinal length of magnet cell (mm) | 34
Cell number of magnet | 26
Even mode impedance of magnet (Ω) | 10
Length of magnet (mm) | 889
Total mechanical Length of magnet (mm) | 963
Inductance of magnet cell (nH) | 24.5
Total inductance of magnet (nH) | 637
Capacitance of magnet cell (pF) | 245
Total capacitance of magnet (nF) | 6.37
Magnetic strength (Gs) | 450
Exciting current of magnet (A) | 2255
Voltage between HV plate and ground potential plate (V) | 22550
Main parameters of delay-line NLK

## Slide 17: Simulation and verification of delay-line NLK
Chart: X/mm
OPERA-2D model of the NLK
Horizontal magnetic field distribution on the central plane
Magnetic field distribution of center plane at different time
Magnetic flux density distribution
Delay-line NLK PSpice model
Delay-line NLK PSpice simulation result
X=-8.4

## Slide 18: Comparison of design requirements with simulation results
Summary of performance indicators for DNLK
Parameters | Unit | Design requirements | Simulation results
Integral magnetic strength | T•m | 0.04 | 0.04
Total rising time | ns | 200 | 146
Total falling time | ns | 200 | 146
Pulse width | ns | 440~2420（adjustable） | Determined by the pulse generator
Beam pipe aperture（H×V） | mm | 75×56 | 75×56
Kicker aperture（H×V） | mm | 100×80 | 100×80
Magnetic field strength | Gs | 450 | 453
Injection point position | mm | X<11.31 | -9＜X＜-7.8
Injected beam region | mm | ＞0.99 | 1.2
Field uniformity | — | ±1.5% | ±1%
Max. flux density | Gs | ＜3000 | 600

## Slide 19: Calculation of thermal power deposition of eddy current shielding plate
Chart: t/ns
| 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200 | 4400 | 4600 | 4800 | 5000
单位长度功率W/mm | 0 | 3.22 | 6.02 | 5.06 | 4.47 | 4.04 | 3.69 | 3.41 | 3.17 | 2.97 | 2.8 | 2.65 | 0.94 | 1.74 | 1.3 | 0.97 | 0.76 | 0.67 | 0.5 | 0.41 | 0.34 | 0.29 | 0.25 | 0.21 | 0.18 | 0.16
Thermal power on the eddy current shielding plate:
Beam power deposition
Eddy current shielding effect
Beam power deposition: when the beam passes through DNLK’s eddy current shielding plate, power loss occurs due to the beam impedance effect.
-loss factor（Z ），-beam current，-bunch number，-cyclotron frequency
Opera-2D current density distribution of eddy current shield plate
Shielding plate power calculation per unit length
Unit length power of shielding plate at different times
Temperature distribution (natural air cooling)
Temperature distribution (forced air cooling)
Eddy current shielding effect: power loss due to eddy current effect on the shielding plate.
Total thermal power on the eddy current shielding plate
After applying forced air cooling
Shielding plate: Max. temperature 50℃→33℃
Ferrite core：Max. temperature 46℃ (in the normal operating temperature range√)
In order to achieve better heat dissipation, we will weld the vacuum chamber and shielding plate together, then add two water-cooled pipes.

## Slide 20: 3.3 Mechanical design, machining and assembly of DNLK-vacuum chamber
Chart: Thickness of Wall/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
Octagon | 5.18 | 6.38 | 7.59 | 10.1 | 13 | 19 | 27.7 | 46.9 | 93.7
Race track | 4.15 | 4.92 | 5.91 | 7.18 | 8.82 | 11.3 | 13.2 | 19.7 | 28.7
Oval | 3.97 | 4.45 | 5.7 | 6.63 | 8.67 | 10.6 | 12.7 | 16.1 | 20.1
Chart: Thickness of Wall/mm
| 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1
Octagon | 2.37 | 3.17 | 4.38 | 6.38 | 9.83 | 16.4 | 30.5 | 66.2 | 172
Race track | 1.78 | 2.29 | 3.04 | 4.15 | 5.83 | 8.34 | 12 | 17.5 | 25.4
Oval | 1.4 | 1.73 | 2.24 | 2.95 | 4.01 | 5.49 | 7.4 | 10.2 | 13.5
Ceramic material: 99% AL2O3,
L=1.2m，thickness=5mm
Max. stress=4.5MPa, Max. deformation=3.1×10-3 mm
√
TiN-Ag film with ladder pattern

## Slide 21: Performance test and design of nickel-zinc ferrite core
In order to make ferrite core with similar performance to CMD5005, we tested the magnetic properties of 11 batches of sample ferrite magnetic rings.
Hysteresis loop, relative permeability and Curie temperature point test and results
Complete the design and machining of the ferrite core

## Slide 22: 3D modeling and engineering drawing of DNLK

## Slide 23: Kicker magnet parts machining and prototype assembly
Kicker magnet parts machining
Performance prototype assembly

## Slide 24: Adjustment of DNLK performance prototype
Installation and measurement of eddy current shielding plate
Important dimension measurement

## Slide 25: 3.4 Prototype performance measurement - characteristic impedance
TDR(Time Domain Reflectometry):
measure characteristic impedance
According to the principle of reflection, there is a reflection coefficient ：
（Note: -the amplitude of the reflected wave，-the amplitude of the incident wave, -the impedance of the component under test, -the characteristic impedance of TDR）
Vector Network Analyzer
Line impedance=10Ω
Common-mode
Impedance=5Ω
Kicker area
Kicker area
Structural components at the transition part
Install the adapter structural components
Line impedance measure
Common-mode impedance measure

## Slide 26: Integrated magnetic field measurement
Principle of magnetic field measurement:
Use the long coil measures the integrated magnetic field：
（Note: -turns per coil，-effective coil area，-time constant of integrator ）
Pulse power supply
Coaxial cable and kicker magnet connection
Attenuator and integrator
Mobile platform of magnetic field measurement
PCB magnetic field measurement coil
Current transformer
Device of magnetic field measurement
Layout of magnetic field measuring device

## Slide 27: Integrated magnetic field measurement
200ns pulse flat top width
1.1μs pulse flat top width
2μs pulse flat top width
Clock signal
Input voltage
Output voltage
Chart: X/mm
| -13.75 | -12.75 | -11.75 | -10.75 | -9.75 | -8.75 | -7.75 | -6.75 | -5.75 | -4.75 | -3.75 | -2.75 | -1.75 | -0.75 | 0.25 | 1.25 | 2.25 | 3.25 | 4.25 | 5.25 | 6.25 | 7.25 | 8.25 | 9.25 | 10.25 | 11.25 | 12.25 | 13.25 | 14.25 | 15 | 16.25
Actual magnetic field B(A) | 47.594 | 49.39 | 50.288 | 52.084 | 53.88 | 56.6189 | 58.37 | 52.982 | 21.552 | 6.286 | 1.796 | 0.898 | 0.898 | 0.898 | 0.898 | 0.898 | -0.898 | -0.898 | -0.898 | -19.756 | -43.104 | -52.982 | -55.676 | -54.778 | -52.982 | -52.084 | -50.288 | -49.39 | -47.594 | -46.696
Theoretical magnetic field B(T) | 53.4891 | 54.4213 | 55.6351 | 56.8098 | 58.3674 | 59.6143 | 59.7944 | 55.6251 | 38.4551 | 16.3781 | 5.7465 | 1.8482 | 0.6925 | 0.2576 | 0 | -0.2584 | -0.6975 | -1.8808 | -5.615 | -16.3681 | -38.6707 | -55.7292 | -60.3957 | -59.6691 | -58.3066 | -56.9006 | -55.5432 | -54.4007 | -53.3408 | -52.5662
Nonlinear magnetic field strength distribution under 300A excitation current

## Slide 28: Experimental results of delay-line NLK
Comparison of experimental results with design indicators and simulation results
Parameters | Unit | Design requirements | Simulation results | experimental results
Line impedance | Ω | 10 | — | 10（less slightly）
Common-mode impedance | Ω | 5 | — | 5（less slightly）
Total rising time | ns | <200 | 146 | 160
Total falling time | ns | <200 | 146 | 160
Pulse flat top width | — | 0~1980ns (adjustable) | 0~1980ns (adjustable) | 0~2000ns (adjustable)
Magnetic field strength（300A） | Gs | 59.7 | 59.7 | 58.4Gs （difference 2%）

## Slide 29
4. Summary

## Slide 30: Summary
Parameters | Dipole kicker | DNLK
Magnet type | Dual-C delay-line | Dual-C delay-line
Aperture of magnet (mm) | 100×80 | 100×80
Characteristic impedance of magnet (Ω) | 6.25（odd mode） | 10（even mode）
Cell number of magnet | 26 | 26
Cell inductance of single side (nH) | 28.3 | 24.5
Magnet inductance of single side (nH) | 735.8 | 637
Cell capacitance of single side (pF) | 724 | 245
Magnet capacitance of single side (nF) | 18.824 | 6.37
Magnetic field strength (Gs) | 425 | 450
Exciting current (A) | 2703 | 2255
Voltage of magnet (V) | +/-16895.5 | +/+22550
Exciting mode | Differential mode | Common mode
Pulse waveform | Trapezoid | trapezoid
Rise/fall time (ns) | 200 | 200
Flat-top width of pulse (ns) | 40~2000 adjustable | 40~2000 adjustable
Filling time of magnet（ns） | 117.728 | 63.01
Rise/fall time of pulser（ns） | 80 | 80
Repetition rate (kHz) | 1 | 1
Design parameters of trapezoidal wave kicker system

## Slide 31: Summary
The physical design, simulation and preliminary mechanical design of delay-line kicker magnet are completed.
A new type of kicker magnet scheme – delay-line nonlinear kicker magnet is proposed and the performance prototype is developed .
1.2m ultra-long ceramic vacuum chamber is developed.
The characteristic impedance measurement of the delay-line kicker is completed.
The integrated magnetic field measurement of small aperture and large length kicker magnet is completed.
Next, we will complete the design of CEPC injection & extraction system delay-line kicker magnet engineering prototype based on TDR in two years.

## Slide 32
Thank you for your attention!

## Slide 33
Backup slides

## Slide 34: kicker magnet of injection and extraction delay-line
Injection and extraction system：Most high-energy accelerators are operated by multiple accelerators in series from low energy to high energy, including multiple injection and extraction links.
Injection:Referring to the accurate (spatial and temporal injection) of beam delivered by the transport line into the orbit of the next accelerator, and the extraction process is reversed.
System composition：A set of septum magnet & kicker magnet.
Septum magnet:Formation of strong fields and no fields in space
Kicker magnet:Generate a fast pulse deflection magnetic field in time
CERN Accelerators cluster
Characteristics of Kicker magnet:
The pulse magnetic field ：must be established and disappear quickly, and the magnetic field must be strong ;
The entire Kicker magnet ：is placed in a vacuum chamber or use a special ceramic vacuum box ;
Magnetic core:Only ferrite ['feraɪt] with high frequency or hollow [ˈhɑloʊ] structure.
Special requirements :vacuum performance and low beam impedance.
(Precision[prɪˈsɪʒ(ə)n] high voltage, high current, fast pulse electromagnetic device)

## Slide 35: Ceramic vacuum chamber with metallic coating
35
The ceramic vacuum chamber prototypes have been fabricated by a domestic company.
In house，Magnetron sputter coating is applied to achieve Ti-N-Ag film, which has higher conductivity of .
10 Pa coating atmosphere
180℃ substrate temperature
Central field deformation caused by different pattern films
Pulse B field measurement
Beam impedance measurement
A discontinous film of ladder pattern was achieved successfully to well balance shielding effective between pulsed B-field and beam wake-field.