## Slide 1: CEPC MDI Overview
Sha Bai
On behalf of CEPC MDI group
The 2023 International Workshop on the High Energy
Circular Electron Positron Collider
Oct 23-27, 2023

## Slide 2: Outline
Introduction
IR beam pipe structure
Background estimation
Mitigation design efforts
  Masks
  Collimators
  Shielding
Thermal Analysis
  HOM heating
  Synchrotron radiation
  Beam loss backgrounds
  Beam pipe thermal analysis
IP BPM
SC magnet supporting system
Fast luminosity tuning system
Summary

## Slide 3: MDI layout and IR design
The Machine Detector Interface (MDI) of CEPC double ring scheme is about 7m long from the IP.
The CEPC detector superconducting solenoid with 3T magnetic field（2T in Z）and the length of 7.3m.
The accelerator components inside the detector are within a conical space with an opening angle of cosθ=0.993. Detective angle: acos0.99
The e+e- beams collide at the IP with a horizontal angle of 33mrad and the final focusing length is to 1.9m.

## Slide 4: MDI parameters
 | range | Peak field in coil | Central field gradient | Bending angle | length | Beam stay clear region | Minimal distance between two aperture | Inner diameter of beam pipe | Outer diameter of beam pipe | Critical energy (Horizontal) | Critical energy (Vertical) | SR power (Horizontal) | SR power (Vertical)
L* | 0~1.9m |  |  |  | 1.9m |  |  |  |  |  |  |  | 
Crossing angle | 33mrad |  |  |  |  |  |  |  |  |  |  |  | 
MDI length | 7m |  |  |  |  |  |  |  |  |  |  |  | 
Detector requirement of accelerator components in opening angle | 8.11˚ |  |  |  |  |  |  |  |  |  |  |  | 
Q1a/Q1b |  | 3.5/2.8T | 142/85T/m |  | 1.21m | 14.9/18.2mm | 62.71/105.28mm | 20/23mm | 26/29mm | 724.7/663.1keV | 396.3/263keV | 212.2/239.23W | 99.9/42.8W
Q2 |  | 3.3T | 96.7T/m |  | 1.5m | 24.48mm | 155.11mm | 32mm | 38mm | 675.2keV | 499.4keV | 472.9W | 135.1W
Lumical | 0.95~1.11m |  |  |  | 0.16m |  |  |  |  |  |  |  | 
Anti-solenoid before Q1 |  | 8.6T |  |  | 1.1m |  |  |  |  |  |  |  | 
Anti-solenoid Q1 |  | 3T |  |  | 2.5m |  |  |  |  |  |  |  | 
Anti-solenoid Q2 |  | 3T |  |  | 1.5m |  |  |  |  |  |  |  | 
Beryllium pipe |  |  |  |  | 85mm |  |  | 20mm |  |  |  |  | 
Last B upstream | 64.97~153.5m |  |  | 0.77mrad | 88.5m |  |  |  |  | 33.3keV |  |  | 
First B downstream | 44.4~102m |  |  | 1.17mrad | 57.6m |  |  |  |  | 77.9keV |  |  | 
Beampipe within Q1a/Q1b |  |  |  |  | 1.21m |  |  |  |  |  |  | 1.19/1.31W | 
Beampipe within Q2 |  |  |  |  | 1.5m |  |  |  |  |  |  | 2.39W | 
Beampipe between Q1/Q2 |  |  |  |  | 0.3m |  |  |  |  |  |  | 26.5W | 

## Slide 5
Crotch point at 805mm，with slope，breeches pipe starting point at 855mm，cone，interface point at 700mm
The central beampipe design
From IP(mm) | Shape | Inner diameter(mm) | Material | Marker
0-85 | Circular | 20 | Be | 
85~180 | Circular | 20 | Al | 
180~655 | Cone | 20~35 | Al | Taper: 1:70
655~700 | Circular | 35 | Al | 
700~780 | Circular | 35 | Cu | 
780~805 | Cone | 35~39 | Cu | 
805~855 | Race-track | 39~20 double pipe | Cu | 

## Slide 6: IR beam pipe structure
The center of the beam pipe adopts a double-layer beryllium pipe structure, with an overall length of 350mm.
The thickness of the inner beryllium pipe is 0.2mm, and the outer beryllium pipe is 0.15mm.
A 0.5mm cooling gap between the double layer beryllium pipes, which is filled with coolant.
The coolant enters through the left amplification chamber, passes through the gap between the double layer beryllium pipes, and finally is discharged through the right amplification chamber, taking away the HOM heat from the inner wall through cooling.
Central beryllium pipe
Epitaxial aluminum tube structure
when both ends of the beam pipe are supported, the maximum sink at the center during the simulated installation is 0.0025 mm, and the maximum stress is 2.7 MPa, which meets the requirements and ensures the overall structural safety.

## Slide 7: Background estimation
Background sources
  Photon backgrounds: SR, Pair production
  Beam loss backgrounds
    Radiative Bhabha scattering
    Beam Gas scattering
    Beam Thermal photon scattering
  Injection background
Real beam
  Errors
  Beam-beam effect
  Beam tail
  Solenoid
Multi-turn tracking
  Using built-in LOSSMAP with one step ahead output
  SR emitting on
  RF on
  Radtapper on
Photon BG
Beam loss BG
Injection BG
A. Natochii
A. Natochii

## Slide 8: Synchrotron radiation
No SR photons hitting the central beam pipe directly in normal conditions, which is generated from the last bending magnet in the upstream of IP
However, some secondaries generated within the beam pipe of QD would hit the detector beampipe, even the beryllium part. Therefore, the mitigation methods has been studied.
SR photons generated from the FD magnets will hit downstream of the IR beam pipe, and the once-scattering photons will not go into the detector beam pipe but goes to even far away from the IP region.

## Slide 9: Radiation background
Including Radiative Bhabha scattering, Beam-Gas scattering, Beam Thermal Photon scattering.
Beam loss background from Beamstrahlung almost no in upstream IP, but mainly from pair-production distribution.
Beam loss particle distribution with collimator design.
Collimator design meet requirements of beam-stay-clear region, impedance, phase etc on.
4 sets of collimators were implemented per IP per Ring(16 in total)
  2 sets are horizontal(4mm radius), 2 sets are vertical(3mm radius).
One more upstream horizontal collimator sets were implemented to mitigate the Beam-Gas background

## Slide 10: Injection background
Mode | tt | Higgs | W | Z
Bunch Number | 37 | 240 | 1230 | 3840
Bunch Charge | 0.96 nC | 0.7 nC | 0.73 nC | 0.8 nC
Beam Current(mA) | 0.11 mA | 0.51 mA | 2.69mA | 9.2 mA
Beta_func (x/y) | 200/55 | 200/55 | 200/55 | 200/55
Emittance (nm) | 2.83 | 1.26 | 0.56 | 0.19
Bunch Length (mm) | 2.0 | 2.0 | 1.7 | 0.96
Injection beam parameters
RBB is taken into account in all cases
A simplified model of top-up injection beam
Tails from imperfectly corrected X-Y coupling after the injection point
some tolerances to imperfect beams from the booster (e.g. too large emittances)
non-Gaussian distributions existing/building up in the booster and being injected into the main rings
Gaussian beam with 3sigma
Circular beam
Injection beam
Gaussian beam with 40sigma
Large emittance ~10times
Large emittance ~1000times
Double gaussian beam
Uniform beam
Almost no beam loss background in the upstream of the IP, while significantly increased downstream.
The existed collimation system can well cope
No effect on the inner layer detector but may damage the outer layer or the endcap detector
BG downstream may damage the SC magnet coils and cause quench.
Tungsten shielding demanded in the IR.
Since the very tight space in the IP region, a tungsten-alloy beam pipe is under design.

## Slide 11: SR mitigation – mask and Au shielding
Masks design(two masks/IP/ring) :
  Tungsten
  One locates at -1.21m with 4mm height and 10mm long
  The other at -4.2m with 0.6mm height
Lots of photons are secondaries, generated within Q1
Methods | Photon hitting number on Be/BX | Deposition power on Be(W)
No mask | 39400.0 | 30.57*e-5
1.21-mask-Cu | 1736.0 | 1.45*e-5
1.21-mask-W | 1698.0 | 1.36*e-5
2.2-mask-Cu | 1147.0 | 0.94*e-5
1.21-mask-Cu-5㎛Au | 216.0 | 0.273*e-5
Photons hitting number on Be/BX reduced by two orders of magnitude
~216 photons/BX could hit Be
  ~2.73x10-6 W deposition power on Be beampipe

## Slide 12: Shielding
1. Tungsten IR beam pipe,
2. Combined iron and tungsten yoke of SC magnet
solution
Key Issues on Calculation and Simplification of Beam pipe model
White: Vacuum
Gray: Tungsten Pipe
Light Green: Helium
Heavy Green: Stainless Steel Vassel
Pink: Coil
Beam loss in the downstream IR with a large amount, due to the process of radiative bhabha scattering, beamstrahlung, beam-gas scattering, beam thermal photon scattering.
Radiation dose may damage the SC magnet coil and the detector.
Pure tungsten IR beam pipe with 4mm thickness without cooling taken into account, simulate the Absorbed Dose on Coil (Region)
Beam-Gas beam loss is taken into account until now
Take the loss rate calculated by SAD into account:
  ~0.00166 Gy/s(0.166rad/s)
  ~14.35 Gy/day
  ~36662.49 Gy/lifetime(Higgs plans to run 10 years)
  Limit is 100000 Gy/lifetime

## Slide 13: Movable collimators
Located in straight section between two dipoles, the length is 800 mm.
SR power: 7.5kW @Higgs, 30MW
Highest temperature: 124 ℃
  Particle deposition:
  Jaw material: Cu
  Total heat generation: 91.6 W
  Maximum temperature raise by particle-material reaction: 2℃

## Slide 14: HOM power distribution
results for MDI 20mm-20mm
Transition region: Racetrack (including materials)
σz=5mm: Two beam in the IR
Loss factor Trap in IR @k_trap: 0.032v/pc
Ptrap: H/W/Z/tt: 24.0w/117.1w/1160.8w/6.67w
Position | Position Start-end（mm） | material | Length (mm) | Higgs(w) & (w/cm2) | W (w) & (w/cm2) | Z(w) & (w/cm2) | ttbar（w） & (w/cm2)
Be pipe (w) | 0-85 | Be | 85 | 1.13 & 0.021 | 5.587 & 0.105 | 55.295 & 1.35 | 0.31 & 0.005
Be pipe transition(w) | 85-180 | Al | 95 | 0.61 & 0.01 | 2.950 & 0.049 | 29.280 & 0.491 | 0.172 & 0.007
Transition pipe (w) | 180-655 | Al | 475 | 6.99 & 0.017 | 34.48 & 0.085 | 341.562 & 0.83 | 1.958 & 0.005
Transition （w） | 655-700 | Al | 45 | 0.62 & 0.015 | 2.95 & 0.071 | 29.28 & 0.701 | 0.172 & 0.004
RVC bellow（w） | 700-780 | Cu | 80 | 0.52 & 0.007 | 2.532 & 0.034 | 25.002 & 0.337 | 0.14 & 0.002
Transition on Y-crotch | 780-805 | Cu | 25 | 0.16 & 0.007 | 0.785 & 0.032 | 7.822 & 0.316 | 0.05 & 0.002
Y- crotch (w) | 805-855 | Cu | 50 | 0.33 & 0.005 | 1.572 & 0.024 | 15.626 & 0.241 | 0.091 & 0.002
Quadrupole pipe(w) | 855-1100 | Cu | 245 | 1.58 & 0.005 | 7.735 & 0.024 | 75.594& 0.24 | 0.434 & 0.002
Total | 0-1100 | - | 1100 | 12.0 &0.011 | 58.594 &0.056 | 580.46 & 0.56 | 3.331 & 0.003

## Slide 15: Heat load from SR
In normal conditions, there is no SR photons hitting the central beam pipe.
Single layer beam pipe with water cooling, SR heat load is not a problem.
Region | SR heat load | SR average power density
0~780mm | 0 | 0
780mm~805mm | 23.04W | 256W/cm2
805mm~855mm | 53.39W | 296.6W/cm2
855mm~1.9m(QDa entrance） | 4.32W | 1.15W/cm2
QDa | 3.28W | 0.75W/cm2
QDa~QDb | 22.92W | 79.58W/cm2
QDb | 3.96W | 0.91W/cm2
QDb~QF1 | 71.04W | 65.8W/cm2
QF1 | 7.26W | 1.34W/cm2
In abnormal conditions, SR photons hitting the bellows (no cooling) and berrylium pipe under the extreme beam conditions , since it is a transient effect, heat load is not a problem.
In extreme cases ~ at least 10 times per day. The beam will be stopped within 0.5ms when abnormal.
The background of the detector and radiation dose should be considered under abnormal conditions.

## Slide 16: Heat load in IR from beam loss background
Region | RBB | Beamstrahlung | Beam-Gas | BTH
Berryllium pipe | 6.7mW | 0 | 0 | 0
Detector beam pipe | 0.024W | 0 | 4.8uW | 1.2uW
Accelerator beam pipe before Q1a | 0.17W | 0 | 4.2uW | 1.2uW
Q1a~Q1b | 2.13W | 3.8uW | 5.9uW | 1.8uW
Q1b~Q2 | 0.01W | 3.8uW | 0.5uW | 0.6uW
Q2 | 0.26mW | 0 | 3.7uW | 0.66uW
Beam loss particles from the process of radiative Bhabha scattering, Beamstrahlung, Beam-Gas scattering, and beam-thermal photon scattering hitting the IR beam pipe
Heat load in IR from beam loss background is so small, compared to synchrotron radiation and HOM.
The photons generated from the process of radiative Bhabha scattering, Beamstrahlung, and Beam-Gas scattering with small angle and large energy, still under analysis.

## Slide 17: Beam pipe thermal analysis
Calculation model and condition
Extending pipe:
2 inlet pipe, 2 outlet pipe
Coolant: water
Inlet temperature: 20℃
Inlet velocity: 0.5m/s（1.7L/min）
Be pipe:
4 inlet pipe, 4 outlet pipe
Coolant: water
Inlet temperature: 20℃
Inlet velocity: 0.5m/s（0.8L/min）
Extending pipe:
2 inlet pipe, 2 outlet pipe
Coolant: water
Inlet temperature: 20℃
Inlet velocity: 0.5m/s（1.7L/min）
Heat source distribution
Calculation results:
Temperature difference ~5.10C between two sides of the first layer detector
Temperature low, temperature difference small, meet the requirement

## Slide 18: IP BPM
Considering response time and calibration difficulty, two 4 button electrodes BPM in double pipe and one 2 button electrodes BPM in single pipe at each side of CEPC IR are adopted.
2 button electrodes BPM for measuring the arrival time.

## Slide 19: SC magnet support system
After the optimization of the supports in the cryostat, the total weight of the cryostat and the devices inside is 2790 Kg.
The cryostat is about 5.6m long. The cantilever length is 5283mm.
The resolution requirement of the adjusting mechanism < 5 μm.
Vacuum vessel
Helium vessel
Support rods
Q1a
Q2
Anti-solenoid
Q1b
Thermal shield

## Slide 20: Fast luminosity tuning system
Motivation
With very small beam sizes at IP and the presence of strong FFS quadrupoles in the CEPC, the luminosity is very sensitive to the mechanical vibrations, It is essential to the fast luminosity measurements and IP orbit feedback.
In principle, there are two possible methods used for the IP orbit feedback system.
  Beam-Beam deflection driven method for vertical
  Fast luminosity monitor for horizontal
IP
1
2
3
 | Position1 | Position2 | Position3
Average Number detected/BX | ~3.4(Two sides) | ~3(One Side) | ~3.2(One Side)
Average Bhabha Number /1ms | ~2830 | ~2500 | ~2670
Expected measurement accuracy | 1.9%@1kHz | 2%@1kHz | 1.95%@1kHz
Average Energy of Pris | ~24 GeV | ~70 GeV | ~75.3 GeV
Average Hitting Angel | ~1.7E-4 rad | ~7E-4 rad | ~7E-4 rad
Tmax in mm | 88.32 | 103.85 | 104.91
Detector Size assumed | 5*20 cm2 | 3*15 cm2 | 3*15 cm2
Backgrounds | SR Photons in 1 Side | - | -
Pros | Measurement affected by beam-beam deflection angle, two detectors | signals only on one side, measurement quite independent of beam-beam deflection angle | 
Detector technology | LGAD; SiC; Diamond |  | 
Average Number detected/BX | ~3.4(Two sides) | ~3(One Side) | ~3.2(One Side)
Average Bhabha Number /1ms | ~2830 | ~2500 | ~2670
Expected measurement accuracy | 1.9%@1kHz | 2%@1kHz | 1.95%@1kHz
Average Energy of Pris | ~24 GeV | ~70 GeV | ~75.3 GeV
Average Hitting Angel | ~1.7E-4 rad | ~7E-4 rad | ~7E-4 rad
Tmax in mm | 88.32 | 103.85 | 104.91
Detector Size assumed | 5*20 cm2 | 3*15 cm2 | 3*15 cm2
Backgrounds | SR Photons in 1 Side | - | -
Pros | Measurement affected by beam-beam deflection angle, two detectors | signals only on one side, measurement quite independent of beam-beam deflection angle | 
Detector technology | LGAD; SiC; Diamond |  | 
Currently,
  Using 4 sets of BPMs each ring and located at or near the largest beta function can be used for vertical orbit feedback in principle.
  The Fast Luminosity Monitor are needed as input to luminosity optimization and feedback. We already have some candidate positions and potential detector solutions.
  Generate and track radiative Bhabha electrons at zero degree, find possible positions where the loss rate is large enough and radiative Bhabha at zero degree process dominates over the sum of other particles loss processes.

## Slide 21: Summary
The MDI layout is compatible and no interference for the design.
Φ20mm~ Φ20mm IR beam pipe is well designed.
The estimation of the radiative background from photon background, beam loss background and injection background has been estimated with real beam.
The mitigation efforts of every kinds of background dedicated to the mask, collimator and shielding has been designed.
The thermal analysis including HOM heating, synchrotron radiation, beam loss background and beam pipe thermal analysis meet the requirement.
Considering response time and calibration difficulty, two 4 button electrodes BPM in double pipe and one 2 button electrodes BPM in single pipe at each side of CEPC IR are adopted.
The SC magnet supports inside the cryostat are designed and optimized.
Fast Luminosity Tuning System, including fast BPMs and fast luminosity monitor, would be necessary for CEPC. In future, more detailed simulations needs to study more, including determine the detailed location and quantity of BPMs and the reaction between the primary Bhabha scattering electrons and beam pipe, as well as the design of detectors and feedback.

## Slide 22
Thanks