## Slide 1
Progress in the mechanical design
of CEPC /MDI detector
Junsong Zhang，Quan Ji ，Shu Chang，Xia Shang, He Longyan

## Slide 2
Content:
General introduction
Progress of MDI design
Iron yoke
Superconcuction solenoid
ECAL
Beam pipe
summary

## Slide 3
General introduction
Updated design in 2023 :
1) Beam pipe:LumiCal and BPM
2) Yoke:Muon: 7 layers
3）Structure of ECAL
4）Superconducting solenoid: coil support structure
iron yoke
HCAL
superconductiion solenoid
ECAL
beam pipe
iron yoke
HCAL
ECAL
superconductiion solenoid
end-iron yoke
end-iron yoke

## Slide 4
Content:
General introduction
Progress of MDI design
Iron yoke
Superconcuction solenoid
ECAL
Beam pipe
summary

## Slide 5
CEPC yoke
height：8.5m
long：11.1m
MDI total weight：3000T
yoke total weight：1000T
Design progress in 2023
added 2 muon detectors
easy to assemble
structure reliability
CEPC MDI profile structure
General introduction of yoke

## Slide 6
2018.12
thickness: 600mm
Muon: 3 layers
height: 9600mm
weight: 920 t
2020.1
thickness: 1460mm
Muon: 4 layers
height: 12120mm
weight: 3180 t
2021.3
thickness: 600mm
Muon: 5 layers
height: 8520mm
weight: 760 t
added muon detector
cost reduction
symmetric type
spiral type
2023.6
thickness: 600mm
Muon: 7 layers
height: 8520mm
weight: 520 t
Computational check
Design process of iron yoke

## Slide 7
According to the preliminary verification calculation, the model is adjusted as follows:
end-yoke：Seven-layer muon detector，thickness：900mm；
barrel-yoke：Seven-layer muon detector，thickness：600mm；
symmetry
yoke uint of symmetry style
yoke uint of spiral style
spiral
end-yoke
Objective: To improve the resolution of detector.
Progress: At present, the design model has been modified. The next step is to calculate the deformation of the yoke iron under the action of gravity and magnetic field when the space of seven-layer µon detector is placed.
New progress for iron yoke

## Slide 8
parameter：
thickness: 600mm
Muon: 7 layers；
materials：T10 ；
loading：560T；
Under the action of gravity, the structural strength of spiral structure is greater than that of symmetrical structure. This is because the spiral structure has some rid plates in the middle of barrel .
maximum stress77.591MPa
maximum deformation1.667mm
symmetry
spiral
maximum stress151.74MPa
maximum deformation40.979mm
Yoke iron simulation calculation
Result No.1

## Slide 9
Number of layers | 3 | 5 | 7
deformation | 3.2192 | 7.8251 | 40.979（35+35+30）
 |  |  | 19.161（65+65+20）
 |  |  | 19.322（95+35+20）
Result of self-weight deformation of symmetrical barrel iron yoke
When the upper plate and the lower plate thinkness of the yoke uint are added, the stiffness of the yoke iron can be increased. There is same result for spiral structures.
Upper and lower plate: 65mm, layers: 20mm（65+65+20）
Yoke iron simulation calculation
Result No.2

## Slide 10
The number of yoke supports will also affect the stiffness of the yoke. When the number of support of the symmetrical yoke structure is increased to 5, the overall deformation will be greatly reduced.
Yoke iron simulation calculation
Result No.3

## Slide 11
Content:
General introduction
Progress of MDI design
Iron yoke
Superconcuction solenoid
ECAL
Beam pipe
summary

## Slide 12
Superconducting solenoid general design
Design of coil hoisting structure。
The design goal is to secure the coil inside the thermostat
coil
The maximum distence from coil to vacuum devar is 37mm. Space is very limited. The distance from the inner surface of the coil to the surface of the vacuum inner dewar is 21mm. The design is difficult.

## Slide 13
Vertical support structure
Axial positioning structure
The superconducting coil fixing scheme adopts two vertical support structures and four axial positioning structures. The vertical support structure carries the overall weight of the coil. One end of the support structure is fixed on the aluminum support barrel and the other end is fixed on the vacuum dewar.
The coil support of the superconduction solenoid design

## Slide 14
axis of rotation
belleville spring
link plate
The rotating shaft allows the support structure to adapt to the deformation of the coil at low temperature, and the disc spring and long groove are installed at the position of the mounting hole to achieve the fixation under low temperature deformation.
The coil support of the superconduction solenoid design

## Slide 15
Content:
General introduction
Progress of MDI design
Iron yoke
Superconcuction solenoid
ECAL
Beam pipe
summary

## Slide 16
ECAL General design
The composition of detector module：
Horizontal and vertical crystal strips
The detector module are fixed together in radial direction and axial direction.
整体排布示意

## Slide 17
ECAL design
“有”PCB的结构优化
PCB plate
Group 1:37X2 + 41X2 = 156
Group 2:37X2 + 42X2 = 158
Group 3:37X2 + 43X2 = 160
Group 4:37X2 + 44X2 = 162
Group 5:37X2 + 45X2 = 164
Group 6:37X2 + 46X2 = 166
Group 7:37X2 + 47X2 = 168
Number of crystal every group in one module.
unit hight：28X10=280mm(<300)
unit size(7 group)：413，423，433，443
453，463，473
ECAL longth：373 X 17
detector module size
ECAL module
The installation of detector PCB board was increased, and the size of detector module and the number of crystal strips were adjusted accordingly

## Slide 18
Overall honeycomb structure
400mm
280mm
Electromagnetic calorimeter adopts carbon fiber structure processing frame, detector frame structure as shown in the figure.
When installing the detector , install the detector module in the top column, and then rotate the fixed angle to install the next column.
ECAL total weight 180 tons;
There are 476 crystal units;
There are 539784 crystal bars in total.
It will be studied whether the frame structure meets the load-bearing requirements
The manufactury process is very diffcult.
Can aluminum or carbon fiber meet the stiffiness for the honeycomb structure ?
ECAL installation scheme design

## Slide 19
Content:
General introduction
Progress of MDI design
Iron yoke
Superconcuction solenoid
ECAL
Beam pipe
summary

## Slide 20
General introduction of beampipe
d. Carbon fiber cylinder
c. Air channel
b. The central Be pipe
a. The extending Al pipe
Vertex
LumiCal
LumiCal
BPM
BPM
General drawing
Extending pipe
Both sides : Double
Top and Bottom : Single
Basic Structure:
1) Components : a, b, c, d and e
2) Detectors : BPM, LumiCal and Vertex
e. Combination flange
Updated design :
1) Added detector : BPM
2) Extending pipe : The Extending pipe is designed from conical pipe to runway profile
3) Thermal analysis of Beampipe
Total length : 1400 mm

## Slide 21
Detailed Structure
Three detectors --- BPM and LumiCal
Installation position
BPM
1. A 2 or 4 electrode-BPM is installed in
each flange
LumiCal
1. Near the flanges, axial length is 120mm
BPM : 2 or 4 electrodes
LumiCal
The runway type structure is for greater installation space for the lumical

## Slide 22
Detailed Structure
The extending Al pipe --- Gradient runway type
Installation space for LumiCal
Thickness of single layer beryllium sheet : 1.5 mm
The extending Al pipe
Double layer
construction
Double layer
construction
HOM heat
Take away
HOM heat
Take away
Coolant : H2O
Total length : 525 mm

## Slide 23
Detailed Structure
Three detectors --- Vertex
Air-cooled channels and support structures
Air-cooled inlet
Air-cooled inlet
Air-cooled outlet
Air-cooled outlet
Cooled structure :
Three layer air cooled channel
Take away
The heat generated
by chips and electronics
Three double layers
Four inlets , four outlets
Design requirement
T ≤ 20 °C
△T < 10 °C or 7 °C
Vibration < 1μm (?)
The Vertex detector contains only barrel part which
consists of three double layers
In the next step, we need to calculate the air cooling effect and stability of vertex detector

## Slide 24
Simulation analysis
Thermal analysis --- Beampipe
Try to decrease the surface temperature further to meet the requirements of detectors
Outer surface temperature of the beampipe : ≤ 20 °C
For the design of the new beam pipe, it is necessary to carry out temperature check calculation
The design principle is to keep
the outer surface temperature as low as possible

## Slide 25
Simulation analysis
Thermal analysis --- Beampipe
Inlet temperature: 16℃
Inlet velocity : 0.8 m/s
Laminar
Coolant : Paraffin or H2O
4 inlet, 4 outlet
Inlet temperature: 16℃
Inlet velocity : 1 m/s
Turbulent
Coolant : H2O
2 inlet, 2oulet
Inlet temperature: 16℃
Inlet velocity : 1 m/s
Turbulent
Coolant : H2O
2 inlet, 2 outlet
Results
Of the overall
Coolant : paraffin
Coolant : H2O
The temperature of the central pipe meets the design requirements
Highest temperature position(Transition section)
T(Max) : 31.1℃
T(Max) : 26.7℃
We need to study the corrosion of water to beryllium next step.

## Slide 26
Simulation analysis
Thermal analysis --- Beampipe
Results
Of the extending Al pipe
Top temperature
Bottom temperature
Temperature of Be sheet
Section temperature distribution(x=585mm)
Outer surface temperature
of the extending Al pipe

## Slide 27: summary
Based on the installation of spiral yoke mechanism, the next step is to optimize the design of yoke base, crane and installation station
The structure of superconducting magnet must be calculated and optimized in more detail
For ECAL, the material for the frame structural needs to be studied, and the thickness of the frame structure and the crystal module size need to be optimized
The next step is to perform air-cooling simulation analysis on the vertex detector of the beam pipe, and simulate the vibration generated by air cooling ,and verify the cooling effect ,and study corrosion of water to beryllium.
they will be disigned after the physical requirements are given
Iron yoke
Superconducting soleniod
ECAL
Beam pipe
Other detectors

## Slide 28
Thanks