## Slide 1: Thermal bonding Micromegas and its application in TPC and muon tracker
Zhiyong Zhang
For the USTC MPGD group
State Key Laboratory of Particle Detection and Electronics, China
University of Science and Technology of China

## Slide 2: Outline
  Thermal bonding Micromegas
  Method and performance
Readout for TPCs
  Low and high pressure
Muon tracker
  Large detector and muography
Summary

## Slide 3: Outline
  Thermal bonding Micromegas
  Method and performance
Readout for TPCs
  Low and high pressure
Muon tracker
  Large detector and muography
Summary
1
Method and resistive anode
2
Detector performance
3
Ultra-low IBF with DMM and TMM

## Slide 4: The thermal bonding method
The thermal bonding method provides a concise and etching-free mass-productive process to fabricate Micromegas-like detector.
Micromegas in a Bulk
No etching, no pollution
Easy to handle at lab
Easy to make new structures
Easy to extend to large area
Less than 1% spacer area
High efficiency
Thermal bonding processing

## Slide 5: A novel resistive anode using a germanium film
2D sheet resistivity distribution of the Ge film sample with Non-uniformity of RMS/mean =6.7%
~ m2 coating area, 100 nm -1 μm film thickness
Sheet resistivity changes as a function of time for different thicknesses of Ge films
Jianxin Feng, Zhiyong Zhang, Jianbei Liu et al., NIM-A 1031 (2022) 166595.

## Slide 6: Fabrication site for production
600×600 mm2
400×400 mm2
Dedicated site for mass production (540 m2 )
Full-developed equipment and fabricating process
M2 scale capability

## Slide 7: Basic Performance
X-ray test（5.9 keV）
  Gas gain：~105 (Ar+7%CO2)
  Energy resolution：~15% (FWHM)
  Non-uniformity: ~5% for 30×30 cm2
Electron beam（5GeV）
  Efficiency：>98%
  Spatial resolution：65μm
~105
σX=65 μm
ε >98%
RMS/MEAN=~5%
~15% (FWHM)
Jianxin Feng, Zhiyong Zhang, Jianbei Liu et al., NIM-A 989 (2021) 164958.

## Slide 8: High counting rate
Border grounding
Grid-dot grounding
The counting rate here is for 8 KeV x-rays, the case of MIPs should almost be 10 times higher due to its much lower energy deposition.
Which is successfully used in a high rate neutron detector for BNCT beam monitoring
Zhujun Fang, Zhiyong Zhang*,NIM-A, A 1053 (2023) 168361.
> MHz/cm2

## Slide 9: Motivation of low IBF
UV light：CsI，~mC/cm2
Visible light：Bi-alkali, ~μC/cm2 ！
A. Lyashenko et al. , NIM A 598(2009) 116-120
Gas-PMT：
F-R-MHSP_GEM_MHSP
IBF: 0.03%
  ALICE upgrade, ILD, CEPC R&D
    To minimize field distortion due to ion space charge
    Continuous readout to keep up with high event rate
CEPC-TPC
ALICE-TPC
Quadruple GEM, IBF < 1%
Gain×IBF<~5，IBF <~ 0.1%
  High rate TPC
  Gas photon detection
    High gain: to be sensitive to single photons
    Very low IBF

## Slide 10: Low IBF with the DMM
DMM: Double Micro-Mesh gaseous structure
Hole-type → mesh-type : to strongly reduce IBF
Double mesh: cascading avalanche for high gain
~0.2 mm
~0.1 mm
PA
SA
Drift region
~3-5 mm
To push IBF down to very low level:
low PA electric field
large PA gap
high mesh density
crossing mesh setting
Zhiyong Zhang et al., NIM-A 889 (2018) 78–82
BinbinQi et al., NIM-A 976 (2020) 164282
The product of IBF and gain to < 1 at 2000 gas gain, fulfills the CEPC TPC requirements.

## Slide 11: Ultra-low IBF with the TMM
TMM: Triple Micro-Mesh gaseous structure
One more mesh on the DMM
More stable gain, lower IBF from second avalanche…
Test with a laser, high gain above 106 for single photon and very low IBF of 3×10-5 are achieved, which is 10 times better than that of the DMM.
~0.2 mm
~0.1 mm
PA
TA
Drift region
~3-5 mm
SA
~0.2 mm

## Slide 12: Outline
  Thermal bonding Micromegas
  Method and performance
Readout for TPCs
  Low and high pressure
Muon tracker
  Large detector and muography
Summary
1
  12C(12C,α)20Ne reaction experiment
2
  PandaX-III experiment

## Slide 13: Study of the 12C+12C fusion reaction
The 12C+12C fusion reaction is crucial in stellar evolution
  A large uncertainty in the reaction cross section at stellar energies ((Ec.m.<3MeV)
  The main products of 12C+12C are n, p and a
  A TPC technique was developed to measure lower stellar energies with high intensity beam
  LEAF has delivered 50puA, the highest beam intensity ever realized in the carbon fusion experiments
Collimator
Si wall
Window
TPC
Target
Low Energy Accelerator Facility (LEAF)
Courtesy of the nuclear astrophysics group (IMP)

## Slide 14: Challenges for TPC detector
Detector challenges
  30-100mbar He based gas
  High gain for proton measurement
  Low event rate long term stability
  High x-ray radiation
  high rate capability, low IBF to reduce the space charge
Solutions
  Simulation to optimize the design for low pressure
  Resistive anode with fast grounding
  DMM to improve the gain and suppress the IBF

## Slide 15: Fabrication and test of the detectors
Thermal bonding Micromegas
Garfield simulation
50 mbar He+CO2
Test with carbon beam
120 mm × 240 mm
Gain
Avalanche gap (mm)
Detector design
  500 μm avalanche gap for low pressure
  High opening rate mesh (~63%) for electron collection
  Ge coated anode for high gain and long term stability
  Fast grounding to deal with high X-ray radiation from the target
  DMM are used for high gain and low IBF
Ea/Ed
Transparency

## Slide 16: PandaX-III experiment
Requirements for detector
  Low radioactive background
  Long-term stability at 10 bar Xenon (1%TMA)
  Energy resolution 3% @ 2.458 MeV
  20×20 cm2 MMs for charge readout (52)
Neutrino physics
  Lepton number non-conservation
  Neutrino nature: Dirac () or Majorana ()
  Absolute neutrino mass scale
  The type of neutrino mass hierarchy (normal, inverted)

## Slide 17: Design and fabrication of the detectors
Stainless steel mesh
Thermal bonding film
Flexible PCB
  Ge anode
  Copper strip
Pure copper substrate
Design for High radiopurity
<20% (FWHM) energy resolution
>10000 gas gain
Test at 10bar Ar(2.5% Iso) with a 5.9 keV X-ray source
>150 hours
12/2019
02/2020
04/2020
08/2020
11/2020
V1
V2
V3
V5
V4
V6
06/2021-now
Very low background rate: μBq/cm2
Sample |  |  |  |  | 
Thermal bonding | 3.55±1.64 | <0.01 | 11.98±1.68 | 24.96±9.22 | 0.37±0.31
Micro-bulk | <9.3 | <13.9 | 26.3±13.9 | 57.3±24.8 | <3.1
Sample |  |  |  |  | 
Thermal bonding | 3.55±1.64 | <0.01 | 11.98±1.68 | 24.96±9.22 | 0.37±0.31
Micro-bulk | <9.3 | <13.9 | 26.3±13.9 | 57.3±24.8 | <3.1

## Slide 18: Assembly for 52 detector prototype
Readout plane with 52 Micromegas
Detectors installation completed
There are still some key issues to overcome before the operation of the prototype

## Slide 19: Outline
  Thermal bonding Micromegas
  Method and performance
Readout for TPCs
  Low and high pressure
Muon tracker
  Large detector and muography
Summary
1
  Large area muon tracker
2
  Muography

## Slide 20: MPGD in collider experiments
Demands for muon tracker
  Large area: ~m2
  high spatial resolution: ~100 μm
  High counting rate: 10 k- 1M Hz/cm2
 | Vertex | Inner tracker | PID | Hadronic CAL | Muon tracker
ATLAS | GOSSIP/ InGrid |  |  |  | 1200 m2 MM
ALICE |  | TPC (130 m2 GEM) | VHPMID (CsI THGEM) |  | 
CMS |  |  |  | FCAL (GEM,MM) | 1000 m2 GEM
CEPC (R&D) |  | TPC(GEM,MM) | RICH(THGEM, MM,DMM) | DHCAL (GEM, THGEM,RPWELL） | 
ATLAS NSW muon detector:
600 -15k Hz/cm2 counting rate ~2-3 m2 for a single detector, 1280 m2 in total
CMS muon spectrometer:
~50 kHz/cm2 （ME0）~0.3 m2 for a single detector, ~350 m2 , ~1000 m2 foil，in total

## Slide 21: Muon tracker Micromegas
150×150 mm2
400×400 mm2
600×600 mm2
Size | Readout design | Spatial resolution | Efficiency
150×150 | Single side | < 100μm | >95%
400×400 | Single side | ~500μm | ~95%
600×600 | Back to back | ~350μm | ~95%
Single side
Back to back
400μm strip pitch
Larger detectors usually have worse resolution most possibly due to S/N ratio, alignment, PCB bending.
Back to back design can improve the resolution by reduce the PCB bend caused by tension mesh and gas flow
More alignment, correction are needed to improve the results

## Slide 22: Muography facilities
μSTC: μ(muon) Scattering tomography & Transmission imaging faCility
2 cm
Yu Wang, Zhiyong Zhang, Shubin Liu et al., IEEE TNS, vol. 69, no. 1, pp. 78–85, Jan. 2022.
Small prototype:
6 layers of 15×15cm2
~100 μm resolution
Schematic design :
Larger prototype:
8 layers of 40×40cm2
60×60cm2
~100 μm resolution

## Slide 23: Tomography study with small size prototype
Yu Wang, Zhiyong Zhang, Shubin Liu et al., IEEE Transactions on Nuclear Science, vol. 69, no. 1, pp. 78–85, Jan. 2022.
https://doi.org/10.1109/TNS.2021.3137415.
2 cm
4-hour exposure
24-hour exposure

## Slide 24: Radiography of Mt. Dashu
An ancient volcano formed 65 million years ago
Adjacent to the urban area of Hefei city
Altitude of the mountain and facility location is 280m and 60 m respectively
The prototype was set at horizontal angle
Recording muons from both mountain side and the other side (for reference)
Test for duration of ~100 days
The plotted data used: ~15 days

## Slide 25: Summary
Thermal bonding method
  High performance Micromegas with large area
  New structures of DMM and TMM for high gain and ultra-low IBF
Readout for TPC
  Low pressure TPC for nuclear physics experiment
  High pressure TPC for rare event searching
Muon tracker
  Large area detector with high spatial resolution
  Facility for muography study
Thank you

## Slide 26: High pressure xenon test
Signal of a cosmic muon
One of the key issues is stable operation under high pressure xenon
We have recently made landmark progress:
  Gas 10 bar Xe+1%TMA
  Duration：~10 days
At a gas gain of ~1000

## Slide 27: Assembly and test of 7 detector prototypes
1-10 bar Ar+2.5%Iso gas
Using X-ray sources of 55Fe, 241Am, 137Cs
No-signal channels due to the bad connections