## Slide 1: An Instrumentation suite for the HBS
Okt 16, 2023 I Jörg Voigt
UCANS 10, Budapest
Notes: Alle Vorträge mit derselben Titelfolie; Nur der Untertitel (also Volume 1, 2, 3, 4) und Namen der AutorInnen wird geändert

## Slide 2
Published summer 2023, https://hbs.fz-juelich.de/
HBS project
Notes: 2

## Slide 4
Accelerator Based Neutron Sources
From CANS* to HiCANS**
0.01 kW | 0.1 kW | 1 kW | 10 kW | 100 kW
0.001-0.01 mA | 0.01-1 mA | 0.5-5 mA | 1-20 mA | 50-100 mA
~1011 n/s | ~1012 n/s | ~1013 n/s | ~1014 n/s | ~1015 n/s
10 Mio EUR 500 Mio EUR
Running CANS facilities:
LENS, Indiana University (USA)
HUNS, Hokaido University (Japan)
RANS, RIKEN (Japan)
NUANS, Nagoya University (Japan)
CPHS, Tsinghua University (China)
IREN, JINR Dubna (Russia)
HiCANS projects:
HBS, JCNS (Germany)
SONATE, CEA LLB (France)
ARGITU, ESS Bilbao (Spain)
LENOS, INFN LNL (Italy)
SARAF, SOREQ (Israel)
(*Compact Accelerator based Neutron Source , ** High-Current Accelerator based Neutron Source)

## Slide 5: Optimization from Source to detector
Optimal pulse length
Medium pulse good resolution w/o chopper
Optimal frequency
Pulse pattern for novel high energy applications
Optimal spectrum
Fast and resonance neutrons
Low frequency wide band & pulse shaping
High frequency Narrow band  ideal secondary time frame
Cold neutrons deep from para lH2
Long pulse low resolution & pulse shaping
Thermal neutrons
HBS: A High Current Accelerator-driven Neutron Source (HiCANS)
Notes: Multi target facility: Uncompromised properties for specific application
Weak source strength: Adapt, exchange or add target station with reasonable effort

## Slide 6
Still compact: The target-moderator-reflector unit
6/37
Target-Moderator-Reflector Unit
Compact TMR design + high current accelerator:
Efficient coupling of neutron production and moderation
Confined thermal neutron cloud
High neutron thermal peak flux
Good coupling of cryogenic moderators
→ High Brilliance
Target
Reflector
Moderators
Ta
Top view
Side view
Thermal neutron cloud in PE moderator
Confinement is crucial
Notes: Wedge shaped target within moderator
Cold “finger moderator”
Direct coupled neutron optics

## Slide 7: Different pulses for different applications
96 Hz 24 Hz
1.6%
τproton : 167 µs
τneutron: 252 µs
τproton : 667 µs
τneutron: 665 µs
Consequence:
An instrument of 4 times the length installed on the 24 Hz station has the same bandwidth and about 33% less wavelength uncertainty compared to one on the 96 Hz station
Sufficient ToF-resolution
Medium bandwidth
FOM: Mean Brightness / pulse width
Low ToF-resolution or pulse shaping
Broad bandwidth
FOM: Pulse Brightness

## Slide 8: Moderator contribution to resolution vs. Bandwidth
Long pulse source
  Low resolution SANS & Reflectometry N(R )SE methods
  High resolution Pulse shaping instruments
Short(er) pulse source
  Modest resolution Single Xtal diffraction Diffuse scattering
  1 Å < ∆l < 4 Å Focusing specific dynamic range

## Slide 9: Multi Beam Reflectometer
From small samples to GISANS

## Slide 10: Instruments for tiny samples
Novel neutron optics to illuminate sub mm samples
Macro-molecular diffractometer
Perfect illumination of virtual source
E.g. 2 Å < l < 4 Å, dl = 0.05 Å
Flux ≈ MaNDI@SNS (relaxed ToF-resolution)
Notes: Small samples  extract small beams
Needs a bright cold neutron source

## Slide 11: Polarized diffuse neutron scattering (PDNS)
  Diffuse (magnetic) scattering
  H2 moderator
  96 Hz target station
  21 m length (moderator to detector)
  Polarization and avoidance of direct line of sight by mirror stack
  Detector range: 120° in 2° - 160°
  Bandwidth: 2.0 Å, standard: 2.0 – 4.0 Å
  Wavelength range: 2.0 – 6.0 Å
  Wavelength resolution: 1.2% – 2.4% (θ > 30°)
  Estimated flux (polarized): 5·107 n/(cm²s)
W. Schweika et al.
PRX May 2022
DNS
Frustrated
Magnetism

## Slide 12: Crystal analyzer spectrometer
Narrow bandwidth for focused view in reciprocal space
Crystal analyzer Spectrometers
  The TAS successor
  108 n/cm2/s within Dl = 0.7Å
Weber et al. Science 375 (2022)
Skyrmion Excitations
Full pulse
∆l = 0.7 Å
2º x 2º collimation
 108 n/cm2/s
Notes: Indespensible tool to study order or disorder and excitation of spins
spectral range below 6 Å essential
natural bandwidth and resolution at high frequency target

## Slide 13: Thermal powder diffractometer (TPD)
Narrow l resolution: Pulse shaping + wavelength frame multiplication (WFM)
  Powder diffraction on novel materials
  Thermal moderator
  Low frequency (24 Hz, 667 µs)
  80 m total length, 2 frames
  Detector range: 7° - 175°
  Bandwidth: 2.06 Å, standard: 0.62 – 2.68 Å
  d-range : 0.22 – 7.1 Å
  High-Resolution option (100 µs pulse)
    Resolution: 0.11 – 0.82% (θ>90°)
    Estimated sample flux: 5.5·105 n/(cm²s)
  High-Intensity option (667 µs pulse)
    Resolution: 2.2 – 4.7% (θ>90°)
    Estimated flux at sample: 1.6·108 n/(cm²s)

## Slide 14: Crystof
Monochromator + Multiplexing  Flux ~ TOPAS @FRM2

## Slide 15: Neutron Imaging & Analytics
Car, aviation,
building industry
Energy materials
Magnetic materials
Hydrogen storage
Cultural heritage
Geology
Environment
Archeology
Paleontology
N. Kardjilov et al., Materials today 21, 652 ff (2018)
Notes: Emerging field of applications
Potential to raise new users from industry and arts
Explore specimen deep below the surface non-destructively

## Slide 16: Neutron imaging and Analytics
ToF-PGNAA (1 meV - 100 eV)
Target station 24 Hz
ToF analysis adds information about element distribution
PGAINS (10 keV - 10MeV)
Target station Epi
Cold NI
Bragg-edge imaging
Dark-field imaging
Polarized neutron imaging
Thermal NI
Bragg-edge imaging
Dark-field imaging
Polarized neutron imaging Real-time radioscopy
Resonance NI
Special pulse pattern for Tof analysis
Fast NI
Large and dense objects
Notes: Exploit full range of the neutron spectrum
Use the tof analysis to extract more information

## Slide 17
Large structure Instruments
Diffractometers
Spectrometers
Imaging and Analytics

## Slide 18: Conclusion
HBS can cover the full range of neutron scattering applications
Excellent performance of dedicated instruments
Intense small beams
Low Background
ToF enhanced imaging and analytics instruments
New opportunities for science, industry and arts
Flexibility: Lean design to adapt to new challenges and develop new ideas

## Slide 19
HBS Team
J. Baggemann
Th. Brückel
T. Claudio-Weber
T. Cronert (†)
Q. Ding
P.-E. Doege
T. Gutberlet
J. Li
K. Lieutenant
Z. Ma
E. Mauerhofer
N. Ophoven
U. Rücker
N. Schmidt
A. Schwab
E. Vezhlev
J. Voigt
P. Zakalek
- Core group: design, verification,
instrumentation
ZEA-1:
Y. Bessler
R. Hanslik
R. Achten
F. Löchte
M. Strothmann
- Engineering
IKP-4:
O. Felden
R. Gebel
A. Lehrach
M. Rimmler
R. Similon
- Nuclear physics
INM-5:
B. Neumaier
- Radio isotopes
S. Böhm
J.P. Dabruck
R. Nabbi
- Nuclear simul.
C. Lange
T. Langnickel
Ch.Haberstroh
M. Klaus
S. Eisenhut
- AKR-2, liquid H2
H. Podlech
O. Meusel
- Accelerator
W. Barth
- Accelerator
/ HIM
Notes: 19

## Slide 20
Accelerator system
From compact to large scale facility
Hi-CANS (HBS):
Average power: 3 x 100 kW
Energy: 70 MeV
Peak current: 100 mA
Particle Type: Proton
Length: 70 m
CANS (RANS):
Average power: 700 W
Energy: 7 MeV
Peak current: 0.1 mA
Particle Type: Proton
Length: < 10 m

## Slide 21
Neutron production
Still compact: The target
High neutron yield
High blistering threshold
Compact design allowing efficient feeding of moderators
Save operation at 100 kW at 100 cm² (1kW/cm²)
Water coolant
Reliable
Neutron yield of 1015 n/s
Tantalum target with microchannel design
70 MeV Protons
Water beamstop
0.35 mm microchannels
Irradiation area
Coolant inlet
outlet
10 x 10 cm2
< 2 cm

## Slide 22: Low Resolution, very wide Band
SANS, Reflectometry and Spin Echo spectrometers

## Slide 23: SANS Suite to cover nm to µm STructures
1Å
10Å
100Å
1000Å
1µ m
SANS
VSANS
SESANS
Q
1Å-1
0.1Å-1
0.01Å-1
0.001Å-1
10µ m
10-4Å-1
10-5Å-1
C
C

## Slide 24: Modest resolution, wide Band

## Slide 25: Instruments for tiny samples
Novel neutron optics to illuminate sub mm samples
Only “good neutrons” leave target
Low Background
Little beamline shielding
Flexible and adaptable
Notes: Small samples  extract small beams
Needs a bright cold neutron source

## Slide 26: Indispensable tool for magnetism
Narrow bandwidth to concentrate the intensity
Single Crystal diffraction
  Diffuse scattering
  Extreme Environments
  Polarized Flux ≈ 5 x DNS@MLZ
Crystal analyzer Spectrometers
  The TAS successor
  108 n/cm2/s within Dl = 0.7Å
Weber et al. Science 375 (2022)
Skyrmion
Excitations
W. Schweika et al.
PRX May 2022
DNS
Frustrated
Magnetism
Notes: Indespensible tool to study order or disorder and excitation of spins
spectral range below 6 Å essential
natural bandwidth and resolution at high frequency target

## Slide 27: Narrow resolution  narrow band

## Slide 28: Very Narrow resolution + Wide Band
Pulse shaping at the long pulse source
Powder Diffraction
&
Backscattering
CrysTof
N(R)SE

## Slide 29: Near Backscattering spectrometer
~ 5 µeV resolution & Polarization Analysis
Using the FARO principle:
Small sample + PSD + focusing analyzer
 Large acceptance + good resolution
Large dynamic range
to access long relaxation times

## Slide 30: ToF enhanced imaging & Analytics
Cold & thermal Imaging, PGNAA

## Slide 31: Adapted Target Stations crucial
Large structure Instruments
Diffractometers
Spectrometers
Imaging and Analytics