## Slide 1: Status of Track Finding for CEPC Drift Chamber
Mengyao Liu2
Yao Zhang1, Wenxing Fang1, Tao Lin1,
Weidong Li1, Xingtao Huang2,Ye Yuan1, Xueyao Zhang2,Chendong Fu1
1. IHEP
2. Shandong University
2023-04-18

## Slide 2: Outline
Motivation
Simulation
Track Finding
Summary

## Slide 3: Drift Chamber(DC) Software
Drift chamber is the key detector in the 4th conceptual detector design to provide PID
  Good PID ability (2s p/K separation at P < ~ 20 GeV/c)
  Precise momentum measurement (eff. ~100%, sp<=0.1%)
Motivation of DC software project
  Development of simulation and reconstruction for DC
  Support the detector design, optimization and performance study
  Support physics sensitivity study
Requirements for DC software
  Modular design and friendly interfaces
  Easily integrated with common tools (ACTS, Genfit etc.)
  Reuse existing algorithms from other experiments
  Application of advanced technic (ML) to simulation and reconstruction
Manpower
  IHEP: Yao Zhang, Tao Lin, Wenxing Fang, Chengdong Fu, Ye Yuan, Weidong Li
  SDU: Mengyao Liu, Xueyao Zhang, Xingtao Huang
Requirements of The CEPC tracker
A PID drift chamber

## Slide 4: DC software
CEPCSW
  Gaudi based framework
  External libraries and tools
Geometry and field map
  DD4hep
  Non-uniform magnetic field: done
Data model
  EDM4hep and FWCore
  dN/dx event model: done
Drift chamber
  DC simulation: done
  DC digitization: done
  Waveform simulation: in progress
  Waveform reconstruction: in progress
  Track fitting with measurement: done
  Track finding: in progress
  dN/dx reconstruction: in progress
  Multi track reconstruction: done
  Performance check: done
The drift chamber software has been developed from scratch
DC digitization
DC track
reconstruction
Waveform
reconstruction
Waveform
simulation
DC simulation
dN/dx reconstruction
N of ionization
Track & track length in cell: X
Drift chamber simulation and reconstruction flow
Genfit
Garfield++&& ML
Geometry & field (DD4hep)
data model (EDM4hep & DC EDM)

## Slide 5: Event Data Model
DC implements the data model following the EDM4hep (commonly used by ILC, FCC, CEPC, CLIC, …)
For drift chamber track simulation and reconstruction: MCParticle, SimTrackerHit, TrackHit, Track

## Slide 6: EDM4hep Extension
Extending the EDM4hep:
  To facilitate dN/dx study: simulation and reconstruction
  The extended EDMs are general and can be used both for the drift chamber and the TPC
  Have been merged into EDM4hep

## Slide 7: Drift Chamber Parameters in CEPCSW
The baseline configuration of DC in CEPCSW
Half length | 2980 mm
Inner and outer radius | 800mm to 1800 mm
# of Layers | 100/55
Cell size | ~10mmx10mm/18mmx18mm
Gas | He:iC4H10=90:10
Single cell resolution | 0.11 mm
Sense to field wire ratio | 1:3
Total # of sense wire | 81631/24931
Stereo angle | 1.64~3.64 deg
Sense wire | Gold plated Tungsten f=0.02mm
Field wire | Silver plated Aluminum f=0.04mm
Walls | Carbon fiber 0.2 mm(inner) and 2.8 mm(outer)
Cell structure

## Slide 8: Silicon detectors Parameters in CEPCSW
Silicon tracker | Number of layer | Radius(mm) | sU (mm) | sV(mm)
VXD | 3 double layers | 16-58 | 2.8/6/4/4/4/4 | 2.8/6/4/4/4/4
SIT | 4 layers | 230-770 | 7.2 | 86
SOT(SET) | 1 layer | 1815 | 7.2 | 86
CRD tracker o1 v01

## Slide 9: DC Simulation
Following the common scheme for detector description
  XML based compact files for drift chamber detector description
    CRD: Detector/DetCRD/compact/CRD_oX_vYY/CRD_o1_vYY.xml
  Geometry parameters can be flexibly configured
Cell partitioning with segmentation
  Consistent between simulation and reconstruction
Simple digitization
  Constant drift velocity: Vdrift=40mm/ns & fixed spatial resolution: s=110um
One stereo layer of drift chamber
Hitmap of MC hits in DC
Software Development for the Drift Chamber, Yao Z.

## Slide 10: Track Finding--- CKF
    CKF(Combinatorial Kalman Filter):
    Track finding using CKF in Drift hamber
      Purpose: Select hits belonging to this track through the existing track seed
      Methods: The reconstructed SiTrack is selected as seed to select DC hits belonging to the same track
  A tracking concept that combines track finding and track fitting in a search-tree-based algorithm.
  Used by many high energy physics experiments
  Can give precise results

## Slide 11: Track Finding---CKFFinding
Based on the track finding algorithm of Belle II
(https://github.com/belle2/basf2)
  CKFToCDCFindlet(main algorithm)
  CDCCKFSeedCreator,CDCCKFStateCreator...
Integration with CEPCSW
  Field
  Geometry
  Data io

## Slide 12: TrackFinding Performance
v.s.
  N2: number of McParticle
  N1: ()>50%
v.s.
Sample: singal particle(=50°)
Without noise
Track finding efficiency is basically maintained at 100%
Low-momentum particle track in circles lead to low hit efficiency

## Slide 13: TrackFinding Performance
Sample: singal particle(=50°,=10GeV)
Momentum resolution:16.34MeV(truth:16.38MeV)
Vertex resolution:4.065um(truth:3.897um)
) v.s.
Fitting track efficiency after track finding
is 2%~3% different from the truth

## Slide 14: Noise Distribution
Noise level: 20%
  uniform,random
Singal + Noise TDC
  Noise time:0~2000ns
time(ns)
The position of the noise on the XY plane

## Slide 15: TrackFinding Performance
With Noise
Sample: singal particle(=50°,=10GeV)
Track finding effiency v.s. Noise level
    N2: number of McParticle
    N1: ()>50%
Noise has a greater impact on track finding

## Slide 16: TrackFinding Performance
With Noise
Sample: singal particle(=50°,=10GeV)
Momentum resolution:16.62MeV
Vertex resolution: 3.994um
) v.s. noise level
The fitting track efficiency remains at 97%

## Slide 17: Summary
The integration of track finding algorithm and CEPCSW has been completed
Geometry and field is available in tracking algorithm
Causes of lower hit efficiency:
  curling tracks
  Not suitable cuts
Future plan
  Optimizing the Track Finding Algorithm
  Optimize tracking cuts
  Improve track efficiency and purity
Thank you!