## Slide 1: Analysis of possible data lost in chip
Xiaomin WEI
April 27，2023

## Slide 2: TaichuPix3 Peripheral Readout
Two level FIFO
1st level （FIFO1）
  Every 32 Dcols share one FIFO tree
  16 FIFO trees in total
  Read out in time order in 32 Dcols.
  Read out evenly between the 32 Dcols.
  Volume presented in next page.
2nd level （FIFO2）
  Four SRAM
  Every 128 Dcols share one SRAM.
  Read out evenly
  Volume: 256 words
When the FIFOs are full, the hits will be blocked in the pixels. Smaller address will be output in priority.

## Slide 3: FIFO tree in 32 Dcols readout
FIFO tree in 32 Dcols readout
6 layers
280 words in total
8.75 words for a Dcol in average
52 words for a Dcol in maximal
Cases (hit Dcols) | Cases example (hit Dcols) | Memory volumn for a Dcol in average (words)
All Dcols | 0,1,2,…,31 | 8.75 (280/32)
Half of Dcols | 0-3, 8-11, 16-19, 24-27 | 13.5 (216/16)
Four Dcols | 0, 8, 16,24 | 26 (104/2)
One | 0 | 52

## Slide 4: Memory for a Dcol
Cases (hit Dcols) | Cases (noisy Dcols) | FIFO1 | FIFO2 | In total
Case1 | All Dcols | 8.75 | 256*4/512=2 | 10.75
Case2 | One in every 32 Dcols | 52 | 256/4=64 | 116
Case3 | One in every 128 Dcols | 52 | 256 | 308
case4 | One for whole chip | 52 | 256 | 308

## Slide 5: No data lost analysis
62.5Mbps
R4<2M words/s
R3:0.5M
R2:125K
Average data rate
Clock frequency
62.5M
2M
15.625M
15.625M
R1:4K
No data lose : the input data rate should less than the output data rate.
Data rate for one Dcol (pixels/s): R1
Data rate for 32 Dcols (pixels/s): R2
Data rate for 128 Dcols (pixels/s): R3
Data rate for whole chip (pixels/s): R4
R4< 2M pixels/s
Cases (hit Dcols) | R3 | R2 | R1
All Dcols | 500K | 125K | 4K
One in every 32 Dcols | 500K | 125K | 125K
One in every 128 Dcols | 500K | 500K | 500K
One for whole chip | 2M | 2M | 2M

## Slide 6: Data lost analysis
62.5Mbps
R4<2M words/s
R3:0.5M
R2
Average data rate
Clock frequency
62.5M
2M
15.625M
15.625M
R1
When the FIFO is full, the hit in the pixel array may be covered.
Suppose all the FIFOs will be full in x s, the FIFO volume in total can be utilized are K words.
R1,R2<<15.625M
x=K/(R1-R3)
R1=K/x+R3
K=10.75~308, x=1800 s (30min)
R1=0.67M（K=308）
R1=0.506M （K=10.75）