## Slide 1: CEPC collider dynamic aperture calculation and error mitigation
Yiwei Wang, Bin Wang
for the CEPC Accelerator Physics Group
The Institute of High Energy Physics, Chinese Academy of Sciences
CEPC day
30 May 2023, IHEP

## Slide 2: Lattice design of the CEPC collider ring
ref: CEPC-CDR; CEPC pre-CDR; K. Oide, arXiv:1610.07170; M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010); A. Milanese, PRAB 19, 112401 (2016);
Basically 2 folded symmetry
2 interaction regions @ IP1 and IP3
  crab waist collision
  local chromaticity correction for the interaction region
  asymmetric interaction region
2 RF acceleration regions @ IP2 and IP4
  shared cavities for two beam @ ttbar, Higgs
  flexible switching between compatible modes
8 arc sections
  dual aperture dipole and quadrupole magnets
  non-interleaved sextupoles
4 short straight section
  on/off axis injection regions for different modes
  beam dumping
Correction of energy sawtooth effects
LS4
LS1
LS2
LS3

## Slide 3: Machine parameters of CEPC
*CEPC AP group, TDR draft ch 4.1
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 266/267 | 266/266 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.3/1.7 | 1.2/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (Bhabha/beamstrahlung) (min) | 39/40 | 80/18000 | 60/700 | 81/23
Beam lifetime (min) | 20 | 80 | 55 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch spacing (ns) | 591 (53% gap) | 23 (18% gap) | 257 | 4524 (53% gap)
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 266/267 | 266/266 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.3/1.7 | 1.2/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (Bhabha/beamstrahlung) (min) | 39/40 | 80/18000 | 60/700 | 81/23
Beam lifetime (min) | 20 | 80 | 55 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5

## Slide 4: Lattice design of the CEPC half ring
ttbar: εx=1.4nm, β=1.04m/2.7mm
Higgs: εx=0.64nm, β=0.30m/1mm
W: εx=0.87nm, β=0.21m/1mm
Z: εx=0.27nm, β=0.13m/0.9mm
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 5
Energy sawtooth effects and correction
With only two RF stations, the energy sawtooth is around 0.4% @ Higgs and 1.3 % @ ttbar
The closed orbit distortion in CEPC collider ring is around 1 mm and becomes 1um after tapering the magnet strength with beam energy.
  adjusting range of magnets strength 2.5%
Higgs: before tapering correction
Higgs: after tapering correction

## Slide 6: Dynamic aperture requirement
 | ttbar | Higgs | W | Z
Horizontal DA requirement from injection | off axis | off axis on axis | off axis | off axis
Beam lifetime requirement from injection [min] | 16.3 | 17.2 | 20.5 | 74
 | ttbar | Higgs | W | Z
Horizontal DA requirement from injection |  |  |  | 
Beam lifetime requirement from injection [min] | 16.3 | 17.2 | 20.5 | 74
by X. H. Cui, Y. Zhang, Y. Wang
DA requirement | ttbar | Higgs | W | Z
with on-axis injection | - | 1.6% | - | -
with off-axis injection | 2.2% | 1.6% | 1.2% | 1.3%
DA requirement | ttbar | Higgs | W | Z
with on-axis injection | - |  | - | -
with off-axis injection |  |  |  | 
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 7: Dynamic aperture @ Higgs and ttbar
Tracking to get DA without errors, with turns for one transvers damping time, with 4 initial phases
DA optimized with 52 knobs (32 arc sextupole families + 8 IR sextupoles families + 4 multipoles families + 8 phase advance)
Totally, 256 arc sextupole families in the whole ring can be used.
The DA w/o errors fulfill the requirements @ Higgs and ttbar.
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
ttbar
Higgs
1.6 %
1.6 %
2.2 %
2.2 %
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 8: Dynamic aperture @ Z and W
Tracking to get DA without errors, with turns for one transvers damping time, with 4 initial phases
DA optimized with 68 variables (48 arc sextupole families + 8 IR sextupoles + 4 multipoles + 8 phase advance)
Totally, 96 arc sextupole families in the whole ring can be used.
The DA w/o errors fulfill the requirements @ Z and W.
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
W
Z
1.3 %
1.3 %
1.2 %
1.2 %
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 9: Solenoid effect on Dynamic aperture @ Higgs
  The anti-solenoid cancel the ∫Bzdz between the IP and the faces of the final quadrupole
The Twiss function was corrected with final quadrupoles.
The solenoid effect on the dynamic aperture is small.
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
Solenoid
Higgs
1.6 %
1.6 %
Higgs with sol
1.6 %
1.6 %
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 10: Correction procedures
Correction of the closed orbit distortion
  Correction of the closed orbit distortion (COD) with sextupoles off is made firstly.
  Turn on the sextupoles and perform COD correction again.
  Orbit correction is applied using orbit response matrix and SVD method.
Dispersion correction
  With dispersion free steering (DFS): orbit manipulation by knob correctors.
Beta-beating correction
  Correct the beta functions with sextupoles on Based on AT LOCO
Coupling correction
  Both coupling and vertical dispersion are controlled.
  Using the trim coils of the sextupoles, which providing skew-quadrupole field, to perform emittance tuning for CEPC.

## Slide 11: Error assumption
With assumption of 100 um transverse misalignments
BPMs placed at each quadrupoles
H/V correctors placed beside focusing/defocusing quadrupoles
The Higgs and ttbar lattices are similar, the Z and W lattices are similar.
  1000 seeds used for the Higgs, 500 lattice seeds used for the Z
  100 seeds used for both W and ttbar energy
Component | x (mm) | y (mm) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.02%
IR Quadrupole | 0.10 | 0.10 | 0.10 | 
Sextupole | 0.10* | 0.10* | 0.10 | 
*implement beam-based alignment techniques to reach rms offsets in the order of 0.01 mm with respect to the beam
with a much larger beta @ IP
BPM resolution is less than 0.001mm

## Slide 12: Result of four modes
RMS | Higgs | Z | W | 
Orbit () | < 50 | < 50 | < 50 | < 50
Dispersion (mm) | 1.8/0.9 | 2.8/1.4 | 2.7/1.8 | 0.6/0.3
Beta-beating (%) | 1.0/2.8 | 2.0/3.0 | 0.5/2.5 | 1.1/1.2
RMS | Higgs | Z | W | 
 | < 50 | < 50 | < 50 | < 50
Dispersion (mm) | 1.8/0.9 | 2.8/1.4 | 2.7/1.8 | 0.6/0.3
Beta-beating (%) | 1.0/2.8 | 2.0/3.0 | 0.5/2.5 | 1.1/1.2

## Slide 13: Dynamic aperture with error @ Higgs and ttbar
—DA w/o error
—mean value
—statistic errors
—requirement
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
Higgs
ttbar
Further optimization is possible
With more families of sextupole: totally 256 arc sextupole families, only 32 arc sextupole families used
Recovery of the –I transformation for the IR sextupole: should help to increase the energy acceptance
With stricter error tolerance in IR: currently with same requirement for the IR and ARC

## Slide 14: Dynamic aperture with error @ Z and W
—DA w/o error
—mean value
—statistic errors
—requirement
Effects included in tracking
Synchrotron motion
Radiation loss in all magnets
Tapering
Crab waist sextupole
Maxwellian fringes
Kinematic terms
Finite length of sextupole
Z
W
Further optimization is possible
With more families of sextupole: totally 96 arc sextupole families, only 48 arc sextupole families used
Recovery of the –I transformation for the IR sextupole: should help to increase the energy acceptance
With stricter error tolerance in IR: currently with same requirement for the IR and ARC

## Slide 15: Dynamic aperture and beam lifetime
K. Oide, FCCIS 2022 workshop, Dec. 06, 2022.
J. Wu, Y. Zhang, Q. Qin, Y. Wang, C. Yu, D. Zhou, NIMA 959 (2020) 163517.
J. Wu, Y. Zhang, Q. Qin, doi:10.18429/JACoW-IPAC2019-MOPGW051, IPAC19.
Y. Zhang et al, doi:10.18429/JACoW-eeFACT2018-TUYBA04, eeFACT2018.
FCC-ee
Larger dynamic aperture does not ensure longer lifetime.
  Diffusion due to lattice nonlinearity affects the beam lifetime.
  Optimize the beam lifetime and DA together.
  Optimization for CEPC Higgs lattice w/o error made
  It can be applied on the lattice w/ errors. More families of sextupoles are available for the optimization.
  Optimization for CEPC Higgs lattice w/o error
  Optimization for FCCee Z lattice w/o error
CEPC
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 16: Summary
  Lattice of the CEPC collider ring designed fulfilling requirements of the parameters list, geometry and key hardware. Nonlinearity correction is made.
Dynamic aperture w/o error for four modes achieved the requirements.
Dynamic aperture w/ main errors for four modes almost reach the requirements. Further optimization is possible.

## Slide 17: backup

## Slide 19: Overall design requirement of the CEPC collider ring
SR power per beam 30 MW (50 MW upgradable), 100 km, 2 interaction points
Compatible modes for H/Z/W/runnig: provide high quality beam energy from 45.5 to 180 GeV
Compatible with SPPC: two machines share the most tunnels except the IP1-IP4
Tunnel in the arc regions
CEPC detectors
CEPC+SPPC complex

## Slide 20: Interaction region for all modes
Crab waist collision, local chromaticity correction, asymmetric interaction region
*ref: Y. Cai, IAS2016, HKUST; K. Oide, arXiv:1610.07170;
P. Raimondi, Proc. of the 2nd SuperB Workshop, Frascati, March 2006；M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010);
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
 | QD | QF
Z | Q1A | Q1B
W/H | Q1A+Q1B | Q2
ttbar | Q1A+Q1B+Q2 | add quad Q3A and Q3B
Strength of other modes doesn’t exceeded the one of Higgs mode.
 | L* [m] | LQ1 [m] | LQ2 [m] | GQ1 [T/m] | GQ2 [T/m] | d [m]
CDR | 2.2 | 2.0 | 1.5 | -136 | 111 | 0.3
TDR | 1.9 | 1.22/ 1.22 | 1.5 | -141/ -85 | +95 | 0.3
ttbar
Q1AIRU
Q1BIRU
Q2IRU
Q3AIRU
Q3BIRU
Q1AIRD
Q1BIRD
Q2IRD
Q3AIRD
Q3BIRD

## Slide 21: Interaction region for all modes (cont.)
Crab waist collision, local chromaticity correction, asymmetric interaction region
*ref: Y. Cai, IAS2016, HKUST; K. Oide, arXiv:1610.07170;
P. Raimondi, Proc. of the 2nd SuperB Workshop, Frascati, March 2006；M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010);
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -141 | -141 | -94 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -56 | +65
Q2IRU | 1.5 | 4.7 | -51 | +95 | +63 | 0
Q3IRU | 3 | 7.2 | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -64 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -47 | +96 | +64 | 0
Q3IRD | 3 | -7.2 | +40 | 0 | 0 | +2
 | QD | QF
Z | Q1A | Q1B
W/H | Q1A+Q1B | Q2
ttbar | Q1A+Q1B+Q2 | add quad Q3A and Q3B
Strength of other modes doesn’t exceeded the one of Higgs mode.
 | L* [m] | LQ1 [m] | LQ2 [m] | GQ1 [T/m] | GQ2 [T/m] | d [m]
CDR | 2.2 | 2.0 | 1.5 | -136 | 111 | 0.3
TDR | 1.9 | 1.22/ 1.22 | 1.5 | -141/ -85 | +95 | 0.3

## Slide 22: Interaction region for all modes (cont.)
Crab waist collision, local chromaticity correction, asymmetric interaction region
*ref: Y. Cai, IAS2016, HKUST; K. Oide, arXiv:1610.07170;
P. Raimondi, Proc. of the 2nd SuperB Workshop, Frascati, March 2006；M. Zobov et al, Phys. Rev. Lett. 104, 174801(2010);
Up to 3rd order chromaticity is corrected with pairs of main sextupoles, phase tuning and additional sextupoles respectively.
Most of the resonance driving terms (RDT) due to sextupoles in 3rd and 4th order Lie operators are almost cancelled.
The tune shift due to the finite length of the main sextupoles is corrected with additional weak sextupoles.

## Slide 23: Lattice design and geometry of the RF region
An electrostatic separator combined with a dipole magnet* to avoid bending of incoming beam for the Higgs and ttbar energy running
Higgs at stage 1/2
ttbar at stage 3
W at stage 1/2/3
Z at stage 1
Esep= 2.0 MV/m
Lsep= 4 m10
x= 10 cm at entrance of quad
Z at stage 2/3
*K. Oide et al, PRAB, vol. 19, no. 11, p. 111005
Details of the RF staging in Jiyuan ZHAI’s talk

## Slide 24: ARC region for all modes
Z and W modes need larger momentum compaction factor p and thus larger emittance εx, Qs
  To suppress the impedance induced instability at Z mode
  To increase stable tune area if considering beam-beam effect and impedance consistently at W and Z modes
stable tune area with both beam-beam and impedance (Z mode 90/90)
Yuan Zhang
Phase advance reduced from 90 to 60 for W and Z modes
    H/ttbar mode 90/ 90
    W/Z mode 60/ 60

## Slide 25: Optimization of ARC aberration for Higgs/ttbar modes
2nd order chromaticity is a main aberration for the optimization of momentum acceptance with one –I sextupole pair scheme.
  In previous versions, 2nd order chromaticity generated in the ARC region are corrected with IR knobs (phase advance or K1).
  However, the IR knobs will generate distortions at IP (beta, alfa and dispersion) especially for the horizontal plane.
A lattice with four –I sextupole pairs scheme for Higgs & ttbar modes
  much less 2nd order chromaticity for the horizontal plane
Q’’=313, 410
Q’’=9, 145
Scheme with one –I sextupole pair
K. Oide, arXiv:1610.07170.
Scheme with four –I sextupole pairs
T. Bian, PhD thesis, 2018.

## Slide 26
The distribution of sextupoles for Higgs & ttbar mode allowed to select –I sextupole pairs for W &Z mode.
  6*6=36 cases for 23 cells
  There are much more combinations if choose different cases in each arc section (184 cells)
1st pair | 2nd pair |  | 
(1A, 2A) | (2B,3B) | (3A,4A) | (3B,4B)
(1B, 2B) | - | (3A,4A) | (3B,4B)
(2A, 3A) | - | - | (3B,4B)
SF
1A
SF
1B
SF
2A
SF
2B
SF3A
SF
3B
SF
4A
SF
4B
SD
1A
SD
1B
SD
2A
SD
2B
SD3A
SD
3B
SD
4A
SD
4B
-I
-I
-I
-I
@ dp/p=1%
2nd and 3rd order dQ@dp/p=1% in x, y
  Optimization of ARC aberration for
  W/Z modes

## Slide 27
+
case {3,4}
case {4,3}+{3,4}
case {4,3}
Cancellation of main aberration has period of 23*3 cells.
  Optimization of ARC aberration for
  W/Z modes (cont.)

## Slide 28
Vertical emittance generated by solenoid field
The detector solenoid are compensated locally with anti-solenoids
  3T for /Higgs/W, 2T for the Z
  cancel the ∫Bzdz between the IP and the faces of the final quadrupole
  exists a transverse fringe field esp. at the fringe of anti-solenoid
The vertical emittance increases due to the fringe field of the anti-solenoid combined with the horizontal crossing angle.
  For the and Higgs, εy=0.05pm and 0.7 pm.
  For the W and Z, the εy will be reduced with softer a bit longer anti-solenoid and keep cancelling of the ∫Bzdz between the IP and the faces of the final quadrupole (or replacing the cryo-module when running at the high luminosity Z).
Optics with solenoid field at Higgs
Chart: Z (m)
Composed field
Detector solenoid field
Anti-solenoid field

## Slide 29: Correction scheme for magnets errors
Correction procedures
  The closed orbit distortion (COD) correction with sextupoles off
  Turn on the sextupoles and perform COD correction again.
  Dispersion correction
  Beta beating correction
  Coupling and vertical dispersion correction
Uniform settings (corrector settings, BPM selection, iteration times, steps and so on) of the batched correction are optimized for all the lattice seeds.
Individual further correction (additional iteration and adjustment of the corrector settings according to correction result) are performed for those un-converged seeds.
by Bin WANG, Yuanyuan WEI, Yiwei WANG

## Slide 30: Result of Higgs lattice functions
decreased from 23.1 mm to 1.8 mm
decreased from 31.9 mm to 0.9 mm
decreased from 5.2% to 1.0%
decreased from 83.2% to 2.8%
The strength of skew quadrupoles for a lattice seed.

## Slide 31: Result of Z lattice functions
decreased from 23.1 mm to 1.8 mm
decreased from 31.9 mm to 0.9 mm
decreased from 5.2% to 1.0%
decreased from 83.2% to 2.8%

## Slide 32
W
1.2 %
1.2 %
W with sol
1.2 %
1.2 %