## Slide 1: Readout Electronics Development and Performance
Anshun Zhou
Particle Detection and Electronics State Key Laboratory
USTC
2023/06/06
Notes: Good morning everyone. First let me introduce myself. I am Anshun Zhou from the Nuclear Detection and Nuclear Electronics Laboratory of the USTC. I’m glad to be here and make a brief presentation of the …. to you.

## Slide 2: contents
Single-layer Readout Electronics Design
Data Acquisition Electronics Design

## Slide 3: contents
Single-layer Readout Electronics Design
  Design
  Test
Data Acquisition Electronics Design

## Slide 4: Baseline
Detector
  Plastic scintillator
  SiPM
Readout
  Spiroc2E
Parameters
  324 channels per layer
  720mm×720mm sensitive area
  40 layers
  12960 channels in total
Basic Structure for Prototype
SiPMs & Scintillators tiled on PCB
iron
Notes: Let me start by giving you some baseline introduction. Absorber PCB sensitive are assembled like sandwitch. Tiled on the PCB.
A dome-shaped cavity is processed in the center of the bottom surface of each scintillator such that the SiPMs could be mounted on the PCB under the scintillators.

## Slide 5: Sub HBU Board Design
Sub HBU Board Design
  3 sub board for each layer
  3 Spiorc2Es per sub board
  108 channels per sub board
SiPM Readout
  Shared High Voltage plane
  Voltage signal injected to Spiroc2E
Notes: As the sensitive area is really big, we proposed the design of the sub board to cover it. Every FEE board is separated to 3 sub HBU board with same size. There . We use flexible printed circuit. This kind of connection is with better vibration resistance.

## Slide 6: Digital Data Readout
Serial Readout
  Default usage
  Daisy chain
  <83Hz
Parallel Readout
  Ping-pong readout in FPGA
  >1kHz in beam test
Parallel Readout Circuit
Ping-Pong Readout Logic
Serial Readout Circuit
Revised
Notes: Let us move on to the digital data readout design. 2 main reasons. Distributed capacitance. prevent the influence of the large distributed capacitance. To reduce the readout time, we come up with the ping-pong readout logic. There are 2 separated FIFOs in the FPGA for each Spiroc2E, so when one of the FIFOs are being read the other one could be used to write the data of Spiroc2E.

## Slide 7: Electrical Calibration Circuit
Analog Circuit of Spiroc2E
  High Gain & Low Gain
  Channel difference
Calibration circuit
  Same waveform with SiPM
  Charge Injection to Probe
Electrical Calibration Circuit
20ns 40ns 60ns
Calibration signal waveform (pspice)
Analog Circuit of Spiroc2E
SiPM waveform

## Slide 8: LED Calibration Circuit
SiPM
  Sensitive to Temperature
  Single photoelectron peak spectrum
LED calibration circuit
  Light pulse of LED
  6 groups
LED Waveform
<10ns
LED Calibration Circuit
LED & SiPM

## Slide 9: Temperature Monitor Circuit
Temperature Monitor Circuit
  48 probes per layer
  Resistor soldered selectively
Temperature Monitor Circuit
NC
NC
Notes: multiplexer

## Slide 10: contents
Single-layer Readout Electronics Design
  Design
  Test
Data Acquisition Electronics Design

## Slide 11: Pedestal
RMS < 10 ADC code
Mean
  Channels of same chip are close
High Gain
Low Gain
RMS

## Slide 12: Electrical Calibration
Gain
  High Gain: ~180 ADC code/pC
  Low Gain:~6 ADC code/pC
Noise
  10/180<80fC

## Slide 13: LED Calibration & MIP
Gain
  ~25 ADC code/p.e.
MIP Result
  SNR>20
  Single Photoelectron Peak Spectrum
  MIP

## Slide 14: contents
Single-layer Readout Electronics Design
  Design
  Test
Data Acquisition Electronics Design

## Slide 15: Structure
Data Acquisition
  Independent Data link for Monitor Data
  Clock, trigger from TLU to sync with other system
Power Supply
  Power -> DAQ board -> DIF board -> HBU
Other
System
  TLU: Trigger Logic Unit
  DAQ: Data Acquisition Board
  DIF: Data Interface Board

## Slide 16: typeC interface
Data link
  clock: B2,B3
  command: B7,B6
  ccientific data:A2,A3
  temperature:A8,B8
  busy:A10,A11
Power link
  VBUS,GND

## Slide 17: DIF
PCB Design
  typeC interface & USB3.1 cable
  Power & Data on same cable
  LVDS Center tap termination
High Voltage
High-density connector
LEMO
  LVDS center tap termination

## Slide 18: DIF
FPGA Logic
  Analyze command from DAQ
  Data packing
  Control Spiorc2E

## Slide 19: DAQ
PCB Design
  40 typeC interfaces
  4 SFP
  Power interface for DIF
  Current monitor circuit
HDMI for TLU
Power
interface
Power
interface
LEMO
  Current monitor circuit

## Slide 20: DAQ
FPGA Logic
  2 SiTCP links
  Scientific data packing
  Monitor data packing
  Cherenkov signal
Cherenkov signal

## Slide 21: Beam Test
Particle Track

## Slide 22
THANKS!