## Slide 1
Overview of Vertex Detector R& D
Zhijun Liang
(IHEP, Chinese Academy of Sciences)

## Slide 2: Vertex detector: Physics goal
Higgs precision measurement
  H → bb precise vertex reconstruction
  H → μμ (precise momentum measurement)
Main technology
  High spatial resolution technology → pixel detector
  Low-mass detector technology
  Radiation resistance technology
Need tracking detector with
high spatial resolution, low material

## Slide 3: MOST2 vertex detector R & D: Research Goal
Produce a world class vertex detector prototype
  Spatial resolution 3~5 μm (pixel detector)
  Radiation hard (>1 MRad)
Preliminary design of prototype
  Three layer, double size ladders
Typical module
Typical tracker
ATLAS/CMS upgrade
（~15 μm）
Alice upgrade
（5~10 μm）
This project（3~5 μm）
Resolution
World
leading
Notes: General description highlighting major points and assessment indicators

## Slide 4: Overview of MOST2 vertex detector R & D
Can break down into sub-tasks:
  CMOS imaging sensor chip R & D
  Detector layout optimization, Ladder and vertex detector support structure R & D
  Detector assembly
  Data acquisition system R & D
CMOS imaging
sensor prototyping
Detector module (ladder)
Prototyping
Full size vertex detector Prototype
Notes: Full size vertex detector

## Slide 5: Research Team in MOST2 silicon project
课题2：IHEP - 中国科学院高能物理研究所
                SDU - 山东大学
                NJU - 南京大学
                NWU - 西北工业大学
4 institutes
Institutes | Tasks
IHEP | Full CMOS chip modeling, Pixel Analog, PLL block Detector module (ladder) prototyping Data acquisition system R & D Vertex detector assembly and commissioning
CCNU/IFAE | CMOS sensor chip: Pixel Digital
NWPU | CMOS sensor chip: Periphery Logic, LDO
SDU | CMOS sensor chip: Bias generation, TCAD simulation Sensor test board design
NJU | Irradiation, test beam organization
Notes: Total 51, average age is 39
Acc: 39=703/18
Silicon: 39=866/22
HCAL: 40=440/11
Total: 39

## Slide 6: Achievement Presentation and Assessment Methods
Silicon Detector
Assessment index
  - Mid-term: produce 25*25 μm pixel size chip
  - Final : 3-5 μm resolution in Beam test
  - mid-term: verified by TCAD simulation
  - Final : Total ionization dose >1 Mrad
Spatial resolution
Radiation hardness

## Slide 7: CMOS Monolithic pixel sensor
CMOS Monolithic pixel (CIS process) is ideal for CEPC application
  low material budget (can be thin down to 50μm)
  This project use TowerJazz CIS 180nm technology
Hybrid pixel technology developed by ATLAS and CMS
  Thickness of sensor is about 200~300 μm
  Need to bump bonding with readout ASIC (ASIC thickness is about 300μm)
  Material budget about silicon sensor is about 10 times larger than CIS process
Hybrid pixel

## Slide 8: CMOS Sensor chip R & D
The existing CMOS monolithic pixel sensors can’t fully satisfy the requirement
Major Challenges for the CMOS sensor
    Small pixel size -> high resolution (3-5 μm)
    High readout speed (<500ns deadtime @40MHz at Z pole) -> for CEPC Z pole high lumi
    Radiation tolerance (per year): ~1 MRad

## Slide 9: New proposed readout architecture in TaichuPix
df
New readout architecture
 reduce power consumption and reduce pixel size
CEPC readout time requirement:
  <500ns deadtime @40MHZ(Z pole)
Taichu-1 Column-drain readout
  Priority based data driven readout; time stamp at EOC
  Dead time: 2 CLK for each pixel (50ns @40MHz CLK)
  Two digital pixel designs: FEI3-like and ALPIDE-like design
2-level FIFO architecture
  L1: column level, to de-randomize injecting charge
  L2: chip level, to match in/out data rate between core and interface
Trigger readout:
  Coincidence by time stamp, matched event read out

## Slide 10: Full-size TaichuPix3 design (engineering run)
Full-size full-functionality Taichu pixel
  1024×512 Pixel array (25μm×25μm pixel size), Process: Towerjazz 180nm
  Size： 15.9*25.7mm
  FE-I3 like Periphery digital readout , high speed data interface
    Time stamp precision: 25ns (modified process）
8-inch wafer
Wafer T212141-02E3

## Slide 11
Completed preliminary version of detector module (ladder) design
  Detector module (ladder)= sensors + support structure+ flexible PCB+ control board
  Sensors will be glued and wire bonded to the flexible PCB
  Flexible PCB will be supported by carbon fiber support structure
  Signal, clock, control , power, ground will be handled by control board through flexible PCB
3D model of the ladder
Detector module (ladder) R & D
Double-side ladder testing
Taichupix chip wire bonded
on FlexPCB

## Slide 12: Detector module (ladder) R & D
Detector module (ladder)= sensors + support structure+ flexible PCB+ control board
  Sensors will be glued and wire bonded to the flexible PCB
  Flexible PCB will be supported by carbon fiber support structure
  Signal, clock, control , power, ground will be handled by control board through flexible PCB

## Slide 13: Support structure of the ladder
Fabricated support structure prototype of the ladder (IHEP designed)
Both side of ladder has wire-bonding on chip  Challenging
  Dedicated tooling for double-side ladder assembly
Double-Side
ladder assembly

## Slide 14: Vertex detector Prototype assembly
6 double-side ladders installed on the vertex detector prototype for DESY testbeam
  DESY beam spot is about 2*2cm
  12 flex PCB , 24 Taichupix chips installed

## Slide 15: Test beam @ DESY
Two round of test beam at DESY (4~6GeV electron)
  1st round (Dec 2022): Taichupix beam telescope  study Taichupix chip level resolution
  2nd round (April 2023) : vertex detector prototype  detector-level performance study
Dec 2022 testbeam:
Taichupix beam telescope
April 2023 testbeam:
Vertex detector prototype

## Slide 16: Test beam @ DESY (detector-level testbeam)
Beam is going through 6 double layers of TaichuPix chip
  Fully captured the Beam spot
TaichuPix
Electron beam

## Slide 17: Test beam results
The spatial resolution improved by lowering the threshold
  Can reach better than 5μm spatial resolution
Dec 2022 testbeam:
Spatial Resolution Vs threshold
April 2023 testbeam:
Spatial Resolution Vs threshold

## Slide 18: Test beam results (April 2023)
Compared to 1st testbeam
  More material in support structure of prototype
  Higher noise in flex compared to PCB (more sensitive to threshold)

## Slide 19: Radiation hardness
Taichupix3 was irradiated in-situ tested up to 3 Mrad
Taichupix2 was irradiated in-situ tested up to 30 Mrad
  Normal chip functionality and reasonal noise performance
Taichupix3 irradiation test
Pixel threshold vs. TID
Taichupix2 irradiation test

## Slide 20: International collaboration
IFAE(Spain): very active in CMOS Sensor design and testing
Liverpool (UK): Tracker mechanical design,
Oxford(UK): CMOS sensor design validation, thermal design
RAL(UK): Pixel module design
Queen Mary(UK): module mechanical design (Zero mass concept)
Strasbourg (FR): CMOS sensor design, Tracker mechanical design
University of Massachusetts (US): Tracker mechanical design, thermal design
Mu3e ladder, Atlas barrel strip stave prototype.
Module of Alice’s OB tracker,
Advance material Lab
Lab visit in Oxford
Labs visit in Liverpool
  In 2019, we have one engineer visited Oxford and Liverpool for 4 weeks, learned a lots about silicon.

## Slide 21: Publications and International talks
International conference talks:
  Joao Guimaraes Da Costa, CepC phys/detectors, Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
  T. Wu , A full functional Monolithic Active Pixel Sensor prototype for the CEPC vertex detector, in proceeding of International Conference on Electronics Circuits and Systems, Nov. 27-29, 2019, Genova, Italy.
  Xiaomin Wei, High data-rate readout logic design for 1024*512 CMOS pixel array dedicated for CEPC experiment, International workshop on radiation imaging detectors, International workshop on radiation imaging detectors, July 2019, Crete, Greece
  Ying Zhang, Overview of the chip design for the MOST2 CEPC vertex project, Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
  Wei Wei, Full size pixel chip for high-rate CEPC Vertex Detector，Workshop on the Circular Electron-Positron Collider,EU Edition, April 15 - 17, 2019, Oxford, UK
JINST 14 (2019) C12012
IEEE ICECS (doi: 10.1109/ICECS46596.2019.8965105.)
Publication:

## Slide 22: Internal organization
Task 2 meetings
  CMOS sensors chip design meeting (weekly )
  Vertex detector overall design meeting (weekly)
  Full-day internal review meeting (every 3 months)
  Institutes worked closely
  Project leader followed closely the progress
Task 2 meetings

## Slide 23: Summary of CMOS Sensor chip R & D
Major achievement: completed the vertex detector prototype and testbeam
    High Spatial resolution
      better than 5um resolution
    Radiation hardness
      Can survive >3Mrad TID radiation

## Slide 24: Mid-term review of MOST2 project
Midterm review meeting (Aug 20-21)

## Slide 25: Mid-term review of MOST2 project

## Slide 26
3~5um good position resolution require high assembly precision
Cooperate with domestic company on R & D Gantry automatic module assembly.
  Pattern recognition with high resolution camera
  Automatic chip pick-up and positioning
  Automatic Glue dispending
Gantry for vertex detector prototype assembly
Gantry system
automatic glue dispending
Pattern recognition

## Slide 27
Completed preliminary version of detector module (ladder) design
  Detector module (ladder)= 10 sensors + support structure+ flexible PCB+ control board
  Sensors will be glued and wire bonded to the flexible PCB
  Flexible PCB will be supported by carbon fiber support structure
  Signal, clock, control , power, ground will be handled by control board through flexible PCB
3D model of the ladder
Detector module (ladder) R & D
Flexible PCB prototype
Profile of flexible PCB
Schematic of ladder electronics

## Slide 28
Support structure of the ladder: 3 layer of carbon fiber, 0.15mm thick
  3 time thinner than conventional carbon fiber
  A few times more rigid than conventional carbon fiber
  for tracks with small cosθ, radiation length ~0.015 X0 (reduce multi-scattering )
Ladder support
structure 3D model
Support structure of the ladder
Flexible PCB prototype
Finite elements analysis
Max def. under full load: 5.3 um
Conventional carbon fiber
0.15mm (1 layer)

## Slide 29
Completed preliminary version of detector engineering design
  3 double layer barrel design
  10 modules in inner layer, 22 modules in 2nd layer, 32 modules in outer layer
  Start thermal design (air cooling)
Physics simulation to optimize vertex detector layout design.
  The length of inner layer pixel should be the same as other two layers
  Inner pixel radium should be as close to beam pipe as possible
3D Model of vertex detector
Vertex Detector Prototype R & D
Impact parameter resolution
Vs beam pipe radius
Dead area in detector
Vertex detector layout
(R-Z view)

## Slide 30: Cooling design
Air cooling is baseline design for CEPC vertex detector
Sensor Power dissipation:
  Taichupix : ≤ 100 mW/cm2. (trigger mode)
  CEPC final goal : ≤ 50 mW/cm2
Cooling simulations of a single complete ladder with detailed FPC were done.
  Need 2 m/s air flow to cool down the ladder to 30 ℃
  Testbench setup has been designed for air cooling , vibration …
Test setup for ladder cooling
Use compressed air for cooling

## Slide 31: Future plan
3rd Year:
  3rd CMOS sensor fabricated and tested
     may be skipped if 2nd MPW chip is fully working
  Final support structure engineering design completed
  Fabricated support structure for ladders
4th Year:
  Competed R & D large area sensor
  Manufactured the support structure for whole detector
  Assembling and installing the detector prototype
  Completed DAQ system for whole detector
5th Year:
  Completed detector assembly and commissioning
  Test beam and data analysis
  Finish assembling of prototype

## Slide 32: International collaboration
IFAE(Spain): very active in CMOS Sensor design and testing
Liverpool (UK): Tracker mechanical design,
Oxford(UK): CMOS sensor design validation, thermal design
RAL(UK): Pixel module design
Queen Mary(UK): module mechanical design (Zero mass concept)
Strasbourg (FR): CMOS sensor design, Tracker mechanical design
University of Massachusetts (US): Tracker mechanical design, thermal design
Mu3e ladder, Atlas barrel strip stave prototype.
Module of Alice’s OB tracker,
Advance material Lab
Lab visit in Oxford
Labs visit in Liverpool
  In 2019, we have one engineer visited Oxford and Liverpool for 4 weeks, learned a lots about silicon.

## Slide 33: backup

## Slide 34: Backup:外围电路模块——高速数据接口

## Slide 35: Power managements in TaichuPix chip

## Slide 41: Goal for the second year
Achieve the target in task book for the 1st and 2nd years
  Completed preliminary engineering designs of support structure for vertex detector prototype
  Completed second sensor CMOS chip prototyping
  Completed data acquisition system for sensor testing

## Slide 42: Main specs of the full size chip for high rate vertex detector
Bunch spacing
  CEPC Z+Higgs (240GeV): 680ns;
  WW threshold scan (160GeV): 210ns;
  CEPC Z pole runing (90GeV) Z: 25ns
High Hit density
  2.5hits/bunch/cm2 for Higgs/WW runs
  0.2hits/bunch/cm2 for Z pole running

## Slide 43: Sensor prototyping
Completed two round of sensor prototyping
  1st Multi-wafer project chip (Taichupix1)
    Submitted in June 2019, received in November 2019
    Test functional blocks
      pixel array ( in-pixel amplifier and digital logic )
      Periphery block: digital readout architecture
      Periphery block：PLL and Serializer
      Periphery block： LDO and power supply
  2nd Multi-wafer project chip(Taichupix2)
    Submitted in Feb 2020, received in July 2020
    Major bugs fixed in Taichupix1
    Radiation hard design (enclosed gate) in pixel analog
Taichupix2
Chip size：5mm×5mm
Pixel size：25μm×25μm
Taichupix1
Chip size：5mm×5mm
Pixel size：25μm×25μm
Taichupix2 on test board

## Slide 44: CEPC vertex detector R & D
Three on-going R & D programs on vertex detector
  Previous update in CEPC day (June 15th) https://indico.ihep.ac.cn/event/11875/
This talk focuses on MOST2 project
  MOST2 aims to build full-size vertex detector prototype
Funding agency | Process | International collaborators | Objectives of the project | schedule
MOST1 | CMOS | Strasburg IPHC | Small pixel size design with in-pixel digitization and low power frontend | 2016.6-2021.5
MOST2 | CMOS | IFAE/Oxford/ Livepool … | full-size vertex detector prototyping ( Full-size sensor support structure, module …) | 2018.5-2023.4
NSFC | SOI | KEK/SOIPIX collaboration | Verification of SOI process with small pixel size and low noise design | 2016-