## Slide 1
Study plan and status for the CEPC collimation
Yuting Wang
2023 CEPC DAY, July 13 2023
Contributors:
G.Y. Tang, H.Y. Shi, H.J. Wang, X.H. Cui, D. Wang, Y.H. Li, et al.

## Slide 2: Content
Motivation
Method for simulation studies
Preliminary arrangement of the global collimators
Current simulation studies
Summary

## Slide 3: Motivation
CEPC is e+e- collider designed for 4 beam operation modes
  The energy stored in the machine is very high
  Such beam is highly destructive
Priority of machine Protection
  Global equipment protection
  Reduce the background near IP
Method of machine protection
  Active protection (beam dump)
    Response time of CEPC active machine protection system ~1ms
  Passive protection(collimators, shielding)
    Very fast beam loss, beam halo, synchrotron radiation (SR)…
Beam Energy (GeV) | 120 | 45.5 | 80 | 180
Bunch Population/1010 | 13 | 21.4 | 13.5 | 20
Number of Bunches | 446 | 13104 | 2162 | 58
Total Energy (MJ) | 1.1 | 20 | 3.7 | 0.33
Beam Energy (GeV) | 120 | 45.5 | 80 | 180
Bunch Population/1010 | 13 | 21.4 | 13.5 | 20
Number of Bunches | 446 | 13104 | 2162 | 58
Total Energy (MJ) | 1.1 | 20 | 3.7 | 0.33
Table 1: Parameters for the CEPC machine protection (@ 50MW)
[1]T. Ishibashi and S. Terui, SuperKEKB collimator design, FCC-EIC Joint & MDI Workshop 2022
Fig.1 Beam dump system
Fig.2 Damage to collimator jaw due to accident beam loss in the SuperKEKB
X.H. Cui

## Slide 4
Motivation
Method for simulation studies
Preliminary arrangement of the global collimators
Current simulation studies
Summary

## Slide 5: Method for Simulation studies
Requirements for simulation studies:
  Multi-turns particle tracking (6D) using the full lattice
  Synchrotron radiation, optics tapering, beam-beam effect
  Aperture model (geometry + beam-stay-clear region + momentum acceptance)
  Beam loss recording (turn, location, phase space)
  Particle-matter interaction inside the collimators
  Deposition and thermomechanical studies
Workflow
Lattice, Aperture model
Particle tracking
Different scenarios
Record beam profile
Collimator model
Particle-matter interaction
Particles
Particles

## Slide 6: Simulation studies
SAD simulations
Different scenarios
  Optimum/acceptable/particular operating conditions:
    Beam halo/tails, Top-up injection
    Change of optics, tuning, collimator aperture setting, etc
  Fast beam loss
    Standard equipment failure, fast equipment, other accident beam loss, etc
    Injection failure, SuperKEK fast beam loss (should be understand if possible)
  Different operation modes
    Higgs, Z, W, ttbar
FLUKA simulations
Beam-matter interactions inside collimators
Optimization by coupling simulations
  Multi-stage collimation
  Collimator: location, gap, length, quantity, material, deposition, taper
  Impedance budget (nonlinear collimators also provide a way to reduce the impedance)
  Movable collimators

## Slide 7
Motivation
Method for simulation studies
Preliminary arrangement of the global collimators
Current simulation studies
Summary

## Slide 8: Preliminary arrangement of the global collimators
CEPC collimation system
Collimator type
Betatron collimators - high beta function
Momentum collimators - high dispersion function
Dedicated collimators with the phase advance of 
SR collimators near IPs
Arrangement
Only single stage collimators for the preliminary design
~50 collimators are inserted into the collider ring
Collimators are inserted both near IPs, RF region, injection/extraction region
All the collimators in the drift sections

## Slide 9: CEPC aperture model
Finding the momentum acceptance and beam stay clear region will allow us to identify the loss locations and the bottlenecks
The bottlenecks must be protected
Beam loss near IPs can cause the background
Quench risk for RF
Quench risk for SCQ
The momentum acceptance
The beam-stay-clear region
Geometry aperture
Beta functions

## Slide 10
Motivation
Method for simulation studies
Preliminary arrangement of the global collimators
Current simulation studies
Summary

## Slide 11: Current studies
CEPC beam loss
Scenarios of the fast equipment failures
  Critical RF failures
  Quenches of superconducting quadrupole magnets
  Powering failures of normal magnets
    bending magnets
    quadrupole magnets
    sextupole magnets
Failure model:
One turn for CEPC ~ 331 𝝁𝒔
for the magnet failures in our simulations
J.Y Zhai
Y.S Zhu
B. Chen

## Slide 12: Critical RF failures
Very fast beam loss can be observed
Clean IP regions with the collimation system
Clean RF regions with the collimation system
Beam loss turn
Beam loss location
0.79%
4.45%
Without collimators
With collimators
Beam loss turn
Beam loss location

## Slide 13: Failures of bending magnets
Beam loss in IP region can be observed
Clean RF regions
Risk for the SCQs
Beam loss turn
0.61%
2.17%
Beam loss location

## Slide 14: Failures of normal quadrupole magnets
Clean RF regions and IP regions
Tight gaps of collimators
Beam loss turn
Beam loss location

## Slide 15: Quenches of SCQs
Very fast beam loss can be observed
Clean IP regions and RF regions
Risk for the collimator tolerance
Beam loss turn
Beam loss location

## Slide 16: Failures of sextupole magnets
Beam loss in IP region can be observed
Clean RF regions
Risk for the SCQs
0.79%
2.67%
Beam loss turn
Beam loss location

## Slide 17: Challenge
Failure cases: bending magnets (A) and sextupole magnets (B)
Beam loss in IP regions
Risk for the SCQ both in conditions of bending and sextupole magnets
High vertical beta function and small pipe size
Dedicated collimators are required (eg. phase advance of )
Further study is required
Layout of the quadrupole in IP
IP1
IP3
IP1
IP3
(A)
(B)

## Slide 18: Coupling simulations
Collimator: toy model
Geometry: like HEPS Coll.
  Two layer: Copper + Carbon
  Gap: 6mm
  Thickness of carbon: 2mm
Beam loss record in collimator
  RF failure
  RF region, downstream IP1
Mechanical structure of the collimator
Collimator model in FLUKA
G.Y. Tang and H.J. Wang

## Slide 19: Particles back to SAD
FLUKA
Selection
SAD simulation
Energy acceptance: 1.7%
Selection:
Energy Acceptance: 1.7%
Horizontal beam:
Vertical beam:
Collimator
Collimator
26053 m

## Slide 20: Summary
Methods for the collimation simulation study
  SAD+FLUKA coupling
The preliminary collimation system is studied
Particle simulations
  Powering failures of the magnets, quenches of SCQs and RF are studies
  Very fast beam loss can be observed in some scenarios
  After the beam-matter interaction, the secondary particles may transfer very long

## Slide 21: Next step
SAD simulations
Different scenarios
  Optimum/acceptable/particular operating conditions:
    Beam halo/tails, Top-up injection
    Change of optics, tuning, collimator aperture setting, etc
  Fast beam loss
    Standard equipment failure, fast equipment, other accident beam loss, etc
    Injection failure, SuperKEK fast beam loss (should be understand if possible)
  Different operation modes
    Higgs, Z, W, ttbar
FLUKA simulations
Beam-matter interactions
Optimization by coupling simulations
  Multi-stage collimation
  Collimator: location, gap, length, quantity, material, deposition, taper
  Impedance budget (nonlinear collimators also provide a way to reduce the impedance)
  Movable collimators

## Slide 22
Thank you

## Slide 23
Backup

## Slide 24
The complexity of the collimation system
[2] DOI:10.1103/PhysRevAccelBeams.23.053501
SuperKEKB
[1] https://inspirehep.net/literature/727805
LHC

## Slide 25
Effects such as synchrotron radiation and optics tapering are required
Details of tapering in BMAD still under study [2]
Tapering: modulating the magnetic strengths around the ring to account for SR energy loss
Lattice translation between accelerator simulation codes[3]
[1] https://kds.kek.jp/event/44647/
[2] https://indico.cern.ch/event/1015718/
[3] https://conference-indico.kek.jp/event/75/