## Slide 1
CEPC LINAC COST
Cai MENG
16. Aug. 2023, Beijing, CEPC Accelerator TDR Cost Review

## Slide 2: Content
Parameters and layout of the CEPC Linac
Cost of the CEPC Linac
  Linac
  Damping Ring
Summary

## Slide 3
Design Parameters / Requirement List
Bunch spacing is 69.2 ns
Parameter | Symbol | Unit | Baseline
Energy | Ee-/Ee+ | GeV | 30
Repetition rate | frep | Hz | 100
Bunch number per pulse |  |  | 1 or 2
Bunch charge |  | nC | 1.5 (3)
Energy spread | σE |  | 1.5×10-3
Emittance | εr | nm | 6.5

## Slide 4: Introduction: ：Layout of the CEPC Linac
Layout
  The tunnel is 1.8km
  The circumference of the damping ring is 147m

## Slide 5: Hardware systems (1)
Power source | 
S-band power source (number, power, frequency) | 34, 80MW, 2860MHz
C-band power source (number, power, frequency) | 236, 50MW, 5720MHz
Solid-state power source (number, power, frequency) | 1, 20kW, 158.89MHz
 | 1, 20kW, 476.67MHz
Accelerating structure | 
Large-aperture S-band accelerating structure (number, gradient, length) | 16, 22MV/m, 2.0m
Normal S-band accelerating structure (number, gradient, length) | 8, 27MV/m, 3.1m
 | 85, 22MV/m, 3.1m
C-band accelerating structure (number, gradient, length) | 470, 40~45MV/m, 1.8m
Subharmonic buncher (number, voltage, length) | 1, 10 kV, 0.8m
 | 1, 120kV, 0.5m
C-band deflecting cavity (number, voltage, length) | 1, 20MV, 1.8m

## Slide 6: Hardware systems (2)
Electron and positron beam switching time within 3.5s
  Magnet power supply switching within 3 s
Magnet |  | PS
Solenoid (number, aperture, field, length) | 4, 90mm, 400Gs, 80mm | 4
 | 17, 210mm, 800Gs, 110mm | 17
 | 1, 118mm, 600Gs, 80mm | 1
 | 15, 400mm, 0.5T, 1m | 15
Quadrupole (number, aperture, gradient, length) | 22, 34mm, 22T/m, 100mm | 11
 | 87, 34mm, 24T/m, 200mm | 49
 | 44, 34mm, 26T/m, 400mm | 44
 | 104, 24mm, 50T/m, 300mm | 52
 | 52, 24mm, 50T/m, 600mm | 52
 | 6, 60mm, 10T/m, 100mm | 3
 | 3, 60mm, 10T/m, 200mm | 3
 | 36, 150mm, 7.9T/m, 300mm | 18
 | 18, 150mm, 7.9T/m, 600mm | 18
Dipole (number, gap, field, length) | 1, 35mm, 0.33T, 262mm | 1
 | 4, 24mm, 1.0T, 5.847m, bidirectional power supply | 4
 | 5, 60mm, 0.42T, 698mm, bidirectional power supply, switching within 3s | 5
 | 5, 35mm, 1.0T, 698mm | 5
 | 4, 35mm, 1.0T, 1.047m, power supply switching within 3s, vertical bending | 4
Corrector (number, gap, field, length) | 1, 50mm, 10Gs, 30mm | 2
 | 1, 136mm, 50Gs, 400mm | 2
 | 25, 150mm, 50Gs, 100mm | 50
 | 2, 50mm, 10 Gs, 24mm | 2
 | 100, 34mm, 450Gs, 100mm | 100
 | 146, 24mm, 0.25T, 200mm | 146

## Slide 7: Hardware systems (3)
Beam position, beam profile, bunch charge
7 energy analyzing station (7 beam dump), not included in cost
Beam diagnostics | 
BPM (number, aperture, resolution, length) | 150, 30/20mm, 10μm, 0.2m
ICT (number, aperture, length) | 63, 35mm, 40mm
PR (number, aperture, resolution, length) | 30, 35mm, 20μm, 0.3m
Beam dump | 
Number, energy, beam size, bunch charge, repetition rate | 1, 60MeV, 2mm*1mm, 10nC, 1Hz
 | 1, 4GeV, 0.5mm*0.5mm, 10nC, 1Hz
 | 1, 250MeV, 1.5mm*1.5mm, 5nC, 1Hz
 | 1, 1.1GeV, 0.5mm*0.5mm, 5nC, 1Hz
 | 1, 6GeV, 0.5mm*0.3mm, 3nC, 1Hz
 | 2, 30GeV, 0.3mm*0.3mm, 3nC, 1Hz
 | 1, 250MeV, 1.5mm*1.5mm, 5nC, 100Hz

## Slide 8: Hardware systems (4)
Damping ring
Name | Type | Number | Length (m) | Value
B0 | dipole | 40 | 0.7 | Gap 38 mm, Field 1.3 T
Br | dipole | 40 | 0.248 | Gap 38 mm, Field 1.3 T
Qarc | quadrupole | 96 | 0.2 | Gap 44 mm, Field 17 T/m
QRF | quadrupole | 8 | 0.2 | Gap 38 mm, Field 30 T/m
SF | sextupole | 36 | 0.1 | Gap 38 mm, Field 94 T/m2
SD | sextupole | 36 | 0.1 | Gap 38 mm, Field 140 T/m2
CORR | corrector | 60 | 0.07 | Gap 40 mm, Field 20 Gs
DRLAM | Lambertson | 2 | 0.5 | Field 0.88 T
DRkicker | kicker | 2 | 1.4 | Field 0.028 T
MBPM | BPM | 40 | 0.1 | Button BPM, Resolution 20µm @ 5mA
RFC | cavity | 2 | 1.4 | 650MHz, 1.25MV/cavity

## Slide 9: Cost：Linac
总造价(RMB)
  18.33亿元
System | Components | Number | Unit Cost | Cost | Total Cost
 |  |  | （10,000￥） |  | （10,000￥）
RF system | Electron Source | 1 | 310.00 | 310.0 | 68245.6
 | Positron Source | 1 | 470.00 | 470.0 | 
 | S-band RF | 34 | 387.28 | 13167.6 | 
 | C-band RF | 236 | 230.08 | 54298.0 | 
RF power source | S-band PS | 34 | 335.00 | 11390.0 | 81010.0
 | C-band PS | 236 | 295.00 | 69620.0 | 
Magnets | Solenoid | 37 |  | 499.0 | 4338.0
 | Dipole | 19 |  | 344.0 | 
 | Quadrupole | 372 |  | 2577.0 | 
 | Corrector | 275 |  | 618.0 | 
 | Field measurement devices | 2 | 150.00 | 300.0 | 
Magnet power supplies | Power supply | 583 |  | 1596.6 | 2069.3
 | Cable （m） | 59200 |  | 256.7 | 
 | DCCT | 610 |  | 150.0 | 
 | Equipment Cabinet | 110 | 0.60 | 66.0 | 
Vacuum system |  |  |  | 14736.4 | 14736.4
Instrumentation | BPM | 150 | 13.00 | 1950.0 | 5010.0
 | ICT | 63 | 40.00 | 2520.0 | 
 | PR | 30 | 18.00 | 540.0 | 
Control system |  |  |  | 5287.0 | 5287.0
Mechanical systems | Vacuum device support | 5589 |  | 804.6 | 2602.5
 | Support | 968 |  | 1797.9 | 
 |  |  |  |  | 183298.8
CDR 9.33亿

## Slide 10: Cost: Damping ring
总造价
  0.583亿元
Components | Type | Number | Unit Price | Price | Total price
Magnets | Dipoles | 80 | 6/4 | 400 | 1528.0
 | Quadrupoles | 104 | 5 | 520 | 
 | Sextupoles | 72 | 4 | 288 | 
 | Correctors | 60 | 2 | 120 | 
 | Field meas. devices | 2 | 100 | 200 | 
Vacuum | Beam pipe | 150 | 0.4 | 60 | 707.5
 | Bellows | 75 | 1.5 | 112.5 | 
 | Ion pump | 100 | 1.5 | 150 | 
 | Molecular pump | 2 | 10 | 20 | 
 | Gate valve | 10 | 0.5 | 5 | 
 | Roughing valve | 25 | 2 | 50 | 
 | Gauge/Residual gas analyzer/Assembly | 8/8/1 | 10/10/150 | 310 | 
Mechanical supports | Dipole support | 80 | 1.5/1.0 | 100 | 320.0
 | Quadrupole support | 104 | 1.8/1.0 | 162 | 
 | Vacuum support/BI support | 335/41 | 0.08/0.2/0.15 | 58 | 
Beam Instrumentation | Beam position monitor | 40 | 13 | 520 | 760.0
 | Average beam current monitor (DCCT) | 1 | 70 | 70 | 
 | Tune measurement | 1 | 170 | 170 | 
RF | Cavity/Waveguide/LLRF/Vacuum | 2 | 350/90/40/45 | 700/180/80/90 | 1050.0
RF Power Source | Solid state amplifier | 2 | 175 | 350 | 350.0
Power Supplies | PS/Cable/DCCT/Cabinet |  |  |  | 444.5
Control |  |  |  |  | 456.0
Injection & Extraction | Kicker/Septum/Field Measurement | 2/2/1 |  | 212.6 | 212.6
 |  |  |  |  | 5828.6

## Slide 11: Cost: Linac + Damping ring
总造价
  18.91亿元
Components | LINAC | DR | Total
 |  |  | （10,000￥）
RF system | 68245.6 | 1050.0 | 69295.6
RF power source | 81010.0 | 350.0 | 81360.0
Magnets | 4338.0 | 1528.0 | 5866.0
Magnet power supplies | 2069.3 | 444.5 | 2513.8
Vacuum system | 14736.4 | 707.5 | 15443.9
Instrumentation | 5010.0 | 760.0 | 5770.0
Control system | 5287.0 | 456.0 | 5743.0
Mechanical systems | 2602.5 | 320.0 | 2922.5
Injection & Extraction | 0.0 | 212.6 | 212.6
 | 183298.8 | 5828.6 | 189127.4
CDR 9.33亿

## Slide 12: Summary
The total cost of the Linac, including the damping ring but not including the transport line between the Linac and DR, is 1.891 billion RMB.

## Slide 13
Thank you for your attention!

## Slide 14
Components | LINAC | DR | Total | CDR | 
RF system | 68245.6 | 1050.0 | 69295.6 | 35564 | 33731.6
RF power source | 81010.0 | 350.0 | 81360.0 | 32190.0 | 49170.0
Magnets | 4338.0 | 1528.0 | 5866.0 | 2597 | 3269
Magnet power supplies | 2069.3 | 444.5 | 2513.8 | 2050.0 | 463.8
Vacuum system | 14736.4 | 707.5 | 15443.9 | 6380 | 9063.9
Instrumentation | 5010.0 | 760.0 | 5770.0 | 6400.0 | -630.0
Control system | 5287.0 | 456.0 | 5743.0 | 5793 | -50
Mechanical systems | 2602.5 | 320.0 | 2922.5 | 1307.0 | 1615.5
Injection & Extraction | 0.0 | 212.6 | 212.6 | 0 | 212.6
 | 183298.8 | 5828.6 | 189127.4 | 92281.0 | 96846.4

## Slide 15: Cost: Linac + Damping ring + TL
Total
  19.05亿
Components | LINAC | DR | TL | Total
RF system | 68245.6 | 1050.0 |  | 69295.6
RF power source | 81010.0 | 350.0 |  | 81360.0
Magnets | 4338.0 | 1528.0 | 532.0 | 6398.0
Magnet power supplies | 2069.3 | 444.5 | 352.4 | 2866.3
Vacuum system | 14736.4 | 707.5 | 228.4 | 15672.3
Instrumentation | 5010.0 | 760.0 | 96.0 | 5866.0
Control system | 5287.0 | 456.0 |  | 5743.0
Mechanical systems | 2602.5 | 320.0 | 122.2 | 3044.7
Injection & Extraction | 0.0 | 212.6 |  | 212.6
 | 183298.8 | 5828.6 | 1331.0 | 190458.4

## Slide 18
RF power source (Ch 6.5.2) |  |  |  |  | 81010
Klystron | 2860MHz/80MW | SET | 34 | 120 | 4080
Modulator | 400kV/500A | SET | 34 | 180 | 6120
Load and auxiliary power supply |  | SET | 34 | 20 | 680
Klystron gain amplifier | 2860MHz/1000W | SET | 34 | 15 | 510
Klystron | 5720MHz/50MW | SET | 236 | 110 | 25960
Modulator | 350kV/400A | SET | 236 | 150 | 35400
Load and auxiliary power supply |  | SET | 236 | 20 | 4720
Klystron gain amplifier | 5720MHz/1000W | SET | 236 | 15 | 3540

## Slide 22
 |  |  |  | CDR |  |  |  | TDR |  |  |  | TDR-CDR | 
No. | Classification | Device | Unit | Specification | Quantity | Unit price / (CNY 10,000) | total Price / (CNY 10,000) | Specification | Quantity | Unit price / (CNY 10,000) | total Price / (CNY 10,000) | / (CNY 10,000) | Note
31 | LINAC | Beam pipe | m | 304 | 1500 | 0.2 | 300 | 316L | 931 | 0.3 | 279.3 | -21 | 磁导率：1.02～1.05，磁铁内1.02，个别1.05
32 |  | Manifold for SIP | one |  | / |  |  | 316L | 3431 | 0.3 | 1029.3 | 1029 | CDR是含在真空盒中
33 |  | Manifold for Gauge & RGA | one |  | / |  |  | 316L | 1352 | 0.3 | 405.6 | 406 | CDR是含在真空盒中
 |  | Manifold for Gauge & RGA | one |  | / |  |  | 316L | 1352 | 0.3 | 405.6 | 406 | CDR是含在真空盒中
34 |  | Bellows | one | 304 | 1760 | 0.3 | 528 | 316L | 4094 | 0.3 | 1228.2 | 700 | 
35 |  | Sputtering Ion pump | one | 100L/s | 1310 | 2 | 2620 | 100L/s | 3431 | 2 | 6862 | 4242 | 数量考虑了波导、束调管、能量倍增器等的需求
36 |  | Molecular pump | one | 400L/s | 10 | 10 | 100 | 400L/s | 10 | 10 | 100 | 0 | 
37 |  | Gate valve | one | CF40 | 30 | 15 | 450 | CF40 | 30 | 15 | 450 | 0 | 
38 |  | Gate valve | one | CF25 | / |  |  | CF25 | 30 | 15 | 450 | 450 | 
39 |  | Roughing valve | one | CF63 | 90 | 1 | 90 | CF63 | 178 | 1 | 178 | 88 | VAT进口阀门
40 |  | Vacuum gauge | one | CCG | 611 | 2 | 1222 | CCG | 1352 | 2 | 2704 | 1482 | 数量考虑了波导、束调管、能量倍增器等的需求
41 |  | Residual gas analyzer | one | RGA | 10 | 10 | 100 | RGA | 10 | 10 | 100 | 0 | 
42 |  | Helium leak detector | one | He | 5 | 30 | 150 | He | 5 | 30 | 150 | 0 | 
43 |  | Vacuum connectors | one |  | 1 | 300 | 300 |  | 1 | 600 | 600 | 300 | 
44 |  | Vacuum heating | one |  | 1 | 50 | 50 |  | 1 | 50 | 50 | 0 | 
45 |  | Vacuum control | one |  | 1 | 100 | 100 |  | 1 | 100 | 100 | 0 | 
46 |  | Vacuum cleaning | one |  | 1 | 50 | 50 |  | 1 | 50 | 50 | 0 | 
 |  | Total |  |  |  |  | 6060 |  |  |  | 14736.4 | 8676 | 能量增加20GeV